## Slide 1: SNS Ring TiN Coating Experience
CERN Anti E-Cloud Coating Workshop
Oct 12-13, 2009
by
M. Plum,
Ring Area Manager

## Slide 2: SNS Accelerator Complex
Front-End:
Produce a 1-msec long, chopped, H- beam
1 GeV LINAC
Accumulator Ring: Compress 1 msec long pulse to 700 nsec
2.5 MeV
LINAC
Front-End
Accumulator Ring
RTBT
HEBT
Injection
Extraction
RF
Collimators
945 ns
1 ms macropulse
Current
mini-pulse
Chopper system makes gaps
Current
1ms
Liquid Hg Target
1000 MeV

## Slide 3: Beam power ramp up
October 1, 2006 to October 5, 2009
Status:
    Production beam with up to ~1.1e14 ppp (18 uC).
    Full design intensity demonstrated at 1 Hz.

## Slide 4
The SNS Accumulator Ring
e-p mitigating features at SNS:
Vacuum chambers coated with TiN to reduce secondary electron yield
Solenoids in the collimation region
Clearing electrode near the stripper foil
BPMs can be biased to use as clearing electrodes
Robust dual harmonic RF system which can help keep the gap clean
Beam in gap kicker
Active damping system
Design ring parameters:
1 GeV beam
Intensity: 1.51014 ppp (24 uC)
Working point (6.23,6.20)
Ring circumference – 248 m
Space charge tune shift – 0.15

## Slide 5: Status of electron control and measurement in the SNS Ring
All vacuum chambers TiN coated except:
  ~7.1 m in RF straight for IPM and electron beam profile monitor development
  ~2.2 m in collimation straight for active damping system development
  ~2 m in vicinity of primary stripper foil, due to Al over-coating
Clearing electrode by primary foil
  Powered for first time on Oct. 6, 2009
Solenoid winding in collimation straight
  Not powered

## Slide 6: Status of electron control and measurement in the SNS Ring (cont.)
BPM electrodes that can be biased
  Present electronics do not allow biasing
Beam in gap kicker system
  Not installed
Active damping system
  Under development
RFA electron detectors
  Have some very preliminary data

## Slide 7
Hseuh et al., Ecloud04 workshop

## Slide 8
Example of e-p instability data
gap
high freq. oscillation
near tail of bunch
700 turns
gap
BPM sum
BPM signal (mm)
(From S. Cousineau et al., HB2008)

## Slide 9
Instability frequency: 60 – 100 MHz.
Vertical preceded horizontal by ~200 turns.
Example of instability frequency
Horizontal
Vertical
(From S. Cousineau et al., HB2008)

## Slide 10: Summary of 2008 e-p data
(From S. Cousineau et al., HB2008)

## Slide 11: Experiment vs theory
Measurements show that the e-p instability is present at charge intensities as low as 3e13 ppp (one fifth full design intensity, 24 kV of h=1 and 16 kV of h=2 RF)
On one occasion so far at full design intensity (1.5e14 ppp), measurements showed that instability can be controlled with Ring RF. (42 kV of h=1, 20 kV of h=2 RF).
Note that ~4.6% of Ring is uncoated.
Based on analytical and computational studies, and comparisons with LANL’s PSR, with no TiN coating
  Stable up to 2e14 ppp for h=1 RF of 15 kV [Blaskiewicz et al., PRSTAB 2003]
Computational simulation including effects of TiN coating
  Stable up to 2e14 ppp for h=1 RF of 13 kV [Shishlo et al., EPAC06]

## Slide 12: SEY of st. steel and TiN vs. scrubbing
 | SEYmax of TiN | SEYmax of St. St.
Unscrubbed | 2.2 | 1.8
Scrubbed | 1.05 | 1.1
Copied from M. Nishiwaki and S. Kato, ECLOUD’07
SNS Ring beam pipes are 316L or 316LN stainless steel, bellows are Inconel 625

## Slide 13: TiN summary
With ~95.4% of our ring coated with TiN, we have seen the instability at about one fifth of design intensity
Theory predicts no e-p instability up to 30% greater than design intensity
PSR experience: TiN coatings sometimes help, sometimes not until after scrubbing [R. Macek et al., ECLOUD ’04 & PAC03]
SNS vacuum chambers were exposed to air for months prior to installation, so our TiN started out unscrubbed, and may still be unscrubbed
Secondary emission yields of stainless steel and TiN seem to be about the same, before and after scrubbing
Is TiN coated stainless steel really better than just plain stainless steel?

## Slide 14: Future plans
Continue to develop active damping system
  400 W, 3 to 300 MHz, each plane
Complete purchase of TiN coating system
  $339k from Kurt J Lesker Co., due ~Jan. 2010
Continue to get all chambers TiN coated
Continue to develop diagnostics and characterize electrons in ring
  RFA electron detectors
  Microwave plasma measurements
Determine effectiveness of TiN coating

## Slide 15: Electrons in vicinity of stripper foil
Convoy electrons from a 1 GeV H− beam have 545 keV energy, gyroradius 12 mm, period 0.29 ns, pitch 16-23 mm. Center of circular motion moves ~14 mm downstream and ~5 mm beam left. Electrons are collected in an “electron catcher”. A 1 MW beam has ~1 kW power in the convoy electrons.

## Slide 16: Electron catcher and clearing electrode
Water cooled carbon-carbon wedges
Undercut prevents secondary electrons from escaping
+/-20 kV biasing system
Inlet and outlet water cooling lines have thermocouples, read out by EPICS and archived

## Slide 17: Electron catcher boroscope image
Al coating
Electron impact

## Slide 18: Graphitization at top of vacuum chamber
152 mm
~24 mm
Could be reflected convoy electrons or trailing-edge multipactoring
Clearing electrode

## Slide 19: Summary
e-p instablility is present in SNS ring at intensities as low as 3e13 ppp (one-fifth design intensity). Theoretical work prior to commissioning predicted no e-p instability up to 30% greater than the design intensity.
e-p instability can be controlled with ring RF system up to full design intensity of 1.5e14 ppp (one time only)
Results from TiN coating are mixed – is it really better than just stainless steel? Note that ring still has ~11.3 m (4.6%) with no TiN coating.
Attempting to coat everything with TiN has been expensive and has caused installation delays. It will be interesting to determine if it has been worth it.

## Slide 20
Thank you for your attention!

## Slide 21
Backup slides

## Slide 22: SNS injection schematic
Closed orbit bump of about 100 mm
Merge H- and circulating beams with zero relative angle
Place foil in 2.5 kG field and keep chicane #3 peak field <2.4 kG for H0 excited states
Field tilt [arctan(By/Bz)] >65 mrad to keep electrons off foil
Funnel stripped electrons down to electron catcher
Direct H- and H0 waste beams to IDmp beam line

## Slide 23: Graphitization
Example of graphitization by multipacting electrons in SRBM11 at PSR. This is not a thermal effect!
(R. Macek, HB2008 & private comm.)