## Slide 1: A CCC for ELENA
Jocelyn TAN (BE-BI)
With the contributions of my BI and CRG colleagues
26th April 2017
GSI & Jena Visit at CERN

## Slide 2: Agenda
Recap on ELENA
Proposal for a CCC
Cost and timeline
Summary

## Slide 3: ELENA for experiment efficiency improvement
ELENA parameters | 
Circumference (1/6 of AD) | 30.4m
Triplet-based optics | 6-fold layout
Machine tunes h/v | 2.3 / 1.3
Ekin range | 5.3 MeV – 100 keV
Relativistic  | 0.11 – 0.01
Nbunches at extraction | 4
Bunch length at extraction | 75 ns (rms)
Factors considered in the synchrotron design
Space constraints: in AD hall
e-cooler: get space + small dispersion
Tune: keep  away from resonances
Bucket to bucket beam transfer from AD
Possibility of a second extraction line

## Slide 4: Facility overview and layout
Transfer line
(magnetic)from AD
Electro-static line towards existing experimental area
Extraction towards new experimental area
External source for commissioning
Courtesy: C. Carli

## Slide 5: ELENA Cycle
eh,v = 15 p mm mrad
DP/P = 1x10-3
eh,v [95%]= 6/4 p mm mrad
DP/P = 2x10-4
Lbunch (max) = 1.3 m
Cycle length about 20 seconds
ELENA parameters | 
Ekin range | 5.3 MeV – 100 keV
Frev | 1.1 MHz – 100 kHz
Total Nparticles | 3 – 1.8 x 107
DC current range | 5.2… 0.3 A
Beam aperture | 63 mm

## Slide 6: Steps for instrumentation upgrade
Phase1: Two LPUs, scaled down from AD system
  Commissioning, LLRF, beam intensity, tomography
  Combined 4 decade BW = [3kHz - 30MHz]
  Ferrites, bakeable
Phase2: Equivalent of a “large Schottky PU”
  Superposition of 20 BPMs signals : LLRF, dp/p, intensity
Phase3: A CCC instead of LPUs (if poor performances). But feasibility study should start now.

## Slide 7: AD Cryostat: Starting point
1032
840
Pulse tube
+ He hose
Safety valves
Instrumentation
+ vacuum equip.
Courtesy: A. LEES

## Slide 8: AD cryostat: Work during winter 2015-16
A lot of effort from CRG was put to optimise the CCC sub-assemblies
  MLI completely renewed: no gaps where 300K surface and 4K surface could see one another
  Solution for Ti-rod supports : machined to smaller cross section and MLI insulation
  Beam pipe => MLI on both sides at warm & cold surfaces
  No strain gauges and respective cabling on Ti-rods anymore
  All wiring was optimized for low heat load (eg with Manganin wires) for instrumentation.
  Cold test with LHe => evaporation rate after first cooldown =0.55W
  Upgrade of the reliquefier performance to =1.2W (was 0.93W in vendor’s config).

## Slide 9: ELENA cryostat: Hints to further improve performance
Reduce monitoring inside the cryostat  less wires
Better insulation between warm beam pipe and thermal shield : now 63mm beam aperture (100mm for AD)
Improve insulation vacuum: Reduce He diffusion through Al2O3 gaps (test of material…).
The use of 316L for the He Vessel would allow the use of standard components, helping to reduce cost and weight.
Increase cooling power: New Cryomech pulse tube PT420 provides 2W.
Would a more compact cryostat help in terms of heat in-leak ?
Synergy with GSI’s design ?

## Slide 10: Integration options
LPUs in Section 2
1.25m drift tube
in Section 1: near septum and kicker

## Slide 11: Section2: magnetic environment
697 mm
Quadrupole
Sextupole
Corrector dipole
Bending magnet
CCC
1087 mm
899 mm
1286 mm
1589 mm
1 m
Field from beam current:
  Aperture: 60 mm (now 63 mm)
  Distance: 54 mm
  Current: 5.2 … 0.3 μA
  Bθ field: 19.2 … 1.05 pT
Assuming:
  Infinitely straight current
  Calculated at mid-point between rinner and router of a CCC with dimensions proportional to that of GSI (rinner=69mm and router=112mm)
Quadrupole
Courtesy: M. Fernandes
Study performed in 2013

## Slide 12: Section2: magnetic environment
CCC region
QUAD-1
QUAD-2
DIP.-CORR.
CCC region
DIP.-CORR.
Transverse component
Longitudinal component
Only closest quadrupoles and dipole corrector simulations are available
Maximum magnetic field was considered
Field obtained in XZ plane at Y=0
In XZ-plane long. component of quadrupole field is zero (this should remain small in other longitudinal planes)
  |z|<300 mm → |Btrans|<50 µT
Courtesy: M. Fernandes
Study performed in 2013

## Slide 13: Section 2: CCC integration
LPU_A LPU_B
1035

## Slide 14: Cost breakdown: AD vs ELENA
Cryogenics parts | AD [kCHF] | ELENA [kCHF] | 
Cryo parts | 13 | 13 | 
Cryocooler | 79 | 79 | New PT420 with 2W cooling power !
Ceramic gaps + Ti coating | 23 | 16 | 1 spare of each only, instead of a pair
Ti rods with strain gauges | 46 | 34 | w/o strain gauges, 8weeks delivery instead of 4
CERN store | 137 | 45 | -33%: 316LN 316L
Cryogenics jobs | AD [kCHF] | ELENA [kCHF] | 
Design office | 51 | 5 | With slight changes (~100 h)
Vac. Test, cryo controls, He recovery line | 18 | 18 | Not much savings
Cryostat production and assembly | 273 | 150 | -30%: 316LN 316L, -15%: assembly
GRAND TOTAL | 888 | 608 | Swiss price EN13445 standard: Qualification of cold parts for pressure and vacuum operations
CCC & Acq chain | Cost [kCHF] | New cost [kCHF] | Comments
Niobium shielding + Core | 140 | 140 | If we keep the same monitor
SQUID & current generator | 26 | 26 | 
Cabling, network, electronics | 18 | 18 | 
Ring modifications | Cost [kCHF] | New cost [kCHF] | 
Vacuum sectorisation | 53 | 53 | ELENA: Not an official quotation from VSC group !
Chilled water, power supply, etc | 11 | 11 | 
340 kCHF: fixed expenses
548 kCHF  268 kCHF

## Slide 15: Options for cost reduction
Outsource the CCC production
We could benefit from series production for FAIR, assuming:
  GSI’s CCC is compatible with standalone operation,
  both ELENA and FAIR installation planning are in phase (2021?)
NB: not an official planning. Transfer line installation might take place in 2020

## Slide 16: Summary
New CCC project in a lower-constrained time scale than with AD
Risk mitigation with high production EN 13445 standard
ELENA’s CCC is 30% cheaper, yet still an expensive device.
Hidden cost: expertise and support of CRG group
  Conceptual design
  Tests and commissioning
  Risk analysis
  Helium supply
Open point: future collaboration with GSI and Jena

## Slide 17: Acknowledgement
I’m grateful to my colleagues who helped me for preparing this talk, namely:
Miguel Fernandes
Lars Soby
Gerard Tranquille
Rhodri Jones
Torsten Koettig
Andrew Lees