## Slide 1: Layout and lifecycle
26/4/16
A. Vamvakas
for the TBM team

## Slide 2: Outline
Reminder of possible alignment options
Assumptions and evaluation
4 proposed permutations

## Slide 3: Longitudinal options
Girder
Component
(SAS, DBQ, etc)
Component
(SAS, DBQ, etc)
WPS
WPS
Girder
Component
(SAS, DBQ, etc)
Component
(SAS, DBQ, etc)
WPS
WPS
Girder (just for transportation)
Component
(SAS, DBQ, etc)
Component
(SAS, DBQ, etc)
WPS
WPS
Active
Active
Active
Passive
Passive
Rigid support
  Withstands transportation
  No re-alignment needed
Adjustable support
  Tunnel based adjustment
  Passive adjustability
  Requires metrology equipment
Independent support
  Actuated support
  Active (remote) alignment
3/3/17

## Slide 4: Girder options
Full common girder
‘RF’ girder
Independent beams
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS

## Slide 5: Too many options
All the mentioned strategies can be mixed
  3x3
Different approaches can be used for the two beams
  (3x3)2
Some are automatically excluded
Total possible solutions >30
Need to narrow down

## Slide 6: Assumptions
380 GeV
T1-T2 dominant
DB:
  More than 2m long not possible
  Independent DBQ might be preferable
  Snake possible
MB:
  Max length 2m (MBQ too frequent for other configurations)
  Min length 1m
  No snake (MBQ too frequent)
RF units assembled before conditioning (28/10/16)

## Slide 7: Evaluation
Criteria:
Tolerances
Number of parts
Number of assembly steps/difficulty
Suitability for conditioning
Transportation robustness
Tunnel installation effort
Temperature sensitivity
Maintainability

## Slide 8: 2m girder – rigid
CDR approach
Components fixed on 2m girders
  10μm precision
Robust for transportation
  LHC -> 0.5g max acceleration load
V-supports need revisiting
  Not repeatable
  Fixed method needed (brazing, welding, etc)
No solution for DBQ yet
actuators
Transportation test under way to verify

## Slide 9: 2m girder – adjustable
2m girders
Everything is on adjustable supports
Final alignment in the tunnel
Effort for tunnel adjustment to be studied
  Feasibility is ok (PACMAN)
  How long does it take?
  How much can it be automated?
actuators
adjustable
Design of an adjustable support under way

## Slide 10: Common RF girder
All RF components on a fixed support
  1m long, Lightweight
  Independently supported
  Used as manufacturing/conditioning jig
  Longitudinal positioning/phasing not a problem
Each DBQ is independent
  Two beams cannot be coupled (X.Meng presentation)
Small, robust components
  Easy installation in the tunnel
High number of movers
  Initial study shows not an issue (3/3/17)
actuators

## Slide 11: Independent Beams
1m long AS block with its own support
PETS are supported by adjacent DBQ
  Relaxed tolerances for PETS allow for it
Snake possible for DB
10μm
actuators
100μm
1m unit
1m unit

## Slide 12: Summary
All are feasible in principle, but need detailed studying
Studying those contains all information
  still possible to revert to other combinations
Main considerations for comparison:
  Possibility of rigid transportation
  Effort (cost/time) of realignment in the tunnel
  RF phasing
  Cost of actuators/controls
  T1-T2 compatibility
  Overall lifecycle considerations
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
PETS
DBQ
2x SAS
Rigid
Adjustable