## Slide 1: The CELESTA 1U CubeSat Project Design and Status
Raffaello Secondo
10th May 2017
CERN – ESA Meeting

## Slide 2
CELESTA: CERN Latchup Experiment and STudent sAtellite
The scientific Payload of the first CERN-driven Small Satellite.
Why CELESTA? - Mission GOALS
CubeSat-Payload version of the CERN RadMon V6.
Nanosatellites radiation qualification procedure at CHARM.
Comparison of radiation effects between LEO space environment and CHARM.
SRAM Latch-up Experiment: Compare radiation levels between equator and poles.
Test the ROBUSTA platform.

## Slide 3: Workplan
Two Low Earth Orbits (LEO) proposed:
  Circular: 600 km x 600 km Perigee/Apogee.
  Elliptical 300 km x 1200 km Perigee/Apogee.
Simulations: STELA + OMERE + CREME.
SEU Prediction  (SRAM CY62157EV30): 2500 SEU circular orbit 14000 SEU elliptical.
Comparison with CHARM Environment
TID: 84 Gy.
Total Fluence (HEH>20 MeV): order of 1010 HEH/cm2 , elliptical.
Impact of radiation on a given orbit
STEP 1
Prototype Boards.
Characterization of sensors and full system at CHARM.
Design of Final Payload.
Feasibility Study – Mission Constraints
STEP 2
3D Model - FASTRAD
STEP 3

## Slide 4: Mission Analysis

## Slide 5: CERN Payload: Selection of COTS – Testing Effort
CHARM: Cern High Energy AcceleRator MixedField/Facility
The PSI-PIF Irradiation Area
PSI:
Focused Mono-energetic proton beam.
COTS Characterization.
CHARM:
Mixed-particle field
Testing at System Level
Representative radiation fields

## Slide 6: First Feasibility test
FIRST PROTOTYPE test board
SEU: Cypress SRAM CY62157EV.
Dose: Tyndall RadFet 100 nm.
Latchup Experiment: Brilliance SRAM BS62LV1600EIP.
UART communication using MODBUS protocol.
COTS selected in terms of TID, SEE and temperature (-20 to 80)

## Slide 7: SEL SRAM Characterization
test locations
CHARM position: 4
CHARM position: G0
Simple Power Supply control.
Commercial equipments: GUARD
CERN LatMon: 2µs sampling period, fast recovery of current profiles.

## Slide 8: COTS Tests and Selection
Mission Analysis and first test on a prototype board
SEL characterization
Tests on candidates COTS at PSI (ADC, Voltage regs, opamps…)
CAN transceiver

## Slide 9: The Payload
Mass: 52 g.
Modular: “Mother Board” + Mezzanine.
180 mW average power.
300 mW peak power.
ROBUSTA compatible, CAN compatible.

## Slide 10: Test at CHARM

## Slide 11: Snapshot of Sensors Results

## Slide 12: CSU Facilities
Mechanical and thermal tests
Integration analysis
Compliant with FYS

## Slide 13: Conclusions
Waiting for FYS approval.
Evaluating new sensors/upgrades (floating gates?)
Possible launch in 2019 ( according to FYS schedules eventually)