## Slide 1: Simulation of SEE with Sentaurus TCAD
Including an example on a very simple VDMOS model
Pablo Fernández Martínez
R2E/FDA Update Meeting
11th May 2017

## Slide 2
Outline
Introduction:
What TCAD Simulations are and how they work
Example:
Threshold LET of SEB in a power MOSFET
Conclusion:
What TCAD simulations can and what they can’t do for you

## Slide 3
Semiconductor Device Simulation (a.k.a. TCAD Simulation):
    Find the solution of the semiconductor equations for a model of a semiconductor device, under some specific boundary conditions, taking into account the solid state physics and by using numerical (Finite Difference / Finite Element) methods.
Boundary Conditions
Poisson:
Semiconductor
e Continuity:
h Continuity:
Drift-Diffusion
Formalism:
Drift
Diffusion
Alternative formalisms (less simplified):
  Thermodynamic: Including temperature
  Hydrodynamic: Taking into account Energy balance
Device Model
Structural:
  Dirchlet (space-charge neutrality on the contacts), Neumann (reflecting on the edge), etc..
Operational:
  Bias, Charges, etc…
Layout details:
  2D or 3D, full/partial model, etc…
Technological details:
  Materials, Doping profiles, etc…
Solid State Physics (Models)
Numerical models:
  Recombination (SRH, Auger…), Generation, Impact Ionization (Avalanche), High Field effects, Tunneling, Carrier Scattering, etc..
Semiconductor Equations
More details: W. Fichtner, et al. “Semiconductor Device Simulation”, IEEE TNS 30, 9, 1018-1030 (1983)

## Slide 4
Finite Element Technique: How to solve Partial Differential Equations (PDE) in a Computer
Discretization of the solution region into a finite number of elements
Setting the equations for a typical element (Test Functions)
Assembling all elements in the solution region (Variationals)
Solving the system of equations obtained (Iteration Solver: Newton, Bank-Rose, etc..)
Test Function
Test Function
in terms of finite
element vertex
values
Element Variational
(potential energy)
Total Energy
PDE Solution in discretized region
is the variational minimum
1
2
3
4
More details: R. Bank, et al. “Numerical Methods for Semiconductor Device Simulation”, IEEE TNS 30, 9, 1031-1041 (1983)

## Slide 5
How simulate the effects of Radiation:
Displacement Damage (cumulative effect):
  We include localized states (carrier traps) in the bandgap
    The Energy, trapping/detrapping Cross Section and Concentration of the carrier traps is correlated with the received Fluence
    Occasionally, some physical properties (e.g. carrier mobility or lifetime) can be also modified in correlation with Fluence.
Total Ionizing Dose (cumulative effect):
  We include Charge Densities in the semiconductor/dielectric Interface (or within the dielectric bulk)
    The Charge Concentration is correlated with the Total Absorbed Dose
    Very often, Interface states (carrier traps) can also be included. Their properties are also correlated with the Dose.
Single Event Effects (stochastic effect):
  We act on the physical model for the carrier Generation, including a Charge Distribution in a specific region of the semiconductor and then we simulate its evolution.
    The Charge Distribution Profile (amount of charge, length, width… ) is correlated with the incident radiation properties (LET, range, etc…)
    but the relationship is not calculated in the TCAD Simulation (we need the input from FLUKA or similar….)

## Slide 6
Reference example: A. Luu et al. “Sensitive volume and Triggering Criteria of SEB in Classic Planar VDMOS”, IEEE TNS 57, 4, 1900-1907 (2010)
2D
Half Cell
Sentaurus TCAD
Model
N/N++
transition
N+ Substrate
N- Epitaxy
Gaussian transition
P+
N+
P Body
Gate Oxide (100 nm)
Drain
Source
Gate
Refinement for the SEE
Parametrized position and shape
(can be displaced and redefined)
N+ source
P Body
N Epitaxy
N+ Substrate
Example:
(Silvaco TCAD model
would be quite similar)

## Slide 7
Simulation Flow:
1st Creation of the Structure
  With a proper refinement mesh for both the electrical and the SEE simulation
  Different particle positions require different mesh, i.e. different structure files
2nd Electrical Simulation
Initial electrical conditions: Vg = Vs = Vd = 0 V
Quasi-stationary ramp up to the target Vd (e.g. Vd = 500 V)
Final solution is save to be used in the next step
Current level is not quantitatively relevant
(only half of a 2D cell has been simulated)
Distributions of the Electric Field, Electrostatic Potential, Charge Carriers, Carrier Currents, etc… are saved in the final solution
500 V
480 V
420 V
380 V
320 V
260 V
180 V
460 V
100 V
0 V
Electrostatic
Potential

## Slide 8
Simulation Flow:
3rd Single Event Simulation
  Load the previous solution
    Bias conditions
    Electric field distribution, electrostatic potential, charge carriers density, etc…
Transient simulation (time is the running variable)
  Holding the same bias conditions on the electrodes
  At a given time (e.g. t = 4 ps), SE charge density is introduced
  For every time step, the simulation calculates the new situation:
    The new charge distribution, considering the boundary conditions at this precise time step
    The new boundary conditions, considering the charge distribution at this precise time step
HeavyIon (
Direction= (0,1)
Location= (@Xpart@, 0)
Time= 4.0e-12
Length= @Length@
Wt_hi= @rpart@
LET_f= @LET@
Gaussian
PicoCoulomb
)
Transient (
InitialTime=0 FinalTime=1e-8
InitialStep=1e-13 MaxStep=1e-10 MinStep=1e-15
Increment=1.3
)
{ Coupled { Poisson Electron Hole }
Plot ( Time= (1.0e-12; 4.0e-12; 5.0e-12)
}
(0,1) = perpendicular, downwards
e.g. (30,0) = located at x = 30 µm and the front surface (y = 0 µm)
HI charge density is introduced at t = 4 ps
e.g. 20 = HI range is 20 µm
e.g. 0.05 = HI with is 0.05 µm
e.g. 0.01 = LET is 0.01 pC/µm
The charge density has a lateral Gaussian profile (with Wt_hi the characteristic width)
LET is expressed in pC/µm, and distances in µm.
Time interval of the simulation (e.g. from t = 0 to t = 10 ns)
Parameters to modulate de size of the time steps
For each time step: Coupled calculation of Poisson equation and the Continuity equations for electrons and holes
- i.e. the new boundary conditions (Efield/potential), and the new carrier distribution
Save solutions at given t
(e.g. 1, 4 and 5 ps)

## Slide 9
Example:
Different @Length@ values (Range)
Different @LET@ values
LETth = 0.09 pC/um
1st Creation of the Structure
  X_part = 30 µm (SE position)
    r_part = 0.05 µm (characteristic width of the generated charge density)
3rd Single Event Simulation
2nd Electrical Simulation
  Vs = Vg = 0 V (fixed)
  Vd = 500 V (sweep from 0 to 500 V)
  Final solution saved
Transient
Simulation

## Slide 10
VDS = 500 V
We can fiddle with the parameters (VDS, Incidence X position, front or back incidence, etc…) to complete an study of the device sensitivity: sensitive volumes, worst cases, etc…
  See Luu 2010 paper on TNS
Results give a qualitative understanding of the matter. As we didn’t use an exact model for the structure (2D, half a cell, profiles not based on technology, etc...) we cannot extract quantitative conclusions (the HI profile was not even correlated with a real Heavy Ion!)
(IMHO) The most interesting use of TCAD simulations is that they help to understand the failure mechanisms.
4 to 10 hours to run all these experiments
(depending on how busy is the server)
Front-side incidence

## Slide 11
First peak:
Prompt collection
Second peak:
Collection of Secondaries
Burn-Out
Current grows more than 3 orders of magnitude (not shown)
@Length@ = 20 µm
LETth = 0.03 pC/µm

## Slide 12
LET = 0.005 pC/µm
Electron Current Density
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns

## Slide 13
LET = 0.02 pC/µm
Electron Current Density
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns

## Slide 14
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns
LET = 0.03 pC/µm (LETth)
Electron Current Density

## Slide 15
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns
LET = 0.005 pC/µm
Hole Current Density

## Slide 16
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns
LET = 0.02 pC/µm
Hole Current Density

## Slide 17
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns
LET = 0.03 pC/µm
Hole Current Density

## Slide 18
@Length@ = 20 µm
LETth = 0.03 pC/µm
First peak:
Collection of the primary generated charge
Heavy Ion Generation

## Slide 19
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns
LET = 0.005 pC/µm
Electric Field

## Slide 20
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns
LET = 0.02 pC/µm
Electric Field

## Slide 21
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns
LET = 0.03 pC/µm
Electric Field

## Slide 22
@Length@ = 20 µm
LETth = 0.03 pC/µm
Second Peak:
Corresponds to an Electric Field increment at the Epi/Substrate interface
Burnout:
For LETth, the increment in electric Field is high enough to induce avalanche breakdown
Electric Field at this point
Electric Field

## Slide 23
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns
LET = 0.005 pC/µm
Impact Ionization (Avalanche Generation)

## Slide 24
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns
LET = 0.02 pC/µm
Impact Ionization (Avalanche Generation)

## Slide 25
t=0 ps
t=4 ps
t=10 ps
t=0.1 ns
t=1 ns
t=10 ns
LET = 0.03 pC/µm
Impact Ionization (Avalanche Generation)

## Slide 26
Avalanche Generation:
Impact Ionization at the Epi/Substrate interface increases with increasing LET, and leads to breakdown for LETth
Avalanche Gen. at this point
Impact Ionization (Avalanche Generation)

## Slide 27
Conclusion:
  (Goodness, Utility and Limitations of Semiconductor Device Simulation, for the emulation of SEE)
What Sentaurus CAN’T do
What Sentaurus CAN do
Given a certain radiation environment or a even a single ionizing particle, Sentaurus TCAD CANNOT calculate the Generated Charge Profile
  We must better use, for instance, FLUKA
Sentaurus TCAD IS NOT useful to study Rad. Eff. in different Materials
  You can just simulate Semiconductors (Silicon, in particular) and the typical dielectrics (just to a certain extent…)
Sentaurus TCAD CANNOT assess the SEE Cross Section
  TCAD simulations are deterministic, no statistics can be extracted from them
Sentaurus TCAD CANNOT replace Experimental Tests
Given a generated charge profile, Sentaurus TCAD CAN simulate the Transient Evolution of the Carriers
Sentaurus TCAD CAN evaluate the consequences of the Single Event at a Device level
  Is an excellent tool to evaluate Sensitive Volumes, LET/Range thresholds, etc…
  In general, results should be considered qualitative; (although the accuracy can be increased, improving the precision of the models)
Sentaurus TCAD CAN help to understand the physical mechanisms that lead to a SEE

## Slide 28: ¡Muchas Gracias!

## Slide 29
Device Creator
(Sentaurus Structure Editor)
Electrical Simulation
(Sentaurus Device)
Parameters
Xpart = HI position
Rpart = HI charact. width
Vg = Gate voltage
Vd = Drain voltage
Length = HI Range
LET = HI Range
Experiments
Each “line” is a different experiment
(different parameter values)
Sentaurus Workbench

## Slide 30
LET = 0.005 pC/µm
Electron Density

## Slide 31
LET = 0.02 pC/µm
Electron Density

## Slide 32
LET = 0.03 pC/µm (LETth)
Electron Density