## Slide 1
Future Circular Collider Study - Status
Michael Benedikt
http://cern.ch/fcc
FCC
PS
SPS
LHC
Work supported by the European Commission under the HORIZON 2020 project EuroCirCol, grant agreement 654305
gratefully acknowledging input from FCC coordination group global design study team and all other contributors

## Slide 2
Scope of FCC Study
International FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  main emphasis, defining infrastructure requirements
~100 km tunnel infrastructure in Geneva area, site specific
e+e- collider (FCC-ee), as potential first step
HE-LHC with FCC-hh technology
p-e (FCC-he) option, integration of one IP, e from ERL
CDR for end 2018
~16 T  100 TeV pp in 100 km

## Slide 3
CERN Circular Colliders & FCC
Constr.
Physics
LEP
Construction
Physics
Proto
Design
LHC – operation run 2
Construction
Physics
Design
HL-LHC - ongoing project
Physics
Construction
Proto
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2035
~20 years
Design
FCC – design study
2040
Must advance fast to be ready with new research infrastructure for ~ 2040
Goal of phase 1: CDR by end 2018 for next update of European Strategy

## Slide 4
parameter | FCC-hh |  |  | HE-LHC | HL-LHC | LHC
collision energy cms [TeV] | 100 |  |  | 27 | 14 | 14
dipole field [T] | 16 |  |  | 16 | 8.33 | 8.33
circumference [km] | 97.75 |  |  | 26.7 | 26.7 | 26.7
beam current [A] | 0.5 |  |  | 1.12 | 1.12 | 0.58
bunch intensity [1011] | 1 |  | 1 (0.2) | 2.2 (0.44) | 2.2 | 1.15
bunch spacing [ns] | 25 |  | 25 (5) | 25 (5) | 25 | 25
synchr. rad. power / ring [kW] | 2400 |  |  | 101 | 7.3 | 3.6
SR power / length [W/m/ap.] | 28.4 |  |  | 4.6 | 0.33 | 0.17
long. emit. damping time [h] | 0.54 |  |  | 1.8 | 12.9 | 12.9
beta* [m] | 1.1 | 0.3 |  | 0.25 | 0.20 | 0.55
normalized emittance [mm] | 2.2 (0.4) |  |  | 2.5 (0.5) | 2.5 | 3.75
peak luminosity [1034 cm-2s-1] | 5 |  | 30 | 25 | 5 | 1
events/bunch crossing | 170 |  | 1k (200) | ~800 (160) | 135 | 27
stored energy/beam [GJ] | 8.4 |  |  | 1.3 | 0.7 | 0.36
FCC-pp collider parameters

## Slide 5
parameter | Z | W | H (ZH) | ttbar
cm collision energy [GeV] | 91 | 160 | 240 | 350
beam current [mA] | 1400 | 147 | 29 | 6.4
no. bunches | 71000 | 7500 | 740 | 62
bunch intensity [1011] | 0.4 | 0.4 | 0.8 | 2.1
bunch spacing [ns] | 2.5 / 5.0 | 40 | 400 | 5000
SR energy loss / turn [GeV] | 0.036 | 0.34 | 1.71 | 7.72
total RF voltage [GV] | 0.25 | 0.8 | 3.0 | 9.5
long. damping time [turns] | 1280 | 235 | 70 | 23
horizontal beta* [m] | 0.15 | 1 | 1 | 1
vertical beta* [mm] | 1 | 2 | 2 | 2
horiz. geometric emittance [nm] | 0.27 | 0.26 | 0.61 | 1.33
vert. geom. emittance [pm] | 1.0 | 1.0 | 1.2 | 2.66
bunch length with SR & BS [mm] | 4.1 | 2.3 | 2.2 | 2.9
luminosity [1034 cm-2s-1] | 130 | 16 | 5 | 1.4
FCC-ee collider parameters

## Slide 6
Implementation - new footprint baseline
Optimisation criteria
tunneling rock type,
shaft depth accessibility
surface points, etc.
Tunneling
Molasse 90%, Limestone 5%, Moraines 5%
Present status on implementation
90-100 km fits well geological situation in Geneva basin
LHC suitable as potential injector

## Slide 7
Full integrated lattice existing
Beam dynimcs studies confirm design goals
Focus on optimization of collimation system and extraction system performances
Two high-luminosity experiments (A & G)
Two other experiments combined with injection (L & B)
Two collimation insertions
  Betatron cleaning (J)
  Momentum cleaning (F)
Extraction insertion (D)
Clean insertion for RF only (H)
Compatible with LHC or SPS as injector
FCC-hh layout and optics
Based on EuroCirCol DS
Contributions from EPFL

## Slide 8
Nb3Sn conductor program
Nb3Sn is one of the major cost & performance factors for FCC-hh / HE LHC
Main development goals until 2020:
Jc increase (16T, 4.2K) > 1500 A/mm2 i.e. 50% increase wrt HL-LHC wire
R&D collaborations with TU Wien and Uni Geneva (amongst others)
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
Impact on coil section and conductor mass

## Slide 9
HE-LHC integration aspects
  Requirement: No major CE tunnel modifications
  Maximum magnet cryostat external diameter compatible with LHC tunnel ~1200 mm
  Classical 16 T cryostat design based on LHC approach gives ~1500 mm diameter!
Strategy: develop a single 16 T magnet, compatible with both HE LHC and FCC-hh requirements:
  Allow stray-field and/or cryostat as return-yoke
  Active compensation with (simple) shielding coils
  Optimization of inter-beam distance (compactness)
   Smaller diam. also relevant for FCC-hh cost optimization

## Slide 10
16 T dipole design activities and options
Cos-theta
Blocks
Common coils
Short model magnets (1.5 m lengths) will be built from 2017 - 2021
Swiss contribution
Canted
Cos-theta
H2020
INFN
CEA
CIEMAT
PSI
LBNL
FNAL

## Slide 11
FCC-hh beam screen test @ ANKA
FCC-hh beam-screen test set-up at ANKA:
Complete system installed in the ANKA ring;
Beam tests since June 2017
X-ray fan
2.5 GeV ANKA storage ring
One of the most critical elements for FCC-hh
Absorption of synchrotron radiation at ~50 K for cryogenic efficiency (5 MW total power)
Provision of beam vacuum, suppression of photo-electrons, electron cloud effect, impedance, etc.

## Slide 12
Prototyping launched of main dipole and quadrupole magnets (~1 m units)
FCC-ee dual aperture main magnets
Dipole:
twin aperture yoke, single busbars as coils
Considerable savings in Ampere-turns and power consumption by novel dual aperture designs
Power consumption twin quad: 22 MW at 175 GeV with Cu coil (half of single-aperture quads) and power consumption twin dipole: = 17 MW at 175 GeV with Al bus bar
Quadrupole:
twin 2-in-1 design

## Slide 13
Development of new klystron bunching technologies to increase RF power production efficiency to almost 90%, was initiated at CERN in 2013 (HEIKA), essential for FCC-ee
See I. Syratchev’s talk on Tuesday
Towards fabrication of the first high efficiency CSM tube
Presently negotiations with industry for protoype production for end 2018
Single beam, 1.4 MW, 0.8 GHz, 134 kV, 12.55 A
85.7% efficiency in simulations
Efficient klystron technology
Notes: HEIKA = High Efficiency International Klystron Activity
Bunching technologies developed for different frequency band (this has to do with the specific parameters (e.g. power requirements) and klystron length (e.g. L-band klystron
With COM method would be too long)

## Slide 14
SC wires at low temperatures for magnets (Nb3Sn, MgB2, HTS)
Superconducting thin films for RF and beam screen (Nb3Sn, Tl)
Turbocompressor for Nelium refrigeration
Magnet cooling architectures
13 Beneficiaries
12 Partners
EASITrain Marie Curie Training Network
I-CUBE
European Advanced Superconductivity Innovation and Training Network
selected for funding by EC in May 2017, start 1 October 2017

## Slide 15
FCC Collaboration & Industry Relations
25
Companies
32
Countries
111
Institutes
EC
H2020

## Slide 16
  Confirmed parameter sets for FCC-hh, FCC-ee, HE-LHC and FCC-he as solid basis for the Design Report end 2018
  Work ongoing on optimisation of machine designs as well as on technology R&D topics
  International FCC collaboration is growing steadily, addressing all the challenging subjects and research lines
  Strong contributions from Austrian and Swiss Institutes and Universities to the FCC Study
Summary and outlook
FCC WEEK 2018
AMSTERDAM
9-13 April 2018