## Slide 1
Update on Lattice Design and Synergies with JLEIC
  Alex Bogacz
  for JLab's Study Group on PERLE*
  *A. Bogacz, D. Douglas, A. Hutton, F. Marhauser, C. Tennant, R. Rimmer, Y. Roblin
LHeC and FCC-eh Workshop
CERN, 11-13 September 2017

## Slide 2: Motivation for PERLE
Bridge between 1 MW and 100 MW scale ERLs
  Present state-of-art 1 MW scale, single-pass ERLs (IR/UV JLAB FELs) have already posed several beam dynamics challenges:
    Formation and merging of CW train of high-charge, space-charge dominated bunches
    Acceleration and delivery of beam with properly configured phase space to warrant efficient energy recovery
    Preservation of beam quality/stability in presence of collective effects, errors and imperfections
  The LHeC 60 GeV ERL (100 MW scale ERL), would need a ‘stepping stone’ - test facility, such as PERLE (10 MW scale, 3-pass ERL) to ‘leap’ two orders of magnitude in beam power.
  Synergy with JLEIC Cooler, where similar beam dynamics issues need to be studied: e.g. CSR, micro-bunching, halo formation.
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 3
1 kW
10 kW
100 kW
1 MW
10 MW
100 MW
1 GW
legacy
operating
under construction
proposed
S-DALINAC
(CCR Driver)
JLEIC
(“Light”
Cooler)
State of Art ERL Landscape
LHeC and FCC-eh Workshop
CERN 11-13 September 2017
CW with Pbeam>PRF

## Slide 4: PERLE Downsizing
45 m
14 m
CDR (900 MeV)
Alessandra Valloni
Alex Bogacz
24 m
5.5 m
‘Lean’(400 MeV)
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 5: PERLE@Orsay - Layout
DC = lRF/2
5 MeV
DE = 65.5 MeV
DE = 65.5 MeV
5 MeV
400 MeV
24 m
0.8 m
5.5 m
1 : 3 : 5
2 : 4 : 6
dump
injector
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 6: PERLE@Orsay - Layout
DC = lRF/2
Three passes ‘up’ + Three passes ‘down’
5 MeV
DE = 65.5 MeV
DE = 65.5 MeV
5 MeV
400 MeV
24 m
0.8 m
5.5 m
1 : 3 : 5
2 : 4 : 6
dump
injector
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 7: Linac, Cryo-module - Layout
9.72
0
10
0
BETA_X&Y[m]
BETA_X
BETA_Y
Cryo-module (8.491 m)
Re-injection chicane
8.491 m
Linac length: 26 × lRF
801.58 MHz RF, 5-cell cavity:
l = 37.40 cm
Lc = 5l/2 = 93.50 cm
Grad = 17.5 MeV/m (16.4 MeV per cavity)
DE= 65.5 MeV per Cryo-module
SNS-like cryomodule
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 8
Multi-pass ER Optics
59.2518
0
12
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
E6
E5
E4
E3
E2
E1
Einj
Acceleration
59.2518
0
12
0
BETA_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Einj
E1
E2
E3
E4
E5
E6
Deceleration
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 9: Flexible Momentum Compaction Arc
7.70429
0
10
0
2
-2
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
399 MeV
Quadrupoles:
Q1 L[cm] =10 G[T/m] = - 23.6
Q2 L[cm] =15 G[T/m] = 28.2
Q3 L[cm] =10 G[T/m] = - 22.4
Q4 L[cm] =10 G[T/m] = 8.6
triplet: Q1 Q2 Q3
singlet: Q4
triplet: Q3 Q2 Q1
Qx,y = 1.25
4×450 bends
Dipoles: (91.2 cm long)
B = 1.2 Tesla
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 10: Vertical Switchyard CEBAF-like Architecture
Energies1 : 3 : 5
Energies1 : 2 : 3
T. Michalski
Dipoles: (20 and 40 cm long)
B = 0.8 Tesla
Dipoles: (30 cm long)
B = 1.2 Tesla
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 11
4.27981
0
20
0
1
-1
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Vertical Spreaders - Optics
vertical step I
vertical step II
vertical chicane
Spr. 1 (71 MeV)
Spr. 5 (333 MeV)
4.023
0
20
0
1
-1
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 12: Arc 1 Optics (71 MeV)
15.71
0
20
0
2
-3
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
1800 Arc
2-step vert. Spreader
Arc dipoles :
4450 bends
L = 45.6 cm
B = 4.5 kGauss
2-step vert. Recombiner
Spr. dipoles:
4 450 bends
L = 20 cm
B = 9.5 kGauss
Rec. dipoles:
4 450 bends
L = 20 cm
B = 9.5 kGauss
quads: L = 10 cm G  1 kGauss/cm
Isochronous Arc
pathlength: 42 × lRF
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 13: Vigorous R&D Program towards TDR
Linear lattice optimization
Initial magnet specs
Momentum acceptance and longitudinal match
End-to-End simulation with synchrotron radiation, CSR and micro-bunching
Correction of nonlinear aberrations (geometric & chromatic) with multipole magnets (sextupoles, octupoles)
RF cavity design, HOM content BBU studies
Injection line/chicane design
Space-charge studies at injection
Diagnostics & Instrumentation
Multi-particle tracking studies of halo formation
Final magnet specs
Engineering design
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 14: JLEIC Cooler (Circulating Cooler Ring + ERL)
Same-cell energy recovery in SRF cavities
Uses harmonic kicker to inject and extract from CCR
Assumes high charge, low rep-rate injector (with subharmonic acceleration and bunching)
ion beam
ion beam
magnetization flip
top ring: CCR
bottom ring: ERL
injector
beam dump
linac
fast extraction kicker
fast injection kicker
De-chirper
Re-chirper
circulating bunches
extracted
injected
septum
vertical bend
magnetization flip
B < 0
B < 0
B > 0
B > 0
septum
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 15: PERLE vs JLIC Cooler - Baseline Parameters
Name | EIC cooler | PERLE
Institute | JLab | LAL Orsay
# Re-Circulations | 1 | 3
RF Frequency [GHz] | 0.952 | 0.8
Bunch Frequency [MHz] | 8 | 40
Energy gain / linac [MeV] | 50 | 65.5
Bunch charge @ inj [pC] | 3200 | 375
Bunch length [ps] | 21.0 | 10
Transverse emittance [gamma mm mrad] | 36 | 6
Av. Current @ inj [mA] | 140 | 15
Injector Energy [MeV] | 5 | 5
Max beam energy @ end of accel [MeV] | 55 | 400
Max beam power @ end of accel [MW] | 7.7 | 6
Max total current in cavity [mA] | 280 | 90
Power on dump [MW] | 0.7 | 0.075
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 16: PERLE/JLEIC Cooler Synergy
High charge/current/beam power – constitutes unexplored performance regime
  Behavior of high charge and low Dp/p beam in SRF environment
Host of collective effects come into play; mitigation needed
  CSR, Longitudinal S-C micro-bunching
  resistive wall, IBS, Touschek scattering, BBU
Interaction of beam with environment lies in uncharted territory
  Beam-gas scattering, ion accumulation, wakes/impedance
Both ERL’s performance is critically dominated by halo
  Mechanisms for halo formation, characterization, evolution and control
LHeC and FCC-eh Workshop
CERN 11-13 September 2017

## Slide 17: Summary
PERLE is a unique ‘test bed’ for next generation of high power ERLs
  Testing multi-pass beam dynamics in energy recovery mode
  Probing limits of transporting non-equilibrium beams with high ratio of beam power to installed RF power
  Mitigation of longitudinal phase-space distortion due to wakes, including CSR and longitudinal S-C
  Preservation of beam quality/stability in presence of collective effects, errors and imperfections
Arc Optics Architecture
  Isochronous Arcs with Flexible Momentum Compaction (FMC) Optics
  Configured with two styles of 1.2 Tesla ‘curved bends’
Switchyard
  Two-step, Vertical Spreaders/Recombiners with matching sections: Linacs-Arcs
Synergy between PERLE and JLEIC Cooler, where similar beam dynamics issues need to be solved
LHeC and FCC-eh Workshop
CERN 11-13 September 2017