## Slide 1: Update of LHCb at High Luminosity
R. De Maria
WP2 Meeting 23/5/2017

## Slide 2: LHCb
 | Run II | Run III | Run IV | Run V-VI
Duration [years] | 3.5 | 3 | 3.5 | 5
L [1032 cm-2s-1 ] | 4 | <20 | 20 | 100-200
Int. L [fb-1] | ~81) | ?3) | 502) | 3002)
Ppb [1011] | 1.1 | 1.1→2.2 | 2.2 | 2.2
Bunches in IP8 | 2036→ 2378 | 2572 or 2378 | 2572 or 2378 | 2572 or 2378
Emit [µm/γ] | 2.8 | 2.8→2.1 2.5→1.7 | 2.1 or 1.7 | 2.1 or 1.7
1)Assuming 5.8 fb -1 , 2 fb -1 in 2016 with 4 1032 cm-2s-1 and 2036 bunches, extrapolating to 2378 bunches and same efficiency.
2) target.
3) Scaling in Run IV gives 35 fb -1, then target in Run III does not need strictly need higher levelled luminosity.
Notes: 2017 2fb-1 at 4e32 for 2036 2572

## Slide 3: Peak and Integrated luminosity
Large impact of spectrometer polarity on luminosity.
Difficult to reach the final target of 300 fb -1,
unless extending the target of Run IV beyond 50 fb -1.
Estimates for 2.5 µm/γ and 2378 colliding bunches based on scalings from a 250 fb -1 fill for ATLAS and CMS.

## Slide 4: Aperture and crossing angle
Horizontal crossing aperture limited by TCDDM (Beam 2) then triplet
Vertical crossing aperture limited by triplet
Crossing angle limited by orbit corrector strength to 310 µrad (with 20 µrad margin and repaired MCBY)
Protected aperture 14.6 σ (best aperture for worst phase advance from MKD)
β* [m] | H* [µrad] | H [µrad] | V [µrad]
1 | ±220 | ±165 | ±115
1.4 | ±270 | ±220 | ±160
2 | ±310 | ±265 | ±205
3 | ±310 | ±310 | ±250
Maximum crossing angle without or (*) with new TCDDM

## Slide 5: Ramp and squeeze
Present ramp and squeeze:
H Crossing -170 µrad → -250 µrad [0.45 → 7TeV]
V Separation -3.5 mm → -1 mm [2 → 7TeV]
V Angle offset -40 µrad → 0 [2 → 7TeV]
β* 10 m → 3 m [2 → 7TeV]
Most of the LR above 30σ,
Minimum is still about 20σ
Bad polarity

## Slide 6: Ramp and squeeze
Pushed case β*=1, ramp and squeeze:
H Crossing -170 µrad → -220 µrad [0.45 → 7TeV]
V Separation -3.5 mm → -1 mm [2 → 7TeV]
V Angle offset -40 µrad → 0 [2 → 7TeV]
β* 10 m → 1 m [2 → 7TeV]
Bad polarity
All LR in between 12 and 18 σ

## Slide 7: Ramp and squeeze
Pushed case β*=1, ramp and squeeze:
H Crossing -170 µrad → -220 µrad [0.45 → 7TeV]
V Separation -3.5 mm → -1 mm [2 → 7TeV]
V Angle offset -40 µrad → 0 [2 → 7TeV]
β* 10 m → 1 m [2 → 7TeV]
Good polarity
All LR in above 16 σ

## Slide 8: Ramp and squeeze
Vertical crossing β*=1, ramp and squeeze:
Crossing -170 µrad → -115 µrad
Separation -3.5 mm → -0.5 mm [2→7 TeV]
Crossing plane 0 → 90° [from 2→7 TeV]
V Angle offset -40 µrad → 0 [from 2→7 TeV]
β* 10 m → 1 m [from 2→7 TeV]
Previous case required exchange of TCDDM, however now all LR around 10 σ.

## Slide 9: Ramp and squeeze
Vertical crossing β*=1.4, ramp and squeeze:
Crossing -170 µrad → -160 µrad
Separation -3.5 mm → -0.5 mm [2→7 TeV]
Crossing plane 0 → 90° [from 2→7 TeV]
V Angle offset -40 µrad → 0 [from 2→7 TeV]
β* 10 m → 1.4 m [from 2→7 TeV]
Increasing to β*=1.4, put LR to about 14 σ.
Overall vertical crossing does not seem too advantageous.
However one needs to solve the TCDDM problem.

## Slide 10: Ramp and squeeze
Pushed case β*=1.4, ramp and squeeze:
H Crossing -170 µrad → -270 µrad [0.45 → 7TeV]
V Separation -3.5 mm → -1 mm [2 → 7TeV]
V Angle offset -40 µrad → 0 [2 → 7TeV]
β* 10 m → 1.4 m [2 → 7TeV]
Bad polarity
Most LR above 22 σ.
Assuming new TCDDM.

## Slide 11: Ramp and squeeze
Pushed case β*=1.4, ramp and squeeze:
H Crossing -170 µrad → -220 µrad [0.45 → 7TeV]
V Separation -3.5 mm → -1 mm [2 → 7TeV]
V Angle offset -40 µrad → 0 [2 → 7TeV]
β* 10 m → 1.4 m [2 → 7TeV]
Bad polarity
Most LR above 19 σ.
With present TCDDM.
One could look at flat beams for higher luminosity

## Slide 12: Back-up

## Slide 13: Luminosity scenarios
Scenario with large (2.7 1034 cm-2s-1 )IP8 virtual luminosity
Small impact on Atlas/CMS

## Slide 14: HL-LHC Targets
HL-LHC: mid 2026 to end 2039 after LS4
Reach ≥ 3000 fb-1 by
  Maximize availability, levelled luminosity per bunch, number of bunches, bunch population, brightness.
  Crab-cavities to alleviate geometric reduction factor to small β* and long bunches and pile-up density.
After LS4, proton physics days increase from standard 160 days to 200 and after LS5 to 220

## Slide 15: Injector Brightness and LHC Filling Schemes
Production scheme | ppb [1011] | ε [μm] | Inj. | BPI | Colliding 1,5/2/8
Standard | 1.3→2.3 | 2.8→2.1 | 13 | 288 | 2748/2494/2572
BCMS | 1.3→2.3 | 2.5→1.7 | 20 | 144 | 2544/2205/2308
 |  |  | 12 | 288 | 2736/2258/2378
8b+4e STD | 1.6→2.5 | 2.4→2.1 | 13 | 144 | 1960/1163/1806*
8b+4e BCMS | 1.6→2.5 | 1.2→1.8 | 20 | 96 | 1696/1470/1538*
80b | 1.3→2.3 | 1.3→2.1 | 14 | 240 | 2732/2476/2549
 |  |  | 12 | 320 | 2800/2246/2606
50 ns | 1.8 | 1.8 | 13 | 144 | 1374/1247/1286
Single | >3.0 | >1.5 | n/a | 1 | n/a
New scheme thanks to 200 ns rise time, BCMS very close to standard for IP1/5.
288bpi BCMS and 320bpi 80b cannot be tested in Run II due to transfer line limitations.
Will always short non-colliding train be needed, can they at least collide?
H. Bartosik, G. Iadarola, X. Buffat, C. Schwick
RunII → HL-LHC
*scaling

## Slide 16: Velo upgrade references
2013, Velo TDR
LHCb Tracker Upgrade TDR
20/7/2014, Velo Approval
Neglects crossing angle effects, assume levelling but also 1.7 1011 for run III
M. Giovannozzi, Velo aperture, 9th TREX 5/11/2015
R. Appleby et, al, VELO aperture considerations for the LHCb Upgrade, CERN-ATS-Note-2012-101