## Slide 2: Wire scanner calibration application
By Marta Vicente Romero
BI-SW

## Slide 3: Wire scanner calibration application
  Introduction
  Calibration Bench
  Analysis
  Overview ExpertGUI
  Architecture
  Demo
  Future and conclusions
  Questions

## Slide 4: 1 Introduction
  Application used to perform the position calibration of currently operational wire scanners in PS and PSB
  Aim is to automatize the construction of calibration tables of scanners before their installation in the corresponding machine
    For different speeds
    For both movements, in/home

## Slide 5: 2 Calibration Bench
Based on the acquisition of laser beam for a set of known positions
Result: A table of projected position versus the observable : potentiometer value
Two different calibration benches -> different calibration configuration
Laser
Splitter
Photodiode
Combiner

## Slide 6: 3 Analysis
  Needs
      Problems detected by the use of the application
      New requirements (by the “calibration team”)
  Obsolete architecture

## Slide 7: 3 Analysis
Needs
    Problems detected by the use of the application.
      Difficulties to follow the workflow
      Tedious handmade tasks
          Deploy calibration files
          Edition of the result

## Slide 8: 3 Analysis
Needs
    New requirements:
        Automation of handmade task
        New features:
            Edition: calibration tables edition, peak tables edition, application settings edition.
            Deploy calibration tables and save to a repository
            Task simplification
        Addition of data visualization:
                Charts: calibration tables visualization, position check errors.
        Improve the workflow
            Less steps for the user
            Usability

## Slide 9: 3 Analysis
  Obsolete architecture
      Difficult to maintain and add new requirements.
      Serious improvements were needed.
Obsolete!
New Application
Using old data structures
Solution!!

## Slide 10
Wire scanner
(BWSINJ)
Device Control
4 Overview ExpertGUI
FESA CLASSES
Stepping Motors
(BOSTEP)
Laser
Splitter
Photodiode
Combiner
PSB.867.LASER
PSB.867.LASER
CAL.BWS.867.PSB
CAL.BWS.867.PS
PS.867.LASER
PS.867.DIODE

## Slide 11
Device Control
Acquisition
FESA
Wire Scanners & Stepping Motors
Settings

## Slide 12
Application Settings
Acquisition
Settings
Device Control
FESA
Wire Scanners &
Stepping Motors

## Slide 13
Acquisition
Settings
Scans Logging
Application Settings
Device Control
FESA
Wire Scanners &
Stepping Motors

## Slide 14
Acquisition
Settings
Analysis and Tables
Scans Logging
Application Settings
Device Control
FESA
Wire Scanners &
Stepping Motors

## Slide 15
Acquisition
Settings
Analysis and Tables
Edition
Application Settings
Scans Logging
Device Control
FESA
Wire Scanners &
Stepping Motors

## Slide 16
Application Settings
Edition
Deploy
Git
Scans Logging
Analysis and Tables
Device Control
FESA
Wire Scanners &
Stepping Motors

## Slide 17: 4 Overview ExpertGui
Main functionality:
  Hardware initialization
  Single Scans
  Calibration
  Import Scans
  Check
  Analysis (calculations and visualization)

## Slide 18: 4 Overview ExpertGui
Workflow overview
HW Initialization
Single Scan
Import
(Old Calibration)
Calibration

## Slide 19: 4 Overview ExpertGui
Data Visualization
Calibration Files
Calibration

## Slide 20: 4 Overview ExpertGui
HW Initialization
Edit Results
Calibration

## Slide 21: 4 Overview ExpertGui
Check Scan
HW Initialization
Calibration
Edit Results

## Slide 22: 4 Overview ExpertGui
HW Initialization
Calibration
Edit Results
Check Scans
Deploy
Wire scanners

## Slide 23: 5 Architecture
  New BI Software guidelines:
  ExpertGUIs moving to JavaFX
  Unification under common architecture base on Model – View – Controller (MVC)
      modularity, reusability, maintenance, extensibility.

## Slide 24: 5 Architecture
  ExpertGUIs moving to JavaFX
  BI – SW section utilities.
    Tools develop by the section
    Common development guidelines
  CO standard components have been included. (https://wikis.cern.ch/display/GUI/Reference+Guide)
    General frame.
    RBAC Authentication.
    Logger utilities.
  Current state: Combination of JavaFX with Swing components.
        Property system and bindings, fxml, css.
         Missing features from swing

## Slide 25: 5 Architecture
  Using a variation of the MVC
  Model - View - Presenter
      Model: Business logic: Scans data, analysis data, lookup tables calculation, errors, scan parameters, application settings.
      View: fxml files with view controls
      Presenter:
              Receives the user inputs from the view. It asks to the model to operate accordingly.
              Presentation of the data in the view.

## Slide 26: 5 Architecture
  Using a variation of the MVC
      Model - View - Presenter
    This project:
    Decoupling existing content
    Focus in modularity in the business logic
    Group views and components

## Slide 29
  The new application is:
    easier to maintain and take over by other persons.
    ready to be extended.
  Improvement in the calibration process.
      avoid handmade tasks
      better visualization adapted to the user needs
7 Future and Conclusions

## Slide 30
Questions
Thank you

## Slide 31
BWSINJ
(Wire scanner Injection)
Device Control
3 Overview ExpertGui
FESA CLASS
CAL.BWS.867.PSB
PSB.867.LASER
CAL.BWS.867.PS
PS.867.LASER
PS.867.DIODE
Devices
BOSTEP
(Step In Motors)
PSB
PS