## Slide 1: ODR/OTR emittance station at ATF2
M. Bergamaschi1,2, A. Aryshev 3, K. Kruchinin 1,
P. Karataev 1,R. Kieffer2, T. Lefevre2, S. Mazzoni2
John Adams Institute at Royal Holloway, Egham, United Kingdom
CERN European Organisation for Nuclear Research, Geneva, Switzerland
KEK High Energy Accelerator Research Organization, Tsukuba, Japan

## Slide 2
Motivations and Goals:
Develop a non-invasive transverse profile station for CLIC/ILC beams that can be scaled up
Develop, install and test a combined Optical Transition Radiation (OTR) and Optical Diffraction Radiation (ODR) emittance station at ATF2 at High Energy Accelerator Research Organisation (KEK)
To optimize sensitivity to micron and sub-micron beam sizes, we plan to observe ODR/OTR in the visible and far-UV wavelength range, down to approximately 200 nm
Overview

## Slide 3
Overview
Manpower |  | 
RHUL | P. Karataev | Scientific coordination Beam tests
 | M. Bergamaschi | Simulations, Beam test, Instrumentation
 | K. Kruchinin | Beam test, Instrumentation
CERN BI | R. Kieffer | Beam test, Instrumentation
 | S. Mazzoni | Overall coordination Beam test
 | T. Lefevre | 
KEK | A. Aryshev | Beam test

## Slide 4
OTR-ODR experiment at KEK ATF2
ODR/OTR experiment location

## Slide 5
The tank installed in February 2016 at the virtual interaction point of ATF2 where vertical beam can be focused to < 1um
OTR-ODR experiment at KEK ATF2
Notes: Installation in Feb 2016

## Slide 6
OTR-ODR experiment at KEK ATF2

## Slide 7
Optical Transition Radiation (OTR)
Forward OTR
Beam
Screen
Backward OTR
e-
1  1
Vacuum
2  1
1  1
Vacuum
Screen
Backward OTR photons
Forward OTR photons
The transverse component of the particle electric field produces surface polarization currents on the dielectric target. Target’s atoms are polarized, their relaxation lead to the emission of OTR photons (femtosecond time response)
As predicted in 1946 by Frank and Ginzburg1, Optical Transition Radiation is a broadband electromagnetic field emitted by a relativistic charged particle when it crosses boundary between two mediums of different dielectric constants.
1 V. L. Ginzburg and I. M. Frank, Zh. Éksp. Teor. Fiz. 16, 15 (1946); J. Phys. (Moscow) 9, 353 (1945)

## Slide 8
A Gaussian fit works fine down to approximately 10 microns beam size.
As the beam size decreases, the projected OTR vertical polarization component is dominated by the point spread function PSF of the OTR => smaller beam sizes using the visibility (Imin/Imax)
OTR Point Spread Function (PSF) for beam size measurements
Beam size 42 um
Beam size from 0.6

## Slide 9
Lens
Aluminium coating
sCMOS
Camera
Linear Translational stage
Quadrupole
QM14FF
Quadrupole
QM1FF
BPM
BPM
OTR experiment at ATF2
Notes: In vacuum-lens to minimize spherical aberration of the system

## Slide 10
OTR beam size measurement at ATF2
OTR images for different value of QM14FF current => PSF sensitivity to different beam sizes

## Slide 11
OTR beam size measurement at ATF2
Smallest beam size measured 600nm, emittance calculated with quadscan and thin lens approximation 13.034 pm

## Slide 12
Slit target
The transverse component of the electric field from the charged particle produces surface polarization currents on the dielectric slit. Atoms on the edge of the slit are polarized, their relaxation lead to the emission of ODR photons
ODR
photons
ODR
photons
Polarization currents
a
Optical Diffraction Radiation (ODR)
Classical electrodynamics, John David Jackson

## Slide 13
Optical Diffraction Radiation
The ODR photons yield is strongly dependent on the effective electric field radius and the slit aperture a (impact parameter)
OTR
ODR
No radiation
Deep UV
Infra Red

## Slide 14
ODR experiment at ATF2
The target as 4 slits for ODR (49.7 to 201.7 um)
A couple of vertical and horizontal mask slits can be inserted 12.5cm upstream the target
ODR
Masks
TARGET
e- Beam
Synchronous Imaging and Angular acquisition for position filtering in angular

## Slide 15
ODR in imaging
There is no visible beam size dependency of the pattern in imaging.
But the vertical position into the slit change the profile asymmetry => Optical Beam Position Monitor (BPM)
Offset

## Slide 16
ODR imaging as an optical BPM
Slit: 56um
Beam size: 1um
30 shots statistics
Position resolution: about 1um
Steering magnet to scan the beam inside the slit
Pmax
Pmin
Steering -0.85A
Asymmetry = (Pmin-Pmax)/(Pmax+Pmin)
Resolution ~1um
Range 45um

## Slide 17
ODR for beam size measurements
The beam size is extracted from the visibility Imin/Imax of the projected vertical component of the ODR angular distribution
An horizontal slit is used to measure a vertical beam size.
We use a polarizer to select only the vertically polarized ODR photons and 40nm BW filters to select the wavelength
The angular distribution is obtained using a camera located at the focal plane of an optical lens (effective infinity)
ODR source
Aperture
Lens
CCD camera
On focal plane
d
f
Angular magnification
Polarizer
Filter

## Slide 18
ODR angular distribution
Both beam size and beam divergence have an effect on the visibility of the ODR pattern
In the ATF2 case, using low emittance beams the impact of the beam divergence (nrad) on the visibility is negligible compared to the beam size

## Slide 19
ODR angular distribution at ATF2
Beam 1um (100images)
Beam 18um (100images)
Beam 30um (100images)
Filter:450nm Slit:105um Mask:202um Electron beam @ 1.3GeV ,1.2nC
Beam 1um
Beam 18um
Beam 30um

## Slide 20
ODR beam size measurement
ATF2 ODR interference measurement for different target and mask combination
at 450 nm
ATF2 ODR interference measured profiles for different beam sizes at 450nm

## Slide 21
DR at ATF2 upgrade
Upgrading the setup to perform UV/Far-UV (200nm) angular beam size measurement
From visible range to UV
Enhance the sensitivity: (Imin/Imax)
Imply the use of a smaller slit to respect the rule:
Give the possibility to measure smaller beam sizes!
Optical line under 1mBar vacuum needed.

## Slide 22
Angular
PCO
DICAM
Intensified
Camera
PCO
sCMOS
Imaging
Filter
Wheel
Beam
Splitter
Mirror
Lens
F: 400mm
2%
98%
Lens
F: 200mm
Polarizer
Mirror
3 inches Mirror
Linear stage
UV nitrogen tank
Hamamatsu Intensifier
Lens
F: 75mm
Filter
flipper
Mirror
Mirror
DR at ATF2 upgrade

## Slide 23
Synchrotron Radiation contribution
TR angular distribution without mask
TR angular distribution with mask

## Slide 24
Summary
OTR achievements
Sub-micrometer beam size sensitivity has been demonstrated
Emittance measurement by the OTR PSF method are in good agreement with the measurements performed by conventional multi-otr system installed at ATF
ODR achievements
Possibility to use DR as an optical beam position monitor has been tested
Sensitivity to beam size of tenth of micrometers has beam demonstrated
Mask contribution to block synchrotron radiation has been observed

## Slide 25
Thank you for your attention!

## Slide 26
Backup slides

## Slide 27
SR contribution
TR angular profile before (a) and after (b) beam orbit optimization

## Slide 28
ODR beam size measurement
Quad scan in same condition then TR PSF,
beam size range 0.8 um to 10 um
, mask, target

## Slide 29
DR simulations
, mask, target
Target size
[1]
Simulated Visibility vs Gaussian beam size
for different target slit sizes
DR profile for different beam sizes
[1] A. Cianchi et al., Non-intercepting electron beam size monitor using optical diffraction radiation interference, Phys. Rev. ST Accel. Beams 14,102803 (2011)

## Slide 30
Slit 1 201.7um
Slit 2 100.6um
Slit 3 77.2um
Slit 1 399um
Slit 2 198.9um
Slit 3 149.2um
Slit 4 100um
TARGET
Mirrored areas
6x4mm2 around slits
MASK
Fully Mirrored
Slit 4 49.57um
Target details

## Slide 31
ODR light intensity with different mask
ODRI
ODR
ODRI
ODR
Mask
202um
Target
105um
Mask
405um
Target
105um
Mask
405um
Target
220um
ODRI
ODR
Beam
Beam
Beam
With a distance of 12.5cm between Mask and Target at 1.3GeV the ODR Interference is constructive and increases integrated image intensity
Filter: 450nm

## Slide 32: ATF2 ODR Optical line upgrade (October 2016)
Angular
PCO
DICAM
Intensified
Camera
PCO
sCMOS
Imaging
Filter
Wheel
Beam
Splitter
Mirror
Lens achromat
F: 100mm
2%
98%
Lens achromat
F: 100mm
Polarizer
Mirror
Mirror
Linear stage
AIM: Synchronous Imaging and Angular acquisition for position filtering in angular.