## Slide 1
Sergey Kazakov
22 June 2017
RF couplers for PIP-II

## Slide 2
PIP-II linac technology map
HWR
SSR1
SSR2
LB650
HB650
Bunching cav.
Performance parameter | 
Linac beam Energy | 800 MeV
Linac Beam Current | 2 mA
Linac Pulse Length | 0.55 ms
Linac Pulse Repetition Rate | 20 Hz
Linac Upgrade Potectial | CW

## Slide 3: PIP-II linac includes:
Room temperature cavities:
RFQ room temperature cavity.
Bunching cavity x 4.
5 types of SC cavities:
HWR x 8,
SSR1 x 16,
SSR2 x 35,
LB 650 x 33,
HB 650 x 24 elliptical cavities.
Each cavity requires a coupler.
Total number of couplers: 122 (RFQ uses 2 couplers).

## Slide 4: Operating parameters of cavities determine the requirements to couplers:
RFQ coupler:
Frequency 162.5 MHz
Power 75 kW, CW
HWR coupler:
Frequency 162.5 MHz
Power 10 kW, CW
SSR1 & SSR2 coupler:
Frequency 325 MHz
Power 30 kW, CW
LB & HB 650 coupler:
Frequency 650 MHz
Power 110 kW, CW
All couplers were designed and some prototypes were built and tested.
Buncher coupler:
Frequency 162.5 MHz
Power 3 kW, CW
(Requirements meets parameters of upgrade version of PIP-II with 5 mA current.)

## Slide 5: Principles of design:
Simplicity of vacuum part of coupler:
no moving parts, no bellows.
simple configuration – more reliable, easy to clean, less expansive.
Air cooling of antennas (no water) – Not so severe consequences in case of leak.
Ability to apply high voltage bias to suppress a multipactor.
Avoid a copper coating of stainless steel.
Based on this principles the RFQ, SSR1 & SSR2, LB & HB 650 couplers were design.
RFQ and SSR1 & SSR2 couplers were built and tested.

## Slide 6
Electrical configuration
Overall sizes
RFQ coupler:
Frequency 162.5 MHz
Power 75 kW, CW

## Slide 7
Some features of RFP coupler:
Not grounded loop (HV bias applicable)
Air cooling

## Slide 8: Ceramic window assembly:
Custom Rotatable
Flange SS316
3 1/8 Fixed coaxial flange
Viton O-ring
RF seal
Beryllium Copper C175 Alloy 10
(Bal Seal Spring )
Copper 101 Tube OD .25”
Al2O3 ceramic disc
Copper sleeves

## Slide 9: RFQ coupler connected to RFQ cavity:
DC block

## Slide 10: Results of testing:
Two couplers with four ceramic window units were produced.
Couplers were tested at RFQ cavity up to 65 kW in pulse and CW modes.
CW mode integrated time was ~ 500 hours.
Two windows were broken. The reason is not clear enough.
The most probable reasons are not enough air cooling or/and
low quality of window brazing.
Remaining two windows are installed to RFQ cavity and operating in pulse mode now.

## Slide 11: Backup RF windows:
We decided to design and build “backup” ceramic windows units with bigger and replaceable ceramics. Ceramic disk will be vacuum sealed by Viton rings or aluminum diamond seals. We expect that new window will be powerful enough. In case of broken window the ceramic disk can be change easily for new one.
Ceramic diameter 6’’ (was 3’’)
Ceramic thickness 4 mm (0.16’’)

## Slide 12
Window units are interchangeable.

## Slide 13
Relatively and absolute losses in Viton (rubber) rings.
Ceramic thickness was chosen 4 mm

## Slide 14: SSR1 & SSR2, 325 MHz coupler:
“5K” intercept
“80K” intercept
Heater
Ni-Cu bellows
Antenna
Ceramic window
3’’x 0.0158’’
stainless steel tube
e-pickup port
Arc detector
Air inlet
Spring to compensate
thermal expansion
3-1/8’’ coaxial input
Cryomodule flange
Cold flange
Matching bump
Outer conductor:
SS, ID 73mm (2.78’’), 0.4mm wall thickness, no Cu coating.
P, kW | “2K “, W | “5K”, W | “70K”, W
0 | 0.06 | 0.58 | 2.02
3 | 0.10 | 0.81 | 2.35
6 | 0.15 | 1.03 | 2.68
20 | 0.35 | 2.07 | 4.25
30 | 0.50 | 2.82 | 5.36
Thermal properties of coupler:
Design power:
30 kW, CW, full reflection
RF Window:
Single, room temperature, alumina, OD 73mm (2.87’’),
ID 12.7mm (0.5’’), thick. 6mm (.236’’)
Antenna:
Copper 0.5’’, air cooled, HV bias.
Impedance 105 Ohm

## Slide 15: Results of testing, 325 MHz couplers:
Three prototypes were produced and tested in test stand at room temperature.
Pair of couplers were successfully tested up to 30 kW, CW, full reflection, 90 dgr. step reflection phase.
Then couplers were tested up to failure. Window was destroyed at 47 KW, CW, full reflection.
One prototype was successfully tested with SSR1 SC cavity in cryomodule up to 10 kW, CW. Coupler demonstrated designed thermal parameters.
10 couplers are under production.
Test stand of 325 MHz couplers

## Slide 16
4 coupler produced by “Mega Ind.” were successfully tested at test stand up to 20 kW, CW, full reflection, 90 dgr step. 1.5 hour at each step.
Two coupler made of “Mega Ind.” were tested with cavity up to 10 kW, CW. One of them was tested twice. Last coupler (tested twice) got ‘mysteries’ leak. Leak happen after test in midnight without RF power during cavity warming up. But window is always warm, temperature of window T ~ room temperature. Small leak appeared In the middle of ceramic, no visible damages. We do not understand what happened.

## Slide 17
325 MHz coupler test stand
SS cavity under vacuum:
325 MHz coupler test stand configuration:
Size of the cavity was chosen big enough to avoid multipactor .

## Slide 19
We test couplers in standing wave mode (full reflection). To increase testing power we use resonance. Resonance tined by movable reflector. Testing power can be 5 times higher then power of RF source.
RF source: SS, 10 kW, CW, 325 MHz.
Testing power: up to 50 kW, CW

## Slide 20
Multipcator in all couplers (different frequencies) is suppressed by HV bias.
To decouple and protect RF source against HV,
‘DC blocks’ installed between RF source and coupler.

## Slide 21
Structure of 650 MHz coupler, new design
Design power 100 kW, CW, TW
Window Al2O3, 102mm x 6mm
Outer conductor (vacuum) 72mm
Antenna D 12.7mm
Cooling Air
Multipactor HV bias

## Slide 22
Conventional coupler
New approach

## Slide 23
Two version of vacuum outer conductor were design:
New with electromagnetic copper shields
Conventional with copper coating
Outer conductors are interchangeable.
No copper coating
With copper coating

## Slide 24
Configuration with ‘conventional’ outer conductor

## Slide 25
 | 2K, W | 5K, W | 70K, W | 293K, W | T window, K, min/max
New, 0 kW | 0.15 | 0.6 | 3.3 | -2.7 | 288/288
New, 100 kW | 0.55 | 0.93 | 6.2 | 21 | 334/347
Conv., 0 kW | 0.41 | 1.46 | 3.0 | -3.1 | 288/288
Conv., 100 kW | 0.97 | 4.1 | 11.4 | 20 | 331/344
New = 0.55*960 + 0.93*220 + 6.2*20 ~ 857 W
Conv. = 0.97*960 + 4.1*220 + 11.4*20 ~ 2061 W
Cryo-plant power consumption:
New configuration requires 2.4 times less power
of cryo-plant to compensate cryo-loading.
Thermal properties of 650 MHz coupler
Two couplers are under production.

## Slide 26
650 MHz coupler test stand is under design

## Slide 27
650 MHz coupler test stand

## Slide 28
Challenge: slots between screens should be ~ 0.5 mm to avoid multipactor in them. Special jigs will be used for assembling.
1.3 GHz coupler was designed for potential industrial SC accelerator.
Supposed cavity temperature is 4K (no 5K thermal intercept).
Coupler has TTF-III output flange.

## Slide 29
Chart: Total cryogenic loads, 20 kW transmitted power
| 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120
4.5K | 0.38465 | 0.45608 | 0.53779 | 0.62688 | 0.72036 | 0.81896 | 0.92346 | 1.0337
77K | 4.0742 | 4.0835 | 4.0665 | 4.1091 | 4.12 | 4.0859 | 4.0369 | 3.9698
Two couplers were produced.
We suppose to test them before October.

## Slide 30
Other projects.
Team of Illinois Accelerator Research Center (IARC) works for 650 MHz superconducting industrial accelerator. Each SC cavity will consume 250 kW, CW RF power. It will be accelerator with conducting cooling of accelerating structure (without liquid Helium). Available 4K commercial cryocoolers exist with a refrigeration power of 2 W at 4K temperature and several vendors are developing higher capacity units. It means that cryo-loading from coupler should extremely low, ~ 1W at 4K for ~ 250 kW transmitted power. We are working for design of this coupler.

## Slide 31
Backup

## Slide 32
P = 100 kW, TW, Air = 3.0g/s
Loss in antenna = 77W +20W = 97W
ΔT_air ≈ 38C
T_tip ≈ 34C
P_rad = 0.17W

## Slide 33
P = 300 kW, TW, Air = 5 g/s
Loss in antenna = 230W+58W = 288W
Δ_Tair ≈ 72C
T_tip ≈ 44C
P_rad = 0.19W

## Slide 34
Pressure drops:
Inner pipe: OD 9.5 mm, ID 7.7 mm, Length ~ 1m
Antenna ID 10.9 mm, Length ~ 0.41 m
Pressure drop at inner pipe:
3 g/s: ΔP = 0.06 bar, V = 64 m/s
5 g/s: ΔP = 0.16 bar, V = 107 m/s
Pressure drop at antenna:
3 g/s: ΔP = 1.3 bar, V = 113 m/s, Convection ~ 550 W/(K*m2)
5 g/s: ΔP = 3.2 bar, V = 189 m/s, Convection ~ 830 W/(K*m2)
Inlet pressure ~ 2 bar for 3 g/s
~ 4 bar for 5 g/s
Air cooling of antenna

## Slide 35
Antenna tip and coupling.
“Goose foot” shape improves a coupling and allows to change coupling by rotation of antenna

## Slide 36
LB 650 MHz cavity coupling:

## Slide 37
HB 650 MHz cavity coupling: