## Slide 1: TE-MSC at Mid Term: An Incomplete Snapshot and a Message
L. Bottura, 27 June 2017

## Slide 2: LHC is back
Is there a significant memory ?
Extrapolate to 7 TeV:
550 quenches expected
A31L2 (MB1375) exchanged during EYETS 2016-2017
There is hope (and desire) to increase the energy
Notes: The call of physics is not yet clear. Whatever the question, the solution is more energy

## Slide 3
QBQI.31L2 : Line N removal
QBBI.A31L2 : Ready for transport
QBBI.A31L2 : de-solder
QBBI.A31L2 : line E cutting

## Slide 4
New A31L2 magnet ready in SMI2
New A31L2 magnet installation
New instrumentation
Notes: Fond memories. We work to serve our accelerator complex, the first priority (after safety)

## Slide 5
QBBI.A31L2 : splice and shunts soldering (M3)
QBQI.30L2 : Line N assembly
QBQI.30L2 : N box
QBBI.A31L2 : shunt installation (M2)

## Slide 7: Dipole diodes
!?!

## Slide 8: Dipole diodes
Cleaning of the diode boxes
Systematic reinforcement of the insulation and additional protection against debris

## Slide 9: Simplified workflow
4. Consolidate electro-mechanical insulation
5. QA/QC of the consolidated insulation
6. Reclose cold mass volume (Welding)
7. Diode test [ElQA]
8. Intermediate leak test
(Clam shell [TBC])
9. Reclose interconnections
10. Final leak test
1. Open outer bellows and thermal shields
2. Give access to the diodes busbars (Mechanical cutting)
3. Clean the diode box and cold mass extremity

## Slide 10: LS2: global overview
Courtesy M Bernardini

## Slide 11
Long Shutdown 2
JM. Jimenez
11
2017-02-06
Defending LHC dipole diodes #3 – Indico 616383 J.Ph. Tock
J.Ph. Tock # 146
Consolidating LHC dipole diodes
Open/Close IC
#25
Diodes cons. #20
Special interventions “SIT” #18
HL-LHC (CC/11T)
Cryomagnets exchange
PIMs
Specific issues
Heavy NCs
Opening/ Closure of IC W bellows & ther. shields
Quality Assurance
# 26
Electrical QC: # 12
-Welding QC: # 3
ICIT: : #6
QA manager support: #2
Audits: #2
ELQA [TE-MPE]
#21
Continuity
HV test
Leak Test [TE-VSC]
#15
Beam lines
Cryogenics lines
Insulation vacuum
Project Leader’s Office #8
Radiation protection
Safety, Access
General logistics
Pressure test
Link to visits, media
Coordination with Survey, BLM, Instrumentation, Transport, planning, QPS, cryogenics, VSC, MPE, CRG, … Test teams on a chain of IC
Reporting tools
Administrative support (Budget, human resources, scientific secretary)
Cutting&Welding [EN-MME] #13
- Opening
- Rewelding
Cleaning
Consolidation
Experts
Also contains replacement of cryomagnets and installation for High Lumi

## Slide 12: Reliable operation of the injectors
Effective strategy of preventive maintenance (inspections, diagnostics & consolidation)
and of corrective maintenance (inspections, piquet service, workshops)
Major problem is the lack of resources (2 technicians missing)

## Slide 13: LIU advances well (LS2)
A considerable quantity of preparation work (new magnets, new coils, new PFWs)
Space to be found/consolidated to perform the work during LS2
Personnel resources to be found (agreements) to perform the work during LS2
PSB & TLs
PS & TLs

## Slide 14: In summary, on Operation & Co.
The maintenance and consolidation of the accelerator complex remains our high-priority work
Though we can (and will) count on collaborators for much of the work, it is important to focus and maintain full control of the technical “details”
This work requires careful preparation, and will draw considerably on us during LS2

## Slide 15: 11T, the next major milestone
2x2+2 11 T dipoles to be installed in the LHC during LS2 (2019-2020)
Complete model program
Build and test the first prototype
Procure required components
Produce and test the collared coils, cold mass, cryomagnets

## Slide 16: 11T models
MBHDP102, second twin aperture model
In preparation for test, final validation of collaring procedure and coil performance (RRP)
Further model work is in support of the final magnet construction, and future technology (towards FCC)

## Slide 17: 11T prototype
First collared coil assembly !
All production steps have been completed (mock-up SC coils)
Production of prototype proceeding on a tight schedule
IT-4282/TE/HL-LHC dispatched to firms last week:
Provision of Services for the Manufacturing of Collared Coils for the 11 T Dipole Magnet of HL-LHC at CERN
Test planned early 2018

## Slide 18: Layout - 11T Nb3Sn collared coil production
Invitation to tender out !
A comment on the contribution of industry

## Slide 19: QEP and QEN
Connection cryostat
Extremities with bus-bars
Warm by-pass for collimators
Review OK…

## Slide 20: QEN prototype
Proto vacuum vessel and thermal shield delivered
Vacuum vessel series fabrication contract to be signed June 2017
Thermal shield series fabrication by EN/MME job being launched
… and now to production !

## Slide 21: The rest of HL-LHC: QXF
QXF entering final qualification phase…
MQXFS5

## Slide 22: The rest of HL-LHC: QXF
… and preparation for production
8+2 Q2 magnets to be installed in the LHC during LS3 (2024-2026)
Prototype in construction
Industry, upcoming IT
Copper coil impregnated
CR101 impregnated
CR102 in preparation for impregnation
CR103 just reacted
CR104 just started winding

## Slide 23: Nb3Sn production – 1/2

## Slide 24: Nb3Sn production – 2/2
Ic data : Good correlation, small systematic difference
  Initially CERN was measuring about 5 % lower values (due to different strain state)
  New sample mounting procedure implemented, now CERN measures about 2 % higher values (with improved reproducibility)
RRR data: good correlation, significant spread
A large effort, but important and systematic follow-up

## Slide 25: The rest of HL-LHC: other magnets
D1: very significant improvement in training
Still requires some careful engineering (KEK)
D2: entering engineering phase for the short model construction
D1, D2, (Q4, Q5, Q10)

## Slide 26: The rest of HL-LHC: other magnets
Novel CCT concept:
will it work as expected ?
HO correctors now in the hands of our colleagues at INFN
MCBXF: successful collaring test of short mock-up
Still much delicate work to do to have a full magnet built
MCBXF, MCBRD, HO, (MCBY)

## Slide 27: MgB2 SC Link for IR1/IR5
SC link cable manufacturing in EU industry

## Slide 28: SC Link activities in Bdg. 927
Pulling bench with 60 m long cryostat and dummy cable
Cryostat handling
Cryostat unspooling

## Slide 29: In summary, on HL-LHC
We have in front of us a period of critical demonstrations
  11T model and prototype (6 months)
  SC link and feedboxes (6…12 months)
  QXF prototype (12…18 months)
We are moving from the magnet model and prototyping phase into production (components procurement, industry contracts, quality and inspections)
Priority should be given to resolving the pending technical issues, and making sure we have enough margin (performance, resources, time)
The coming two years are a crucial point:
  for the new Nb3Sn technology for accelerator magnets
  for the demonstration and engineering of SC links
  for the success of HL-LHC and of future projects that depend on it

## Slide 30: FRESCA2 – training
1202
3401
3402
1201
1
2-6
Left
Right
Left
1202
3401
3402
1201
Repaired splice
Images by E. Rochepault
1
2-6
12.2 T

## Slide 31: FRESCA2 – QH failure – 1/2
At the ramp following quench 6 the protection tripped. At 1 ms after heater discharge the heater circuit (QH7) showed anomalies
Heater currents
Heater resistance
80-110 cm
40-70 cm

## Slide 32: FRESCA2 – QH failure – 2/2

## Slide 33: FRESCA2 – reborn
This is one of our battle-horses of the future
Coil exchanged
Magnet re-assembled and ready for test

## Slide 34: Test stations in SM-18 – 1/2
Total overhaul of powering in Cluster A
Tested at:
16.5KA for 8 hour (QXF nominal)
18KA for 1 hour (QXF ultimate)
20KA for 5 minutes
Preparation for HL-LHC series tests
Notes: Prepare the test stations, but also the procedures, the MM equipment, and the teams

## Slide 35: Test stations in SM-18 – 2/2
HFM test station
Cluster D test station
superleak
superleak
Last measurement 37.9 +/- 11.9 W

## Slide 36: Eppur Si Muove ! (Et pourtant ça tourne !)
MQXFS_5 (PIT)
MQXFS_3 (RRP)
Training of MQXFS3 performed in the HFM test station
20 kA
30 kA

## Slide 37: HIE-Isolde approaching completion !
Cavity of CM1 reconditioned successfully !
HIE-Isolde is a beautiful piece of technology and a working accelerator experiment, also (and much) thanks to the contribution of the group
Handing over now to operation and BE-RF
Notes: We are focusing back to core mandate in the next years, and other projects outside of the mandate will be given lower priority

## Slide 38: The HIE-Isolde solenoids
Whatever the project, Magnets R Us !
1
a
b
2
3
4
5
6
Danfysik Coil
OXINST Coil
Yoking
Cold Tests (in Test Vessel for coil training)
Test Station
Helium Vessel Assembly
Cold Tests (magnetic measurements, TF)
Completed Magnet
Notes: Magnets are our core activity, we need to respond to magnet calls for all CERN accelerator complex. There is no shirking possible

## Slide 39: Projects, studies, …

## Slide 40: Diversity programs
East Area (energy management, re-organization of lines, safety, accessibility)
North Area (energy management, consolidation)
SHIP (Spectrometer magnet)
AD (permanent magnet quadrupole target area)
n-Tof EAR1 (permanent magnet cleaning dipole)
Completed: Elena, Awake protons, Awake electrons, Hie-Isolde, Sesame

## Slide 41: In summary, projects and studies
This is a delicate balance:
  With no R&D there is no future, and traditionally we are a very strong motor of progress and innovation
  Some of the challenges of the coming years require focus and concentration of our efforts to fulfill the mission
A discussion is on-going (SLM) to see how to cope with our priority activities
A part of our program may need to be delayed or redirected to benefit the high priority work

## Slide 42
By courtesy of M. Jimenez
TE Department Retreat
27-28 March 2017
P0
P1
P2
P3
P4/P5

## Slide 43
E. Todesco
J. Axensalva
A. Devred
T. Bampton
I am aware that the pressure is high

## Slide 44: Conclusions
This is a time of high demands
  LS2 and LIU, MB diodes, 11T dipoles and cryostats, cold powering, testing (and upgrades)
This is a time to focus on what is important
  Critical technical issues and organization to meet mandatory deadlines for LS2 and LS3
This is a time to build and make a difference
  LIU magnets, HL-LHC magnets
This is a time to enjoy