## Slide 1
Recap of transverse beam dynamics I + II
H.Schmickler, CERN
Corresponds to the
expected Level of the “successful student” after the Introductory CAS
Future High Energy Colliders, Zϋrich, 21.2-5.3.2018

## Slide 2
16 hours of compact lectures summarized in 2 hours.
Only possible by leaving out most of the mathematics and by explaining the concepts behind.

## Slide 3
Basics (only 5 minutes):
Phenomenology of Special relativity, formulae for relativistic beams
simple examples of E-fields and B-fields, multipole expansion of B-fields
Linear Optics:
Hamiltonian formalism derivative of Hill’s equation from Hamiltonian Hamiltonian in different Coordinate Systems, weak focusing
- linear optics: motion of single particle in a lattice, phase space plots
- trajectory, closed orbit, dispersion, weak focusing - strong focusing, tune, chromaticity - linear Imperfections, down-feed, coupling - “A taste” of non-linear dynamics
Liouville’s Theorem:
Definition of emittance
emittance preservation in conservative systems
filamentation due to non-linearities
Phenomenology of Collective Effects:
- Space Charge - Touschek and Intrabeam Scattering - Wakefields
Slides partially or fully taken from
the lecturers in Budapest: S. Sheehy W. Herr B. Holzer G. Franchetti
A. Wolski
R. Tomas
F. Tecker V. Kain (Erice 2017)
A. Cianchi (Egham 2017)

## Slide 4
1: Relativistic particles
Conservation of transverse momentum
A moving object in its frame S’ has a mass m’ =
Or + ) (approximation for small v)
Multiplied by :
Interpretation:  Total energy
For small velocities the total energy is the sum of the kinetic energy plus the rest energy
Particle at rest has rest energy
Always true (Einstein): =

## Slide 5
Relativistic momentum
=
From page before (squared):
= ( = ( = (
+ (
Or by introducing new units [E] = eV ; [p] =eV/c ; [m] = eV/c2
+
Due to the small rest mass electrons reach already the speed of light with relatively low kinetic energy, but protons only in the GeV range

## Slide 6
For those, who really want to calculate…

## Slide 7
Electromagnetic Fields and forces onto charged particles
Described by Maxwell’s equations and by the Lorentz-force
Lots of mathematics, we will only “look” at the equations
Only electric fields can transfer momentum to charged particles  EM cavities for acceleration  F. Tecker
Magnetic fields are used to bend or focus the trajectory of charged particles  construction of different types of accelerator magnets
Also electrostatic forces can bend and focus beams; but since the forces are small we often neglect this part

## Slide 8
But: for specific cases we also use electrostatic elements
quadrupole
Separators for electron and positron beams in the same vacuum chamber

## Slide 9
We need real magnets in an accelerator…not any arbitrary shapes of magnetic fields, but nicely classified field types by making reference to a multipole expansion of magnetic fields:

## Slide 11
Back to relativity: transformation of fields into a moving frame
Lecture of W. Herr

## Slide 12
Transverse Beam Dynamics
??? high intensity beam described in 6D phase space??? No…
Starting point: - Single particle in single magnetic element - complete decoupling of long., hor.& ver. motion
- particle with nominal momentum
My first accelerator: - Single particle in many magnetic elements - circular structure: synchrotron - twiss parameters, orbit, tune…
Off-momentum particle: - Dispersion - Momentum compaction - Chromaticity…a taste of non-linearities
Finally a beam of many particles (not too many!) - emittance - Liouville’s theorem - adiabatic damping and radiation damping
But:

## Slide 13
Linear Optics – Hamiltonian (1/3)
A little reminder of classical mechanics:
Take a set of “canonical conjugate variables” (q, p in a single one dimensional case)
q is called the generalized coordinate and p the generalized momentum
Construct a function H, which satisfies the dynamical equations of the system:
H “= the Hamiltonian “ of the system is a constant of motion (= H does not explicitly depend on t) .
The Hamiltonian of a system is the total energy of the system: H = T +V (sum of potential and kinetic energy)
and
Proof:
Used x instead of q just to test your attention

## Slide 14
Linear Optics – Hamiltonian (2/3)
This leads immediately to the question: What are canonically conjugate variables? * Complete answer: Lecture of W.Herr later this course Short answer: Several combinations are possible, the most relevant for us are - x (space) and p (momentum) - E (energy) and t (time).
We can learn most of the physics, when we construct quantities from these canonical variables, which are constants of motion (energy, action…)
* Hint to a more complete answer:
Describe the particle motion by a Lagrange function of generalized coordinates and generalized velocities and time. - define an action variable and assume that nature is made such that the action between any two points of particle motion is stationary
This is fulfilled for Lagrange functions satisfying the Euler-Lagrange equation
And this leads finally to the definition of generalized momenta instead of generalized velocities, the definition of the Hamiltonian function and then to the two equations of motion as shown on the last slide.

## Slide 15
Recall: what is the “action” variable; what is phase space
qx
px
Define action “S”:=
“Stationary” action principle:= Nature chooses path from t1 to t2 such that the action integral is a minimum and stationary  we have a new invariant, which we can use to study the dynamics of the system
This shows only one of the three phase-spaces

## Slide 16
x
x’
x
px
Trace space
Phase space
Warning: We often use the term phase space for the 6N dimensional space defined by x, x’ (space, angle), but this the “trace space” of the particles. At constant energy phase space and trace space have similar physical interpretation

## Slide 17
Linear Optics – Hamiltonian (3/3)
Example: Mass-spring system
k + = E
Hamiltonian formalism to obtain the equations of motion:
= or p=m = mv
= -kx
We are used to start with the force equation:
= - kx
With the well known sinusoidal solution for x(t).
Instead we look at the trajectory of the system in a phase space. In this simple case the Hamiltonian itself is the equation of the ellipse.

## Slide 18
A further look at phase-space plots
t = +
The particle follows in phase space a trajectory, which has an elliptic shape.
In the example, the free parameter along the trajectory is time ( we are used to express the space-coordinate and momentum as a function of time)
This is fine for a linear one-dimensional pendulum, but it is not an adequate description for transverse particle motion in a circular accelerator  we will choose soon “s”, the path length along the particle trajectory as free parameter
Any linear motion of the particle between two points in phase space can be written as a matrix transformation: ()= ()
In matrix annotation we define an action “J” as product J:= () ().
J is a motion invariant and describes an ellipse in phase space. The area of the ellipse is
Why all this? Later we will define the emittance of a beam as the average action variable of all particles… but for the moment we stick to single particles … and we follow them through magnetic elements.
Increasing t

## Slide 19
Why at all “Hamiltonians”?
Why not just Newton’s law and Lorentz force? Newton requires rectangular coordinates and time ; for curved trajectories one needs to introduce “reaction forces”.
Hamiltonian equations of motion are two systems of first order <-> Lagrangian treatment yields one equation of second order.
Hamiltonian equations use the canonical variables p and q, Lagrangian description uses q and and t p, q are independent, the others not.
Several people use Hill’s equation as starting point: - always needs an “Ansatz” for a (periodic) solution: No real accelerator is built fully periodically - Hill’s equation follows directly out of a simplified Hamiltonian description (later slide)
Last not least: (material of the CAS advanced course: ) The Poisson brackets of p or q with the Hamiltonian encode the time behaviour of p and q: Basis for any numerical integration (Werner Herr, Non Linear Dynamics II)

## Slide 20
Particle Motion through accelerator components
Linear treatment: matrix multiplication
()= ()
More general treatment: application of a map:
()= ()
the map can be any function of x and x’, but must not depend on the input parameters x (s0) and x’(s0);
the map must be symplectic ( more details: again W. Herr this course) (by the way: every matrix is a map, but not every map is a matrix) Symplecticity:  energy conservation
Following a particle through various elements is equivalent to multiplying the maps.
First (simple) case:

## Slide 21
Back to the Hamiltonian for a moment:
So far we have been switching from time-dependent variables to s-dependent variables without paying attention to it: In a linear 1 D motion this is a equivalent since s= vt But if we want to describe motion transverse to a curved reference line, we must use “s” as independent variable. At every moment we have perpendicular to the tangent vector of the particle trajectory a transverse Cartesian coordinate system.

## Slide 23
Where are we now? - we describe every element in the trajectory of a particle with the corresponding Hamiltonian. - we describe the particle motion through an element by a matrix (map) multiplication onto its phase-space vector. - we generate more complex accelerator configurations by multiplying the maps of the induvial elements. - we have changed the coordinate system and describe now the trajectory of a particle as a function of “s” and not of “t”. - But: we are still treating single particles in a single passage through an accelerator component.
What comes next? - We show that Hill’s equations come naturally out of the Hamiltonian formalism
- We look at transverse focusing…in particular a FODO lattice - We look again and again at phase space diagrams.

## Slide 25
Such a field (force) we need for focusing

## Slide 26
Weak focusing from dipoles
This means that we can construct a focusing circular accelerator based only on dipoles… in particular when ρ is small. This has been done in the 1950’s and it was called “ a weak focusing synchrotron” For this evening (with a cold beer): How about the vertical plane? There are no dipoles. Or why do the particles not fall down?

## Slide 27
We need stronger focusing….quadrupoles
Negative = focusing

## Slide 28
The negative sign in the Hamiltonian makes the same quadrupole defocusing the other plane.
Positive = defocusing

## Slide 30
Transfer Matrix in 6-D
In order to calculate numbers one usually defines a FODO cell from the middle of the first F-quadrupole up to the middle of the last F-quadrupole.
Hence the resulting transfer matrix looks a little different:
M= (2() ()

## Slide 32
More details on the Illustrating Example
1mm

## Slide 35
Our first synchrotron
The previous example of 100 consecutive FODO cells describes very well a regular transport line or a linac (in which we have switched off the cavities).
If we add dipoles into the driftspaces, the situation for the transverse particle motion does not change (neglecting the weak focusing part).
So actually with the previous description we also describe a very simple regular synchrotron. The phase space ellipse we can compute provided we know the total transfer map (matrix) Mtot:
J= () ()
The phase space plots will look qualitatively the same as in the previous case.
Definition: trajectory (single passage) or closed orbit (multiple passages): (1) Fix point of the transfer matrix…in our cases so far the “0” centre of all ellipses.

## Slide 36: Orbit Acquisition
Horizontal
Vertical
This orbit excursion is too large!

## Slide 37: Orbit Correction (Operator Panel)

## Slide 38: Orbit Correction (Detail)

## Slide 39
Courant – Snyder formalism / Twiss parameters
Same beam dynamics
Introduced in the late 50’s by
The classical way to parametrize the evolution of the phase space ellipse along the accelerator
Basic concept of this formalism:
1) Write the transfer matrix in this form (2 dimensional case):
I =; A=
2) M must be symplectic  = 1
3) Four parameters: , with one interrelation (2)  Three independent variables
4) Again, the preserved action variable J describes an ellipse in phase-space:
( + p + )

## Slide 41
Example: Propagation of twiss parameters along s between two focusing quadrupoles
Example: Beta function between two strong focusing quadrupoles
=

=
Drift M =
Starting from waist
And in Matrix-Annotation:
= = =
Using: = 1
=
- 2SC +

## Slide 42
Interpretation of the Twiss parameters (1/2)
1) Horizontal and vertical beta function
Proportional to the square of the projection of the phase space ellipse onto the space coordinate
Focusing quadrupole  low beta values
Although the shape of phase space changes along s, the rotation of the particle on the phase space ellipse projected onto the space co-ordinate looks like an harmonic oscillation with variable amplitude: called BETATRON-Oscillation

## Slide 43
α indicates the rate of change of β along s α zero at the extremes of beta (waist)
ds
Phase Advance: Indication how much a particle rotates in phase space when advancing in s
Of particular importance: Phase advance around a complete turn of a circular accelerator, called the betatron tune Q (H,V) of this accelerator
=
Interpretation of the Twiss parameters (2/2)
2.)
3.)

## Slide 44
The betatron tunes
Part of the most important parameters of a circular accelerator
The equivalent in a linac is called “phase advance per cell”
For a circular accelerator it is the phase advance over one turn in each respective plane.
In large accelerators the betatron tunes are large numbers (LHC ˜ 65), i.e. the phase space ellipse turns about 65 times in one machine turn.
We measure the tune by exciting transverse oscillations and by spectral analysis of the motion observed with one pickup. This way we measure the fractional part of the tune; often called
Integer tunes (fractional part= 0) lead to resonant infinite growth of particle motion even in case of only small disturbances.

## Slide 45
Importance of betatron tunes
The couple (QH ,QV ) is called the working point of the accelerator.
Below: tune measurement example from LEP

## Slide 46
Slides on “off-momentum” particles in a synchrotron
What happens: A particle with a momentum deviation > 0 gets bent less in a dipole.
In a weakly focusing synchrotron it would just settle to another circular orbit with a bigger diameter
In an alternate gradient synchrotron it is more complicated: The focusing/defocusing is also dependent on the momentum, so the resulting orbit follows the optics of the accelerator.
We describe the dispersion as a function of s as ; the resulting position of a particle is thus simply: = +
Typical values of D(s) are some meters, with = the orbit deviation becomes millimeters

## Slide 47
Measurement example
HERA Standard Orbit
dedicated energy change of the stored beam
 closed orbit is moved to a
dispersions trajectory
HERA Dispersion Orbit
This gives also an example of an orbit measurement.
More on this: again R.Jones (BI)

## Slide 48: Momentum compaction factor
If a particle is slightly shifted in momentum it will have a different orbit and the orbit length is different.
The “momentum compaction factor” is defined as:
p+p
p
Typical numbers: … ; 
 Much more on this in long. dynamics (F. Tecker).

## Slide 50: Finally: a beam
We focus on “bunched” beams, i.e. many (10 11) particles bunched together longitudinally (much more on this in the RF classes).
From the generation of the beams the particles have transversally a spread in their original position and momentum.
Source: ISODAR (Isotope at rest experiment)

## Slide 51: Gaussian beam profile in x and p

## Slide 52: Liouville’s Theorem (1/2)
All particle rotate in phase space with the same angular velocity (in the linear case)
All particle advance on their ellipse of constant action
All constant action ellipses transform the same way by advancing in “s”
 Since volumes in phase space are preserved, (1)-(3) means That the whole beam phase space density distribution transforms the same way as the individual constant action ellipses of individual particles.

## Slide 53: Liouville’s Theorem (2/2)
We now define the emittance of a beam as the average action of all particles!
 Since the action J of a particle is constant and the phase space area A covered by the action ellipse is we can represent the whole beam in phase space by an ellipse with a surface = *  all equations for the propagation of the phase space ellipse apply equally for the whole beam
!!! In case we talk about a single particle, the ellipse we draw is “empty” and any particle moves from one point to another; if we consider a beam, the ellipse is full of particles!!!
There are several different definitions of the emittance ε, also different normalization factors. This depends on the accelerator type, but the above definition describes best the physics.
Another often used definition is called RMS emittance or attention: the first definition describes well the physics, the second describes what we eventually can measure
*

## Slide 54: RMS emittance
Notes: 11 m

## Slide 55: Importance of RMS emittance
Even when the phase-space area is zero, if the distribution lies on a curved line its rms emittance is not zero.
RMS emittance is not an invariant for Hamiltonian with non linear terms.

## Slide 56: Remarks
We have already identified the action as a preserved quantity in a conservative system   the emittance of a particle beam is preserved in a conservative beam line.
The sentence above is often quoted as Liouville’s theorem, but this is incorrect. Liouville’s theorem describes the preservation of phase space volumes, the preservation of the phase space of a beam is then just results from the Hamiltonian description.
We can identify the constant in the previous equation:

## Slide 57: More on beam emittance
The reference momentum increases during acceleration
we can show:
So the transverse emittances scale with the product
For this reason we define:
Other ways to influence the emittance (advanced subjects): - make it bigger by error (injection errors….) - make it smaller by cooling (stochastic cooling; electron-cooling….)
Not to be confused with: Radiation damping = Reduction in emittance due to the emission of photons as synchrotron radiation
normalized emittance : = and we call the geometric emittance The “shrinking” of the transverse emittance during acceleration is called “adiabatic damping” (only scales with energy)

## Slide 58: What do we normally measure from the phase-space ellipse?
At a given location in the accelerator we can measure the position of the particles, normally it is difficult to measure the angle…so we measure the projection of the phase space ellipse onto the space dimension: called a profile monitor
+ D
Attention! The standard 2 D image of a synchrotron light based beam image is NOT a phase space measurement

## Slide 59: Phase space mapping
Measurements
Simulations

## Slide 60: Phase space evolution
A. Cianchi et al., “High brightness electron beam emittance evolution measurements in an rf photoinjector”, Physical Review Special Topics Accelerator and Beams 11, 032801,2008

## Slide 61: A first taste of non-linearities (1/6)
So far we have completely neglected the longitudinal plane
Still, we will not couple the motion in the longitudinal and transverse plane (advanced course), but we need to consider “off momentum particles” with a longitudinal momentum .
We already defined the Dispersion function, which describes the change in orbit
Now we look at what happens to the focusing in the quadrupoles:

## Slide 62: A first taste of non-linearities (2/6)
Due to the change in focusing strength of the quadrupoles with varying momentum, particles have different betatron-tunes:
Definition: Chromaticity (H,V) := Dependence of tune on momentum
or relative chromaticity
Is this bad? : Yes, the working point gets a “working blob”
We need to correct. How? i) Inserting a magnetic element where we have dispersion (this separates in space particles with lower and higher momenta ii) Having there a “quadrupole”, for which the strength grows for larger distances from the centre: a sextupole

## Slide 63: A first taste of non-linearities (3/6)
We will have a high price to pay for this chromaticity correction!  we have introduced the first non-linear element into our accelerator
The map M (no longer a matrix) of a single sextupole represents a “kick” in the transverse momentum:
We choose a fixed value k2L = - 600 m-2 and we construct phase space portraits after repeated application of the map.
We vary the phase advance per turn (fractional part of the tune) from

## Slide 64: A first taste of non-linearities (4/6)

## Slide 65
A first taste of non-linearities (6/6)

## Slide 66
Another useful example: Injection missteering
Example:

## Slide 73
Linear Imperfections
Up to now we have constructed an alternate –gradient focusing synchrotron
We have a well chosen working point
We have corrected chromaticity
(We still cannot accelerate!  see F. Tecker (long. Dynamics)
We assume: - All magnetic elements have the calculated field strength and field quality - All magnetic elements are in the right place and powered with the right polarity
Reality tells us: - Magnets have field errors, have other multipole components, have time varying fields due to ripple in the connected power converter - Magnets are wrongly mounted with horizontal and/or vertical offsets, rotations or tilts
These effects influence: - the beta functions and phase advance around the ring (implicitly the tunes) - the closed orbit - the coupling between horizontal and vertical motion …
We need to diagnose and correct: Strong interaction between beam measurements and corrections (see also R.Jones BDI talks)

## Slide 74
Dipole Errors

## Slide 75
Quadrupole Errors (1/2)

## Slide 76
Quadrupole Errors 2/2

## Slide 77
Beta-beating (1/2)

## Slide 78
Beta-beating (2/2)

## Slide 79
Quadrupole Errors 3/3
Any tilted quadrupole is seen as a normal quadrupole plus another quadrupole tilted by 450. (skew quad)
Note that in a skew quad
Fx = ksy and Fy = ksx produce coupling between the x and y planes
Additional skew quads in an accelerator are used to compensate coupling

## Slide 80
Coupling control is most important in synchrotron light sources, since small vertical emittance (yielding high brightness of the photon beams) is predominantly achieved by decoupling the x and y planes.

## Slide 81
Last not least: Sextupole errors (1/2)

## Slide 82
Last not least: Sextupole errors (2/2)
A horizontally (vertically) displaced sextupole is seen as a centred sextupole plus an offset quadrupole (skew quadrupole)

## Slide 83
Correction summary
Effect of dipole kicks () on closed orbit (CO)
Effects of strength error in quadrupoles
Best correction: identify error source and repair(realignment; coil repair…)
If not: Typically close to every quadrupole small dipole correctors are installed. So by measurement campaigns and data analyses corrections strength for these small dipoles and to (skew) quadrupoles are applied.
More on this in the diagnostics lecture and the advanced part.

## Slide 84
Last not least: Collective effects
Collective effects:
= Summary term for all effects when the coulomb force of the particles in a bunch can no longer be neglected; in other words when there are too many particles…
We distinguish: i) self interaction of the particles within a bunch: 1) space charge effects
2) Intra beam scattering 3) Touschek scattering leads to emittance growth and particle loss
ii) Interaction of the particles with the vacuum wall concept of impedance of vacuum system leads to instabilities of single bunches and multiple bunches
iii) Interaction of with particles from other counter-rotating beam  beam-beam effects ( more later this school)
Most is very advanced matter  here only concepts and buzz-words

## Slide 85
Space-charge Forces

## Slide 86
Space Charge: Scaling with energy
Electrical field : repulsive force between two charges of equal polarity Magnetic field: attractive force between two parallel currents after some work:
 space charge diminishes with scaling  each particle source immediately followed by a linac or RFQ for acceleration
Recall from relativity

## Slide 87
Space Charge Tune Shift

## Slide 88
“footprint” of particles with space charge tune shift.
The effect dramatically reduces at higher energies
Space charge always
defocusing

## Slide 89
Intrabeam Scattering

## Slide 90
Touscheck effect

## Slide 91: Interaction of beam with vacuum chamber

## Slide 92: Bunch in a conducting pipe with sudden change
v
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
v
v
v

## Slide 93: All together
beam
Accelerator
L
C
R
beam

## Slide 95: Impedance
Impedance
The real (resistive) part dissipates energy, the imaginary part creates instabilities

## Slide 96: Consequences of impedances
Energy loss on pipes  heating (important in a superconducting accelerator)
Tune shift
long bunch
short bunch
Broad
Band
Model
narrow
resonances
Single bunch instabilities (head-tail)
Multibunch instabilities

## Slide 97
1) Back to school: relativity, EM fields, magnets…
2) Hamiltonian and canonical variables  equations of motion + invariants; map-approach 3) Single particle in various magnetic elements…action as invariant 4) multiple elements; circular accelerator
5) Twiss parameters
6) Finally a beam: emittance and emittance preservation
7) A taste of non-linearities
8) Linear imperfections (and some corrections)
9) Collective effects
Summary

## Slide 98
Recommended reading:
A. Wolski, Beam Dynamics in high energy particle accelerators, Imperial College Press, ISBN 978-1-78326-277-9
CAS proceedings and references therein