Trigger/DAQ design:
from test beam to medium size experiments
ISOTDAQ 2018
Vienna – Technical University
17 February 2018

---
credit to Sergio Ballestrero
most material from his talk at ISOTDAQ 2015

---
Trying to move …
from here:
to here:

---
Medium/Large DAQ: constituents

---
trying to get there in 5 steps ...
- Step 1: Increasing the rate
- Step 2: Increasing the sensors
- Step 3: Multiple Front-Ends
- Step 4: Multi-level Trigger
- Step 5: Data-Flow control

---
Trigger & DAQ in HEP
Trigger
rate
DAQ
ev. size
different issues → different solutions
no magic, unique solution for all cases

---
step one: increase rate
Single-event readout:
- wait for data (poll/irq)
- read ADC
- clear & re-enable ADC
- re-format data
- write to storage
trigger
dataflow

---
LHC (collider) → synchronous
… nevertheless, high luminosity & high cross sections
        → high rate, high-pileup, large events:
→ most events uninteresting
→ good events (triggers) uncorrelated (unpredictable)
→ de-randomisation still needed
→ dataflow is an issue

---
Dead Time  de-randomise
Processing → bottleneck ?
Buffering → decouple problems
Dead time ~ (1+x)-1 ~ 50%
[ for x = 1/(f·τ)‏ ~ 1 ]
Dead time ~ (∑0..N rj)-1 ~ 1/(N+1)
[ N = buffer depth ]
[ r = f(out)/f(in) ]

---
buffering solve all problems ?
FIFO
1) filling at very variable input flow
2) emptying at smoothed output flow
 the Leaky-Bucket problem
Q: how often may overflow ?

---
off-topic: some very basic queueing theory
N-event buffer ... single queue size N:
Pk : % time with k events in	PN = no space available  dead time
∑Pk=1 [ k=0..N ]
rate(jj+1) = λ·Pj (fill at rate λ)
rate(j+1j) = μ·Pj+1 (empty at rate μ > λ)
steady state: λ·Pj=μ·Pj+1 ⇒ Pj+1=ρ·Pj=ρj+1·P0 where ρ = (λ/μ) <~1
for ρ~1 ⇒ Pj~Pj+1 ⇒ ∑Pk~(N+1)·P0=1 ⇒ P0~PN~1/(N+1)
⇒ dead time ~ 1/(N+1)
want ≤ 1% ⇒ N ≥ 100

---
off-topic: some very basic queueing theory
N-event buffer ... single queue size N:
Pk : % time with k events in ; PN = no space available  dead time
∑Pk=1 [ k=0..N ]
rate(jj+1) = λ·Pj (fill at rate λ)
rate(j+1j) = μ·Pj+1 (empty at rate μ > λ)
steady state: λ·Pj=μ·Pj+1 ⇒ Pj+1=ρ·Pj=ρj+1·P0 where ρ = (λ/μ) <~1
for ρ~1 ⇒ Pj~Pj+1 ⇒ ∑Pk~(N+1)·P0=1 ⇒ P0~PN~1/(N+1)
⇒ dead time ~ 1/(N+1)
want ≤ 1% ⇒ N ≥ 100
Take care: analytic calculation possible for pretty simple systems only

---
de-randomisation
1/f = λ

We can now attain a FIFO efficiency ~100% with:
τ ~ 1/f
“moderate” buffer size
Two degrees of freedom to play with
This dead time often managed by trigger system itself (“complex dead time”)
FIFO

---
Complex Dead Time
1) Simple dead time: avoid overlapping (conflicting) readout window
2) Complex dead time: avoid overflow in front-end buffers (protection against trigger bursts)
e.g. ATLAS: simple leaky-bucket algorithms with 2 parameters:
max X triggers (X = FIFO depth) in any (sliding) time window = (X*readout time)

---
Game over ?
many other possible limits even in a simple DAQ

---
→ the sensor
- Sensors limited by physical processes such as:
  - drift times in gases
  - charge collection in Si
- (possibly) choose fast processes
- analog F.E. imposes limits as well
- split the sensors, each gets less rate:
  “increase granularity”

---
→ the ADC
- A/D F.E. is also limited
- Faster ADCs pay the price in precision (# of bits) and power consumption
- Alternatives:
  - analog buffers
- You may need integration (or sampling) over quite some time
[ see Detector Readout and FE lectures ]

---
An example
- HPGe + NaI Scintillator
  High res spectroscopy and beta+ decay identification
- minimal trigger with busy logic
- Peak ADC with buffering, zero suppression
- VME SBC with local storage
- 3×12 bits data size
  + 32 bit timestamp
- Root for monitor & storage
- Rate limit ~14 kHz
  - HPGe signal shaping
    for charge collection
  - PADC conversion time

---
→ the trigger
- simple trigger: ~fast
- complex trigger logic: not obvious [ even when all in hw ]
- some trigger detectors may be far away / slow → latency
- trigger signal is one: all information at a single point
  - in one step:
    too many cables
  - in many steps:
    delays
→ discrete modules: ~ 5-10 ns delay → tot. latency ≥ 20-30 ns ←

---
DREAM (2006→): a Testbeam Case
R&D on dual-readout calorimetry, setup:
Crystals
Scintillating/cherenkov fibers in lead/copper matrices
Scintillator arrays as shower leakage counters
Trigger/veto/muon counters
Precision chamber hodoscope
… always evolving
Acquiring: waveforms, total charge, time information

---
DREAM (2006): a Testbeam Case
a possible SPS cycle
duty cycle:
~2 s / 14.4 s
(flat top)
flat top
slow extraction
Trigger = ( V×T1×T2 | ped )  easy !

---
Spill-driven (asynchronous) Trigger
Trigger = V×T1×T2 | ped
Busy
Veto
Spill
Fast Gate
Trigger OR
to xDC.s
T1×T2
FADC Trigger
(oscilloscope)‏
from DAQ
Re-enable
to DAQ
Ped Veto
Other signals  monitoring/debugging‏
Ped Tr.
First discrete, then FPGA (Xilinx Spartan 3AN evaluation board)

---
DREAM DAQ
1 PC  2 VME crates (access via CAEN optical interfaces) + 1 PC  storage
6 x 32 ch xDC.s (x = Q, T : CAEN V792, V862, V775 )
1 x 34 ch (CAEN V1742) 5 Gs/s Digitizer (single event: ~34x1024x12bit)
1 x 4 ch Tektronix TDS7254B 20 Gs/s oscilloscope
… few VME I/O & discriminator boards
DAQ logic spill-driven (no “real time”, scientific linux desktop)
in-spill (slow extraction)
a) poll trigger signal … if trigger present:
b) read all VME boards (w/ DMA, whenever possible)
c) format & store on a large buffer (FIFO over RAM)
d) re-enable trigger
out-of-spill
a) read scope (in case)  size is fixed at run start
b.1) monitor data (produce root files)
b.2) store on disk files (beam and pedestal files) over network
rate ~ O(1 kHz)

---
→ the dataflow
- Data Processing may be ~ easy and scalable
- Data Transport may not be easy
- Final storage is expensive
  (and at some point not easy either) → can't store all data you may acquire

---
step two: increase # of sensors
- More granularity at the physical level
- Multiple channels
  (usually with FIFOs)
- Single, all-HW trigger
- Single processing unit
- Single I/O
ADC
storage
N channels
Trigger
Processing

---
multi-channels, single PU
- common architecture in test beams and small experiments
- often rate limited by (interesting) physics itself, not TDAQ system
- or by the sensors
ADC
storage
N channels
Trigger
Processing

---
bottlenecks: PU and storage
- a single Processing Unit can be a limit
  - collect / reformat / compress data can be heavy
  - simultaneously writing
    storage
- final storage too:
  - VME up to 50MB/s
    -> 1TB in 6h
    too many disks in a week!
Laptop SATA disk: 54MB/s; USB2: ~30MB/s
ADC
storage
N channels
Trigger
Processing

---
→ decouple storage from PU
- data transfer data → dedicated “Data Collection” unit to format, compress and store
- more room for smarter processing or decreased dead time on non-buffered ADCs
ADC
storage
N channels
Trigger
Processing
Data
Collection

---
bottlenecks: trigger
- to reduce data rates
  (to avoid storage issues)
  → non-trivial trigger
- complexity may already hit manageability limits for discrete logic (latency!)
- integrated, programmable logic came to rescue (FPGA)
  → latency may go down to O(few ns)
ADC
storage
N channels
Trigger
Processing

---
another example: NA43/63
- Radiation processes: coherent emission in crystals and structured targets, LPM suppression...
- 80/120 GeV e- from
  CERN SPS slow extraction
- 2s spill every 13.5s
- Needs very high angular resolution
- Long baseline + high-res, low material detectors
  → drift Chambers
- 10 kHz limit on beam for radiation damage
- results in typical 2-3 kHz physics trigger

---
NA43/63
- 30-40 TDC, 6-16 QDC, 0-2 PADC
  (depending on measurement)
- CAMAC bus
  1 MB/s, no buffers, no Z.S.
- single PC readout
- NIM logic trigger
  (FPGA since 2009)
  - pileup rejection
  - fixed deadtime

---
step three: multiple PU (SBC)
- e.g.: CERN LEP experiments
- complex detectors,
  moderate trigger rate,
  very little background
- little pileup, limited channel occupancy
- simpler, slow gas-based main trackers
LEP
- 105 channels
- 22μs crossing rate
  - no event overlap
- single interaction

---
NOMAD (1995-1998)
- Search for νμντ oscillations at the CERN WA neutrino facility (WANF)
- 2.4×2.4 m2 fiducial (beam) area
- Two 4ms spills with 1.8×1013 P.o.T. each (ν spills)
- One (2s) slow-extraction spill (μ spill)
- 14.4s cycle duration
trigger counters
veto counters
→ DAQ layout

---
WANF - SPS SuperCycle
14.4 s cycle length
2 × 4 ms neutrino spills (f/s extractions)
1 × 2 s muon spill (slow extraction)
f/s extractions
slow extraction

---
Triggering once more ...
menu for NOMADs:
ν-spill triggers
μ-spill triggers
~3m
veto counters (central shaded area is V8)
~3m

---
Triggering  FPGA.s at work
MOdular TRIgger for NOmad (MOTRINO):
6 VME boards providing local and global trigger generation and propagation

---
NOMAD DAQ
- ~30(?) (64 or 96 channel) Fastbus xDC [ x=Q,P,T ] boards
- Typically:
    - ~15 evts in each 4ms spill (neutrino triggers)
    - ~60 evts in each 2s spill (muon triggers)
    - 256-events in off-spill calibration cycles (calibration triggers)
  - On spill(cycle): on-board buffering of up to 256 events (no way to read event-by-event)
  - End of spill(cycle): block transfer to 5 VME PU.s (motorola 68040 FIC8234 board, OS9 real-time system)
  - Event building and storage on another VME PU
  - Monitoring and control on SunOs/Solaris workstations
     on-board buffering
     data processing done off-spill (i.e. off-beam)

---
bottlenecks ?
- trigger complexity ↔ storage
- single HW trigger not sufficient to reduce rate
- add L2 Trigger
- add HLT

---
step four: multi-level trigger
Typical Trigger / DAQ structure at LEP
- more complex filters
- → slower
- → applied later in the chain
see Trigger lectures
LEP
- 105 channels
- 22μs crossing rate
  - no event overlap
- single interaction
- L1 ~103 Hz
- L2 ~102 Hz
- L3 ~101 Hz
- 100kB/ev → 1MB/s

---
ATLAS!
LHC
- 107 channels
- 25ns crossing rate
  - high event overlap
- 20 interactions
- L1 ~105 Hz
- L2 ~103 Hz
- L3 ~102 Hz
- 1MB/ev → 100MB/s
ATLAS T&DAQ Why & How, L. Mapelli @ISOTDAQ 2010

---
ATLAS Run-1 Architecture
- Still 3-level trigger
- buffers everywhere
- L2 on CPU, not HW, but limited to ROIs
- L3 using offline algorithms
- “economical” design: the least CPU and network for the job
see “TDAQ for the LHC experiments and upgrades” lecture

---
ATLAS Run-2 Architecture
→ Merge L2 and L3 into a single HLT farm
  - preserve Region of Interest but dilute the farm separation and fragmentation
  - increase flexibly, computing power efficiency

---
Off-Topic: Event Selection Latency
- L1 : O(1 μs in real-time), let say = 2.5 μs
- L2 : O(10 ms) → let say = 40 ms
- L3(HLT) : O(s) → let say = 1 s
    Q: do these 3 numbers mean the same thing ?

---
Latency and Real-Time
real time: system must respond within some fixed delay
→ Latency = Max Latency
→ over fluctuations bad, will create dead time
non-real-time: system responds as soon as it’s available
→ Latency = Mean Latency
→ over fluctuations fine, shouldn’t create dead time
real time o.s. :
very stable time delay in responding to events
standard unix kernels are not real time:
    a system call can in principle take any time

---
Off-Topic: Real-Time Linux
Low-latency patch
(Ubuntu Studio):
Interruptible linux kernel
RTAI: linux kernel runs as a higher priority application

---
CMS!
CMS TDAQ Design - S. Cittolin @ISOTDAQ 2010

---
CMS Architecture
- Only two trigger levels
- Intermediate event building step (RB)
- larger network switching
see “TDAQ for LHC” lecture
- upgrade: no architectural changes but:
  - all network technologies replaced
    - Myrinet → Ethernet
    - Ethernet → Infiniband
  - file-based event distribution in the farm
    - full decoupling between DAQ and HLT

---
Evolution for Run 2
  ATLAS:
- more like CMS
… still using “L2” ROI, but as first step of a unified L2/EB/HLT process
    CMS:
  - more like ATLAS
- … still doing full EB, but analyse ROI first
DAQ@LHC Joint Workshop 2013 :
http://indico.cern.ch/conferenceOtherViews.py?view=standard&confId=217480

---
step five: dataflow control
- Buffers are not the <final solution> they can overflow due to:
  - bursts
  - unusual event sizes
- Discard
  - local, or
  - “backpressure”,
    tells lower levels to discard
Who controls the flow?
FE (push) or EB (pull)

---
a push example: KLOE
- DAΦΝΕ e+e- collider in Frascati
- CP violation parameters in the Kaon system
- “factory”: rare events in a high-rate beam
- 105 channels
- 2.7 ns crossing rate
  - rarely event overlap
  - “double hit” rejection
- high rate of small events
- L1 ~104 Hz
  - 2μs fixed dead time
- HLT ~104 Hz
  - ~COTS, cosmic rejection only
- 5 kB/ev → 50 MB/s [design]

---
KLOE
- deterministic FDDI network
- not real need for buffering at FE
- push architecture
  vs pull used in ATLAS
  see DAQ Software lecture
- try EB load redistribution before resorting to backpressure
EB
Which LHC experiment has a somewhat similar dataflow architecture ?

---
LHCb: dataflow is network
The LHCb Data Acquisition during LHC Run 1
CHEP 2013
more info in “TDAQ for the LHC experiments”

---
Looking forward to LS2 and beyond
On some long term, all experiments looking forward to significant increase in L1 trigger rate and bandwidth. ALICE and LHCb will pioneer this path during LS2
DAQ@LHC Workshop
- First level trigger for Pb-Pb interactions 500 Hz → 50 kHz
- 22 MB/event
  - 1 TB/s readout → 500 PB/month
- Data volume reduction
  - on-line full reconstruction
  - discard raw-data
- Combined DAQ/HLT/offline farm
  - COTS, FPGA and GPGPU
- 1 MHz → 40 MHz readout and event building → trigger-less
  - trigger support for staged computing power deployment
- 100 kB/event
  - on-detector zero suppression → rad-hard FPGA
  - 4 TB/s event-building

---
Trends
- Integrate synchronous,
  low latency in front end
  - limitations do not disappear, but decouple (factorise)
  - all-HW implementation
  - isolated in replaceable(?) components
- Use networks as soon as possible
- Deal with dataflow instead of latency
- Use COTS network and processing
- Use “network” design already at small scale
  - easily get high performance with commercial components

---
take care, lot of issues not covered:
  Hw configuration
  Sw configuration
  Hw control & recovery
  Sw control & recovery
  Monitoring
  …

---
Lost & Found
(off-topics)

---
Appendix A: Cables and Transmission Lines
Spoken about signals, amp.s, digitisers, … but ...
… almost nothing about how signals are transmitted over long distances. Is there any issue ?
    Q(1): what is a cable (for a single signal) ?
        a couple of ideal conductors (R=C=L=0) ?
    Q(2): which speed can it reach ?
    Q(3): what’s its impedance ?
    Q(4): what does it to your signal ?
    Ok the full line must be properly matched:
              Z(out) = Z(cable) = Z(in) That’s all ?

---
Cables and Transmission Lines
Lossless transmission line:
Lossy transmission line:

---
Cables
1. Cable element (dz):
2. R depends on the frequency (skin effect)‏
  G should be negligible
3. Z = (L/C)½
        vp = (LC)-½ = (με)-½
size 12{L approx { {μ} over {"2π"} } "ln" left ( { {b} over {a} } right )" " left ["H/m" right ]} {}
size 12{C approx { {2 ital "πε"} over {"ln" \( b/a \) } } " " left ["F/m" right ]} {}

---
Cables
Equation for standing waves:
solution:
R usually dominated by the skin effect:
R(ω) = r*D/(4*δ)
1. ‏
  r = resistance per unit length
  D = diameter internal conductor
  δ = skin depth ~ 1/√ω
size 12{ { { partial rSup { size 8{2} } V} over { partial z rSup { size 8{2} } } } ital "=LC" { { partial rSup { size 8{2} } V} over { partial t rSup { size 8{2} } } } + \( ital "LG+RC" \) { { partial V} over { partial t} } ital "+RGV"} {}
size 12{alignl { stack { { {d rSup { size 8{2} } V} over { ital "dz" rSup { size 8{2} } } } = \( ital "R+iωL" \) \( ital "G+iωC" \) ital "V=γ" rSup { size 8{2} } V {} # ital "γ=α+ik=" sqrt { \( ital "R+iωL" \) \( ital "G+iωC" \) } {} } } } {}

---
Cable Losses
Neglecting the transconductance G:
50-Ohm fast (v = 4 ns/m) CERN-store cables:
        04.61.11.F - COAXIAL CABLE 50 OHM - TYPE C-50-6-1
        04.61.11.H - COAXIAL CABLE 50 OHM - LOW LOSS - TYPE C-50-11-1
f(-3db, 40 m, cable C-50-6-1) ~ 120 MHz
        f(-3dB, 40 m, low loss cable) ~ 640 MHz
size 12{alignl { stack { ital "α=R" left (ω right )/ left ("2Z" rSub { size 8{0} } right ) "~" c sqrt {ω} {} # ital "k=ω" sqrt { ital "RC"} ital "=ω"/ left ( ital "βc" right ) {} } } } {}
size 12{alignc { stack { V \( ital "z,t" \) ital "=V" rSub { size 8{1} } "exp" \( - ital "αz" \) "exp" left [i \( ital "ωt" - ital "kz" \) right ] {} # {} } } } {}

---
Signal Distortions
Time parameter:
μz ~ 32*E-6 (C-50-6-1), 14E-6 (low loss cables)‏
*** Take care: would like τ0 << τ(signal)‏
size 12{alignl { stack { α "~" μ sqrt {f} {} # τ rSub { size 8{0} } = left ( ital "μz" right ) rSup { size 8{2} } /π {} } } } {}
size 12{alignl { stack { τ rSub { size 8{0} } "~" "320" ital "ns" left (C - "50" - 6 - 1 right ) {} # τ rSub { size 8{0} } "~" "60" ital "ns" left ( ital "lowlosscables" right ) {} } } } {}

---
Digital Pulse Distortions
size 12{alignl { stack { "for " ital "α " "~" a sqrt {f} {} # τ rSub { size 8{0} } = \( ital "a z" \) rSup { size 8{2} } /π {} } } } {}

---
Bandwidth Effects – Analog Signals
~1ns analog-signal response for
BW ~ 300, 150, 75, ... MHz
signal in
signal out

---
Appendix B: backtrace
Segfaulting ? Have a look at backtrace:
https://www.gnu.org/software/libc/manual/html_node/Backtraces.html
BACKTRACE(3) Linux Programmer's Manual BACKTRACE(3)
NAME
       backtrace, backtrace_symbols, backtrace_symbols_fd - support for application self-debugging
SYNOPSIS
       #include <execinfo.h>
       int backtrace(void **buffer, int size);
       char **backtrace_symbols(void *const *buffer, int size);
       void backtrace_symbols_fd(void *const *buffer, int size, int fd);

---
HowTo
1) file “my_segf.cxx” : install a signal handler to print the backtrace
#include <stdio.h>
#include <execinfo.h>
#include <signal.h>
#include <stdlib.h>
#include <unistd.h>
void handler(int sig) {
  void *array[10];
  size_t size;
  // get void*'s for all entries on the stack
  size = backtrace(array, 10);
  // print out all the frames to stderr
  fprintf(stderr, "Error: signal %d:\n", sig);
  backtrace_symbols_fd(array, size, STDERR_FILENO);
  exit(1);
}
void baz() {
 int *foo = (int*)-1; // make a bad pointer
 printf("%d\n", *foo); // causes segfault
}
void bar() { baz(); }
void foo() { bar(); }
int main(int argc, char **argv) {
  signal(SIGSEGV, handler); // install our handler
  foo(); // this will call foo, bar, and baz. Baz segfaults.
}

---
2) compile with -g debug flag on:
g++ -g -rdynamic my_segf.cxx -o my_segf
3) get the crash:
[roberto@bob-laptop ~]$ ./my_segf
Error: signal 11:
./my_segf(_Z7handleri+0x1c)[0x400a52]
/lib64/libc.so.6(+0x347e0)[0x7fa55f1c07e0]
./my_segf(_Z3bazv+0x14)[0x400aab]
./my_segf(_Z3barv+0x9)[0x400aca]
./my_segf(_Z3foov+0x9)[0x400ad6]
./my_segf(main+0x23)[0x400afc]
/lib64/libc.so.6(__libc_start_main+0xf1)[0x7fa55f1ac731]
./my_segf(_start+0x29)[0x400969]
handler
libc
my crash
4) crash is at (_Z3bazv+0x14) ... the function name is “_Z3bazv” (c++ function name mangling). How to get it ?
5) Demangle it thanks to:
http://demangler.com/
6) Take the Answer:
 → crash is at (baz+0x14)
baz()

---
7) crash is at (baz+0x14) ... open the debugger: gdb my_segf
(gdb) info address baz
Symbol "baz()" is a function at address 0x400a55.
8) so crash is at address (0x499a55+0x14) … then:
(gdb) info line *(0x400a55+0x14)
Line 24 of "my_segf.cxx" starts at address 0x400a65 <baz()+16>
   and ends at 0x400a7c <baz()+39>.
9) got it ! That’s not yet the reason but ...

---
Appendix C: Profiling
Take care: optimize your code – first of all - where it really needs. To get it, you may use of profiling.
for C/C++ code, look (for example) at this gprof tutorial:
        http://www.thegeekstuff.com/2012/08/gprof-tutorial/
Very simple, at least for standalone code ...

---
Appendix D: Trigger Coincidence
T1
T2
linear output
(bad for trigger)
veto
clock enable
shaped output
clock
(ok for trigger)
MM
MM = Monostable Multivibrator = One-shot Pulse Generator

---
Exercise: Time Analysis
1) Linear Output = T1 and T2 and not Veto
2) Shaped Output = Fixed-duration Pulse at ((rising edge of (T1 and T2)) and not Veto)
1) Veto must completely overlap T1 and T2
     Out-of-time veto may change the duration of (T1 and T2) coincidence
     Early (out-of-time) veto may cause the (T1 and T2) coincidence rising edge to jitter
2) Veto must only overlap the rising edge of (T1 and T2) → very short in-time veto is required
     Out-of-time veto may only veto the pulse generation but can’t never produce shorter or jittering pulses

---
Thank you for your patience …