## Slide 1: The CERN Neutrino Platform
CERN, 1st August 2017
Marzio Nessi, CERN & University of Geneva

## Slide 2: 2013 European strategy

## Slide 3: 2013 European strategy
Short and Long baseline in Europe under evaluation
LBNE in the US with a detector on the surface (10KT), MINOS operational
Very succefull T2K experiment taking good data and thinking about the future
Several non-accelerator based experiments producing important results (Daya Bay,..)
Evident need, at least in Europe, to give coherence and support to a fragmented community

## Slide 4: CERN n Platform Initial Mandate (2015)
Assist the various groups in their R&D phase (detectors and components) in the short and medium term and give coherence to a fragmented European Neutrino Community
Provide the n community with a test beam infrastructure (charged particles)
Bring R&D to the level of technology demonstrators in view of major construction activities
Continue R&D on n beam, as a possible basis for further collaborations
Support the short baseline activities (infrastructure & detectors)
Support the long baselines activities (infrastructure & detectors)
Be a partner in the physics exploitation

## Slide 5: We react on demands from the community : MOU framework
https://edms.cern.ch/document/1353815
~ 60 EU institutions
As of Today we have 6 MOU addenda active !!
& cooperation agreements with US-DOE and JINR
SPSC committee as an entry point

## Slide 6: We react on demands from the community : MOU frame
- 6 Projects presented to the SPSC and approved:
NP01: WA104, ICARUS as far detector for the US SBN
NP02: protoDUNE WA105, demonstrator + engineering prototype for a double ph. TPC
NP03: PLAFOND, an generic R&D framework
NP04: ProtoDUNE, engineering prototype for a single phase TPC
NP05: Baby Mind, a muon spectrometer for the WAGASCI experiment at T2K
Argon Cube : a modular TPC R&D
- A few Projects in the pipeline : T2K near detector, DUNE near detector, HPgas TPC, ENUBET, ….
- COOPERATION PROTOCOL with the US Neutrino Program (Neutrino Protocol signed in 2015, Addendum 1 just signed in 2017)

## Slide 7: How to continue and formalize new projects?
The SPSC committee will open a call for proposal of new Neutrino experiments in October 2017
After an analysis, there will be a recommendation to the CERN Research Board, for an approval and for further project details
The timing for the approval will depend on the required CERN resources
R&D on small projects or R&D projects preparation, if fitting in the Neutrino Platform existing possibilities, should go ahead without much delays. Best prepare the field with direct discussion with us.
For the ND280-II upgrade project we need to have soon a clarification discussion with the CERN Directorate. EOI submitted, status not fully clear.
In the mean time we have launched a generic ND preparation activity (see Stefania Bordoni next talk)

## Slide 8: Our Strategy
Act on direct requests from the community
Support in an effective way new inedit R&D proposals (hardware and software)
Try to bring in synergies between Neutrino community and the LHC community on specific technologies (DAQ, computing, electronics, …)
Host at CERN specialized researchers to make these projects more effective in the initial stage
Support large new projects with the necessary infrastructure, which just a big lab can offer
Offer to the community the collaborative experience and models, developed for the LHC

## Slide 9
LAr TPC (time projection chambers) technology emerged as the solution to be adopted in both, Short and Long baselines, in the US facilities
The technology for near detectors is more vague (both in US and Japan):
  Atmospheric or pressure TPCs
  Modular liquid argon TPCs
  Various trackers, calorimeters and muon spectrometers
All solutions need R&D (hardware & software) and an approach in steps, given the size and the complexity

## Slide 10: Wagasci experiment (P59) at JPARK
-- 3% precision H2O/CnHn cross-section ratio
-- Study of  energy reconstruction
-- wide angle  coverage
-- complementary to ND280
novel fine grain target

## Slide 11
Baby-MIND LAYOUT

Magnet module thickness:
50 mm (30 mm Fe)
Detector module thickness:
38 mm (31 mm CH).

## Slide 12
Wagasci/Baby-MIND Status and plans(II)
All magnetic and detector modules assembled
Full detector designed as 4 blocks
First tested in T9 test beam at CERN in May17
Full detector assembled and tested June-July’17
Ship to Japan in by Nov’17
Installation in B2 starting in Sep’17
Commissioning Oct’17-Mar’18
Start full data taking WAGASCI+ BabyMIND Apr’18
Baby-MIND
assembly of magnet modules at CERN
transport of first 20ton module in Apr’17
taking data at CERN in T9
NOW

## Slide 13: SBL @ FNAL
ICARUS T600
476t Active Mass
MicroBooNE
89t Active Mass
SBND
112t Active Mass
  A Multi-detector program will address the unexplained anomalies which together could be hinting at new physics (steriles?)

## Slide 14: SBL @ FNAL
2015 ICARUS moved from Gran Sasso INFN Laboratory to CERN
@CERN detector reshaped, new cryostats
2017 ICARUS moving to FNAL
2017-early 2018 installation at FNAL
2018 commissioning
mid 2018 operation (far detector, ICARUS)
2019 near detector installation and commissioning

## Slide 15
– new PMTs – new cabling - rework on cathodes – new cryostats – new electronics - ……

## Slide 16
http://cenf-wa104.web.cern.ch/wa104org/icarus-transportation-cern-fnal

## Slide 17: LBNF / DUNE : high intensity facility
FAR detector : ~40KT LAr eff. Mass
NEAR detector : ?

## Slide 18: DUNE : physics Int. Collaboration
Near Detector(s ?) : R&D just starting
FAR Detectors : 2 possible technologies based on LAr : single phase (ICARUS like), double phase (new)
Large computing activities and physics preparation (pattern recognition, trigger, systematics, …)

## Slide 19: LBNF Plans
Begin execution by DOE/FNAL of Sanford Lab “Reliability Projects” such as Ross Shaft refurbishment, to reduce risk during main excavation operations
Complete Preexcavation final design for Far Site conventional facilities
Execute Lease for LBNF exclusive use areas at Sanford Lab
Award CM/GC contract June 2017
Hold groundbreaking summer 2017 (scheduled on 21 July 2017)
Start construction activities at Sanford Lab in summer 2017
Start final design for cavern and drift excavation and surface facilities in summer 2017
Reach decision on optimized beamline preliminary design features in 2017
Complete underground and surface rock handling systems in 2018
Initiate major cavern excavation construction work in 2019
Complete first cryostat and cryo systems construction to enable detector install to begin in 2022, with commissioning in 2025
Produce neutrino beam in 2026

## Slide 20: KEY ISSUE : CRYOSTATS
LAr technology requires very special cryostats and cryogenics
  Large volume (~20 Ktons/cryostat)
  Installation underground with a difficult access
  Modular construction technique
  High purity requirements (ppb)
  Very high temperature and liquid stability
 LNG transport technique

## Slide 21: Membrane cryostats (LNG industry technology)
SS 1.2 mm primary membrane in contact with the liquid (primary containment)
secondary membrane : composite laminated material (secondary containment)
Insulation : reinforced polyurethane foam (5-6 W/m2)

## Slide 22: Demonstrator and Prototypes
Cryostats and Cryogenics need to be demonstrated and the techniques acquired
Single phase LAr detectors have to be extrapolated to the new scale (x 100), starting from the ICARUS and MicroBooNE experience. Cold electronics and automatic data reconstruction are the next challenges
Double phase LAr detectors have to be proven as concept and then extrapolated to the new scale

## Slide 23: DOUBLE PHASE Demonstrator (WA105/NP02)
The 3x1x1 m3 dual phase LAr TPC
LNG and cryogenics first lesson!
LAr TPC double phase demonstrator

## Slide 24
2015
2015-16. 3x1x1 DP first membrane cryostat at CERN
2016. 3x1x1 DP detector installation

## Slide 25: Next step : ~800 ton LAr prototypes
NP02 proximity cryogenics
NP04 proximity cryogenics
External cryogenics
H4 beam line
H2 beam line
DAQ & computing rooms
NP04 proximity racks
NP02 proximity racks
NP02 DP
NP04 SP
SPS : new EHN1-1 experimental area

## Slide 26: protoDUNE strategy
Modular structure that will be repeated many times inside DUNE
ProtoDUNE prototypes as DUNE module 0, as basis for the final detector construction and assembly
Full engineering done as a basis for the final production (PRRs), both for detectors and cryostat/cryogenics
Check detector response with cosmics (DCS, DAQ, Computing, Reconstruction, …)
Calibrate with charged beam the response to leptons and hadrons
Very ambitious program :
- detectors cooled by April 2018
- in beam in 2018 before LS2 shutdown

## Slide 27: 2016-2017 : ProtoDUNEs ~800 ton LAr cryostats
NP04: single phase
NP02: double phase

## Slide 28: 2016-2017 : ProtoDUNEs ~800 Lar tons cold cryostats

## Slide 29: SP detector components
29
Field cage
Cathode plane
Support system
Field cage made out of Al extruded profiles

## Slide 30: Resistive Cathode Concept
With a conventional metallic cathode assembly, in the DUNE LAr-TPC layout, several tens of J of energy on each interior cathode are stored when energized to -180kV.
In the event of a discharge from a cathode edge to the facing cryostat wall, there is a risk of physical damage to either the cathode or the membrane. The voltage on an all-metal cathode will also collapse very quickly (ns), injecting high current into the cold electronics, risking damage to the front end ASICs.
To minimize these risks, it has been proposed to use a cathode made out of insulating material with a resistive coating in the MΩ to GΩ/square range. This will greatly reduce the peak power transfer to the cryostat and peak current injection into the front-end ASICs in a HV discharge.

## Slide 31
Steel Support Structure
Insulation
Primary Membrane
Protego Inline Safety Valve
Detector
Internal Piping
LAr
LAr Filters
LAr circulation pumps
Condenser
LAr Phase sep.
LN2 Phase sep.
LAr storage tank
(NP-02/NP-04)
LN2 storage tank
(NP-02/NP-04)
LAr Filters Regeneration
(NP-02/NP-04)

## Slide 32: BIG data … DAQ, event reconstruction
New DAQ in synergy with LHC upgrade developments (ATLAS FELIX=Front End LIink eXchange)
Detector Front-End
FELIX
Detector Infrastructure
Detector Control System
Commands & settings
Status
Commands & settings
Status
Clock Distribution
Trigger Distribution
Detector Busy
DAQ Event Builder
DAQ Storage System
Online Processing
Permanent Storage
DAQ Data Handler
Data
Optional data reduction
Including Tier0 dedicated infrastructure

## Slide 33: … and online processing farm
Online computing farm
First DAQ racks

## Slide 34: LBNF cryostats design, first cryostat financed by CERN
65.84m
39 frames (1.6m)
18.94m
17.84m
8 frames (1.6m)
LAr = 17’432 tons (95% liquid)
~ 13’000 m3 of cold cryostat volume

## Slide 35: LBNF LAr proximity cryogenics design
35 m
12 m
2.3 m
7.7 m
Steel Support Structure
Insulation
Primary Membrane
Protego Inline Safety Valve
Valve Actuator
Valve Body
Detector
Internal Piping
LAr
Protego Inline Safety Valve
Steel Support Structure
Insulation
Detector
Valve Actuator
Valve Body
Primary Membrane
Internal Piping
NB: External cryogenics designed by FNAL

## Slide 36
Summary:
CERN offers a platform for Neutrino detectors R&D and later construction. CERN is supporting this platform in an active way both for the infrastructure and for the detectors construction, installation and commissioning
A large neutrino test area (EHN1-1 extension) with charged beams capabilities has been constructed and is being made operational
We will assist the EU neutrino community in their long term common plans. We are reacting on demands from the community, in particular for many R&D aspects. Entry point for medium/large projects: CERN SPCS
In the short term, the CERN Platform is helping in getting a Short Baseline operational at FNAL with an agreed physics program … and later a Long Baseline. Near detectors are now appearing as new R&D projects.