## Slide 1: Crab cavities, RF noise and operational aspects (counter-phasing, Full Detuning). An update
P. Baudrenghien, R. Calaga CERN-BE-RF
T. Mastoridis California Polytechnic State University, San Luis Obispo, CA
E. Yamakawa Lancaster University, U.K.

## Slide 2: Content
Recap of Analytical Derivations
Expected growth rate and required jitter
Mitigations: Use CC as transverse kicker
Making cavities invisible during filling and ramping
Full detuning scheme
Conclusions

## Slide 3: Recap of Analytical Derivations
Emittance growth caused by CC phase and amplitude noise

## Slide 4: Phase noise [1]
Depends on the overlap between phase noise spectrum and betatron tune distribution
Phase noise spectrum is aliased at frev
The “geometric factor” decreases with bunch length

## Slide 5: Amplitude noise
Depends on the overlap between phase noise spectrum and betatron tune distribution
Amplitude noise spectrum is aliased at frev
The “geometric factor” increases with bunch length

## Slide 6: Transverse damper
The LHC transverse damper acts bunch per bunch: it measures the transverse position averaged over all particles in one bunch and generates a correcting kick
It cannot correct for the effect of CC amplitude noise (as head and tails move in opposite direction)
It can correct part of the phase noise effect
Its effectiveness is a race against filamentation. It will depend on the ratio of damping time over filamentation time
The damper efficiency drops quickly as bunch length increases. The damper kick is uniform along the batch while the effect of phase noise is strong in the core but weak in the tails. Increasing the damper kicks therefore excites the tails

## Slide 7: Damper reduction factor (phase noise)
With
f(u),g(u) are scaled versions of the real and imaginary parts of the Beam Transfer Function.
The damper efficiency drops quickly as bunch length increases. The damper kick is uniform along the batch while the effect of phase noise is strong in the core but week in the tails. Increasing the damper kicks therefore excites the tails

## Slide 8: Expected growth rate
Scaling the ACS RF noise
Bound on RF noise

## Slide 9: Parameters
Beam
CC
ADT
CC LLRF
Frev (Hz) | bcc (m) | nx | en (mm rad) | Eb (TeV) | sf (rad) | snb
11245 | 4000 | 62.31 | 2.5 | 7 | 0.628 | 0.003
V0 (MV) | Nbr cavities per beam.plane
3.4 | 4
G | Rd
0.04 | 0.097
Fdbk Closed-loop BW | TX Polar Loop effectiveness
100 kHz | 40 dB reduction up to 1 kHz

## Slide 10: Scaling the ACS. Phase noise
Single-Sideband phase noise power spectral density in dBc/Hz. Plateau at -136 dBc/Hz. Total rms phase noise s = 143 mrad
With reduction of phase noise effect from ADT, the emittance growth rate is 16%/hour

## Slide 11: Scaling the ACS. Amplitude noise
Single-Sideband amplitude noise power spectral density in dBc/Hz. Plateau at -136 dBc/Hz
Total rms amplitude noise s= 685 V
The emittance growth rate is 63%/hour

## Slide 12: Summing it up
The amplitude noise is the limiting factor
To get reasonable lifetime we must improve the demodulator noise level
With -147 dBc/Hz (@ 3 kHz offset), plus filtering of the reference RF to reduce the noise level on the first betatron line (3 kHz), we get
  Phase noise: rms s = 34 mrad resulting in 0.94 %/hour emittance growth rate
  Amplitude noise: rms s = 165 V resulting in 3.7 %/hour emittance growth rate
Challenging but possible

## Slide 13: Mitigation
Transverse feedback using the CC

## Slide 14: Idea
Measure the bunch transverse displacement (head+tail), and the tilt (head-tail)
Use the Sum signal to feedback on the CC phase
Use the Difference to feedback on the CC amplitude

## Slide 15: Very promising in simulations
Amplitude noise (left) and phase noise

## Slide 16
With measurement noise added
Synergy with ADT upgrade (reduction of measurement noise)
The CC excites only low modes (closed-loop BW ~ 100 kHz) so we can average over few bunches -> improves SNR
Being studied. Collaboration with Cal Poly (T. Mastoridis)
Paper in preparation.

## Slide 17: Making cavities invisible
Counter-phasing during filling and ramping

## Slide 18: Operational scenario
The RF is ON, with strong RF feedback and tune controls at all time. Cavities are on-tune at all time.
During filling, ramping or operation with transparent crab cavities:
  Small cavity field as required for the active Tuning system
  We use counter-phasing to make the total field invisible to the beam
  A strong RF feedback keeps the Beam Induced Voltage zero if the beam is off-centred.
ON flat top:
  We drive counter-phasing to zero
  Any adiabatic field manipulation is possible by synchronously changing the voltage or phase in each cavity (luminosity levelling for example).

## Slide 19: Precision
The RF feedback has measurements of the Antenna of all 4 cavities (per IP.beam) and generate the 4 TX drives
We can reduce voltage by at least factor 10 (300 kV/cavity)
Assuming 5 degree (0.09 rad) phase error (between the two counter-phased cavities), the total voltage will be about 3 105 0.09 = 26 kV

## Slide 20: Emittance growth during filling
The un-normalized emittance growth scales as (V/g)2
The normalized emittance growth scales as V2/g
So, as long as the cavity voltage is reduced by 4 (< 0.75 MV/cavity), the growth rate at injection is lower than in physics
Strong octopoles and chromaticity increase the betatron tune-spread. That impacts only the phase noise reduction factor that comes from ADT. But recall that the effect of amplitude noise dominates
Large betatron tune-spread will also reduce the effectiveness of the CC feedback (same mechanism as with ADT). Being studied (Cal Poly collaboration)

## Slide 21: Full detuning
Consequences of bunch phase modulation

## Slide 22: Bunch phase modulation (1/2)
The CC field cannot be modulated at Frev (QL=500000)
The CC RF will therefore slip w.r.t. the bunch core
Calculations have been done on the effect of longitudinal displacement on Lumi. For symetric bunch 1-2 displacements:
  A 100 ps displacement of bunch core w.r.t. CC RF zero phase results in 2% reduction in lumi
  A 200 ps displacement results in 8% loss in lumi
  We expect 100 ps pk-pk displacement with HiLumi intensity, that is 50 ps max displacement

## Slide 23: Bunch phase modulation (2/2)
Calculations have also been done for asymetric longitudinal displacements
An 100 ps shift of one beam only will result in 6 % decrease in Lumi
We conclude that the CC RF phase must be controlled with a precision better than 5 RF degree @ 400 MHz (35 ps)
Simulations will follow
Work done with the HiLumi collaboration (Emi Yamakawa, Lancaster University)
Results will be presented and published soon

## Slide 24: Conclusions

## Slide 25: Conclusions (1/2)
Use of the RF receiver designed for the ACS cavities (in 2005) will result in 16 %/hour (phase noise) and 63 %/hour (amplitude noise) emittance growth rate, including ADT reduction
An upgrade, reducing the noise level by 11 dB and filtering the 400.8 MHz reference would lead to an acceptable 0.94 %/hour (phase noise) and 3.7 %/hour (amplitude noise) emittance growth rate. ACCEPTABLE

## Slide 26: Conclusions (2/2)
A proposed mitigation is a feedback system acting on the CC phase and amplitude. Promising. Performances limited by the accuracy of transverse measurements. Studies (calculations plus simulations) ongoing (CalPoly collaboration).
The situation during physics and ramp is more favourable than in physics
The impact of the Full Detuning scheme is limited. Simulations needed to confirm the calculations (Cockcroft collaboration)
The accuracy required on the CC cavity phase does not appear too demanding.

## Slide 27: References
[1] P. Baudrenghien, T. Mastoridis, Transverse emittance growth due to RF noise in the high-luminosity LHC Crab Cavities, PRST AB, 18, 101001 (2015)