## Slide 1: Review of Expected Crab Cavity Heat Loads Due to Impedance
Sergey Antipov, Nicolo Biancacci, Benoit Salvant, Francesco giordano, and Elias Metral
13.06.17

## Slide 2: Some HOMs close to a multiple of the bunch spacing frequency might cause massive heat load
Example: DQW design (update of 10.2016)
Shunt impedance (Ω) | Quality factor | HOM Frequency (Hz)
9.34E+07 | 2.17E+10 | 4E+08
2.13E+04 | 1.60E+03 | 5.64E+08
0.005098 | 1.05E+03 | 5.69E+08
5.401713 | 1.04E+03 | 5.69E+08
1.15E+05 | 2.63E+03 | 5.86E+08
0.206092 | 6.71E+03 | 6.81E+08
417.1959 | 2.34E+03 | 6.82E+08
6.313443 | 1.06E+03 | 6.83E+08
0.205469 | 5.37E+00 | 8.53E+08
0.662133 | 5.39E+00 | 8.54E+08
3.30E-07 | 7.95E-01 | 8.6E+08
0.002906 | 6.09E+02 | 9.28E+08
1.14E+04 | 1.17E+03 | 9.6E+08
2209.216 | 2.62E+05 | 1.04E+09
55.08195 | 7.83E+02 | 1.07E+09
High R + close to a beam harmonic

## Slide 3: Why is this not an issue in normal RF cavities?
The main mode is transverse, not longitudinal
  The HOMs are lower in frequency
The crab cavities sit in the places with high β
  Low Q of the HOMs is needed to ensure transverse stability
See also:
  N. Biancacci et al., Effect of tail cut and tail population on octupole stability threshold in the HL-LHC, HSC Meeting, 05.10.15
  E. Metral, Impedance update (other components than Crab Cavities), Joint LARP CM26/Hi-Lumi Meeting, SLAC, 19.05.16
  E. Metral et al., CC: Impedance status, International Review of the Crab Cavity Performance for Hi-Lumi, CERN, 05.04.17

## Slide 4: Simulation procedure
Take the actual beam spectrum
Sum the contributions of all the HOMs
N. Biancacci’s code:
  Adding an extra ±3 MHz spread to the HOM frequencies to account for manufacturing uncertainties
  Equidistant Gaussian bunches
B. Salvant’s code:
  Actual filling pattern
  Gaussian or cos2 distribution
No. bunches
p per bunch
Courtesy F. Giordano

## Slide 5: Double Quarter Wave: Total heat load has increased
In reality, not all the buckets are filled
The power loss will be lower
2.2x1011 ppb
25 ns spacing

## Slide 6: The sidebands of the beam spectrum significantly affect the power loss. It is quadratic with the number of bunches only if only the main line contributes
F. Giordano, B. Salvant, Update on power loss for resonator impedance with various filling schemes, APB HSC Meeting, 08.05.17
If is true, in the LHC a is almost never equal to 2.

## Slide 7: Going to 9 cm rms bunch length decreases the peak power loss
The effect is more prominent at 1 GHz and higher
8.1 cm rms bunch length
9.0 cm rms bunch length

## Slide 8: The most dangerous modes
560 MHz
760 MHz
960 MHz
The recipe of high loss:
High R 28 kΩ
Low Q 300
Close f 761 MHz
We need the HOMs to have low Q to ensure the transverse stability

## Slide 9: Intersection of the mode line with the peak in beam spectrum leads to kW-scale power losses
DQW
RFD
For a more realistic cos2 spectrum the losses are lower. Up to a factor of 2 for a 1 GHz mode in DQW

## Slide 10: Need to look at all potentially dangerous modes
The modes may shift significantly during the tuning
  As far as 50 MHz
  No way of controlling the individual frequencies
To be safe, one might need to take into account all potentially dangerous modes
  Not only the ones that are close to beam harmonics at the moment
Adding a ±25 MHz spread to HOM frequencies
The modes with peak power loss > 100 W are highlighted

## Slide 11: DQW: Stay at least 2 MHz away from the critical HOMs
Intensity | 2.2x1011 ppb
No. bunches | 2748
Bunch distribution | Cos2
Mode frequencies | 586 MHz
Q-factor | 2600
Shunt imp. | 115 kΩ
500 W level

## Slide 12: DQW: Stay at least 2 MHz away from the critical HOMs
Intensity | 2.2x1011 ppb
No. bunches | 2748
Bunch distribution | Cos2
Mode frequencies | 960 MHz
Q-factor | 1100
Shunt imp. | 11 kΩ
Can significantly reduce the losses from the
2nd potentially dangerous mode

## Slide 13: RFD: Stay at least 5 MHz away from the critical HOM
Intensity | 2.2x1011 ppb
No. bunches | 2748
Bunch distribution | Cos2
Mode frequency | 760 MHz
Q-factor | 290
Shunt imp. | 28.7 kΩ
500 W level

## Slide 14: What can be measured at SPS?
Cos2 bunch profile
Intensity | 1.35x1011 ppb
No. bunches | 288
Bunch length, extraction | 1.65 ns
Bunch length, injection | 4.0 ns
injection
extraction

## Slide 15: RFD: up to 50 W at extraction
Injection, 4.0 ns bunch length
Extraction, 1.6 ns bunch length
760 770
frequency (MHz)
760 770
frequency (MHz)
Power loss (W)
0.10
0
Power loss (W)
54.4
0
Power loss (W)

## Slide 16: DQW: up to 2 kW, very narrow peak
Injection, 4.0 ns bunch length
Extraction, 1.6 ns bunch length
0.3 MHz
590 600 610
frequency (MHz)
590 600 610
frequency (MHz)
2.4
0
Power loss (W)
2140
0
Power loss (W)

## Slide 17: DQW: HOM damping system is designed to take up to 1 kW
DQW has several HOM couples
J. A. Mitchel et al., IPAC’16, Busan, Korea
Thermal breakdown might be an issue
A dedicated breakdown test is foreseen
The coaxial line can transport up to 1 kW of HOM power load out of the cavity

## Slide 18: Summary
If a high-impedance HOM is close to a beam spectrum line, it may lead to a high power loss
  kW-scale losses!
HOM lines can be quite broad (low-Q), making it challenging to avoid
Would like to have at least 2-5 MHz from the harmonics of 40.08 MHz to keep the beam induced heating below 500 W
  How feasible it actually is?
As measurement in SPS might reveal some information
  Substantial power loss
  Tens of Watts can be achieved at extraction
  May be hard to tune on certain lines