## Slide 2: Design of the Beam Gas Curtain
Introduction of the Mechanical Design of the BGC

## Slide 3: BGC: First prototype design
1. Elements of the BGC system
2. Changes to the existing system
3. Agreed interfaces between the systems
4. Alignment of the system
5. Vacuum system and expected pressures
6. Flexibility of the system
7. Integration of the system

## Slide 4: 1. Elements of the BGC system
Nitrogen
gas jet
Electron beam

## Slide 5: 1. Elements of the BGC system
Expansion
section
Dumping
section
Interaction
section

## Slide 6: 1. Elements of the BGC system
Expansion section
Pressure sensors
Gas inlet valve
Nozzle pumping valve
Laser system viewport
Skimmers chamber
Alignment tables
Transition chamber
Turbopumps
Nozzle chamber

## Slide 7: 1. Elements of the BGC system
Expansion section

## Slide 8: 1. Elements of the BGC system
Expansion section
Front view
Back view
Ø = 30 μm
Nozzle
Nozzle holder
Nozzle tube
Ø = 180 μm
1st skimmer
Ø = 400 μm
2nd skimmer
□ = 4 x 0.4 mm
3rd skimmer

## Slide 9: 1. Elements of the BGC system
Interaction section
Calibration LEDs
Electron collector
Turbopump
Optical system
Pressure sensor
Electron gun

## Slide 10: 1. Elements of the BGC system
Dumping section
Front view
Back view
3D movable gauge
Pressure sensor
Alignment table
Turbopumps
Retractable mirror

## Slide 11: 1. Elements of the BGC system
Dumping section
Nitrogen
gas jet

## Slide 12: 2. Changes to the existing system
Fully bakeable system up to a minimum of 200 °C
Alignment of the skimmers at metrology
Lower vacuum background pressure expected
Expected pressure of 10-9 mbar without gas jet
Fast pressure recovery after opening
Flexible system in case we want to change the skimmers
If we want to integrate the system in a setup with magnets, we would only need to change the interaction chamber

## Slide 13: 3. Agreed interfaces between the systems
Electron gun
170 mm*
55 mm*
CF DN63
*We would need to add a 115 mm extension vacuum pipe to cover the new electron gun's requirements

## Slide 14: 3. Agreed interfaces between the systems
Optical system
150 mm
CF DN40

## Slide 15: 4. Alignment of the system
Ø = 30 μm
Nozzle
Ø = 180 μm
1st skimmer
Ø = 400 μm
2nd skimmer
□ = 4 x 0.4 mm
3rd skimmer

## Slide 16: 4. Alignment of the system
Ø = 30 μm
Nozzle
Ø = 180 μm
1st skimmer
Ø = 400 μm
2nd skimmer
□ = 4 x 0.4 mm
3rd skimmer
 | Distance
Nozzle – 1st skimmer | 2 – 20 mm
1st skimmer – 2nd skimmer | 20 mm
2nd skimmer – 3rd skimmer | 325 mm

## Slide 17: 4. Alignment of the system
Source: V. Tzoganis

## Slide 18: 4. Alignment of the system
1. Align the nozzle holder to the 1st and the 2nd skimmer in a metrology environment
2. Mount the assembly to the skimmers chamber (possibility to note the internal centre line to external targets)
3. The nozzle tube must have a really good manufacturing concentricity

## Slide 19: 4. Alignment of the system
Nozzle holder
Ø = 400 μm
2nd skimmer
Ø = 180 μm
1st skimmer

## Slide 20: 4. Alignment of the system
Ø = 30 μm
Nozzle

## Slide 21: 4. Alignment of the system
Top view
Nozzle chamber alignment targets
Skimmers chamber alignment targets
Interaction chamber alignment targets

## Slide 22: 4. Alignment of the system
3D movable gauge
Laser system

## Slide 23: 4. Alignment of the system
3D printing is not an option
Alignment of Beam Gas Curtain (BGC) test plates
Starting investigation on how to align three
elements in the micron range
Analysis of Additive Manufacturing Technologies for the Beam Gas Curtain (BGC) instrument
EDMS 1708792 v.1
EDMS 1708789 v.1

## Slide 24: 5. Vacuum system and expected pressures
Baseline pumps
300 L/s
700 L/s
700 L/s
300 L/s
800 L/s

## Slide 25: 5. Vacuum system and expected pressures
Baseline and optional pumps
300 L/s
700 L/s
700 L/s
300 L/s
800 L/s
300 L/s
300 L/s

## Slide 26: 5. Vacuum system and expected pressures
Static pressure < 10-9 mbar
10-3 mbar
Dynamic pressure ranges (order of magnitude)
10-6 mbar
High
10-9 mbar
High
10-9 mbar

## Slide 27: 6. Flexibility of the system
Source: M. Ady
700 L/s
differential pumping
700 L/s
pumping
1400 L/s
pumping

## Slide 28: 6. Flexibility of the system

## Slide 29: 6. Flexibility of the system

## Slide 30: 6. Flexibility of the system
SmarTeam code: ST0858286_01

## Slide 31: 7. Integration of the system

## Slide 32: Thank you!