## Slide 1
Final Results From the CLIC Test Facility (CTF3)
Roberto Corsini
For the CLIC Collaboration

## Slide 2: CLIC in a nutshell
CLIC will be built in stages of increasing collision energy: starting from 380 GeV, then ~ 1- 2 TeV, and up to a final energy of 3 TeV.
To limit the collider length, the accelerating gradient must be very high - CLIC aims at 100 MV/m, 20 times higher than the LHC.
CLIC is based on a two-beam acceleration scheme, in which a high current e- beam (the drive beam) is decelerated in special structures (PETS), and the generated RF power is used to accelerate the main beam.
The feasibility of CLIC has been demonstrated and documented in the
CLIC Conceptual Design Report
CLIC International Collaboration

## Slide 3: CLIC Timeline

## Slide 4: The CLIC study

## Slide 5: What matters in a linear collider ?
Luminosity
High gradient
X-band normal conducting
Acceleration efficiency Two-beam scheme
Generation of small emittance Damping rings
Conservation of small emittance Wake-fields, alignment, stability
Extremely small beam spot at IP Beam delivery system, stability
Energy reach
Ecm ≈ Llinac Gacc
CLIC specific Issues
N.B.:

## Slide 6
DRIVE BEAM LINAC
COMBINER RING
CLIC Test Facility (CTF3)
DELAY LOOP
CLEX
TBL
Two Beam Module

## Slide 7: Two-beam scheme issues
All covered in CTF3

## Slide 8: CTF3 – the original mission
High current, full
beam-loading operation
Operation of isochronous lines and rings
Bunch phase coding
Beam recombination and current multiplication by RF deflectors
12 GHz power generation by drive beam deceleration
High-gradient two-beam acceleration
4 A, 1.4us
120 MeV
30 A, 140 ns
120 MeV
30 A, 140 ns
60 MeV
First beam – June 2003

## Slide 9
CTF3 in 2015-2016
TBL deceleration
Two Beam Module,
Wake-field monitors…
Phase feed-forward experiment
Diagnostics R&D using CALIFES
Last beam – December 2016
Dogleg Beam loading experiment

## Slide 10: Drive Beam Generation
SiC load
damping
slot
10 m
RF pulse at output
RF pulse at structure input
95.3% RF to beam efficiency
Stable high current acceleration
Factor 8 current & frequency multiplication
Full beam loading acceleration
Factor 8 combination
Most RF power
to beam
High beam current
RF in
No RF to load
“short” structure – low Ohmic losses

## Slide 11: Drive Beam Generation
Beam recombination
Fast bunch phase switch in SHB system
Operation of isochronous rings and beam lines
6 ns

## Slide 12: Drive Beam Stability
Phase stability 2.5° @ 12GHz
Emittance εx,y ≤ 150μm
Transverse jitter ≤ 0.3σ
Current stability 1 ×10-3
Phase stability 0.2° @ 12GHz
RF power stability 0.2%
RF phase stability 0.05°
Current stability 0.75 ×10-3
CLIC Drive Beam requirements
Verified in CTF3
0.21%
0.035°
0.2 ×10-3
Tests in CTF3
εx ≤ 250μm, εy ≤100μm
≤ 0.1σ
Verified in CTF3
~1° @12 GHz
Verified in CTF3
1 to 3 ×10-3
< 0.2°
Feed-forward tests in CTF3

## Slide 13: Drive Beam Stability
Pulse charge stability at end of the linac better than CLIC requirements
P [MW]
RF power feedback, MKS 13
Time [h:m]
Feedback on
Feedback off
Feedback on
Repeatibility and long term current stability greatly improved in final years.
Many feed-back loops operational, for temperature, RF phase and power and gun current.
Charge stability – Factor 8
5 10-4
2 10-3
General lesson from CTF3 (and SLC): Diagnostics, tuning procedures and feedbacks are vital

## Slide 14: Power production in the Two-Beam Test Stand
t [ns]
135 MW
CLIC target
Two-Beam Test Stand
(TBTS) Layout
CLIC target
PETS operated routinely above 200 MW peak RF power
providing reliably pulses ~ 100 MW to accelerating structure.
About twice the power needed to demonstrate 100 MV/m acceleration in a two-beam experiment with the nominal CLIC structure.

## Slide 15: TBTS – PETS On-off mechanism
Demonstration of PETS of-off mechanism
Feasibility issue
  Switch off power from individual PETS to accelerating structure in case of breakdown
  Reduce substantially power in PETS, to cope with PETS breakdowns
PETS on-off principle fully tested
Conditioned at high power
(135 MW - nominal) by recirculation
System routinely used in CTF3 for power enhancement and tuning
PETS , forward RF
ON
OFF
Simulation vs. experiment
Spectra
comparison

## Slide 16: Two-Beam Acceleration
TD24
Maximum stable probe beam acceleration measured: 31 MeV
 Corresponding to a gradient of 145 MV/m
Two-Beam Acceleration demonstration in TBTS
Up to 145 MV/m measured gradient
Good agreement with expectations
(power vs. gradient)
CLIC Nominal, loaded
CLIC Nominal, unloaded
Drive beam ON
Drive beam OFF

## Slide 17: Two-Beam Module Experimental Program 2015-2016
  CLIC two-beam module tests
Power production, stability + control of RF profile
RF phase/amplitude drifts along TBL, PETS switching at full power
Two-beam acceleration, power transfer & phasing, breakdown detection and effects of breakdowns…
Alignment tests, with and w/o beam, including Wake-Field Monitors and main beam prototype BPMs
  Aim: gather all possible information, to feed back into next generation Two-Beam Module design
Two-beam acceleration in TBM thoroughly tested
Verified again power production/energy gain vs. expectations
Operated at nominal CLIC gradient and pulse length, ~ 100 MV/m and 240 ns
Experiment on control of RF profile (beam loading compensation) done

## Slide 18: TBM – accelerating gradient in 2016
  Accel. Grad. = 110 MV/m

## Slide 19: TBM – wake-fields effect
Low charge
Low charge
High charge
Beam at the centre of the ACS
Wake (girder movers)
  85.3 kV/nC/mm/m
Wake (corrector scan)
  85.5 kV/nC/mm/m

## Slide 20: Test Beam Line
14 Power Extraction & Transfer Structures (PETS)
installed and running from 2015
Full beam transport to end-of-line spectrometer, stable beam
Power produced (90 MW/PETS) fully consistent with drive beam current (24 A) and measured deceleration.
PETS tank during installation
TBL line in CLEX
About 1.3 GW of 12 GHz peak power!
Beam deceleration, measured in spectrometer and compared with expectations
41%

## Slide 21: Drive beam phase feed-forward
Goal: stabilize drive beam phase to the CLIC requirement 0.2° @ 12 GHz (50 fs)
DB feed-forward results, 2015
  Drive-beam phase feed-forward tests in 2016
From about 1° to
0.2° @ 12 GHz, or 50 fs

## Slide 22: CTF3 Exp. Program 2015-2016 – Beam Loading Experiment
Drive beam 1-3A
130-50 MeV
12 GHz RF from klystron
CLEX
LINAC
DELAY LOOP
COMBINER RING
BL - BDR experiment
CTF3
Unloaded
Loaded (CLIC)
Increasing current
Gradient along the structure
Average gradient 100 MV/m
Beam loading changes the field distribution for the same average gradient ⇨ how is the break-down rate affected?
12 GHz accelerating structure

## Slide 23: Beam Loading Experiment
A BDR reduction by beam loading up to an order of magnitude was measured.
BDR seems dominated by the peak gradient, confirmed by the measured distribution inside the structure, which follows roughly the gradient profile.
Possibility to further optimise the CLIC structure by targeting a flat gradient along the structure during the operation with beam.

## Slide 24: CTF3 Exp. Program 2015-2016 – Instrumentation Tests
  Main beam BPM prototypes
  Sub-micron resolution measured
  Time resolution (50 nm) OK
  Wake-Field Monitors
  4 um resolution
  Studies of DB noise
  Confirmed by new version
  2014 TBTS data
  4um resolution
  Optical Fiber Beam Loss Monitors in TBL
  Localization of losses below 2 m (2015)
  Multi-loss location case
  Drive Beam BPM
  Confirm 2.5 um resolution
  Rad hardness

## Slide 25: Wake Field Monitors
Wake field monitors precisely determine the beam position with respect to the electrical center of an accelerating structure
In CLIC, WFM signals will be used to center the beam in the structure and minimize transverse wake-fields
Requirement: 4.5 um resolution

## Slide 26
CLIC Test Facility (CTF3) ✝ 2016

## Slide 27
CERN Linear Electron Accelerator for Research (CLEAR) ꙳ 2017

## Slide 28: The CLEAR (CERN Linear Electron Accelerator for Research) proposal
CTF3 ended operation in December 2016
However, the probe beam injector CALIFES will become the focus of a new multi-purpose facility, CLEAR
CLEAR, among other activities, will continue some CLIC related studies on high-gradient and diagnostics

## Slide 29: CONCLUSIONS
CTF3 has addressed and solved the CLIC issues related to drive beam generation, power production and two-beam acceleration.
CTF3 successfully completed its planned experimental program in December 2016 as planned, and stopped operation.
The experience gathered in CTF3 is now being documented, in view of the update of the European Strategy in 2019.
The approval of the CLEAR program gives the opportunity to maintain local testing capability at CERN for CLIC instrumentation and high-gradient structure testing with beam, alongside with other non-CLIC activities.

## Slide 30
The CLIC Test Facility has been the collective effort of a large collaboration over more than a decade.
Many thanks to all individuals who participated over this period to the conception, design, construction, commissioning and operation of CTF3!