## Slide 1
Results of the Beam-Beam Long-Range compensation experiment in LHC
Y. Papaphilippou, A. Rossi and G. Sterbini on behalf of the BBLR compensation team
HL-LHC Meeting, 13-16 November 2017, CIEMAT, Madrid
Notes: Good morning,
thank you for the opportunity to present on behalf of the team the results fo the Beam-beam long-range in LHC
1

## Slide 2
Outline
2
Introduction of the wire compensation
The LHC wires prototypes
The experimental results
Conclusions and plans
Results of the Beam-Beam Long-Range compensation experiment in LHC
Notes: After having introduced the wire compensation concept, I will describe the experimental 2017 experiment in LHC, first introducing the experiment condition and then the results.
2

## Slide 3
Beam-Beam Long-Range compensation, the journey
3
2004, wires in SPS
2008, technical investigation in LHC
2017, wires prototypes in the LHC
Synergic efforts between BE-BI, Collimation Team, EN-STI, EN-MME and TE-EPC to transform an idea into a prototype.
1997
V. Shilsev et al.
e- Q-compression
2000
J.-P. Koutchouk
DC wires for LHC
March 2017
2nd Workshop on (HL-)LHC
Wire Compensation
1st Workshop on (HL-)LHC
Wire Compensation
December 2015
Experiment in the LHC
July 2017
J.-P. Koutchouk et al.
Wires in the SPS
Since 2004
2015
S. Fartoukh et al.
PRST-AB 18, 121001
W. Fischer et al.
Wires in RHIC
2006
2008
U. Dorda
PhD Thesis
2012
T. Rijoff
M.Sc.Thesis
F. Zimmermann et al.
Specification of the
LHC prototypes
2013
C. Milardi et al,
Wires in DAFNE
Since 2006
Notes: The first idea to use a DC wire in LHC is of the 2000, after it several tests were done in hadron machine (SPS, in RHIC), in lepton machine Dafne the wire is an operational device.
In 2013 the specification of the LHC prototype were defined, and thanks to the synergic effort between several expert
WG 2,5,13

## Slide 4
The wire compensation principle
4
The long-range kick (BBLR effect) can be compensated by using a DC wire.
The wire compensation is not in the HL-LHC baseline (see R. Tomàs talk).
Its potential for HL-LHC with flat optics or in combination with crab-crossing was shown by S. Fartoukh et al., PRST-AB 18, 121001, 2015.
Since 2017 two wire prototypes (BBCW) are installed in LHC. In this presentation, the HW setup and the latest LHC experimental results of the LHC wire compensation will be reported.
BBCW
B2, left
The BBCW principle
BBCW
B2, right
BBCW
B1, right
BBCW
B1, left
Results of the Beam-Beam Long-Range compensation experiment in LHC
Notes: Here you can see a plot of the …
4

## Slide 5
Integration of the wire in the collimator jaws
5
The wire-beam distance has to be of the order of few mm (function of qc and s-position): LHC wires prototypes are embedded in the jaw of two operational tertiary collimators.
Max. temperature at IW=350 A: 161 oC
During the 2017, BE-BI, EN-STI and the Collimation teams performed a complete test campaign to ensure the correct functioning of the wire interlocks, the collimator motors and PUs when the wire is powered.
Courtesy of F. Carra
Top view
Side view
≈1 m
3 mm
Results of the Beam-Beam Long-Range compensation experiment in LHC
Notes: The wire-beam distance has to be of the order of few mm.
5

## Slide 6
The BBCW position in LHC
6
The 2 BBCWs were installed in two H-collimators of B2 in IR5 (TCTPH.4R5.B2 and TCL.4L5.B2), close to the D2 separation dipoles.
Longitudinal position of the BBCW and optics used in the experiment
The ideal s-position of the BBCW is ±159 m from the IP5. The actual s-position are -150.03 and +147.94 m.
H-plane position of the BBCW
Results of the Beam-Beam Long-Range compensation experiment in LHC
Notes: 6

## Slide 7
Objectives of the experiment
7
Prove the beneficial effect of the BBCW in a regime dominated by long-range beam-beam effect, ensuring in the mean time that the linear effects of the wire (orbit and tunes) are compensated.
Our privileged observable is the bunch “effective cross-section”:
Intensity loss-rate
Instantaneous luminosity
The IDEAL compensation, 2 bunches in B2
Luminosity
dominated
Long-range
dominated
Wire
compensation
STEP 1
STEP 2
STEP 3
Results of the Beam-Beam Long-Range compensation experiment in LHC
Notes: 7

## Slide 8
Asymmetric filling scheme
8
To approach the wire to the beam the B2 has to be <3e11 p (“safe” limit).
We will mainly concentrate on the two bunches of B2 (Only HO and HO+BBLR).
All but 1 bunch in the B1 train do not have head-on encounters:
stability issues.
All BB encounters will occur in IR1 and IR5 but BBCW only in IR5.
Results of the Beam-Beam Long-Range compensation experiment in LHC
BCMS train

## Slide 9
9
Vertical alignment of beam-wires
Important vertical offset (up to 5 mm) to be corrected with the vertical alignment procedure. Not trivial due to lack of V PUs [credit to N. Fuster and S. Redaelli].
Luminosity
dominated
STEP 1
Results of the Beam-Beam Long-Range compensation experiment in LHC

## Slide 10
10
Pushing B2 to the BBLR regime
To increase the BBLR effect:
B2 H-emittance blown-up to 5-6 mm mrad [credit to D. Valuch, S. Papadopoulou and M. Fitterer].
The tunes were set to a sub-optimal working point (0.31, 0.32).
And the half-Xing angle was reduced to 120 mrad. Important synergy with the OP experience of the crossing angle anti-leveling [credit to M. Hostettler].
50% H-emittance blow-up
from 150 to 120 mrad
Long-range
dominated
STEP 2
Results of the Beam-Beam Long-Range compensation experiment in LHC

## Slide 11
11
There are practical limits in the positioning of the wire with respect to the beams even for low intensity MD beams.
Given this constraint, the current can be used as a knob to cancel the effect of one specific magnetic multipole.
Approaching the wires to the beam
Results of the Beam-Beam Long-Range compensation experiment in LHC
Notes: 11

## Slide 12
12
Switching ON/OFF the compensation
The wires were switched ON-OFF for several powering cycles.
During the powering of the wires, the tunes of the beam (and its position) has to be controlled with high precision: dipolar and quadrupolar contributions of the wires were compensated with feed-forward trims [credit to M. Solfaroli and G.-H. Hemelsoet].
IWMAX=350 A
Results of the Beam-Beam Long-Range compensation experiment in LHC
Wire
compensation
STEP 3

## Slide 13
13
Results on the compensation (I)
Compensation seen from the seff [credit to N. Karastathis].
Clear effect on the BBCW when switching-off: signal compatible with a contraction of the dynamic aperture of the machine.
ON ⇾ OFF
ON ⇾ OFF
Results of the Beam-Beam Long-Range compensation experiment in LHC
Wire
compensation
STEP 3
Notes: 13

## Slide 14
First results from LLRB MD
14
Result on the compensation (II)
Using dBLM signals to compute the cross-section [credit to A. Poyet, A. Gorzawski]: improved time resolution.
A constant calibration factor was adopted to rescale the BLM reading to the FBCT losses.
ON ⇾ OFF
ON ⇾ OFF
Results of the Beam-Beam Long-Range compensation experiment in LHC
Wire
compensation
STEP 3
Notes: 14

## Slide 15
15
Result on the compensation (III)
From the bunch-by-bunch intensity signals we can measure the effectiveness of the compensation on the losses [credit to M. Hostettler].
Clear effect of the BBCW.
ON ⇾ OFF
ON ⇾ OFF
Perfect compensation
Results of the Beam-Beam Long-Range compensation experiment in LHC
Wire
compensation
STEP 3
Notes: 15

## Slide 16
16
Analysis of the BBCW compensation
Given the constraint on the minimal beam-wire distance, it was not possible to compensate all the resonances excited by the B1.
We used the maximum current of the wires (350 A) to attack as much as possible the BBLR octupolar term.
The octupolar terms induced by the BBLR in IR5 was reduced by 75%.
Strong-beam driven resonance
BBCW driven
resonance
S. Fartoukh et al.
PRST-AB 18, 121001
Results of the Beam-Beam Long-Range compensation experiment in LHC
Notes: 16

## Slide 17
17
Compensation studies: from LHC to HL-LHC
In the beam-beam team significant efforts are put on the wire compensation tracking studies with the two-fold aim to benchmark the LHC results and optimize the HL-LHC scenario with the wires.
For HL-LHC, preliminary results without a full optimization of the longitudinal and transverse wire position, are showing an additional gain of the order of 30 mrad for the half-crossing angle.
+ 30 mrad
Preliminary.
HL-LHC start of the levelling
Results of the Beam-Beam Long-Range compensation experiment in LHC
Distance Beam-Wire [s, en=2.5 mm]
21
8.4
12.6
16.8
Courtesy of D. Pellegrini
Notes: 17

## Slide 18
18
Summary and plans
During 2017 it was observed for the first time in LHC the effect of a direct compensation of the BBCW. Present understanding indicates that it can be related to the partial compensation of the octupolar effect.
In two weeks: new MD (compensation at b*=30 cm). AIM: explore the parameter space and correlate it with the analytical model and the tracking results. Margins of improvements on the beta-beating and the orchestration of the feedforward trims, the systematic measurement of the B2 profiles, the B2 tail re-population during the compensation…
In YETS17/18: two vertical wires will be installed in IR1 (s-position of the wires less favorable than in IR5 for the compensation).
In 2018: compensation experiment in IR1 and IR5.
In parallel to the experimental studies, significant efforts put in simulation studies to benchmarking the LHC results and to study in more details the wire potential for the HL-LHC.
Results of the Beam-Beam Long-Range compensation experiment in LHC
Notes: 18

## Slide 19
Thank you for the attention!
BBLR compensation MD team: D. Amorim, H. Bartosik, R. Bruce, X. Buffat, L. Carver, G. Cattenoz, E. Effinger, S. Fartoukh, M. Fitterer, N. Fuster, M. Gasior, M. Gonzales, A. Gorzawski, G.-H. Hemelsoet, M. Hostettler, G. Iadarola, R. Jones, D. Kaltchev, K. Karastatis, S. Kostoglou, I. Lamas Garcia, T. Levens, A. Levichev, L. E. Medina, D. Mirarchi, J. Olexa, S. Papadopoulou, Y. Papaphilippou, D. Pellegrini, M. Pojer, L. Poncet, A. Poyet, S. Redaelli, A. Rossi, B. Salvachua, H. Schmickler, F. Schmidt, K. Skoufaris, M. Solfaroli, G. Sterbini, R. Tomas, G. Trad, A. Valishev, D. Valuch, C. Xu, C. Zamantzas, P. Zisopoulos and all participants to the design, production and commissioning of the wire compensator prototypes (WP2, WP5, WP13 and LHC MD coordinators).

## Slide 20
20
BACK-UP SLIDES

## Slide 21
21
PACMAN bunches and Iw modulation
The needed Iw modulation BW is of the order of 4 MHz (x10 lower than the bunch frequency).
The wavelength in vacuum of a 4 MHz EM wave is ~75 m.

## Slide 22
22
MD2202
10 h MD.
The FILL5898 was dumped (RF on B1, not clear the reason, RF experts suggest a glitch on the interlock). Half-RF detuning.
The observations we report concern the FILL5900. Full-RF detuning.

## Slide 23
23
Numerical results from the RDT
We will use the RDT criterion presented and described in details in
Goal: compensate the BBLR RDTs by using 2 BBCs per IP.
Assuming
  the same Nw and dw for both BBCWs,
  that the strong beam acts as a DC wire,
  that the phase advance between BBLRs and BBLRs/BBCW is 0 or 180 deg.
the paper gives Nw and dw to compensate 4 RDTs (p1q1, q1p1, p2q2, q2p2) in closed form.
It is shown as a numerical evidence that by compensating 4 RDTs one can minimize ALL RDTs if the position of BBCW is conveniently chosen.
Using the paper’s formalism, we will show numerical results on the present LHC (2017 ATS).
Strong-beam driven RDTs
BBCW driven RDTs
Notes: 23

## Slide 24
24
IDEAL CASE: 2 BBCW for IP at sopt=+-159 m
The green boxes are the 4 RDTs used to set Nw and dw
in color code
RDT compensation map
As expected (under the mentioned assumptions) the compensation is covering many more RDTs than the 4 used to set the BBCWs (green boxes). The p+q=1 and p+q=2 could be addressed by using “local” linear magnets (Q4s and the Q4 correctors).
dipole driven
quad driven
Notes: 24

## Slide 25
25
The MD results and the RDT
Real phase advance considered
Ideal phase advance considered (b*→0)
The observed effect of the BBCW can be related to a partial compensation of the detuning terms.
Notes: 25

## Slide 26
26
IDEAL CASE: considering the phase advance.
One can quantify a posteriori the effect of the phase advance.
The compensation of the RDT does degrade. The compensation of detuning terms (Q-footprint compression) is not affected.
Real phase advance considered
Ideal phase advance considered (b*→0)
Notes: 26

## Slide 27
DA simulations with Wire in MD-like conditions I
First results from LLRB MD
27
Good agreement between footprints from MADX and Sixtrack.
Improvement observed but no clear identification of the optimum.
MD-like conditions: dw=8 mm. LR in IR1/5 but wire only in IR1, real aspect ratio at wire position, phase advances.
A modest gain of DA is observed for 8 mm wire-beam distance.
Optimal DA for 800 A.
With no rematch of the chromaticity (as in the MD), the gain of DA is improved.
K. Skoufaris

## Slide 28
DA simulations with Wire in MD-like conditions II
Push dw to 6 mm
Still not ideal conditions: LR in IR1/5 but wire only in IR1, aspect ratio at wire position, phase advances.
1σ (@2.5 μm) DA gained for an optimal wire current of ~400 A.
Clear improvement over all the angles.
First results from LLRB MD
28
0 A
400 A
K. Skoufaris

## Slide 29
Standard Strong Beam Zero-emittance-long-range Strong Beam
“Strong beam”-wire equivalence: tracking
The zero-emittance-LR strong beam does not show a better DA.
Effect of phase advance? Plans to test with the wire at ~70 m for better phases.
K. Skoufaris

## Slide 30
30
“Strong beam”-wire equivalence
For bx≠by the “strong beam”-wire equivalence is not valid anymore
We compare the strong beam field and the wire field in terms of multipoles
Case 1: bx=by , perfect equivalence
Case 2: bx=4*by , see plot below
Case 2: by=4*bx , plot below
We assume bi-Gaussian density (4 s cut)

## Slide 31
First attempts of BBCW in HLLHC1.3
β* = 60 cm | H Beta [m] | V Beta [m]
wire_l1.b1 | 1052 | 1181
wire_r1.b1 | 1178 | 1054
wire_l5.b1 | 1054 | 1182
wire_r5.b1 | 1181 | 1055
B1 tracking with operational settings for emittance, tunes, chroma, octupoles.
4 wires (L/R IP1/5) installed in the crossing plane.
The wires are arbitrarily placed at +/-150m from the IPs.
The distance is tuned so that the beam-wire normalised separation is the same as the normalised crossing.
Likely a suboptimal configuration to be further refined.
31
β* = 20 cm | H Beta [m] | V Beta [m]
wire_l1.b1 | 3006 | 3641
wire_r1.b1 | 3649 | 2999
wire_l5.b1 | 2995 | 3645
wire_r5.b1 | 3636 | 3003

## Slide 32
32
BBCW MD: sanity checks on H/V-position
The H-position of the beam is well under control.
The V-position and correctors behaviour confirm a very good V-alignment of the BBCW.

## Slide 33
33
BBCW MD: Q trims
The Q-trims are mostly due to the feedforward.

## Slide 34
34
BBCW MD: dipolar trims
The correctors trims are mostly due to the crossing angle settings.

## Slide 35
35
BBCW MD: optimizing HO collision

## Slide 36
36
BBCW MD: wires H-positioning
The hectic activity on the BBCW positioning.

## Slide 37
37
BBCW MD: instability of B1
During next MD we will use stronger octupole settings to avoid the instability of the non-colliding bunches in B1.

## Slide 38
38
ATS 2017 optics

## Slide 39
39
RDT criterion for ATS 2017 and qc=150 mm
By plotting the Nw(s) and dw(s) for different RDT minimization strategy, one sees there are specific s-positions, sopt, that minimizes more than the usual 4 RDTs.
The BBCW is positioned ~10 m apart with respect to the optimal position.
Notes: 39

## Slide 40
40
sopt, Nw and dw on crossing angle
There is no dependence of sopt on the crossing angle.
Nw dependence on the crossing angle is marginal (smaller crossing angle, smaller Nw).
dw is linearly dependent on the crossing angle.
Notes: 40

## Slide 41
41
PACMAN bunches and sopt
The sopt depends on the PACMAN pattern.

## Slide 42
42
BBCW impact of the beam profiles (I)
A very detailed presentation by Miriam and Stefania at https://indico.cern.ch/event/658908/
Longitudinal profiles

## Slide 43
43
BBCW impact of the beam profiles (II)
A very detailed presentation by Miriam and Stefania at https://indico.cern.ch/event/658908/
Transverse profiles