## Slide 1: Detection of beam losses in the triplet and cold BLM sensitivity
A. Tsinganis, F. Cerutti, A. Lechner (EN/STI/FDA)
with A. Mereghetti, Y. Zou (BE/ABP)
7th Annual HiLumi Collaboration Meeting – Madrid, November 13-16, 2016

## Slide 2: Outline
Introduction
Layout and optics
Loss scenario
Results
  Peak power density in coils
  BLM response
  “cryoBLM” response
Summary

## Slide 3: Introduction
Goals of this study:
  First calculation of BLM pattern in the Hilumi triplet for stable operation and for a loss scenario in IR5
    Disentangling of losses and collision debris
  Evaluation of “cryoBLM” effectiveness with respect to conventional BLMs

## Slide 4: Layout, optics and loss scenario

## Slide 5: Simulated geometry (triplet-D1)
HL-LHCV1.3 (255μrad half crossing angle, β*=20cm)

## Slide 6: Simulated geometry (triplet-D1)
Several BLMs placed to obtain a finer-grained information

## Slide 7: Scoring for “cryoBLMs”
Additional scoring added on the interconnect flanges

## Slide 8: Loss scenario
Tracking calculations performed by Y. Zou & A. Mereghetti with:
  7.0 TeV beam momentum, 𝜷∗=15cm, 295μrad half crossing angle
  Open TCTs in IR1/2/5/8
    Aim: to simulate missing protection from TCTs
  Open TCLA in IR7, TCSG in IR6, TCDQ in IR6
    Aim: to increase losses in the triplet
  TCLs open
Highest losses recorded right of IP5 (incoming beam)

## Slide 9: Loss scenario
Only losses on horizontal plane were considered (dominant contribution)
In FLUKA, events were sampled from the fitted distributions in s, x, x’, y, y’
Losses concentrated between Q3 and Q2B

## Slide 10: Triplet-D1: Peak power density profile (Debris, L=5.0x1034 cm-2 s-1)

## Slide 11: Triplet-D1: Peak power density profile (Losses)
Normalised in order to reach the 4mW/cm3 design limit in the MCBX corrector when added to the debris load
MCBX corrector

## Slide 12: Triplet-D1: Peak power density profile (Debris and losses, 4mW/cm3 maximum value)
Corresponds to 3.0x108 p/s lost locally  5.39x1012 p/s global loss rate
Two minutes of beam life-time, ~6 MW of power lost
Such an abnormally low life-time is dumped in the collimation system, hence local detection is not essential

## Slide 13: BLM pattern

## Slide 14: Normal BLM response to collision debris
“cryoBLM”
positions
This high-resolution pattern could guide the optimisation of the BLM placement

## Slide 15: Normal BLM response: debris and losses
Highest sensitivity at end of Q2B

## Slide 16: “cryoBLM” response: debris vs. losses comparison
“cryoBLM” values have a strong azimuthal dependence  their exact placement is critical
The maximum values were considered for this study
Dist. from IP [m] | Min. [Gy/s] | Max. [Gy/s]
32.97 | 0.018 | 0.028
43.75 | 0.021 | 0.064
54.55 | 0.026 | 0.065
65.67 | 0.019 | 0.039
73.6 | 0.019 | 0.032
“cryoBLM” values (debris)

## Slide 17: “cryoBLM” response: debris and losses
Highest sensitivity also at end of Q2B
Not comparable to the normal BLM sensitivity gain due to the less favourable positioning

## Slide 18: Summary
Abnormal losses in the triplet would only represent an operational threat for beam life-times that are sufficiently low to induce a dump in the collimation region by design
Even for the corresponding extreme loss rate, the presence of cold BLMs does not necessarily increase the detection sensitivity compared with what could be achieved with conventional BLMs, whose placement is less constrained and can be optimised to maximise pattern changes