## Slide 1: Beam Gas Vertex status and upgrade plans
Sotiris Vlachos for the BGV collaboration
HL-LHC Collaboration meeting, Madrid 14 Nov. 2017

## Slide 2: Beam Gas Vertex Detector Non destructive beam size measurement for HL-LHC not limited by accelerator luminosity
Demonstrator built around Beam 2, in Pt4
Demonstrator fully commissioned,
Data analysis ongoing
Tracks from beam-gas interactions to reconstruct beam spot
Ne @ 10-8 mbar injected at interaction volume
Goals:
statistical uncertainty: 5% in 3 min for 10^11 p/bunch
systematic uncertainty (vertex resolution): 5%
Should allow ε measurements with similar precision

## Slide 3: First look at BGV real data
A typical BGV event,
Blue lines : SciFi strips with significant energy deposit
Red lines : reconstructed tracks

## Slide 4: Vertex distribution in the BGV gas volume
Vertex x-y distribution cannot be used directly for beam profile:
Convolution of beam width and
depends heavily on z (long extrapolation ~ 1 metre)
Vertex reconstruction

## Slide 5: X-projection of vertex distribution
2-prong vertices
3-prong vertices
4-prong vertices
∝
High prong vertices allow also better event selection, gaussian position distribution

## Slide 6: Vertex reconstruction, Focus along beam direction
Run 2626,
used to estimate corrections
Run 2723,
High statistics,
same corrections used
Raw data
After relative plane
alignment O(1mm)

## Slide 7: Beam width measurement
IP and ɸ of particles from the same primary vertex are correlated.
This correlation for pairs of tracks (1,2 from the same event, with angles 1 and 2) is given by:
(being the beam spot variance along x (y) and the angle of the beam spot ellipse
If =
This correlation does not depend on

## Slide 8: IP correlation @ 6.5 TeV
= 177 ± 37 (stat) μm
Preliminary results, no systematic errors, no calibration
Fill #6358, BGV run duration 500 sec
For comparison, BSRT values:
= 178 μm, = 186 μm
Fill #6358: Physics pp run, 6.5 TeV, 1868 bunches, 2.28e14 p

## Slide 9: Beam energy dependence of
450 GeV → = 500 ± 63 μm
450 GeV – 3 TeV → = 314 ± 41 μm
3 TeV – 6 TeV → = 200 ± 38 μm

## Slide 10: BGV beam width measurements
Three 6.5 TeV runs at fills:
#6358 (2.28e14 p, 1868 b)
#6358 (2.09e14 p, 1868 b)
#6364 (1.38e14 p, 1868 b)

## Slide 11: BGV for HL-LHC == BGV2
BGV2 = Optimized BGV design for best vertex resolution
Two important detector design considerations for best IP and vertex resolution:
Good spatial resolution at each detector plane (≤ 100 μm)
Thin detectors in radiation lengths to minimize multiple scattering effects
In addition
Choice of BGV2 placement in LHC (optimal beam width to be measured wrt vertex resolution)
Min. possible reduced beam pipe diametre (currently 54 mm) to reduce extrapolation error

## Slide 12: BGV2 detector design considerations
Detector technology
and thickness
  Si-Strips
  MSGS (Micro-Megas)
Gas volume exit window
  Be
  Thin Al
Number of detectors along z
Exit Window
Additional detector plane

## Slide 13: BGV2 detector options
Thin, high precision detectors:
Si-Strip detectors: ‘industry standard’ 300 μm thick, 200 μm pitch → σ ~ 60 μm, max. sensor size 10x10 cm2
MicroMegas (micro pattern gas detector): 150 μm thick, 400 μm pitch → σ ~ 70 μm, sensor size 30x30 cm2
Both can be built in x-y configurations
Alternatively SciFi based detectors can also be considered

## Slide 14: MicroBulk MM
To be used in high rate environments, with a resistive strip plane
(BGV ~ 1KHz/cm2)

## Slide 15: Technology comparison
Silicon Strip sensors
300 μm thick planes
200 μm strip pitch
Industry-made sensors
Available analog R/O F/E chip, digital chip under development
‘Commercial’ DAQ and control system
Required interconnections between sensors
~40% more expensive
MicroMegas detector
150 μm thick planes
400 μm strip pitch
Joint CERN-Saclay development
Digital R/O F/E chip under development
Data transmission using GBT chip
Some R/D needed for final design
½ radiation length due to material
X-Y option offers an additional ½ in X0

## Slide 16: Gas volume exit window
Current window thickness 0.9 – 3.2 mm
New window thickness 0.9 mm(?)
Or Be window with current design (similar improvement in resolution)

## Slide 17: BGV Demonstrator Very encouraging first results Final BGV2 design Optimization ongoing Installation schedule compatible with LS3

## Slide 18: Backup Slides
BGV Location
Alignment corrections introduced in analysis
Material Budget
Gas target system
Trigger system
Precision tracker
MM read-out scheme

## Slide 19: BGV location
Single beam demonstrator @ LHC, point 4, beam 2 ring
at ~ -220m , beam 2 has x  y  150 m
at 7TeV and N  2.5μm, beam  0.22 mm
x  y allows beam pipe diameter reduction

## Slide 20: BGV module shifts due to alignment procedure

## Slide 21: BGV Material budget
Be instead of Al → ½ due to exit window
Table from R. Veness et al., Proceedings of IPAC2011
Exit window ~ 3% X0
One detector plane ~ 3% X0
1mm SciFi ~ 1mm Kapton ~ 0.5mm Si in X0

## Slide 22: The gas target
2m long gas volume:
0.75m conical tube (minimal beam impedance)
1.25m long cylinder (main interaction region)
Thin (1 – 3 mm) exit window to reduce multiple scattering
Narrow beam pipe around BGV
(52 – 58 mm instead of nominal 80mm):
Detector close to beam-gas interactions
    Max. acceptance
    Min extrapolation error
Gas flow restriction : Increased gas pressure in target ( mbar)

## Slide 23: Gas target operating conditions
the gas pressure ( mbar)
the proton nucleus cross-section (295 mb for 7 TeV p on Ne target)
the number of protons per bunch ()
the bunch revolution frequency (11.245 kHz)
the gas volume length along the beam axis (100 cm)
Expected beam-gas interaction rate:
per bunch

## Slide 24: The trigger system
Set of three scintillator planes (30x30 cm above and below beam line), not in particles’ path between beam-gas collision and tracking measurements:
VETO (upstream, before precision tracker)
SIGNAL and CONFIRM (downstream, after tracker)
TRIGGER = SIGNAL · CONFIRM ·
Trigger rate ≃ 300 Hz per LHC bunch

## Slide 25: Trigger detector performance
1 ns resolution – easy beam bunch identification
Background contamination < 10-4
Adjusted time difference between
SIGNAL and CONFIRM planes
LHC bunch structure as seen by BGV Trigger
Standalone measurement:
Ghost charge fraction = 0.29% ± 0.03%

## Slide 26
FELIX
FELIX
Micromegas readout scheme
ROC
SCA
Front end board
L1DDC
ROD
Event monitor
Config
DCS
calibration
Trigger monitor
Bidirectional fiber
One way fiber
network
TTC
# of VMMs per FEB:
MM: 8
Off-detector
miniSAS cables
VMM
VMM
...
VMM
VMM
GBTX
On-detector
GBTX
GBTX

## Slide 27: The precision tracker
4 Scintillating fibre (SciFi) (250 μm) modules (x, x’, y, y’) per (NEAR/FAR) station
4 (NEAR), 5 (FAR) SciFi planes per module
m
≃ 50 μm

## Slide 28: Alternative Beam position measurement
ɸ
IP
x0
y0
IP = x0sin(ɸ) – y0cos(ɸ)
Real primary vertex position
beam 2 positioned at (0,0)
of the BGV reference frame