## Slide 1: Beam-Gas Curtain (BGC) profile monitor: Progress with gas jet testing
Hao Zhang (Cockcroft Institute)
With thanks to:
V.Tsoganis, C.Welsch(Cockcroft Institute)
P.Forck, S.Udrea (GSI)
M.Ady, E.Barrios Diaz, N.Chritin, T.Doddington, R.Jones, R. Kersevan, A.Mariet, P.Magagnin, S.Mazzoni, A.Rossi, G.Schneider, R.Veness, (CERN BE-BI, TE-VSC, EN-MME)
7th HL-LHC Collaboration meeting, 15th November 2017

## Slide 2: Outline
Motivation
  Potential diagnostics for e-lens project and HLLHC
  Principle of beam induced fluorescence (BIF) detection with supersonic gas jet
Progress with gas jet testing
  Experimental setup
  Supersonic gas jet generation and gas dynamic simulation
  Characterization of the jet density
  First measurement using BIF with gas jet
Development of second gas jet prototype (version 2)
  Improvement
  Progress of the production

## Slide 3: Principle of detection
BIF detection using residual gas
*Credit: GSI, http://www-bd.gsi.de/dokuwiki/doku.php
Particle Beam propagate to the jet curtain perpendicularly
Gas jet curtain 45 degree tilted
BIF detection using supersonic gas jet
*Credit: GSI, http://www-bd.gsi.de/dokuwiki/doku.php

## Slide 4: Modified monitor (version1) for beam induced fluorescence test
First &Second skimmers
180 mm & 400 mm
Off centred nozzle hole
Nozzle
30 mm
7.2 mm *1.8 mm
4.0 mm * 0.4 mm
Third skimmers

## Slide 5: Generation of supersonic gas jet
3

## Slide 6: Progress of the gas dynamics simulation
Viscous-flow regime before 1st skimmer (ANSYS CFX)
Molecular flow after 1st skimmer (Monte Carlo simulation)
Molflow model：simulated from the 1st skimmer and input from the viscous-flow simulated in ANSYS CFX
Chart: Densities [1/m3]
The model is basic and have a converging issue when the chamber pressure is lower than 10-3 mbar, thus the divergence calculated from CFX is not accurate.
Credit: M. Ady
Credit: P. Magrgnin
Interaction Chamber

## Slide 7: Study of skimmer shape and pumping efficiency
Original ‘pyramid’ skimmer 78x18mm
Thin plate with hole
(theoretical)
Thick plate with hole
(3mm thickness)
3rd skimmer shape VS density
Offset the turbo pump and Tilt the turbo pump for better jet dumping
Credit: M. Ady

## Slide 8: Details on the interaction chamber
s (cross section, N2, 391 nm) | 9.2*10-19 cm2
I (electron current) | ~10 uA
n (gas jet density) | (~10-6 mbar)
d (jet thickness) | 2.8 mm
Ω (acceptance solid angle) | 4π·10-5 sr
T (Transmittance of optics) | 0.65
Tf (Transmittance of band pass filter) | 0.3
hpc (MCP photocathode efficiency) | 0.2
hMCP (MCP detection efficiency) | 0.5
Ng [photon number] ~ 0.08*Dt [t]

## Slide 9: Gas jet image from fluorescence
Shutter time: 8000s, MCP 1.0 V
E-gun: ~10 microA, 3.5keV energy
x
y
ROI
Residual gas image
3.13 mm
4.62 mm
FWHM
FWHM

## Slide 10
Progress of the new gas jet
  Fixed x and y motion of the nozzle
  New electon gun up to 100uA is purchased
New optical system is designed for this system.
See next talk from P. Forck
Larger pumping speed for all the turbo pumps
3.0 meter
Notes: Need a scale for the mechanics

## Slide 11: Open issues
The gas density
  Better nozzle-skimmer alignment
  Combinations of sizes, distances of nozzle and skimmer
  Higher stagnation pressure
The E-gun
  Not reached the maximum current
  Test with other higher current electron source
Gas species
  Nitrogen is tested currently
  Candidates could be Neon, Argon.

## Slide 12: Upgrade the electron gun and optical system
200 s
400 s
1000 s
2000 s
4000 s

## Slide 13: Summary
A prototype beam profile monitor using supersonic gas jet have been built to detect the beam induced fluorescence.
  The setup is modified from the previous beam jet ionization monitor.
  Simulations have been set up for the gas jet generation
  First measurement of a 2D beam image with gas jet using BIF mode.
A second prototype monitor has been designed and in process of production
  The new setup will be ready for testing earlier next year.

## Slide 14: Thanks for your attention
Thanks to the BGC collaboration:
V.Tsoganis, C.Welsch(Cockcroft Institute)
P.Forck, S.Udrea (GSI)
M. Ady, E.Barrios Diaz, N.Chritin, T.Doddington, R.Jones, R. Kersevan, A.Mariet, P.Magagnin, S.Mazzoni, A.Rossi, G.Schneider, R.Veness, (CERN BE-BI, TE-VSC, EN-MME)
7th HL-LHC Collaboration meeting, 15th November 2017

## Slide 15: Nozzle location respected to 1st skimmer
Fix position of the moveable gauge
Scan the nozzle horizontally and vertically
Chart: X_scan
| 11 | 11.1 | 11.2 | 11.3 | 11.4 | 11.5 | 11.6 | 11.7 | 11.8 | 11.9 | 12 | 12.1 | 12.2 | 12.3 | 12.4 | 12.5 | 11.75 | 11.76 | 11.77 | 11.78 | 11.79 | 11.8 | 11.81 | 11.82 | 11.83 | 11.84 | 11.850000000000012 | 11.860000000000012
 | 0.0044 | 0.0046 | 0.0057 | 0.0069 | 0.0073 | 0.01 | 0.016 | 0.0382 | 0.0519 | 0.0302 | 0.0161 | 0.0122 | 0.0095 | 0.0065 | 0.0065 | 0.0044 | 0.0418 | 0.0489 | 0.0504 | 0.0515 | 0.0542 | 0.0533 | 0.0516 | 0.0519 | 0.0498 | 0.0475 | 0.0474 | 0.038
Chart: Y_scan
| 12.9 | 12.8 | 12.7 | 12.6 | 12.5 | 12.4 | 12.3 | 12.2 | 12.1 | 12 | 11.9 | 11.8 | 11.7 | 11.6 | 12.350000000000012 | 12.360000000000012 | 12.370000000000006 | 12.38 | 12.39 | 12.4 | 12.41 | 12.42 | 12.43 | 12.44 | 12.450000000000006 | 12.46

 | 0.0051 | 0.0079 | 0.0053 | 0.016 | 0.0279 | 0.0416 | 0.0303 | 0.018 | 0.0121 | 0.0109 | 0.0087 | 0.009 | 0.008 | 0.0073 | 0.0385 | 0.0424 | 0.043 | 0.0453 | 0.0432 | 0.0441 | 0.0438 | 0.0423 | 0.0398 | 0.0392 | 0.0386 | 0.0355

## Slide 16: Characterizing gas jet density distribution
Third skimmer
Side view of the detection
D: 40 mm
Gas molecule will experience 20000 collision with tube wall per second
Ion current
Emitting current
Sensitivity
Assumption:
Gas molecular from jet entering the slit will immediately evenly distributed inside the tube.
Residual gas in and out is in a equilibrium state.
There is no molecular from the jet escaping the tube.
Tube
Slit
Jet
Front view of the detection
Slit size: Lx, Ly
Jet velocity
Volume of the small chamber

## Slide 17: Density distribution measurement for small skimmer
Iion(X,Y)
Differentiate the data in horizontal axis
1.55 mm
5.44 mm
Jet size in interaction point is estimated as : 4.54 mm * 0.83 mm
sjet = 0.29 mm
Skimmer size | 4×0.4 mm2
Oriental angle | 45˚
Resolution: 1pixel = 0.1mm

## Slide 18: Density distribution measurement for large skimmer
Iion(X,Y)
Differentiate the data in horizontal axis
Jet size in interaction point is estimated as : 10.03 mm * 2.81 mm
15.2 mm
19.2 mm
14.7 mm
15.2 mm
19.2 mm
4.5 mm
sjet = 0.99 mm
Skimmer size | 7.2×1.8 mm2
Oriental angle | 45˚
Resolution: 1pixel = 0.2mm