## Slide 1: Update on BPM development for IR1/IR5 LSS HL-LHC WP13
C. Boccard, N. Chritin, M. Krupa, T. Lefevre, G. Schneider, M. Wendt
7th HL-LHC Collaboration Meeting – Madrid – 15.11.2017

## Slide 2: Outline
HL-LHC inner triplet BPMs
Challenges
Current state of the project
String test
Conclusions and outlook

## Slide 3: BPMs per HL-LHC IP side

## Slide 4: New BPMs per HL-LHC IP side
1x BPMSQTA | cryogenic tungsten-shielded directional coupler, aperture A (small)
5x BPMSQTB | cryogenic tungsten-shielded directional coupler, aperture B (large)
1x BPMSWQ | warm directional coupler
2x BPMWQ | warm (non-directional) button
In total: 9 BPMs x 2 IPs x 2 sides = 36 new BPMs to be installed

## Slide 5: Design priorities
A
B
Main focus on the cryogenic directional couplers BPMSQTA and BPMSQTB which are required for string test in 2020
Minimising differences between the two designs
Studying possibilities of reusing parts of the design for the non-cryogenic BPMSWQ

## Slide 6: Challenges
Both beams in a single vacuum chamber
Octagonal vacuum chamber
Cryogenic BPMs installed in vacuum
Tungsten blocks at H and V planes to absorb collision debris
Heat load due to electron cloud
Complicated integration and alignment

## Slide 7: Electrode design
2016
2017
3D printing of the 2016 electrode very challenging
Major simplification of the electrode shape in 2017
Additional performance improvements achieved

## Slide 8: Electrode simulations - TDR
Goal: electrode impedance stable at 50 ± 0.5 Ω

## Slide 9: BPM directivity

## Slide 10: Electrode simulations - directivity
Dream: 30+ dB directivity → 0.0316 downstream ratio

## Slide 11: Electrode simulations - directivity
Optimisation: temporal bunch separation at BPM locations

## Slide 12: Mechanics, integration and alignment
Courtesy: N. Chritin
Mechanical design well advanced
Integration with the interconnects and
alignment ongoing with other WPs

## Slide 13: Heat load estimations
Main sources of heat load:
Collision debris absorbed by W: 1.5 W
Collision debris absorbed by BPM: 1 W
Electron cloud: 2 W (20 W uncoated)
Beam: 0.5 W
Cables: 0.4 W
Total per BPM: ~ 6 W (coated), ~ 24 W (uncoated)

## Slide 14: Lack of active cooling
Courtesy: M. Pasquali
BPM 220 K above beam screen’s temperature

## Slide 15: With active cooling
Courtesy: M. Pasquali
Cooling inspired by the beam screen solution
Electrodes 5 K above beam screen’s temperature

## Slide 16: Other thermomechanical considerations
Thin skin BPM body deformation due to pressure difference – 60 μm
Electrode-body thermal expansion differential – 100 μm (steady state)
Electrode thermal deformation – ~10 μm
More simulations ongoing

## Slide 17: String test
6 cold BPMs required – 1 x BPMSQTA and 5 x BPMSQTB – verification whether full BPMs are really needed
Possibility of including warm BPMSWQ under study
The BPMs need to be ready in 2020

## Slide 18: Conclusions and outlook
Development of new HL-LHC BPMs on track
Focus put on design of the BPMs required for the string test
Current main activities: advanced transient thermomechanical simulations, full interconnect integration, feedthrough studies

## Slide 19: Thank you for your attention!
Acknowledgements: A. Demougeot, D. Draskovic, D. Duarte Ramos, R. Fernandez Gomez, G. Iadarola, R. Jones, M. Pasquali

## Slide 20: Back up: Tungsten shielding
Courtesy: A. Tsinganis, F. Cerutti

## Slide 21: Back up: Heat load
Courtesy:
G. Iadarola

## Slide 22: Back up: Locations
Number | 1 | 2 | 3 | 4 | 5 | 6 | 7
Type | BPMSTQA | BPMSTQB | BPMSTQB | BPMSTQB | BPMSTQB | BPMSTQB | BPMSQW
Distance from IP [mm] | 21853 | 33073 | 43858 | 54643 | 65743 | 73697 | 86846
Location comments | Between TAXS and Q1A | Between Q1B and Q2A | Between Q2A and Q2B | Between Q2B and Q3A | Between Q3B and CP | Between CP and D1 | After D1, WARM
N | 5.34 | 8.34 | 11.23 | 14.11 | 17.08 | 19.21 | 22.72
Periodicity number |  |  |  |  |  |  | 
Preceding ideal position [mm] | 20,570 | 31,790 | 43,010 | 54,230 | 65,450 | 72,930 | 84,150
N = floor(N) |  |  |  |  |  |  | 
Succeeding ideal position [mm] | 24,310 | 35,530 | 46,750 | 57,970 | 69,190 | 76,670 | 87,890
N = ceil(N) |  |  |  |  |  |  | 
Distance from ideal position [mm] | -1,283 | -1,283 | -848 | -413 | -293 | -767 | 1,044
Towards the IP. Negative number means it's too far from the IP |  |  |  |  |  |  | 
TOF from ideal position [ns] | -4.28 | -4.28 | -2.83 | -1.38 | -0.98 | -2.56 | 3.48
Towards the IP. Negative number means it's too far from the IP |  |  |  |  |  |  | 
Bunch arrival time difference [ns] | 3.92 | 3.92 | 6.82 | 9.72 | 10.52 | 7.36 | -5.51
Negative numbers mean the bunch going towards the IP arrives first |  |  |  |  |  |  | 

## Slide 23: Back up: LHC electrodes
Courtesy: C. Boccard, P. Clergue