## Slide 1: HL-LHC - Residual Dose Rate Estimations in the LSS1 and LSS5 (from TAXS up to Q7) + A Preliminary collective dose estimation exercise for ALARA optimization
C. Adorisio
7th HL_LHC Collaboration Meeting – CIEMAT, 13-16 November 2017

## Slide 2: Outline
Rules and regulations
  Limitation
  Optimization/ALARA
Optimization during design
  Methodology
  Design options
Residual dose rate outlook
  LHC/HL-LHC operation scenario considered
  FLUKA geometry
  Residual dose rate estimations
    Ultimate scenario – LS4
    LSS1 vs. LSS5
    HL-LHC vs LHC (LS4 vs. LS3)
    LS4 vs. LS6
    Nominal vs. Ultimate
RP assessment for the new underground areas in P1 and P5
Example: preliminary dose estimations for the alignment measurement
Summary and Conclusions
A reminder

## Slide 3: Rules and regulations a reminder

## Slide 4: Safety Code F Limitation
Design and operation !
Radiation Workers
Not occupationally exposed workers
Environment
Category A: 20 mSv/y
Category B: 6 mSv/y
1 mSv/y
0.3 mSv/y

## Slide 5: Safety Code F Limitation
Total number of working hours per year: 2000 hours
(example: Supervised Area 3 µSv/h × 2000 h = 6 mSv)
Low-occupancy: < 20% of working time

## Slide 6: Safety Code F Optimization (ALARA)
Design and operation !
Workers on CERN site
100/10 µSv/yr
Outside of CERN (environment)
10 µSv/yr
Optimization by balancing:
individual doses
number of persons exposed
risk
costs
consequences of potential failures

## Slide 7: Safety Code F Limitation / Optimization
6/20 mSv/yr 1 mSv/yr 300 mSv/yr
Radiation Workers
Other workers
Population outside CERN
On CERN site
On CERN site
Optimization / ALARA to be demonstrated
100 mSv/yr 10 mSv/yr 10 mSv/yr
Limits
Optimization Thresholds
Optimized (by definition)
On CERN site

## Slide 8: Optimization during operation ALARA procedure
Primary criteria
Individual Dose
Collective Dose
Secondary criteria
Ambient dose equivalent rate
Airborne activity
Surface contamination
Level I
Level II
Level III
100 mSv
500 mSv
1 mSv
5 mSv
50 mSv/h
5 CA
10 CS
2 mSv/h
200 CA
100 CS
Detailed work-and-dose planning
ALARA committee
ALARA categories for individual interventions
100 mSv / intervention
CERN dose objectives
Operational Periods
Long Shutdowns
3 mSv/yr

## Slide 9: Optimization during design

## Slide 10: Intervention doses Methodology
New design?
Step 1
1. Calculation of residual dose rate maps
→ for cooling times typical for interventions on the respective component
→ based on nominal operational parameters
→ definition of geometry and materials as detailed as needed (and available)
2. Calculation of individual and collective intervention doses
→ based on as realistic as possible work scenarios, including locations, duration, number of persons involved,..
→ identification of cooling times below which work will be impossible
design criterion:
2 mSv/intervention/yr
→ communication of results and constraints to equipment groups
3. Revision of design and/or work scenario
→ start with work steps that give highest individual or collective doses
→ consider optimization measures (distance, tooling, material choices, etc.)
→ identify if remote handling is possible
Revised working scenario?
Step 2
Start of iteration

## Slide 11: Optimization during design Design options
Material choice
Avoid materials for which no radioactive waste elimination pathway exists (e.g., highly flammable metallic activated waste)
Optimized handling
Provisions for fast installation/ maintenance/ repair, in particular, around beam loss areas (e.g., plugin systems, quick-connect flanges, remote survey, remote bake-out)
Limitation of installed material
Install only components that are absolutely necessary, in particular in beam loss areas
Reduction of radioactive waste
Radiation resistant
Foresee easy dismantling of components
Easy access to components that need manual intervention or complex manipulation
Low activation properties to reduce residual doses and minimize radioactive waste (optimization with ActiWiz code, Web-site: https://actiwiz.web.cern.ch)

## Slide 12: Residual dose rate outlook

## Slide 13: LHC/HL-LHC Operational Scenarios
 | Year of (HL-)LHC Operation | Peak / levelled luminosity [cm-2s-1] |  | Integrated luminosity [fb-1] | 
 | ≤2012 | 0.8E+34 |  | 30 | 
LS1 |  |  |  |  | 
 | 2015 | 6.30E+33 |  | 4 | 
 | 2016 | 1.40E+34 |  | 40 | 
 | 2017 | 1.60E+34 |  | 50 | 
 | 2018 | 1.60E+34 |  | 50 | 
LS2 | (2 years) |  |  |  | 
 | 2021 | 2.0E+34 |  | 60 | 
 | 2022 | 2.0E+34 |  | 60 | 
 | 2023 | 2.0E+34 |  | 60 | 
LS3 | (3 years) | Nominal | Ultimate | Nominal | Ultimate
 | 2027 | 5.0E+34 | 7.5E+34 | 250 | 300
 | 2028 | 5.0E+34 | 7.5E+34 | 250 | 300
 | 2029 | 5.0E+34 | 7.5E+34 | 250 | 300
LS4 | (1 year) |  |  |  | 
 | 2031 | 5.0E+34 | 7.5E+34 | 250 | 300
 | 2032 | 5.0E+34 | 7.5E+34 | 250 | 300
 | 2033 | 5.0E+34 | 7.5E+34 | 250 | 300
LS5 | (1 year) |  |  |  | 
 | 2035 | 5.0E+34 | 7.5E+34 | 250 | 300
 | 2036 | 5.0E+34 | 7.5E+34 | 250 | 300
 | 2037 | 5.0E+34 | 7.5E+34 | 250 | 300
LS6 |  |  |  |  | 
~TOT 350 fb-1
TOT ~3050 fb-1
TOT ~2600 fb-1
3 blocks of 3 consecutive years of operation + 1 year Long Shutdown each
  Nominal: 5.0x1034 – 250 fb-1/y
  Ultimate: 7.5x1034 – 300 fb-1/y
HL-LHC
past

## Slide 14: LHC – Simulation geometry
Long Straight Sections in the two interaction regions, IR1 and IR5:
Actual machine layout
Real collimators settings
LHC IR1 LSS
LHC IR5 LSS
Thanks to the FLUKA Team

## Slide 15: LHC – Simulation/measurement comparison
During the year, simulations are performed in order to prepare the Work and Dose Planning (WDP) in advance for each Technical Stop (TS)
Radiation measurement, which performed at the beginning of TS, in order to classify the area and prepare WDP for interventions, used to benchmark the simulation

## Slide 16: LHC - Residual Dose Rate estimation
LS3 – IR1 Ambient dose equivalent rate – 1 month cooling time
Residual dose rate estimations are available for LS2 and LS3 periods and can be used for the individual/collective dose evaluation for the consolidation/dismantling works
~ 4050% more

## Slide 17
Same geometry model developed by the FLUKA team for the energy deposition studies as presented by Andrea Tsinganis @ 6th HL-LHC Collaboration Meeting in Paris
HL-LHC FLUKA Model

## Slide 18: HL-LHC FLUKA Geometry
HL-LHC IR1 v1.3
HL-LHC IR5 v1.3
Thanks to the FLUKA Team

## Slide 19: HL-LHC – Residual Dose Rate estimation
HL-LHC LSS1 – LS4 1 month cooling time
HL-LHC LSS5 – LS4 1 month cooling time
The optics and the collimator settings are the same for IR1 and IR5.
Only difference is crossing angle plane.

## Slide 20: LSS1 vs LSS5
The optics and the collimator settings are the same for IR1 and IR5.
Only difference is crossing angle plane.

## Slide 21: LHC vs HL-LHC – Residual Dose Rate estimation
Inner triplet area - comparing the highest peaks:
LS4Ult vs LS3
Higher of a factor ~8

## Slide 22: LS4 vs LS6
Cooling time | LS6/LS4
1 hour | 1.02
1 day | 1.03
1 week | 1.06
1 month | 1.09
4 months | 1.18
1 year | 1.29

## Slide 23: Nominal vs Ultimate
Cooling time | Ultimate/ Nominal
1 hour | 1.50
1 day | 1.46
1 week | 1.35
1 month | 1.30
4 months | 1.24
1 year | 1.23

## Slide 24: Example: A Preliminary collective dose estimation for ALARA optimization

## Slide 25: Example - alignment
 |  |  |  |  |  | 2 hours (mSv) |  |  | 
aisle | - | 50 | 25 | 10 | 5 | 100 | 50 | 20 | 10
Collective Dose (man.mSv) |  | 1333 | 753 | 311 | 122
First estimation done considering the actual procedure (elements from D1 up to cell 6)
vertical measurements, 2 workers, 10 minutes next to each element, ~2 hours work
measurements have to be done asap the machine stops
alignment, if needed, can be done at longer cooling time
Very high individual and collective doses even at long cooling time
For example:
measurement (1 week cooling time)
+
alignment (all elements (!), 4 months cooling time)
Collective dose: ~1.6 man.mSv

## Slide 26: Example - alignment
Alignment group solution (*):
Permanent remote monitoring system for the equipment up to Q5
Motorized jacks for the main components (D1, TAXN, D2, crab cavities, Q4, Q5)
Fast adjustment system made of plug-in motors to perform remote alignment (estimated time to plug it in and out: 2 minutes)
Access for measurement and alignment needed only on cell 6 elements (TCL6, mask and Q6), as it is done today
(*) See presentation given by Helene at WP15 meetings:
07.04.2017
13.10.2017
 |  | LSS5 (one side only) |  |  | 
 |  | 10 minutes (uSv) |  | 2 minutes (uSv) | 
 | distance from IP (cm) | 1 week | 1 month | 4 month | 1 year
D1 | 7442 | 0.0 | 0.0 | 0.0 | 0.0
 | 8450 | 0.0 | 0.0 | 0.0 | 0.0
TAXN | 12626 | 0.0 | 0.0 | 0.0 | 0.0
 | 13047 | 0.0 | 0.0 | 0.0 | 0.0
TCL4 | 13511 | 0.0 | 0.0 | 23.3 | 8.3
D2 | 13779 | 0.0 | 0.0 | 0.0 | 0.0
 | 15224 | 0.0 | 0.0 | 0.0 | 0.0
crabs | 15600-15900 | 0.0 | 0.0 | 0.0 | 0.0
Q4 mask | 17075 | 0.0 | 0.0 | 0.3 | 0.2
Q4 | 17230 | 0.0 | 0.0 | 0.0 | 0.0
 | 18262 | 0.0 | 0.0 | 0.0 | 0.0
TCL5 | 19705 | 0.0 | 0.0 | 7.2 | 2.3
Q5 mask | 19959 | 0.0 | 0.0 | 1.0 | 0.5
Q5 | 20115 | 0.0 | 0.0 | 0.0 | 0.0
 | 21027 | 0.0 | 0.0 | 0.0 | 0.0
TCL6 | 22062 | 85.0 | 51.7 | 23.3 | 8.3
Q6 mask | 22256 | 11.7 | 6.7 | 3.3 | 1.7
Q6 | 22472 | 8.3 | 5.0 | 1.7 | 0.8
 | 23265 | 1.7 | 0.8 | 0.8 | 0.8
 |  | 107 | 64 | 61 | 23
aisle | - | 50 | 25 | 10 | 5
 | Collective Dose (man.mSv) | 157 | 89 | 71 | 28
For example:
measurement (1 week cooling time)
+
alignment (all elements (!), 4 months cooling time)
Collective dose: 228 man.mSv

## Slide 27: Example – alignment Lesson learnt
The estimation is done considering the first LS in the HL era (ultimate scenario)
Nominal scenario: ~ 30% less
LS6 vs LS4:
  up to 30% more for long cooling times
  few % more for short cooling times
Secondary elements measurement and alignment not taken into account in this example (e.g. vacuum equipment, BPMs…)
For example:
measurement (1 week cooling time)
+
alignment (all elements (!), 4 months cooling time)
Collective dose: 228 man.mSv
For example:
measurement (1 week cooling time)
+
alignment (all elements (!), 4 months cooling time)
Collective dose: ~1.6 man.mSv
Same procedure as in the LHC nowadays
Optimized procedure for HL-LHC

## Slide 28: HL-LHC New Underground galleries

## Slide 29: HL-LHC new underground galleries
New underground galleries will be excavated to put new services in Point 1 and Point 5
RP assessment:
  Shielding requirements to access the new underground during operation
  Excavation spoils activation
Emergency escape
LHC
LHC
Emergency escape
Emergency escape
Emergency escape

## Slide 30: HL-LHC new underground galleries Shielding
Supervised Radiation Area:
< 6 mSv
Accidental scenario
Full beam loss
just in front of the nearest connection
1 m x 10 cm x 10 cm tungsten target
Beam parameters considered:
2808 bunches
2.2·1011 ppb
Effective Dose (mSv)
Effective Dose (mSv)
6 mSv
One tungsten block
(100cm x 10cm x 10cm)
in front of the nearest connection
Escape path

## Slide 31: HL-LHC new underground galleries Shielding
Supervised Radiation Area:
< 3 mSv/h
< 15 mSv/h
Normal proton operation
Ultimate scenario
Levelled luminosity 7.5·1034 cm-2s-1
The attenuation provided by the shielding walls and the concrete stairs in the UPR escape path is evaluated by the accidental case
Effective Dose (mSv)
Effective Dose (mSv)
~10-8
HL-LHC Run at Ultimate intensity
Ambient Dose Equivalent– Stray radiation – Ultimate intensity
Ambient Dose Equivalent Rate (Sv/h)
Max dose rate next to the tunnel wall is 50 Sv/h
 In the underground gallery (UAs) closest accessible point 0.5 mSh/h
Ambient Dose Equivalent Rate (Sv/h)
50
60
40
30
20
10
0

## Slide 32: HL-LHC new underground galleries Spoil activation
 | EYETS 2016-17 (~3 months cooling time) |  | 
UPR | g spectrometry measurements | ActiWiz 3 Creator© | 
 |  | full | only g
concrete | 1.15E-01 | 4.96E-01 | 9.70E-02
soil | 8.17E-03 | 1.65E-02 | 5.30E-03
 | EYETS 2016-17 (~3 months cooling time) |  | 
UPR | g spectrometry measurements | ActiWiz 3 Creator© | 
 |  | full | only g
concrete | 1.15E-01 | 4.96E-01 | 9.70E-02
soil | 8.17E-03 | 1.65E-02 | 5.30E-03
Ca-45 | 68%
Na-22 | 28%
S-35 | 2%
Ca-45 | 80%
Na-22 | 7%
Zn-65 | 3%
Fe-55 | 3%
S-35 | 1%
Mn-54 | 1%
Ca-45 is a pure b emitter: cannot be seen with g-spec
 | LS2 | 
UPR | ActiWiz 3 Creator© | 
 | 1 month | 4 months
1st meter | 5.19E+00 | 4.15E+00
2nd meter | 3.19E-01 | 2.90E-01
3rd meter | 1.87E-02 | 1.70E-02
 | LS2 | 
UPR | ActiWiz 3 Creator© | 
 | 1 month | 4 months
1st meter | 5.19E+00 | 4.15E+00
2nd meter | 3.19E-01 | 2.90E-01
3rd meter | 1.87E-02 | 1.70E-02
The specific and absolute activity of a radionuclide exceeds the exemption limit, which in reality means, since an object contains normally a large number of different radio-nuclides:
Is it radioactive?
During 2016 EYETS some concrete wall and rock samples were taken and analysed

## Slide 33: it is time to summarize and conclude…

## Slide 34: Summary and Conclusions
Simulation are performed using a very long and detailed geometry which reproduce the real accelerator environment in great detail
Fruitful collaboration with the FLUKA team
  the use of the same geometry models they developed
  the consistency with the energy deposition study
Radio nuclide inventory and activity estimation are done using Fluka and the Actiwiz 3 Creator© code
The simulation results are continuously benchmarked with the radiation measurements performed in the LHC machine

## Slide 35: Summary and Conclusions
In the HL-LHC era, the residual radiation levels will be higher and there will be more areas with high residual radiation compared to the actual LHC machine
It is important, in the design phase, to take this into account and do all the possible optimization in order to reduce the individual and collective dose for the interventions in these areas
Design optimization could also minimize the machine downtime
Residual dose rate estimations are available for LSS1, LSS5, LSS8 and for the experimental caverns, for all the Long Shutdowns
LSS7 residual dose rate estimations are under preparation

## Slide 36: Thank you!

## Slide 37: Radiological quantities
Beam operation periods
  dose equivalent to personnel by stray radiation in accessible areas
  activation of water and air and their release into the environment as well as the resulting annual dose to the reference groups of the population
  dose equivalent to personnel and environment in case of abnormal operation or accidents
Beam-OFF periods
  induced radioactivity in accelerator components and related residual dose equivalent rate
  individual and collective doses to personnel during interventions in radiation areas
Decommissioning
  waste minimization
  radionuclide inventory for waste disposal

## Slide 38: Residual Dose Rate Maps
HL-LHC LSS1 – LS4 1 month cooling time
HL-LHC LSS5 – LS4 1 month cooling time

## Slide 39: Residual Dose Rate Profiles

## Slide 40: Residual Dose Rate Profiles

## Slide 41: Residual Dose Rate Profiles

## Slide 42: Residual Dose Rate Profiles