## Slide 1
FCC hh dump kicker - switch topologies and impact on beam
Pieter Van Trappen, Elisabeth Renner
Acknowledgments: Mike Barnes, Wolfgang Bartmann, Florian Burkart, Brennan Goddard, Thomas Kramer

## Slide 2
Outline
Alternative topologies motivation
Electrical simulations
Impact on beam: comparison series connected switch to conventional switch design.
Open questions - Discussion

## Slide 3: Alternative topologies motivation
Assuming that the switch (can be a stack of multiple devices) will self-trigger (a.k.a. erratic) because of R2E SEE or electrostatic discharges
What can be done to reduce the effect (i.e. magnet current) by using alternative topologies?
 Switch series connection vs. crowbar connection

## Slide 4: Electrical simulations
New dump layout yield the below ‘relaxed’ requirements.
Parameters (per module) | Value
Number of modules | 300
B.dl [T.m] | 0.025
k [µrad] | 0.150
Length [mm] | 300
Inductance [µH] | 0.38
Current [kA] | 2.1
Magnet current rise-time | 1 µs
Lumped inductance magnet with a small HV capacitor for fast magnet current rise-time and bigger (slower) capacitor discharge for flat-top.
Focus on most constraining part: fast rising-edge (1 us) capacitor discharge
Cable and stray inductances ignored
COTS Mitsubishi CM1000HA-24H has a complete PSpice model with parasitic components; max IC=2kA; max VCES=1.2kV

## Slide 5: Electrical simulations cont’d
Series connection
bottom-side IGBT blocking full capacitor voltage; Vpfn vs. magnet leakage current
High dV/dt at bottom IGBT can trigger bottom-side IGBT (capacitive divider over Miller capacitance and CGE)
250A
2500A
Nominal kick (0-100% 1.1us, 2.1kA, Vcapa=1400V)

## Slide 6: Electrical simulations cont’d
Crowbar connection
No nominal kick cause single IGBT cannot block 1400V
Detection and triggering circuit delay!
4000A
Is the
U2 collector current vs. 100ns -500ns delay
magnet current

## Slide 7
  Oscillation amplitude*:
  1 sw.: 0.9 sigma
  2 sw. in series: 0.01 sigma
*Values for MKD 1, as worst case scenario
(MKD entrance: m, MKD exit: )
Impact on the beam: oscillation introduced by 1 erratic MKD

## Slide 8
Assumptions
beam profile: gaussian
different numbers of erratic segments considered  worst case scenarios chosen for further analysis:
  first x MKDs erratic
  simultaneous erratics
  phase advance between MKD1 and observation point 90° (full amplitude), although in current design
  If x segments fail, how many bunches can be tolerated to make an additional turn? How many abort gaps are necessary? …
Impact on the beam: load on TCP for x erratic MKDs

## Slide 9
Estimate of load on TCP (7.6 ) by x erratic MKDs
Assumptions
beam profile: gaussian
different numbers of erratic segments considered  worst case scenarios chosen for further analysis:
  first x MKDs erratic
  simultaneous erratics
  phase advance between MKD1 and observation point 90° (full amplitude), although in current design
  If x segments fail, how many bunches can be tolerated to make an additional turn? How many abort gaps are necessary? …

## Slide 10
Estimate of load on TCP (7.6 ) by x erratic MKDs
Energy/power thresholds for load comparison:
~ 500 kW: LHC: TCP load limit to avoid quenches of DS magnets [1]
~ 17 kJ/g: melting heat of graphite [3,4] with a max. energy deposition of and
[1] S. Radaelli et al, Quench tests at the large hardron collider with collimation losses at 3.5 Z TeV, Proceedings of HB2012
[2] Y. Nie, R. Schmidt, Interaction of 50 MeV - 50 TeV protons with solid copper and graphite targets in hadron accelerator complex at CERN, 2017
[3] A. Lechner, Design studies for the FCC-hh beam dump. FCC Week 2017; based on [4]
[4] Jan M. Zazula, LHC Project Note 78 / 97, 19
[2]
But: Very rough estimate! (TCP not graphite etc.) Only for order of magnitude

## Slide 11
Acceptable number of bunches to stay below chosen load at 7.6 sigma for x erratic segments

## Slide 12
Acceptable number of bunches to stay below chosen load at 7.6 sigma for x erratic segments

## Slide 13
Beam impact: Conclusion and open questions
series switch architecture is favorable for ‘1 sigma oscillation’, as load on is TCP negligible
potential to reduce number of segments should be considered

## Slide 14
Beam impact: Conclusion and open questions
series switch architecture is favorable for ‘1 sigma oscillation’, as load on is TCP negligible
potential to reduce number of segments should be considered
But, careful:
600 instead of 300 switches  higher failure rate
series connected switches: erratic elements are missing for extraction after 1 turn.
  how many erratic MKDs can be tolerated to still extract the beam/partial beam safely after 1 turn (all previous erratic MKDs now missing)?
Studies ongoing, discussion appreciated