## Slide 1: 40 m Alternative Triplet
Leon van Riesen-Haupt

## Slide 2: Quads
Before: Triplet made of 2-3-2 pattern of identical magnets
New Triplet
Quadrupole | Sub Quads | Length | Coil Radius | Shielding | k | Gradient | Aperture
Q1 | 2 | 13.6 m | 84.7 mm | 44.2 mm | 0.000637 | 125 T/m | 30 mm
Q2 | 4 | 11.75 m | 84.7 mm | 33.2 mm | -0.000664 | 111 T/m | 41 mm
Q3 | 2 | 13.6 m | 84.7 mm | 24.2 mm | 0.000581 | 110 T/m | 50 mm
Quadrupole | Sub Quads | Length | Coil Radius | Shielding |  | Gradient | Aperture
Q1 | 2 | 13.6 m | 84.7 mm | 44.2 mm | 0.000637 | 125 T/m | 30 mm
Q2 | 4 | 11.75 m | 84.7 mm | 33.2 mm | -0.000664 | 111 T/m | 41 mm
Q3 | 2 | 13.6 m | 84.7 mm | 24.2 mm | 0.000581 | 110 T/m | 50 mm
Quadrupole | Sub Quads | Length | Coil Radius | Shielding | k | Gradient | Aperture
Q1 | 2 | 15 m | 98.3 mm | 44.2 mm | 0.000637 | 106 T/m | 43 mm
Q2 | 3 | 15 m | 98.3 mm | 33.2 mm | -0.000664 | 111 T/m | 54 mm
Q3 | 2 | 15 m | 98.3 mm | 24.2 mm | 0.000581 | 97 T/m | 63 mm
Quadrupole | Sub Quads | Length | Coil Radius | Shielding |  | Gradient | Aperture
Q1 | 2 | 15 m | 98.3 mm | 44.2 mm | 0.000637 | 106 T/m | 43 mm
Q2 | 3 | 15 m | 98.3 mm | 33.2 mm | -0.000664 | 111 T/m | 54 mm
Q3 | 2 | 15 m | 98.3 mm | 24.2 mm | 0.000581 | 97 T/m | 63 mm

## Slide 3: Optics
Old Round
New Round

## Slide 4: Beam Stay Clear
Old Round
New Round

## Slide 5: Comparison
45 m
2-3-2 layout
Identical magnets
Longer triplet
Larger functions
Smaller fields
Larger physical aperture
Large BSC
Optimised shielding
40 m (first iteration)
2-4-2 layout
Different magnets
3.6 m shorter magnetic length
Slightly smaller functions
Larger fields
Smaller aperture
Smaller BSC
Might need to play around with shielding

## Slide 6: Summary
Smaller does yield a shorter triplet
Several things go on so not sure how it affects chromaticity
Aperture suffers
This is only the first iteration