## Slide 1
Future strategies and technologies
http://cern.ch/fcc
FCC
PS
SPS
LHC
Work supported by the European Commission under the HORIZON 2020 project EuroCirCol, grant agreement 654305
M. Benedikt
gratefully acknowledging input from FCC coordination group the global design study team and all contributors

## Slide 2
High energy accelerators & colliders
Using electrical fields (RF cavities)to accelerate and magnetic fields (accelerator magnets) to guide and collide charged particle beams (electrons, protons & anti-particles)
Aim at higher energy accelerators for 2 reasons:
  Production of new heavier particles (according to Einstein): E = mc2 ≤ 2E beam (collider)
  Resolving smaller distances (according to de Broglie): Wavelength l = hc/E for LHC  210-18 cm
Higher energy  Increased potential for discoveries
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 3
Colliders with
superconducting arc magnet system
Colliders with
superconducting RF system
Colliders with
superconducting magnet & RF
Colliders constructed and operated

## Slide 4
Discoveries by colliders
Standard Model
Particles and forces
Colliders are powerful instruments in High Energy physics
for particle discoveries and precision measurements
SPEAR:
charm quark
tau lepton
PETRA:
gluon
SppS:
Z-boson
W-boson
Tevatron:
top-quark
LHC:
Higgs-boson
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 5
LHC: present collider flagship
2012: Higgs boson discovery
    Completes standard model describing known matter, BUT this is only 5% of the universe!
    what is dark matter?
    what is dark energy?
    why is there more matter than antimatter?
    what about gravity?
    etc…
 Upgrade and full exploitation of LHC as first step
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 6
High Luminosity LHC project scope
L. Rossi
More than100 new SC magnets 36 large magnets in Nb3Sn Powering via SC Links and HTS Current Leads
20 new RF cavities
New tunnel and surface infrastructures
New and upgraded cryo plants
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 7
Step 1: HL-LHC upgrade – ongoing
    HL-LHC significantly increases data rate to improve statistics, measurement precision, and energy reach in search of new physics
    Gain of a factor 5 in rate, factor 10 in integral data wrt initial design
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 8
Step 2: Future high energy colliders
For physics beyond the LHC and beyond the Standard Model, under study (synergy of):
    Linear e+e- colliders (CLIC, ILC)
    ECM up to  3 TeV
    Circular e+e- colliders (CepC, FCC-ee)
    ECM up to  400 GeV - limited by e synchrotron radiation. Ideal for precision measurements
    Circular p-p colliders (SppC, FCC)
    ECM up to  100 TeV
    Ideal for discoveries at higher energy frontiers

## Slide 9
High Energy Colliders under study
100 TeV pp  10-19 m
discovery of new particles at 10 TeV mass scale
100 TeV

## Slide 10
European Strategy Update 2013
“CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron-positron high-energy frontier machines.”

## Slide 11
International FCC collaboration (CERN as host lab) to study:
pp-collider (FCC-hh)  main emphasis, defining infrastructure requirements
80-100 km tunnel infrastructure in Geneva area, site specific
e+e- collider (FCC-ee), as potential first step
p-e (FCC-he) option, integration one IP, FCC-hh & ERL
HE-LHC with FCC-hh technology
~16 T  100 TeV pp in 100 km
Future Circular Collider Study
GOAL: CDR and cost review for the next ESU (2019)

## Slide 12
Tevatron (closed)
Circumference: 6.2 km
Energy: 2 TeV

## Slide 13
Large Hadron Collider
Circumference: 27 km
Energy:
- 14 TeV (pp)
- 209 GeV (e+e-)

## Slide 14
Future Circular Collider
Circumference: 80-100 km
Energy:
100 TeV (pp)
>350 GeV (e+e-)

## Slide 15
FCC-hh: 100 TeV pp collider as long-term goal  defines infrastructure needs
FCC-ee: e+e- collider, potential intermediate step
HE-LHC: based on FCC-hh technology
Tunnel infrastructure in Geneva area, linked to CERN accelerator complex;
site-specific, as requested by European strategy
Launch R&D on key enabling technologies in dedicated R&D programmes, e.g.
16 Tesla magnet program, cryogenics,
SRF technologies and RF power sources
FCC Scope:
Accelerator and Infrastructure

## Slide 16
Elaborate and document
- Physics opportunities
- Discovery potentials
Experiment concepts for hh, ee and he
Machine Detector Interface studies
R&D needs for detector technologies
Overall cost model for collider scenarios
including infrastructure and injectors
Develop realization concepts Forge partnerships with industry
FCC Scope:
Physics & Experiments

## Slide 17
Role of CERN
Host the study
Prepare organisation frame
Setup collaboration
Identify R&D needs
Estimate costs

## Slide 18
Strategic Goals
Make funding bodies aware of strategic needs for research community
Provide sound basis to policy bodies to establish long-range plans in European interest
Strengthen capacity and effectiveness in high-tech domains
Provide a basis for long-term attractiveness of Europe as research area

## Slide 19: A sustained decrease in specific cost
Will FCC pass below the specific cost of
100 kCHF/GeV c.m.?

## Slide 20
Constr.
Physics
LEP
Construction
Physics
Proto
Design
LHC – operation run 2
Construction
Physics
Design
HL-LHC - ongoing project
Physics
Construction
Proto
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2035
~20 years
Design
FCC – design study
Must advance fast now to be ready for the period 2035 – 2040
Goal of phase 1: CDR by end 2018 for next update of European Strategy
CERN Circular Colliders & FCC

## Slide 21
Time Indicator
Conceptual studies |  |  |  |  |  |  | 
R & D |  |  |  |  |  |  | 
Development |  |  |  |  |  |  | 
Industrialization |  |  |  |  |  |  | 
Series production |  |  |  |  |  |  | 
Industry participation |  |  |  |  |  |  | 
Total |  |  |  |  |  |  | 
1980
1985
1990
1995
2000
2005
2010
~ 15 years
~ 25 years
Case: LHC superconducting dipole magnets

## Slide 22: Geological background
MOLASSE
(Grès, Marnes)
TERRAINS MEUBLES
(Moraine, Alluvions)
Karsts
CALCAIRE

## Slide 23
Progress on site investigations
Notes: Use the latest slides from John/Charlie.
100 km machines, possibly with both versions intersecting and non-intersecting?

## Slide 24
90 – 100 km fits geological situation well
LHC suitable as potential injector
The 100 km version, intersecting LHC, is now being studied in more detail
Progress on site investigations
Notes: Use the latest slides from John/Charlie.
100 km machines, possibly with both versions intersecting and non-intersecting?

## Slide 25: Tunnelling options for crossing the lake
Open Shield TBM
Slurry TBM
Immersed Tube Tunnel
Superficial
sediments
Moraine
Molasse

## Slide 26
CE schedule studies
4.5yrs
6.5yrs
Total construction duration 7 years
First sectors ready after 4.5 years

## Slide 27
FCC – tunnel integration in arcs
  FCC-ee FCC-hh
  5.5 m inner diameter

## Slide 28
parameter | FCC-hh |  | HE-LHC* | (HL) LHC
collision energy cms [TeV] | 100 |  | 27 | 14
dipole field [T] | 16 |  | 16 | 8.3
circumference [km] | 100 |  | 27 | 27
# IP | 2 main & 2 |  | 2 & 2 | 2 & 2
beam current [A] | 0.5 |  | 1.12 | (1.12) 0.58
bunch intensity [1011] | 1 | 1 (0.2) | 2.2 | (2.2) 1.15
bunch spacing [ns] | 25 | 25 (5) | 25 | 25
beta* [m] | 1.1 | 0.3 | 0.25 | (0.15) 0.55
luminosity/IP [1034 cm-2s-1] | 5 | 20 - 30 | >25 | (5) 1
events/bunch crossing | 170 | <1020 (204) | 850 | (135) 27
stored energy/beam [GJ] | 8.4 |  | 1.2 | (0.7) 0.36
synchrotron rad. [W/m/beam] | 30 |  | 3.6 | (0.35) 0.18
*tentative
Hadron collider parameters

## Slide 29
100 km FCC
Baseline:
3 TeV, directly from LHC, reusing the whole CERN complex
Alternative:
1.5 TeV with new SPS (7 km machine circumference) based on fast-cycling SC magnets, 6-7T, ~ 1T/s ramp
High energy and large size of the ring requires a pre-injector chain:
“gear-box” principle
FCC-hh injector considerations
LHC
SPS
Notes: See talk of Oliver on injection energy
Several options, present baseline is 3.3 GeV
Ínjection at 1.5 TeV studied as alternative, potentially compatible with SPS upgrade

## Slide 30
Physics prospects
Being published as CERN yellow report

## Slide 31
Key Technologies
16 T superconducting magnets
Synchrotron radiation
Affordable & reliable cryogenics
Superconducting RF cavities
RF power sources
Reliability & availability concepts

## Slide 32: High –field SC dipoles
SC dipole: field defined via current distribution
  High current densities close to the beam for high fields
  Only possible with super conductors I > 1 kA/mm2
Ideal coil geometry for dipolar fields:
  Azimuthal current distribution I(f) = I0cos(f) Dipol, (I0cos(2f) Quadrupol)
  2 horizontally displaced circles
I(f)
f
B
I(f)
Cross section

## Slide 33: Cryo-magnet cross sections
LHC FCC-hh
cos theta block coil
Nb3Sn as SC material
0.57 m
0.78 m

## Slide 34
Main SC Magnet system
FCC (16 T) vs LHC (8.3 T)
FCC
Bore diameter: 50 mm
Dipoles:
Quads:
LHC
Bore diameter: 56 mm
Dipoles:
Quads:

## Slide 35
Nb3Sn conductor program
Nb3Sn is one of the major cost & performance factors
Main development goals until 2020:
Jc increase (16T, 4.2K) > 1500 A/mm2 i.e. 50% increase wrt HL-LHC wire
Reference wire diameter 1 mm
Potentials for large scale production and cost reduction
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
Impact on coil section and conductor mass
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 36
Cos-theta
Blocks
Common coils
Short model magnets (1.5 m lengths) from 2018 – 2022
Russian 16 T magnet program launched by BINP recently.
Swiss contribution
Canted
Cos-theta
INFN
CEA
CIEMAT
PSI
LBNL
FNAL
16 T dipole options
under consideration

## Slide 37
Towards 16T magnets
Magnets with bore
(need of margin)
Field records
LBNL HD1
CERN RMC
16 T “dipole” levels reached with small racetrack coils
Berkeley 2004, CERN 2015
Record fields for SC magnets in “dipole” configuration

## Slide 38
15 T dipole demonstrator (US-MDP)
All coil parts, structural components and tooling are available at FNAL
Coil fabrication and the work with mechanical structure are in progress
First magnet test in September 2018
Iron Laminations
AL I-Clamps
Fillers
Axial Rods
End Plates
StSt Skin

## Slide 39: Synchrotron radiation
Charged particles on a curved trajectory irradiate energy:
  DE ~ constg4/r = const(E/E0)4/r = konst(E/m0)4/r
  Energy loss DE must be compensated and corresponding heat has to be removed from cold mass of SC magnets (for hadron collider)
DW= DQ(T – Ttief) / Ttief = DQ(300 – 1.9) / 1.9 ~ 155DQ
  For realistic process efficiency is ~1000: 1 W@1.9 K == 1 kW @ room temp.

## Slide 40
Synchrotron radiation
beam screen prototype
Photon distribution
First FCC-hh beam screen prototype
Testing 2017 in ANKA within EuroCirCol
High synchrotron radiation load of proton beams @ 50 TeV:
~30 W/m/beam (@16 T) (LHC <0.2W/m)
5 MW total in arcs (@1.9 K!!!)
New Beam screen with ante-chamber
absorption of synchrotron radiation at 50 K to reduce cryogenic power
factor 50! reduction of power for cryo system

## Slide 41
Beam screen prototype test
FCC-hh beam-screen test set-up at ANKA/Germany:
beam tests since June 2017, for prototypes,
confirming vacuum design simulations
X-ray fan
2.5 GeV ANKA/KIT storage ring
ANKA e- photon spectrum
= FCC –hh spectrum

## Slide 42
contributions: beam screen (BS) & cold bore (BS heat radiation)
Cryo power for cooling of SR heat
Overall optimisation of cryo-power, vacuum and impedance
Termperature ranges: <20, 40K-60K, 100K-120K
100MW
200MW
300MW
Multi-bunch instability growth time: 25 turns 9 turns (DQ=0.5)

## Slide 43
Beam screen, 40-60 K (50 bar)
Magnet thermal shield 60 K (44 bar)
Support post
Temperature level | [W/m]
1.9 K, cold mass of magnets Beam losses Resistive heating of splices | 1.4
40-60 K, beam screen, thermal shield Synchrotron radiation Beam Image current | 71
Vacuum vessel
Bayonet heat exchanger, 1.85 K saturated
Cold mass, 1.9 K (1.3 bar)
10 cryoplants
20 MW electrical/plant
6 technical sites
Baseline
Cryoplants overall layout
Cryoplant | 40-60 K [kW] | 1.9 K [kW]
 | 592 | 11
 | 618 | 12
Total load
1 MW equivalent @4.5 K
Main cryogenics parameters and layout

## Slide 44
B=6 T, 12 m bore, solenoid with shielding coil and 2 dipoles 10 Tm.
Length 64 m, diam. 30 m, magnet 7000 tons, stored energy 50 GJ
Detector Concepts for 100 TeV pp
Very large volume of high magnetic field needed to measure momentum of charged particles.
Expanding from LHC detector concepts:
Notes: See with Werner about detector

## Slide 45
Detector Magnet Studies
Today’s baseline:
4T/10m bore 20m long Main Solenoid 4T Side Solenoids – all unshielded
14 GJ stored energy, 30 kA and 2200 tons system weight
Alternative challenging design:
4T/4m Ultra-thin, high-strength Main Solenoid allowing positioning inside the e-calorimeter,
280 MPa conductor (side solenoids not shown)
0.9 GJ stored energy, elegant, 25 t only,
but needs R&D!
Tracker
ECAL + HCAL
  Designs for physics-performing and cost-efficient magnet systems
Notes: See with Werner about detector

## Slide 46
MgB2 industrial conductor, He gas cooled
Example HL-LHC (Itot up to 150 kA @ 25 K)
All circuits in single cryostat – compact & efficient
SC links for circuit powering
2x20 kA @ 24 K
2x20 m long CERN cable
Notes: See with Werner about detector

## Slide 47
contributions: beam screen (BS) & cold bore (BS heat radiation)
Beam power & machine protection
Stored energy 8.4 GJ per beam
  Factor 25 higher than for LHC, equivalent to A380 (560 t) at nominal speed (850 km/h). Can melt 12t of copper.
  Collimation, control of beam losses and radiation effects (shielding) are of prime importance.
  Injection, beam transfer and beam dump all critical.
Damage of a beam with an energy of 2 MJ
Machine protection issues to be addressed early on!
Hydrodynamic tunneling:
beam penetrates ~300 m in Cu

## Slide 48
FCC-hh beam dilution system
1.4 km dump insertion
2.8 km collimation insertion
2.5 km dump line
Kicker
Septum
10 mrad bend
Dilution
Absorber
Fluka studies:
Bunch separation >1.8 mm
Branch separation: 4 cm
Keeps T<1500°C
2m
SC septum
Very reliable kickers, high segementation,
new methods for triggering (laser)
Huge energy to be extracted and dumped => need large dump section
Beam rigidity: 167 T.km => need long way to dilute beam ~2.5km!

## Slide 49
FCC Collaboration & Industry Relations

## Slide 50
Future Circular
Collider Study
Large scale technical infrastructures
Conceptual design study 2014 – 2018
Driven by international contributions
Establish long-term liaisons with industry
Collaborate on technology evolution (> 2025)
Notes: CERN