## Slide 1: S’Cool LAB group 1 Quadrupole Ion Trap & Beam Optics
Group Leaders: Lachlan, Fabian & Hector
1. Quadratic Ion Trap: Ayyaz, Thana, Susanna
2. Beam Optics: Bahareh, Kazuoki, Lidwina

## Slide 2
Equipments and Setup:
Quadrupole Ion Trap
Theory
Setup
Problems

## Slide 3: Theory of Quadruple ion trap •Observation of particle when isolated or without material walls Types of traps 1.Penning traps, developed by Dehmelt and Penning, use static electric and magnetic fields, 2.Paul traps, developed by Wolfgang Paul, are operated with alternating electric fields

## Slide 4: Difference between ion trap and group work 1. Uses spores instead of ions 2. Three poles are used instead of four

## Slide 6
Equipments and Setup:
Equipment and Setup:

## Slide 7: Materials:

## Slide 8: Other materials required to perform experiment:
Power Source/Transformer
Spores (Lycopodium Powder)
Perspex tube
Wooden Skewers –
Electric Paint
Notes: Power Source/Transformer – 2-3 kV power source of frequency 50 Hz using a standard variable 20 V AC power source and a transformer with voltage transformation ratio of 200 (coils with N1 = 50, N2 = 10000).
Perspex tube– The spores can be blown out of the trap by the airflow in the room or by breathing students, thus, placing a clear plastic barrier around the electrodes. It is possible to use a Perspex tube of diameter approximately 120 mm or a clear sheet of plastic (for example the slides used on overhead projectors).

## Slide 9: Building Instructions: 3D printing:
Base
Lid
LED Holder
Electrode Stand
Ring Electrode
Spherical Electrode
Notes: a) Base – approximate mass 110 g
b) Lid – approximate mass 55 g
c) LED holder – approximate mass 15 g
d) Electrode Stand – approximate mass 12 g
e) Ring Electrode – approximate mass 2 g
f) Spherical Electrode – approximate mass 2 g
g) Second Spherical Electrode (optional) – approximate mass 2 g
We recommend printing the spherical and ring electrodes in the highest possible resolution as these have small holes designed for screws.

## Slide 10: Building Instructions Cont’d
Notes: Conductive electric paint, two 4mm banana plug sockets, two 10 MΩ resistors, the 3D printed electrodes and two male to female leads.

## Slide 12: Operation Instructions
Safety Notes
Trapping Spores
Notes: Safety Notes
This experiment involves using a high voltage power source (at least Vrms=2000 V), teacher supervision is required, also it is recommended that teachers check the student’s circuit before they switch on their circuit.
Trapping Spores
Once the quadrupole trap is complete it can be used to trap lycopodium powder. The first step is to set up the high voltage power source that will be connected to the electrodes. An AC power source that is capable of reaching at least Vrms= 2000V AC. This can be done by connecting a 20V AC power source to a transformer with voltage transformation ratio of 1:200. See image below:

## Slide 13: Operation Instructions Cont’

## Slide 15
SOURCEheyitscaspian.tumblr.com

## Slide 16
Equipments and Setup:
Problems and Tipps:

## Slide 17: Painting
Have you ever painted with glue? We did.
TIP: Use a brush with stiff hair.

## Slide 18: Project Board
The dots on the outer side connect horizontally.
The dots in the middle connect vertically.
TIP: Stick the electric components deep into the board. Otherwise they are not connected properly.

## Slide 19: Don´t kill the LED!
9 Volt will kill the LED – always use the resistor!!
The short end of most electronic devices must be connected with the negative pole of the battery.
How can you remember this:
You want the negative experiences in life to last a short time!
Tip:

## Slide 20: Connect the capacitors and the diode correctly!
Capacitors:
Diode:
The black ring is the negative connection.

## Slide 21: Put the 2 transistors the right way!
These go to the positive pole.
This goes to the negative pole.

## Slide 22: Don´t mix up the resistors!
100Ω
8.2kΩ
10Ω
10kΩ
10Ω

## Slide 23: GOOD LUCK!!

## Slide 24
OPTICAL INTERFEROMETRY
Theory
Setup
Analogy
Notes: Optical Interferometry is a technique where 2 or more light waves are combined to produce an interference pattern, this interference can be measured to extract information of light.

## Slide 25
Notes: A Michelson Interferometer is a tool used to produce interference between 2 beams of light.
It is the most common design for optical interferometry and the first interferometer invented by Albert Abraham Michelson.

## Slide 26
Notes: The Michelson Morely experiment was for compared the speed of light in perpendicular directions, in an attempt to detect the relative motion of matter through the stationary luminiferous aether.
The result was negative and they found that there is no difference betwen the speed of light in this 2 directions.

## Slide 27
Notes: The Michelson interferometer works by splitting a beam of monochromatic light into 2 equal beams.
One beam hits

## Slide 28
https://www.youtube.com/watch?v=UA1qG7Fjc2A
Notes: There is a kind of laser light and hear is a beam splitter that takes half the light in reflex on way, while leading the other half pass.
Then we have 2 mirrors on either arm of the interferometer reflecting the light right back.
Depending on the difrent distance make destructive or constructive interfierence.

## Slide 30: Set up (Equipments)
Iron plate : 1
He-Ne laser source : 1
(λ= 632.8nm)
Iron stand : 1
Screen : 1
Mirrors* : 3
Lens* : 1
Beam splitter* : 1
(45% Reflection/45% Passing through)
Neodymium magnet : 5
* = Mount them on a stands
made with a 3D printers

## Slide 31: Set up

## Slide 32: Set up
Nd Magnet

## Slide 33: Set up (Alignment)

## Slide 34: Set up (Alignment)

## Slide 35: Set up (Alignment)
✖
✔

## Slide 36: Set up (Alignment)

## Slide 37: Set up

## Slide 38: Analogy
Optical Interferometry = LHC
Red Laser (photon) = Proton
Mirrors = Dipoles
Lenses = Quadrapoles
Screen = Detector
Interference = Collision

## Slide 39: Difficulties
To make sure that all beams are
in a line (need time)
The interference effect might
hard to produce or not to clear
to see

## Slide 40: Limitations
Great amount of time (preparation and execution)
Big size class is not recommended
Need teacher’s supervision

## Slide 41: Recommendation
It might be done at school, but...
Teachers should do some preparations of the experiments before handing it out to students (for example, set up the magnets and the holders).
For the base plate, it is better to use the grid one.
Make it clear to students that LHC is a complicated tool, thus what they get here is a simple analogy.

## Slide 42: Thank you :)