## Slide 1: ECR for wire installation in IR1
TCC 13 July 2017
A. Rossi on behalf of the whole team

## Slide 2: Motivation
Wire-in-jaw collimators for LRBB compensation
  First stage installation in IR5 during EYETS 2016-17
  First demonstration test 1 July 2017 (see G. Sterbini’s talk)
  Now complete the compensation scheme with installation in IR1 during YETS 2017-18

## Slide 3
Vacuum tank
Jaws
Tungsten inserts
(Inermet® IT180)
Cooling pipes CuNi10
Glidcop Al-15 housing and back stiffener
L. Gentini – CERN (EN-MME)
BBLRC wire
Glidcop “T” support
Design:
Thin wire (ØCU≤ 2.5 mm)
In-jaw wire (depth ≤ 3 mm with positioning accuracy of ~0.1mm)
High DC current (up to 350 A)
Maintain TCTP complete functionality!
O. Aberle EN-STI
Recall of design of wire in-jaw collimator
L= 1000 mm
3mm

## Slide 4: LHC – optics RunII 2017 – collision round 40cm
Optimal wire position for LHC at beta ratio β𝒙/β𝒚~1.8 (or 1/1.8) [S. Fartoukh, 10.1103/PhysRevSTAB.18.121001]
ratio
beta (m)
distance from IP1/5 (m)
B2
-250 -200 -150 -100 -50 0 50 100 150 200 250
Vertical collimator require for compensation in Xing plane of IR1
TCL (outgoing beam) only horizontal, need of new slot loss in symmetry

## Slide 5: Replacement of TCTPV.4R1.B2
Installation requires replacement of the existing vertical collimator
Wire connections (junction box to 400mm2 cables + wire voltage)
TCL
TCTPH
TCTPV.4R1.B2
TAN
D1

## Slide 6: 5L1 with new vertical collimator
Q4
E. Page
- 176.17 m

## Slide 7: 5L1 with new vertical collimator
The installation requires :
1 new vertical collimator including 2 pick-ups (+ cabling and rack space), already built and tested.
2 new NEG cambers VCDAN and VCD__ to be fabricated.
1 new VAMTB (= 1 new ion pump + cabling and rack space) – spare available, to be replaced
1 new bellow module VMTBA allowing for the 5th axis movement – spare available, to be replaced.
Necessary supports.
1 new BLM (cabling and rack space), to be confirmed
New water cooling tapping.

## Slide 8: Thank you

## Slide 9: LHC – optics RunII 2016 – collision round 40cm
Chart: 
ratio
beta (m)
distance from IP1/5 (m)
B2
Optimal wire position for LHC at beta ratio β𝒙/β𝒚~1.8 (or 1/1.8) [S. Fartoukh, 10.1103/PhysRevSTAB.18.121001]