## Slide 1
“The neutrino mass experiment KATRIN”
- Florian Fränkle -

## Slide 2: Outline
Neutrino masses and single b-decay
The KATRIN experiment
Commissioning measurements
Summary & outlook

## Slide 3: Neutrino masses
Neutrino flavour eigenstates are related to neutrino mass eigenstates by the lepton mixing matrix (PMNS)
Neutrino oscillations are sensitive to the differences between the squares of neutrino masses
Two mass ordering scenarios possible
The value of the lightest neutrino mass is unknown
ne
nm
nt
m1
m2
m3
Ue1
Um1
Ut1
Ue2
Um2
Ut2
Ue3
Um3
Ut3
=
normal
inverted
m3
2
2
m2
2
m1
2
m2
2
m1
m3
2
2
m
?
2
Dmatm.
ne
nm
nt
2
Dmsol.
?
2
Dmsol.
2
Dmatm.
0
mass ordering

## Slide 4: Neutrino masses
Neutrinos are massive particles, but so far there are only upper and lower limits
Absolute neutrino mass scale is one of the big open questions in particle physics, astrophysics and cosmology
Different approaches to determine neutrino mass:
direct measurements
0nbb decay
cosmology
neutrino mass

## Slide 5: Neutrino mass and single b-decay
Fermi theory of b-decay:
b-spectrum for tritium (E0 = 18.6 keV, T1/2 = 12.3 y):
b-decay: n → p + e- + ne
Neutrino mass influences energy spectrum of b-decay electrons
Neutrino mass determination via precise measurement of the spectral shape close to the endpoint
Model independent method

## Slide 7: The KATRIN experiment
KArlsruhe TRItium Neutrino experiment
Goal: Measure neutrino mass with a sensitivity of 0.2 eV/c² (90% C.L.)
Windowless Gaseous
Tritium Source
Differential and
Cryogenic Pumping sections
Pre-Spectro-meter
Main Spectrometer
Detector
tritium b-decay
decay rate: 1011 1/s
T2 pressure: 10-3 to 10-6 mbar
b-electron transport
tritium retention (factor > 1014)
energy analysis of b-electrons
resolution 0.93 eV @ 18.6 keV
pressure < 10-10 mbar
counting of transmitted b-electrons
~ 70 m

## Slide 8: KATRIN measurement
KATRIN will measure the integrated b-spectrum close to the T2 endpoint E0
The influence of mn is most pronounced a few eV below E0
Optimized measurement time distribution to increase sensitivity

## Slide 9: Gaseous Tritium Source
Stability of T2 density profile of 10-3 (function of T2 injection rate, purity, beamtube temperature stability and homogeneity, pump rate)
Complex cryostat, 16 m length, 27 t weight, > 800 sensors and valves
High isotopic purity (> 95%)
Tritium loop processes 40 g T2 / day (same scale as ITER)
September 10th, 2015
Purpose: delivery of 1011 β-decay electrons per second
WGTS

## Slide 10: Gaseous Tritium Source
Successful commissioning of magnet system at maximum field (3.6 T)
Test of two phase beam tube cooling system: temperature stability exceeds requirements by one order of magnitude!
specification: ± 30 mK/h
preliminary
WGTS

## Slide 11: Differential pumping section
Purpose: reduce T2 flux (105) and magnetically guide b-decay electrons
Differential pumping of T2 by turbomolecular pumps (TMPs)
Electric dipole electrodes for removal of positive ions
Magnet system and beamline successfully tested
DPS

## Slide 12: Cryogenic pumping section
Purpose: reduce T2 flux (107) and magnetically guide b-decay electrons
Cryosorption of T2 on argon frost layer
Beam tube successfully cooled to 3K, simulations predict T2 reduction of < 109
CPS instrumented with 83mKr calibration source and b-activity monitor
Status: gas flow reduction measurements with deuterium and cold system ongoing, first preparation of argon frost layer end of November
condensed crypton source
forward beam monitor
simulated temperature profile
CPS

## Slide 13: Main spectrometer
Purpose: energy analysis of b-decay electrons (DE = 0.93 eV @ 18.6 keV)
Spectrometer mass 200 t, volume 1240 m³, inner surface 689.6 m²
Pressure ~ 10-11 mbar
Inner wire electrode system for fine-tuning of retarding potential
Stable HV system (1 ppm @ -18.6 kV), variable voltage to scan E0 region
MS

## Slide 14: Focal plane detector
pinch magnet 6 T
detector magnet 3.6 – 6 T
90 mm
Purpose: counting transmitted b-decay electrons
Segmented monolithic silicon PIN diode, 148 pixels (44 mm² each)
Energy resolution 1.4 keV (FWHM), dead layer ~ 100 nm
Post acceleration of electrons up to +10 kV
Muon veto and passive shield (Pb, Cu), background 1.2 mcps / keV
FPD

## Slide 15: MAC-E filter
Magnetic Adiabatic Collimation combined with an Electrostatic Filter
Technique used by Mainz and Troitsk neutrino mass experiments
energy
Q = 0°
1
0
qU0
transmission
energy resolution:
Q = 15°
1
0
qU0
Q = 0 .. 90°
1
0
qU0
qU0+DE
magnetic moment:
B
pe
q

## Slide 16: KATRIN – Spectrometer & Detector Section (SDS)
Several SDS commissioning measurement phases since autumn 2013
Main spectrometer successfully operated up to -33 kV
Successful operation of heating / cooling system (baking @ 200 °C)
Transmission characteristics of main spectrometer as expected
Detailed investigations of spectrometer backgrounds
Angular selective
electron source
detector
Main spectrometer
0
-4
-3
-2
-1
0
1
surplus energy / eV
1
normalized rate

## Slide 17: KATRIN backgrounds
e
baffle
µ
H2
e
e
40K, … external radioactivity
210Pb, …
e
a
g
BBR
internal radioactivity
UV
FPD
H+
NR
field emission
Penning discharge
insulator processes
219Rn
cosmic muons
g
Different processes can contribute to the spectrometer background
Several measurement phases were performed to investigate the background processes in detail
vessel
wire electrodes
e
e
H
H*
H-
210Pb ~ 1 kBq

## Slide 18: KATRIN backgrounds
e
baffle
µ
H2
e
e
40K, … external radioactivity
210Pb, …
e
a
g
BBR
internal radioactivity
UV
FPD
H+
NR
field emission
Penning discharge
insulator processes
219Rn
cosmic muons
g
✓
All previously known background processes are efficiently suppressed
Background rate about 50 times larger than design value (10 mcps), presumably due to ionization of Rydberg atoms by black body radiation
KATRIN sensitivity limited by backgrounds
vessel
wire electrodes
e
e
H
H*
H-
210Pb ~ 1 kBq

## Slide 19: KATRIN background & sensitivity
KATRIN sensitivity limited by backgrounds
TDR 2004 optimized for 10 mcps
558 mcps non-optimized
~240 meV
ΔE ~ 2.5 eV

## Slide 20: KATRIN backgrounds – Rydberg model test
Attach 228Th source to main spectrometer
“Contaminate” inner surface with 212Pb
Close valve to 228Th source and check for exponentially decaying background rate
220Rn
T1/2 = 56s
a, 6.4 MeV
T1/2 = 1h
212Bi
b-, 2.3 MeV (64%)
T1/2 = 0.3µs
212Po
a, 9.0 MeV
212Pb
b-, 331 keV
T1/2 = 10.6h
T1/2 = 183s
208Tl
b, 5.0 MeV
228Th
T1/2 = 1.9yr
a, 5.5 MeV
a, 6.2 MeV (36%)
208Pb
stable
228Th
21.3 kBq
220Rn
216Po
212Pb

## Slide 21: KATRIN backgrounds – Rydberg model test
Observed half-life matches 212Pb literature value of 10.64 ± 0.01 very well
Assuming similar processes, 210Pb contamination < 5.1 kBq
background reference
0.6 cps

## Slide 22: KATRIN backgrounds – Penning trap
-18.3 kV
GND
-18.6 kV
PS2
Penning trap between spectrometers, strong Penning discharge observed before baking of spectrometers
At low pressure after baking no indication of Penning discharge
preliminary

## Slide 23: October 14th, 2016 – KATRIN first light
Experiment to Weigh 'Ghost Particles' Starts in Germany
Neutrinos kommen auf die Waage
Experimente zum Wiegen von Neutrinos starten in Karlsruhe
KATRIN celebrates first beam
The KATRIN Tritium Neutrino experiment: A giant scale for the tiniest of particles
Experiment starts to find weight of 'ghost particles'
Forscher geben Startschuss zum Wiegen von Geisterteilchen
Neutrino Mass: Germany’s KATRIN Experiment Aims To Weigh The Universe’s Lightest Particle
Neutrinos auf der Waage

## Slide 24: KATRIN first light – alignment
KATRIN beamline is aligned and in good agreement with simulations
Unobstructed transport of 191 Tcm² flux tube from source to detector
rear wall electron beam
pencil electron beam
pencil electron beam from ion source
rear wall electron beam
90 mm
5 mm
detector
electron sources
61 087 mm

## Slide 25: KATRIN first light – ion blocking
Achieved ion suppression of > 102 with one blocking electrode (preliminary)
ELIOTT ion source
dipole electrodes
blocking electrodes
MS used as ion detector
BE PP5 | rate / cps
Off | 140 ± 2
On (375 V) | 0.9 ± 0.2
Tritium source produces an order of magnitude more positive ions than b-electrons
ELIOTT ion source produces positive deuterium ions
tritium: ~ 1012 ions/s, ~ 10 kBq/s
107 ions/s
preliminary

## Slide 26: 83mKr decay
83Rb
T1/2 86.2 d
83mKr
T1/2 1.8 h
41.6 keV
9.4 keV
stable
IC, g
IC, g
EC
83mKr has well known lines from conversion electrons, for example K-32 (17.824 keV), L3-32 (30.472 keV)

## Slide 27: KATRIN krypton commissioning measurements
Production of 83Rb at NPI cyclotron (51 MBq/h) using natural Kr gas target irradiated with protons, 83Rb deposited in zeolite beads
Injection of 83mKr into the KATRIN source beamtube, no carrier gas
Measurement phase: July 3rd, 2017 – July 19th, 2017
detector
condensed 83mKr source
“spot-like” source, can be scanned across flux tube
83Rb emanator ~ 1 MBq
monitor spectrometer beamline
implanted 83mKr source
83Rb activity ~ 2.5 MBq
gaseous 83mKr source
Kr decays inside WGTS beamtube
83Rb emanator ~ 1 GBq
83Rb emanator

## Slide 28: KATRIN krypton commissioning measurements
Measurement of the L3-32 conversion electron line
The spectrometer retarding voltage is stepped in small increments (0.5V) to less negative values

## Slide 29: KATRIN krypton commissioning measurements
example run (one of many line scans)
only events on detector ring 0 (30x more statistics available)
preliminary
L3-32 line gaseous source
preliminary
stability gaseous source
repeated scans of L3-32 line
line position stability well within KATRIN goal of ± 60 meV

## Slide 30: HV divider calibration
Measure retarding potential of -18.6 kV directly with precision voltmeter and precision HV divider.
Use difference of L3-32 and K-32 lines with gaseous 83mKr source for absolute calibration, systematic effects due to DF and g energies cancel out
2013 (PTB)
M = 1972.4531 (20)
2017 (83mKr)
M = 1972.453 (10)
preliminary
preliminary
L3-32
K-32

## Slide 31: KATRIN status & outlook
Elevated background limits KATRIN sensitivity to about 0.24 eV/c² but further background reduction measures being studied
Successful commissioning measurements with 83mKr , data analysis ongoing
Prepare KATRIN for tritium operation
Start of neutrino mass measurements in 2018
Official KATRIN inauguration on June 11th, 2018

## Slide 32: KATRIN collaboration
October 2017

## Slide 33: xxx
Backup

## Slide 34: HV divider calibration
  Calibration of HV dividers K35 & K65 with nuclear standard: → monoenergetic conversion electrons
  Monitor individual line position over measurement period of two months
  Use relative position of different lines to verify absolute calibration of HV dividers
  K-32 line
  E(ce) = 17824.23(50) eV
  Ebinding(ce) = 14327.26(4) eV
  Erecoil(ce) = 0.120 eV
  L3-32 line
  E(ce) = 30472.19(50) eV
  Ebinding(ce) = 1679.21(3) eV
  Erecoil(ce) = 0.207 eV
Recoil energies
Energy of
transition
Binding energy
Energy of electrons:
Transmission condition:
Work function difference source - spectrometer
Potential decrease in analyzing plane (≈2V)
⇒
Within uncertainties good agreement with PTB calibration in 2013!

## Slide 35: Radon induced background
219Rn emanates from NEG material in the pump ports
Electrons released in the Rn decay are magnetically trapped and create additional electrons via subsequent ionization of residual gas molecules
These electrons resemble the motion pattern of the trapped primary electron and create ring-shaped distributions at the detector
clustered events
“single” events
simulation
measurement

## Slide 36: Radon background suppression
Radon analysis robust with respect to multiplicity cut
Radon is a major background source (about 50% of total background)
Radon activity suppression efficiency of three cold baffles is %
T6.6 J. Wolf

## Slide 37: Cosmic muon induced background
Muon flux through main spectrometer surface about 105 1/s
Special magnetic field to guide electrons from vessel wall to detector
Only a fraction of 14.4 ± 0.7 % of secondary electrons are due to muons (correlation coefficient 0.72 ± 0.06)
correlation plot

## Slide 38: Rydberg atoms – selective field ionization
Spectrometer baking improved background, but same behavior after baking
Rydberg atoms are ionized by the electric field between vessel and electrodes and hence can not reach the inner spectrometer volume
before baking
after baking
vessel
inner electrodes
electric field

## Slide 39: Rydberg atoms – BBR ionization
Spectrometer temperature was increased from 19°C to 43°C
Linear increase expected for large n
Most of background could be due to Rydberg atoms
G.W. Lehman, “Rate of ionisation of H and Na Rydberg atoms by black-body radiation”, J. Phys. B, 1983
slope (average): 0.79 ± 0.12
correlation factor: 0.6

## Slide 40: 210Pb activity on inner spectrometer surface
Characteristic 210Pb peak(s) in energy spectrum
Measurements indicate a 210Pb activity on order of kBq on inner spectrometer surface
210Pb
b-, 17 keV (84%)
b-, 64 keV (16%)
222Rn
T1/2 = 3.8d
a, 5.6 MeV
T1/2 = 5d
210Bi
b-, 1.2 MeV
T1/2 = 138d
210Po
a, 5.4 MeV
T1/2 = 22.2yr
210Pb CE L
30.1 keV, 58 %
210Pb CE M
42.5 keV, 14 %

## Slide 41: xxx