## Slide 1
Removal of distance margin for ATLAS-AFP
MPP/ CWG 24-07-2017
Sune Jakobsen (EP-UAT) on behalf of ATLAS-AFP
With input from:
Christina Yin Vallgren (TE-VSC)
Mario Deile (EP-CMT)
Benoit Salvant (BE-ABP)
Tatiana Medvedeva (BE-BI)
Barbara Holzer (BE-BI)
Markus Albert (BE-OP)
Giulia Papotti (BE-RF)

## Slide 2
Introduction
Sune Jakobsen
Removal of distance margin for ATLAS-AFP MPP/ CWG 24-07-2017
2/9
Extra margin for new system for startup phase: TCT + 3 σnominal + 0.3 mm + 0.5 mm = 12 σnominal + 0.8 mm
General agreed settings for horizontal Roman Pots in 2017:
General Roman Pot setting: TCT + 3 σnominal + 0.3 mm = 12 σnominal + 0.3 mm
Settings for AFP in startup phase:
Minimum 1.5 mm (not relevant for AFP).
Ultimate settings for AFP:
ATLAS-AFP requests to move to the ultimate settings after MD2/vdM.
Introduction Operational experience Temperatures Primary vacuum Slow losses Fast losses UFOs Conclusion
Notes: 2

## Slide 3
Operational experience
Sune Jakobsen
Removal of distance margin for ATLAS-AFP MPP/ CWG 24-07-2017
No beam dumps coursed by AFP interlocks.
3/9
No problems with the sequences used to move in/out AFP (after the “Update absolute position” was made none-parallel).
ATLAS-AFP has not experience any problems with insertions:
No unexpected extractions of Roman Pots.
First fill at intensity step: Not inserted.
Second fill at intensity step: Inserted after 2 hours of Stable Beam.
ATLAS-AFP has been inserted in all allowed fills following the philosophy:
Third fill at intensity step and onwards: Inserted directly after Stable Beam.
Introduction Operational experience Temperatures Primary vacuum Slow losses Fast losses UFOs Conclusion
Notes: 3

## Slide 4
Operational experience – Temperature of the Roman Pots
Sune Jakobsen
Removal of distance margin for ATLAS-AFP MPP/ CWG 24-07-2017
Maximum temperature observed on a Roman Pot is 42 °C (Roman Pots are baked-out at ~200 °C).
By moving the Roman Pot closer to the beam additional heating is expected (+ ~30 %), but the temperatures of the Roman Pots are not worrying (however the detector cooling might need to be revisited => not a LHC safety concern).
4/9
Even for the most pessimistic estimate of thermal expansion (~2 µm/°C) the distance from beam changes less than 1 σnominal for any realistic temperature increase.
Clear correlation between number of bunches and temperature increase of the AFP Roman Pots.
The heating is significantly more pronounced for the B-stations, which has Roman Pots closer to the beam.
B-stations
A-stations
Number of bunches
Temperature [°C]
Introduction Operational experience Temperatures Primary vacuum Slow losses Fast losses UFOs Conclusion
Notes: 4

## Slide 5
Operational experience – Primary vacuum
Sune Jakobsen
Removal of distance margin for ATLAS-AFP MPP/ CWG 24-07-2017
Some indication of heating on the vacuum pressures.
When moving OUT the AFP Roman Pots on the RIGHT side, larger/longer vacuum spikes are observed.
5/9
Minor (~1E-9 mbar) spikes systematically observed when moving the TCLs or AFP Roman Pots.
Overview of intensity ramp up
Vacuum behavior very reproducible from fill to fill.
TCL6s
Indication of heating
One fill
Extraction of AFP Roman Pots and TCL6
Insertion of AFP Roman Pots and TCL6
Roman Pots
Minor spikes
Minor spikes
Roman Pots
TCL6s
Only on RIGHT side
The spikes are observed both with and without beam, which could indicate it comes from friction.
Vacuum layout in backup slides
Introduction Operational experience Temperatures Primary vacuum Slow losses Fast losses UFOs Conclusion
Notes: 5

## Slide 6
Operational experience – slow losses (RS9)
Sune Jakobsen
Removal of distance margin for ATLAS-AFP MPP/ CWG 24-07-2017
BLM threshold (RS09) XRP ~0.007 Gy/s, TCL6 ~0.004 Gy/s, so all losses below 10 % of threshold.
6/9
Movement of TCL6 and AFP Roman Pots clearly visible.
Overview of intensity ramp up
TCL6s
One fill
Extraction of AFP Roman Pots and TCL6
Insertion of AFP Roman Pots and TCL6
Slope of losses when moving Roman Pot
Roman Pots
TCL6s
Slope losses vs Roman Pot position not alarming.
Roman Pots
Analysis repeated for BLM threshold RS12 the results confirmed.
Introduction Operational experience Temperatures Primary vacuum Slow losses Fast losses UFOs Conclusion
Notes: 6

## Slide 7
Operational experience – fast losses (RS2)
Sune Jakobsen
Removal of distance margin for ATLAS-AFP MPP/ CWG 24-07-2017
BLM threshold (RS02) XRP ~7.7 Gy/s, TCL6 ~23.2 Gy/s, so all losses below 1 % of threshold.
7/9
No particular spikes when moving the Roman Pots or TCL6.
Overview of intensity ramp up
TCL6s
One fill
Extraction of AFP Roman Pots and TCL6
Insertion of AFP Roman Pots and TCL6
Roman Pots
TCL6s
Roman Pots
Introduction Operational experience Temperatures Primary vacuum Slow losses Fast losses UFOs Conclusion
Notes: 7

## Slide 8
Operational experience – UFOs
Sune Jakobsen
Removal of distance margin for ATLAS-AFP MPP/ CWG 24-07-2017
UFOs observed at AFP (until 15/7):
8/9
Analysis curtesy of Giulia Papotti and Markus Albert.
Conclusions:
The number of UFOs are not outstanding nor alarming.
Most UFOs are 2-3 % of BLM dump threshold.
No UFO at AFP reached 25 % of BLM dump threshold.
B1: 7 UFOs
B2: 37 UFOs
Introduction Operational experience Temperatures Primary vacuum Slow losses Fast losses UFOs Conclusion
Notes: 8

## Slide 9
Conclusion
Sune Jakobsen
Removal of distance margin for ATLAS-AFP MPP/ CWG 24-07-2017
9/9
Slow losses
Various check made:
Temperature of Roman Pots
Settings for AFP in startup phase:
Primary vacuum (friction observed when moving OUT)
Ultimate settings for AFP:
ATLAS-AFP therefore requests to move to the ultimate settings after MD2/vdM.
Fast losses
No alarming point discovered.
All loss maps performed with ultimate setting (no instabilities or problematic losses).
UFOs
Introduction Operational experience Temperatures Primary vacuum Slow losses Fast losses UFOs Conclusion
Notes: 9

## Slide 10
Sune Jakobsen
Removal of distance margin for ATLAS-AFP MPP/ CWG 24-07-2017
10/9
Backup
Introduction Operational experience Temperatures Primary vacuum Slow losses Fast losses UFOs Conclusion
Notes: 10

## Slide 11
Sune Jakobsen
Removal of distance margin for ATLAS-AFP MPP/ CWG 24-07-2017
11/9
VGPB.232.6L1R
VGPB.4.6L1.R
VGI.85.6L1.R
VGPB.4.6R1.B
VGPB.232.6R1.B
VGI.85.6R1.B
Vacuum layout – cutesy of Christina Yin Vallgren
Introduction Operational experience Temperatures Primary vacuum Slow losses Fast losses UFOs Conclusion
Notes: 11