## Slide 1
Luca D’Angelo
LBNF Cryostat, final design review
SURF, 21-22 August 2017
Structural Analysis of Reinforced Warm Membrane

## Slide 2: Table of Content
Who Am I and Where Have I Been?
Introduction
Reinforced membrane concepts
Baseline concept
Door concept
Membrane welds
Membrane brackets
Documents and References

## Slide 3: Who Am I and Where Have I Been?
Fellow at CERN working on LBNF from August 1, 2016.
Doctoral assistant and research associate at Swiss Federal School of Technology, in Lausanne, from February 2012 to July 2016. Aeronautical Engineer in GECI SkyAircraft (France) from March 2010 to January 2012. Research Assistant at DTU MEK (Denmark) from September 2008 to February 2010.
Expert in structural analysis, fatigue, risk and reliability assessment, probabilistic modelling and simulations. Reviewer for International Journal of Fatigue.
BSc and MSc in Aerospace Engineering. PhD in Civil and Environmental Engineering. Experience in teaching.
Notes: I have been recently appointed as FSF L2 Manager for N2 Cryo Systems and Cryo Fluids, positioned occupied by Barry Norris who deserves all the credit for what I am about to present.
I have started as lead cryostat engineer for the 35 ton prototype and I have then been his deputy for the past 3 years in the Cryogenics Systems, starting from LBNE and then LBNF.
I am currently stationed at CERN acting as liaison between CERN and Fermilab.
My experience is a little shorter than that of some of the people that preceded me, it includes … READ.
I am also a certified PMP.

## Slide 4
Introduction

## Slide 5: Introduction
Roles:
1) Ensure leak tightness
2) Hold the liquid pressure
3) Transfer loads to primary structure
Warm membrane

## Slide 6: Introduction
Roles:
1) Ensure leak tightness
2) Hold the liquid pressure
3) Transfer loads to primary structure
Warm membrane
Warm membrane has to be reinforced to take pressure-induced bending

## Slide 7
Reinforced membrane

## Slide 8: Solutions studied to increase bending stiffness
2)
3)
4)
1)
GRID
RIBS
BOLTED BEAMS
SANDWICH

## Slide 9: Solutions studied to increase bending stiffness
2)
3)
RIBS
BOLTED BEAMS

## Slide 10
Baseline concept

## Slide 11: Concept
HL1100M main column
Outer vessel floor
pitch = 400 mm
S460 ML
Unit Cell : 800 x 400mm
transversal ribs
longitudinal ribs
12mm warm membrane
FLA 150×12mm ribs
4mm fillet welds

## Slide 12: Displacement Analysis Stress Analysis
Nominal loads: gF=1.0
Design loads: gF=1.35 - 1.40
(SLS)
(ULS)
p0+rghmax
p0+rghmax

## Slide 13: Displacement Analysis
Membrane displacement in mm (amplification = 60 x)

## Slide 14: Stress analysis – reinforcing ribs
sVM [MPa] – longitudinal rib
sVM [MPa] – transversal rib

## Slide 15: Local stress analysis of welds – central transversal rib
sVM plot [MPa] – EP analysis
Equivalent plastic strain (<0.8%)
In the other ribs, the equivalent plastic strain is negligible

## Slide 16: Local stress analysis of welds – warm membrane
A
A
Section A-A
sVM plot [MPa] – EP analysis
Equivalent plastic strain
sVM plot [MPa]

## Slide 17: Verification of welds according to Eurocode 3
TW2
S460 ML
a=4mm
TW1
LW1
LW2
LW3
ID | FX [kN] | FY [kN] | FZ [kN] | SEq [MPa] | UF
LW1 | 32.2 | 0.4 | 6.2 | 281 | 65%
LW2 | 23.7 | 2.0 | 7.8 | 210 | 46%
LW3 | 1.1 | 0.2 | 3.2 | 37 | 9%
TW1 | 8.6 | 1.8 | 15.0 | 214 | 49%
TW2 | 16.1 | 24.3 | 66.8 | 419 | 97%
a

## Slide 18: Corners
Global model (shell)
Sub-model (solid membrane)
Total def. [mm] (ULS)
Total def. [mm] (ULS)
(amplification = 50 x)

## Slide 19: Corners
deformed shape (amplification = 20x)
sVM plot [MPa]
Stiffening effect of insulation is neglected (no pressure)

## Slide 20: Conclusions
Maximum displacement of warm membrane < 3 mm;
Ribs take bending moment by remaining in the elastic domain;
EP stress analysis of ribs shows that yield strength is reached very locally on some areas of welds (not through the thickness);
Max EP strain in central transversal weld < 0.8%
EP stress analysis of warm membrane shows that yield strength is reached in external layer at central transversal rib. Eq. pl strain = 0;
50 mm length welds with 4 mm throat allow to take design loads;
Stress level in membrane corner stay below yield strength.
(*) Detailed calculations are given in EDMS doc. N. 1831536

## Slide 21
Door concept

## Slide 22: Concept
Outer vessel floor
pitch = 550 mm
S460 ML
Unit Cell : 800 x 550 mm
Unit cell in the center of the floor: worst case loading scenario
HL1100M main column
12mm warm membrane
IPE 220, l=1540 mm
10 mm fin plate
2 M16 bolts, grade 8.8
(slotted holes)

## Slide 23: Displacement Analysis Stress Analysis
Nominal loads: gF=1.0
Design loads: gF=1.35 - 1.40
Displacement in mm
(amplification = 15 x)
sVM plot [MPa]
(SLS)
(ULS)

## Slide 24: Verification of bolted connection (FEA and Analytical)
FE model of connection is used
Bolts are verified according to Eurocode 3
Stress analysis of bolts and welds is also
performed

## Slide 25: Verification of bolted connection
design case
Envelope for drilling holes

## Slide 26: FE analysis of bolts and welds
Bolts (steel grade 8.8)
sVM plot [MPa]
Vertical weld (aw=5mm)
Horizontal weld (aw=5mm)

## Slide 27: Conclusions
Maximum displacement of warm membrane < 5 mm;
IPE beams take bending moment by remaining in the elastic domain;
Bolted connections passes the Eurocode 3 checks, with all Utilization Factors staying below 85%;
FE analysis of the bolts shows that maximum sVM stays below the yield strength;
5mm throat welds allow to transfer loads from the fin plate to the columns with a considerable safety margin.
(*) Detailed calculations are given in EDMS doc. N. 18315363

## Slide 28
Membrane welds

## Slide 29: Method
S
- Worst case scenario: all longitudinal forces are taken by the membrane
- Shell model of warm membrane
- Equivalent thickness is used
(max deform. = max deform. of the warm vessel)
- Internal forces at section -S are used for weld design
FEd=6.7 MN
FEd=9.2 MN
FEd=3.6 MN

## Slide 30: Welding options:
tm
a
Full penetration:
Partial penetration:
 | Fed [kN] | Fw,Rd [kN] | Fed Fw,Rd
Top | 3570 | 44151 | 8%
Wall | 9221 | 82368 | 11%
Bottom | 6745 | 44151 | 15%
 | Fed [kN] | lw [mm] | aw,min [mm]
Top | 3570 | 8362 | 1.7 (42%*)
Wall | 9221 | 15600 | 2.4 (60%*)
Bottom | 6745 | 8362 | 3.2 (80%*)
(*) for a throat section equal to 4mm

## Slide 31: Results
 | Fed [kN] | lw [mm] | aw,min [mm]
Top | 3570 | 8362 | 1.7
Wall | 9221 | 15600 | 2.4
Bottom | 6745 | 8362 | 3.2
Effect of misalignment:
Probabilistic study EDM N. 1828091
(Scenario 1)
(Scenario 2)
Effect of bending stress in the warm membrane
 | Fed [kN] | lw [mm] | aw,min [mm]
Top | 8587 | 8362 | 4.1
Wall | 18581 | 15600 | 4.8
Bottom | 11762 | 8362 | 5.6
Compatible

## Slide 32: Conclusions
Full penetration butt welds allow to take pressure-induced stresses in the warm membrane with very high safety margin;
Full penetration weld can be replaced by 4 mm throat partial penetration weld.

## Slide 33
Membrane clamps

## Slide 34: Concept
M8 clamping bolts
Y
X
Z
Used to put in contact the membrane with the beam
Clamping system is used during assembly phase to hold the warm membrane
M8 clamping bolt hold the weight of the warm membrane (and insulation)
Same concept of insulation studs: bolted welded on the warm membrane
tolerance bolt -z
tolerance bolt –xy

## Slide 35: Verification of clamping system on longitudinal wall
3 belts
4 M8 bolts x belt (nb=12)
10.9 steel grade
3 mm throat weld, S460 ML
wpanel=5.5 tons

## Slide 36: Verification of clamping system on the roof
3 mm throat weld, S460 ML
Warm membrane is clamped to main beams
12 M8 bolts
10.9 steel grade

## Slide 37: Conclusions
Clamping system with M8 bolts allows to hold longitudinal wall with high safety margin. The same applies to transversal wall;
Clamping system with M8 bolts allows to hold roof membrane with high safety margin;

## Slide 38: Documents and references
EDMS N. 1831536
EDMS N. 1815363
EDMS N. 1828091
EDMS N. 1832537
Eurocode 3, Part 1-1: General rules for buildings
Eurocode 3, Part 1-8: Design of joints