## Slide 1: Measurement of CLICpix2 Power Supply Bounces
Edinei Santin
CERN, July 27th 2017

## Slide 2: Measurement conditions
The VDD measurements were performed as follows:
  After normal power on and configuration sequence (all pixels unmasked), the command “acquire 1 1 filename 0” was called manually and the scope triggered to the rising edge of PWR_ACQ
  PWR_ACQ pulse duration is 100 µs and SHUTTER is 60 µs, starting 40 µs later and finishing simultaneously with PWR_ACQ
  After PWR_ACQ/SHUTTER sequence, the readout is performed
  The VDD’s were measured at PCB level (ac coupled)
Boards used:
  CaR board #3
  Chip board #2
  measurement points 

## Slide 3: VDD,DIG with pp_en_n = 0
PWR_ACQ

zoom in
500 µs
10 ms
There is a bounce of ~ 10 mV when PWQ_ACQ rises, which settles in ~ 25 µs
VDD (ac component)

## Slide 4: VDD,ANA with pp_en_n = 0 (1/..)
zoom in
500 µs
10 ms
There is a bounce of ~ 5 mV when PWQ_ACQ rises, which settles in ~ 25 µs

## Slide 5: VDD,ANA with pp_en_n = 0 (2/2)
zoom out
50 ms
10 ms
There is also a strange bounce pattern preceding PWR_ACQ. The pattern is roughly the same between acquisitions and it happens roughly at the same time wrt PWR_ACQ
It is not clear what causes these bounces, since chip should be quiet during that time

## Slide 6: VDD,DIG with pp_en_n = 1
zoom in
500 µs
10 ms
There is a bounce of ~ 10 mV when PWQ_ACQ rises, which settles in ~ 25 µs. Very similar to the case when pp_en_n = 0.

## Slide 7: VDD,ANA with pp_en_n = 1
zoom in
500 µs
10 ms
There is no bounce when PWQ_ACQ rises, since analog biasing is not switched off (i.e. pp_en_n = 1)
Strange pattern preceding PWR_ACQ is still present

## Slide 8: Conclusion
Despite the strange bounce pattern on VDD,ANA that happens before acquisitions, it doesn’t seem to exist a large VDD bounce that would deteriorate the chip performance