## Slide 1: Report from the CLIC main linac hardware baselining wg
C. Rossi on behalf of the MLHW baselining WG
CLIC WS 2018 – 25th January 2018
CLIC workshop 2018

## Slide 2
OUTLINE
The CLIC Implementation Studies
Main Linac Hardware WG
Key Aspects of Rebaselining
Plans for the Near Future

## Slide 3
The CLIC Implementation Studies
The CLIC Implementation WGs started to meet in September 2016 .
CLIC Design - lead by D. Schulte;
CLIC Main Linac Hardware Baselining - lead by H. Schmickler (C. Rossi as from January 2017);
CLIC Civil Engineering & Infrastructure and Siting - lead by J. Osborne;
CLIC Cost and Power - lead by S. Stapnes.
GOALS:
Focus the attention on the 380 GeV stage and consider all options;
Increase the exchange of information and synergies among the different study areas of CLIC;
Prepare the next update of the European Strategy document.

## Slide 4
CLIC Main Linac Hardware Baselining
Review the specification for the CLIC Module and its integration, by looking also at its environment and lifecycle.
CLIC Main Beam Module as described in the CLIC CDR (CERN-2012-007)

## Slide 5
CLIC Main Linac Hardware Baselining
Provide the required information to refine the study of its integration into the linac tunnel, for the definition of the infrastructure and evaluation of cost.
CLIC Accelerator tunnel as described in the CLIC CDR (CERN-2012-007)

## Slide 6
CLIC Main Linac Hardware Baselining
Mechanical tolerances and pre-alignment requirements reconsidered, also to the light of PACMAN’s achievements. See presentation at CLIC WS 2018 by H. Mainaud-Durand
Include considerations on the module life cycle in the design process, study the impact of the heat load to the infrastructure and operating conditions.
See presentation at CLIC WS 2018 by M. Aicheler
Beam dynamics optimized at 380 GeV for the two possible options: klystron and drive beam-based. See presentation at LCWS2017 by D. Schulte
With the increase of the klystron and modulator efficiencies, the interest for a low energy stage driven by klystrons is growing.
See presentations at CLIC WS 2018 from B. Weatherford and J. Neilson on 24/01
Indicative cost balance based on a semi-analytical model. Model update in progress. (Courtesy D. Schulte)

## Slide 7
CLIC Main Linac Hardware Baselining
New reference parameters for the RF Design based on optimization for beam dynamics and cost, provided for the two design options. CLIC Design - D. Schulte, November 2016.
With constant Luminosity = 1.5 1034 cm-2 s-1

## Slide 8
CLIC two beam accelerator at 380 GeV
DB option optimized for the 380 GeV stage (in Updated baseline for a staged Compact Linear Collider, CERN – 2016 – 004).
2 GHz RF system in PDR and DR

## Slide 9
380 GeV K-based module layout and tunnel integration
Preliminary klystron-based scheme for the 380 GeV stage. The tunnel integration is progressing. see presentation at CLIC WS 2018 by M. Stuart on 25/01.
Courtesy Y. Cuvet

## Slide 10
Module integration at 380 GeV
Tunnel integration for the DB (still CDR version) and K options, still preliminary.
see presentation at LCWS 2017 by M. Stuart
Courtesy M. Stuart

## Slide 11
Upgrade to 3 TeV
With the DB option the 380 GeV modules are moved to the low-energy end.
With the K option the 380 GeV modules will remain in the region before BDS, increasing the flexibility of operation.
Increased tunnel width in the klystron region.

## Slide 12
CLIC Main Linac Hardware Baselining
The CLIC CDR proposal at 3 TeV considers a mix of different Module layouts to adapt to the requirements of the Main Beam and Drive Beam lattices.
T0, T1 and T2 type are needed by the 380 GeV DB layout.
The CLIC Module length is about 2 m long.
Independent supports are required by the Main Beam quadrupoles to assure the required stabilization requested by the challenging beam dynamics.
Only T0 type is needed by the 380 GeV K layout.

## Slide 13
380 GeV Module Sequence - Klystron Option
Sectors of the Main Beam FODO lattice for one Linac
Areas of possible improvement
T0 Module is made of 8 x AS
Q1 is 0.4 m and Q2 is 0.65 m long
FODO Sector | T0 | Q1 | Q2 | Totals |  | AS with 28 cells
1 | 148 | 148 |  |  |  | sequence: 148 x T0Q1
2 | 276 | 138 |  |  |  | sequence: 138 x T0T0Q1
3 | 228 | 76 |  |  |  | sequence: 76 x T0T0T0Q1
4 | 300 |  | 100 |  |  | sequence: 100 x T0T0T0Q2
5 | 504 |  | 126 |  |  | sequence: 126 x T0T0T0T0Q2
Totals | 1456 | 362 | 226 |  |  | 
Quads | 0 | 362 | 226 | 588 |  | 362 x 0.4 + 226 x 0.65
AS | 11648 |  |  | 11648 |  | Module length 2.010 m

## Slide 14
380 GeV K-based module layout
Courtesy Y. Cuvet (CERN), R. Zennaro (PSI) and J. Shi (Tsinghua)
Key RF components are in the design or in the prototyping phase and we plan to test them soon.

## Slide 15
380 GeV Module Sequence – Drive Beam Option
Sectors of the Main Beam FODO lattice for one Linac
FODO Sector | T0 | T1 | T2 | Totals | AS | AS with 33 cells
1 |  | 120 |  | 120 | 720 | sequence: 120 x T1
2 | 150 | 150 |  | 300 | 2100 | sequence: 150 x T0T1
3 | 172 | 86 |  | 258 | 1892 | sequence: 86 x T0T0T1
4 | 124 |  | 62 | 186 | 1240 | sequence: 62 x T0T0T2
5 | 468 |  | 156 | 624 | 4368 | sequence: 156 x T0T0T0T2
Totals | 914 | 356 | 218 | 1488 |  | 
Quads | 0 | 356 | 218 | 574 |  | 356 x 0.43 + 218 x 1.1
AS | 7312 | 2136 | 872 | 10320 |  | Module length 2.343 m
T1 Module is made of 6 x AS, T2 is made of 4 x AS
Q1 is 0.43 m and Q2 is 1.1 m long

## Slide 16
380 GeV DB-based module layout
Courtesy J. Vainola
Considerable simplification work with respect to CDR

## Slide 17
CLIC alignment strategy
Mechanical pre-alignment
Active pre-alignment
Beam based Alignment & Beam based feedbacks
One to one
steering
Dispersion Free
Steering
Minimization of
AS offsets
Make the beam
pass through
Optimize the position of
BPM & quads by varying
the beam energy
Using wakefield
monitors &
girders actuators
Beam on
Beam off
Minimization of the emittance growth
~0.2 - 0.3 mm over 200 m
14 - 17 µm over 200 m
Adopt PACMAN approach to alignment, with adjustable supports.
See details in H. Mainaud Durand’s presentation at CLIC WS 2018 on 23/01.
Courtesy H. Mainaud Durand

## Slide 18
CLIC alignment strategy
Courtesy X. Meng
Drive Beam alignment
Main Beam alignment
Courtesy D. Schulte
Assembly
Pre-alignment
Transport

## Slide 19
CLIC alignment strategy
The 380 GeV beam energy has implications on the required tolerances with respect to 3 TeV. See details in D. Schulte’s presentation at LCWS2017
Courtesy D. Schulte from LCW2017
Most imperfection affect the beam less at 380GeV than at 3TeV
– Structure misalignment leads to 0.3 nm vs. 0.54 nm emittance growth
  • Could relax tolerance by 40%
– BPM misalignment leads to 4.4 times less emittance growth
– Quadrupole jitter leads to 6 times less emittance growth
We decide to maintain specifications
– Ready for energy upgrade
– Less risk or better performance in the first stage
– But review impact of specifications on technology choice/cost reduction
Also preparing ultimate parameter set
– Will take advantage of smaller emittance growth
– And more aggressive tuning

## Slide 20
CLIC Module alignment
Operation
Temperature sensitivity
Transients
Failure rate + maintenance
Ground movement
Human interaction
Courtesy A. Vamvakas
Epument
Mass <50kg
Deformation <1mm
Modal: >400Hz
only two points of support
Lot of space for access
A solution has been studied to keep the coupling between the two RF structures under control
The development of the RF-unit concept provides an interesting alternative

## Slide 21
Developments for the CLIC Module alignment
Assure adjustability of components after installation
Developing adjustable supports that can allow semi-automatic alignment techniques for rapid and very precise adjustment of the component position in the tunnel.
Courtesy J. Vainola

## Slide 22
RF Efficient Design
A. Grudiev and X. X. Huang 5/04/17
Structure | CLIC-G* | CLIC380 | Klystron (K)
frep [Hz] | 50 | 50 | 50
Efficiency: η [%] | 28.5 | 39.8 | 38.7
Rise time: tr [ns] | 22 | 13.1 | 20.3
Filling time: tf [ns] | 65.5 | 55.4 | 62.7
Efficient beam loading time: tb [ns] | 155.5 | 175.5 | 242
Pulse length: tp [ns] | 243 | 244 | 325
Pin [MW] | 62.3 | 59.7 | 41.7
Poutunloaded [MW] | 26.5 | 27.6 | 17.9
Poutloaded [MW] | 9.76 | 6.2 | 4.5
Pbeam [MW] | 27.747 | 33.035 | 21.673
Thermal dissipation [W]: <Pdissipatedunloaded>, <Pdissipatedloaded> | 434.970, 349.394 | 391.620, 289.526 | 386.750, 286.649
Mean power in the load [W]: <Ploadunloaded>, <Ploadloaded> | 321.975, 191.822 | 336.720, 148.935 | 290.875, 128.735
Mean power to the beam: <Pbeam> [W] | 215.729 | 289.879 | 262.241

## Slide 23
380 GeV K-based powering scheme
Example of RF Distribution as presented by I. Syratchev on 21/01/2017
I. Syratchev 21/01/17
8
8
42.5 x 4 = 170MW in 325ns out of BOC
60% RF transfer efficiency of BOC + waveguides
Multiplication factor BOC = 5
Power needed from klystron = 57MW in 1.625ms
Insertion losses have not been considered
Losses in WG = 0.1dB/m, ~ 60 to 100W/m
2 x 57
170MW
my numbers in red
Plug power ranging 20 – 25kW/modulator (without solenoids) for klystron efficiencies 70 – 60%.

## Slide 24
Efficiency is a key parameter
Search for maximum efficiency includes klystron solenoids and waveguides.
RECTANGULAR WAVEGUIDE
With a double-height waveguide, the attenuation is reduced by 40% and electric and magnetic fields are reduced by 30%. See presentation at CLIC WS 2018 by C. Serpico on 23/01
Design Parameters | 
Superconductor (T-operation) | MgB2 (@ 20 K)
Current | 50 A
Central field | 0.7 T
Stored energy | ~ 10 kJ
Cryo-cooler applied | 6.7 W @ 20 K, 13.5 W @ 80 K
AC Plug Power | ≤ 3 kW
With present Cu-based solenoid magnets, the ac-plug power is 20kW/klystron
(40kW/modulator)
See presentation at CLIC WS 2018 by A. Yamamoto on 24/01

## Slide 25
CLIC Module Power Dissipation
Power dissipation and temperature stabilization are critical. Limiting the heat transfer to air in the tunnel is a requirement. Development work is in progress to clarify the picture.
Component | unit | 380 GeV DB | 380 GeV K
MBQ | MW | 1.9 | 1.4
DBQ | MW | 1.1 | 0
MB Beam instrumentation | MW | 0.015 | 0.015
DB Beam instrumentation | MW | 0.077 | 0
MBQ stabilization | MW | 0.1 | 0.1
MB AS loaded | MW | 9 | 9.7
MB AS unloaded | MW | 15 | 15.8
DB RF structures | MW | 0.91 | 0
MB klystrons (klys. h = 70%) | MW | 0 | 18
MB klystron modulators | MW | 0 | 8
Dissipated in the klystron gallery

## Slide 26
CLIC Module Power Dissipation
Developed a strategy for the definition of the parameter space.
Courtesy E. Lam
tuning of coefficient for convection
Experiment
CFD
Temperatures at pre-selected points
Different variable fields for every fluid/ solid domain
Temperature field for solid & heat dissipation values
validation
external models for assumptions (e.g. tunnel wall)
Obtained Results
Approach
FEA Steady-State Thermal
Analytical M.
Temperature at specific points & heat dissipation values
E. Lam, CLIC Project meeting 08.12.2017

## Slide 27
CLIC Module Power Dissipation
Experimental data and heat flux modelizations have been used to evaluate the cooling needs and the heat load to air in the accelerator tunnel.
Courtesy E. Lam
Planned tests on AS in the Xbox Test Stand will contribute to the model benchmarking.

## Slide 28
CLIC Module Power Dissipation
Chart: Air convection + radiation
| 20 | 30 | 40
2.8 l/min/m | 339.9833 | 149.4253 | -43.0953
3.7 l/min/m | 306.2801 | 110.4585 | -87.3696
4.5 l/min/m | 283.8093 | 84.3634 | -117.1185
5.6 l/min/m | 263.278 | 60.435 | -144.4712
Chart: Total ∆T (flow-weighted average)
| 20 | 30 | 40
2.8 l/min/m | 14.4579 | 15.4523 | 16.4486
3.7 l/min/m | 11.2973 | 12.0878 | 12.8917
4.5 l/min/m | 9.2747 | 9.9313 | 10.6232
5.6 l/min/m | 7.4899 | 8.0259 | 8.6098
Higher flow lowers component T (but not below 27°C)
Higher flow lowers heat to air
Higher ambient T lowers heat to air
Zero emission point
Higher flow lowers ΔT of water!
Higher ambient T increases ΔT of water!
Cooling&Ventilation feedback needed
Courtesy M. Aicheler
Parameter range based on the model developed by the Module team, by considering 7.4kW dissipated / T0 DB Module. See presentation at CLIC WS 2018 by M. Aicheler

## Slide 29
CLIC Module Temperature stability requirements
Temperature stability within modules is essential to achieve the luminosity target.
Courtesy A. Grudiev
Synchronous phase: ϕ0 =30o
dV/V < 1%
Loaded case: dT < 0.55 K
Unloaded case: dT < 0.5 K
Synchronous phase: ϕ0 =12o
dV/V < 1%
Loaded case: dT < 1.3 K
Unloaded case: dT < 1.2 K
Transition states should be limited in amplitude and duration.
Acceptable voltage error AS-to-AS < ± 1%.

## Slide 30
Plans for the near future
Areas of possible improvement
Before the end of 2018:
A complete description of the 380 GeV stage will be provided, with emphasis on the klystron option.
A cost estimate will be provided for the 380 GeV stage, in the K and DB configurations, with update of the 3 TeV CDR cost.
Developing and building a K Module with its X-band test station capable of producing nominal field gradient and validate efficiency figures;
Prepare the TDR phase by:
Completing the design of a two-beam RF unit (1m Super Accelerating Structure + 2 PETS) with details of its realization and installation, including acceptance test and initial commissioning scheme;
After 2018 :
Launching industrialization studies and refining the cost and power estimates to the light of results achieved with device efficiencies.