## Slide 1: Z pole scan strategy and √s spread measurement
 | Z | W | H (ZH) | ttbar
beam energy [GeV] | 45.6 | 80 | 120 | 175-182.5
arc cell optics | 60/60 | 60/60 | 90/90 | 90/90
emittance hor/vert [nm]/[pm] | 0.27/1.0 | 0.84/1.7 | 0.63/1.3 | 1.4/2.8
b* horiz/vertical [m]/[mm] | 0.15/.8 | 0.2/1 | 0.3/1 | 1/1.6
SR energy loss / turn (GeV) | 0.036 | 0.34 | 1.72 | 9.21
total RF voltage [GV] | 0.10 | 0.75 | 2.0 | 8.8-10.3
energy acceptance [%] | ±1.3 | ±1.3 | ±1.7 | ±2.4-2.8
energy spread (SR / BS) [%] | 0.038 / 0.132 | 0.066 / 0.165 | 0.099 / 0.165 | 0.15 / 0.20
bunch length (SR / BS) [mm] | 3.5 / 12.1 | 3.0 / 7.5 | 3.15 / 5.3 | 2.75 / 3.80
bunch intensity [1011] | 1.7 | 2.3 | 1.8 | 3.2-3.35
no. of bunches / beam | 16640 | 1300 | 328 | 40-33
beam current [mA] | 1390 | 147 | 29 | 6.4-5.4
SR total power [MW] | 100 | 100 | 100 | 100
luminosity [1034 cm-2s-1] | 230 | 34 | 8.5 | 1.9-1.7
luminosity lifetime [min] | 70 | 24 | 18 | 25
allowable asymmetry [%] | 5 | 3 | 3 | 3

## Slide 2: Z pole scan strategy: # points ? Energies ?
At the Z pole, dEbeam/Ebeam ≃ 0.132% ⇒ dEbeam ≃ 60 MeV
Ebeam (GeV)
s (nb)
GZ
s0
mZ
Z → hadrons
No ISR
Measure Ebeam
Measure integrated luminosity

## Slide 3: Z pole scan strategy without energy spread
Three parameters to fit : mZ, GZ, and s0
  Need (at least) three centre-of-mass energies at and around the Z pole
    With a calibration of the beam energy to 50 keV (A. Blondel’s talk)
    With a relative precision on the absolute luminosity of 10-4 (M. Dam’s talk)
      And a point-to-point relative precision of 5×10-5
  Precision targets
    100 keV on mZ ; 100 keV on GZ; dominated by the above.
    Statistical precision is a few keV with the FCC-ee statistics
  Possible beam energies around half-integer spin tunes n = Ebeam / 0.4406486
n | 99.5 | 100.5 | 101.5 | 102.5 | 103.5
Ebeam | 43.85 | 44.29 | 44.72 | 45.16 | 45.61
√s | 87.69 | 88.57 | 89.43 | 90.31 | 91.21
n | 103.5 | 104.5 | 105.5 | 106.5 | 107.5
Ebeam | 45.61 | 46.04 | 46.49 | 46.92 | 47.36
√s | 91.21 | 92.07 | 92.97 | 93.83 | 94.71

## Slide 4: Z pole scan strategy without energy spread
Result of the 3-parameter fit to a Breit-Wigner
  With 100 ab-1 at the peak (√s = 91.21 GeV)
  With 30 ab-1 + 30 ab-1 at peak ± 1, peak ± 2, peak ± 3, peak ± 4 (in spin tune)
    Standard at LEP
      EWPO measurements would have been statistics limited with ±3 or ±4
    All these options meet the (100 kev, 100 keV) target at FCC-ee
      Need another criterion to decide
  Note: Results of the fit with Peak, Peak ± 2, Peak ± 4
    s(mZ) = 64 keV
    s(GZ) = 97 keV
Scan | ± 1 | ± 2 | ± 3 | ± 4 | (-4,+3) or (-3,+4)
s(mZ) [keV] | 84 | 85 | 91 | 99 | 95
s(GZ) [kev] | 313 | 153 | 116 | 100 | 107
At the expense of a loss of statistics for rare Z decays

## Slide 5: Z pole scan strategy without energy spread
Choice driven by sin2 qWeff and aQED (mZ) determination from AFB(mm)
aQED(mZ)
sin2qWeff
87.9 GeV
94.3 GeV
⨂
AFB(e+e- → m+m-)

## Slide 6: Z pole scan strategy without energy spread
Best energies for AFB
  91.2 GeV for the effective weak mixing angle
  87.9 GeV and 94.3 GeV for the electromagnetic coupling constant
Closest half-integer tunes
  n = 103.5 for the peak
    √s = 91.2 GeV
  n = 99.55 below the peak (Pk – 4)
    √s = 87.8 GeV
  n = 106.55 OR n = 107.5 above the peak (Pk + 3 or Pk + 4)
    √s = 93.9 GeV OR √s = 94.7 GeV (equidistant from 94.3 GeV)
      Favour Pk + 3 for the sake of statistics (rare decays)
Minimal scan strategy within four years and with two detectors
  100 ab-1 at the peak (√s = 91.2 GeV)
  30 ab-1 + 30 ab-1 at peak – 4 (√s = 87.8 GeV) and peak + 3 (√s = 93.9 GeV)
Note: more statistics is always welcome
(3 IPs instead of 2; 6 years instead of 4; 5 points instead of 3; etc.)

## Slide 7: Z lineshape with energy spread
Ds/s (%)
Eb (GeV)
⨂
⇒ Apparent increase of the Z width
GZ → [GZ2 + 8 dE2peak ]1/2
The Z lineshape is slightly modified
  With dE ~ 60 MeV for each beam, ds/s ~ -0.45% at the peak and +0.15% off peak
  If the energy spread dEpeak at the peak is known with an uncertainty s(dEpeak)
    s(GZ) ~ 12 MeV × s(dEpeak)/dEpeak
      1% uncertainty of dEpeak leads to > 120 keV uncertainty on GZ !
    Need to find a way to determine dEpeak to ~0.2%
      Relaxed to ~1% for s(dEoff-peak)/dEoff-peak

## Slide 8: Z lineshape with energy spread
Can mZ, GZ, and s0 and dE be fit altogether with a five-point scan ?
  IFF dE is constant in time, identical at all points, independent of the bunch …
    s(dE)/dE ~ 1%
    s(mZ) = 85 keV
    s(GZ) = 350 keV
  And we certainly do not want to assume that the energy spread
    Does not depend on time
    Does not depend on energy
    Does not depend on the bunch
    Does not depend on anything else
Better idea(s) required

## Slide 9: Note: AFBmm with energy spread
Convoluting AFB with a Gaussian has almost no effect at the peak
  The sampling of √s around √s- = 87.8 and √s+ = 93.9 GeV, however, is not uniform
    Has to weigh the asymmetry by the production cross section:
  Effect is to increase the effective √s- and decrease the effective √s+
    And therefore decrease the absolute value of the asymmetry in both points
Need to know the energy spread to better than 1% at √s±
  To limit the effect on aQED to < 10-5 (same as the effect from the √s knowledge)
    Similar constraint as for the Z lineshape
⇒ DaQED/aQED ~ 10-3
Stat: 3×10-5

## Slide 10: Make use of e+e- → m+m- events
How are the events modified with energy spread (in the c.o.m.) ?
  Generates a longitudinal boost in the centre-of-mass frame
e+ (Eb, Eb-dE+)
e- (Eb, Eb+dE-)
m-
m+
Dq = p
Dq < p
No energy spread
With energy spread
In the e+e- centre-of-mass frame

## Slide 11: Make use of e+e- → m+m- events
Competes with initial state radiation (that you cannot get rid of)
  Need to have good ISR prediction
e+ (Eb, Eb-dE)
e- (Eb, Eb)
m-
m+
Dq = p
Dq < p
No ISR
With ISR
g (dE)
In the e+e- centre-of-mass frame

## Slide 12: Make use of e+e- → m+m- events
Also competes with muon angular resolution …
  Need to have good ISR prediction
  Need to master muon angular resolution
    Over the whole tracker accpetance
e+ (Eb, Eb)
e- (Eb, Eb)
m-
m+
Dqideal = p
Dqmeas < p
Perfect resolution
Finite resolution
In the e+e- centre-of-mass frame

## Slide 13: The FCC-ee frame is not the e+e- c.o.m frame
An e+e- → m+m- event produced at q=p/2, with f=0 or f=p/2
  NB: there might also be a (small) asymmetry between the two beam energies
    Causes additional boost along z
e+
e-
m-
m+
x
y
z
m+
m-

## Slide 14: Total energy-momentum conservation
Assuming one photon emitted along one of the two beams
  Where E± are the measured energies of the m±
  Where a is the beam crossing angle (nominal : 30 mrad),
  Where the z axis is the bisector of the two beam axes,
  Where the two beam axes form the (x,z) plane,
  Where q± are measured with respect to the z axis in the FCC-ee frame,
  Where f± are measured with to the x axis in the plane transverse to the z axis,
  Where √s is the centre-of-mass energy of the collision

## Slide 15: Longitudinal boost xg = pz(g)/√s
Solve (E,p) conservation equations for xg
        With
  As a function of the muon angles only (usually better determined than momenta)
    Assume initially that a and the “natural” (x,y,z) axes are known perfectly
      z axis = bissector of the two beam axes
      (x,z) plane = plane that contains the two beam axes
      y = axis going upwards perpendicularly to that plane
    Assume that these axes match the local (detector) axes

## Slide 16: Distribution of xg
With 106 dimuon events (every 5 minutes at the Z pole)
  Returns the √s spectrum (with asymmetry) for perfect angular resolution and no ISR
    An angular resolution of 0.1 mrad seems adequately small (typical of CLD / IDEA)
    ISR slightly degrades the Gaussian core and add tails, needs to be unfolded
  Returns beam energy relative asymmetry with 10-6 precision
No BS: 0.038%
Nom. BS: 0.132%

## Slide 17: Effect of sq,f and ISR
Fit the core of the xg distribution with a Gaussian and compare to Espread
  With 106 dimuons
  With sq,f = 0 and no ISR
    ~0.1% relative precision
      BINGO !
  Effect of ISR is to increase the xg width by 10%
    Need to be known with a precision better than 1% for a per-mil precision on Espread
  Effect of sq,f = 0.1 mrad is to increase the xg width by 0.5% for nominal BS
    Need to be known with a precision of ~10% over the whole tracker acceptance
  Effect of sq,f = 1 mrad is devastating (similar to energy spread, difficult to control)
No BS
Nom. BS
No BS Nom. BS

## Slide 18: Control the angular resolution to 0.01 mrad ?
Q: How to measure the angular resolution to 10% or better
  For any value of q and f ?
A: Take a muon track in dimuon events
  Refit it with the odd hits, on the one hand, and with the even hits, on the other
    And compare the angles
  Need only 100 tracks in each (q , f) bin for a 10% precision
    106 dimuon events = 5 minutes at the Z pole = bins of 3×3 (mrad)2
  Expected to be stable in time
    Precision (or bin size) improves with dimuon statistics

## Slide 19: Summary (extract from the CDR)
A three-point scan of the Z resonance (87.8, 91.2, 93.9 GeV)
  Is adequate for the measurement of mZ, GZ, sin2qWeff and aQED with target precisions
    If the beam energy spread dE is known to a few per mil (for GZ and aQED)
Dimuon events offer a permanent monitoring of dE
  With adequate precision, every few minutes
    And with the same as those used to measure the EW observables

## Slide 20: Notes added
All these numbers are valid for nominal luminosities / energy spread
  For smaller energy spread, the precision requirement are quadratically less stringent
Example: 0.066% instead of 0.132% at the Z pole (still BS dominated)
  Precision required increases by a factor 4 to 0.8% instead of 0.2%
    Number of events needed decrease by a factor of 16 to 5×104 instead of 8×105.
  In the same time, the luminosity is reduced much less, by a factor 22/3 ~ 1.58
    If the E spread decrease is achieved by increasing the vertical b*
      Keeping beam currents and vertical emittance unchanged
  Therefore the time needed decreases to 25 seconds instead of 4 minutes
All times displayed in the table are absolute maxima
All these numbers were derived from the muon angles only
  Angular resolution must be better than 0.1 mrad, + measured to better than 0.01 mrad
    Angular biasses must be kept below 0.01 mrad too (absolute alignment)
  To be studied: (probably marginal) influence of muon momenta

## Slide 21: Beam crossing angle determination
With 106 dimuon events (every 5 minutes at the Z pole)
  Spread sensitive to anything happening in the transverse plane
    f resolution, pT of emitted photons, and (x,y,z) axes knowledge
No BS: 0.038%
Nom. BS: 0.132%
See also poster
“1000 recipes to use up dimuons”

## Slide 22: Detector alignment
Absolute angle determination is (usually) not an easy task
  Requires alignment of the local (detector) frame with the natural (FCC-ee) frame
    Z axis = solenoid axis vs bissector of the two beam axes
    (X,Z) plane = horizontal plane vs plane containing the two beam axes
Spread of a increases with anything happening in the transverse plane
  E.g., rotation around the Z axis changes both X and Y directions
    Similarly, rotation around the X (Y) axis changes Y (X) direction
Crossing angle (rad)

## Slide 23: Detector alignment
Minimize the spread of the a distribution to find the three Euler angles
  Note: a spread dominated by the f resolution (here 0.1 mrad)
    Precisions quadratically improves with the resolution in f (here 0.1 mrad)

## Slide 24: Detector alignment
Improve the angle corresponding to a rotation around the Y axis
  X and Z information get mixed by such a rotation
    Resuting in a strong (linear) correlation between xg and a:

## Slide 25: Detector alignment
Minimize the correlation between xg and a:
  Improves the precision on that crossing angle by a factor of five.
    Reach a precision of 0.1 mrad on a and of 10-7 on xg
    Variation of the xg spread already insignificant with 100 times less events

## Slide 26: Detector alignment
A finite crossing angle is the key
  A zero crossing angle cannot be determined with precision (sinf+=sinf-, sinq+ = sinq-)
    Spread is infinitely large even with a perfect detector alignment
    Leads to inaccurate absolute alignment
      With corresponding biases on the muon angles
  With a finite crossing angle, only events with sinf+ ~ sinf-~ 0 need to be rejected
    Cut |sinf±| > 0.2 was applied in all previous plots
Possible bonus (to be studied)
  Built-in energy asymmetry between electrons and positrons