## Slide 1
50 ns test and e-cloud considerations
G. Iadarola
with input from LHC and Injectors operation crews,
D. Amorim, G. Arduini, B. Bradu, X. Buffat, L. Carver, P. Chiggiato, C. Schwick, S Hancock, W. Hofle, V. Kain, E. Metral, A. Romano, L. Mether, D. Mirarchi,
G. Rumolo, B. Salvant , M. Solfaroli Camillocci, C. Yin Vallgren
LMC meeting, 26 Jul 2017

## Slide 2
Test with 50 ns beams:
  e-cloud observations
Electron cloud effects in dipole correctors
  Simulations
  Cell-by-cell observations
Update on coherent motion observations
  Considerations on Fast Beam-Ion Instability
Outline

## Slide 3
Test with 50 ns beams:
  e-cloud observations
Electron cloud effects in dipole correctors
  Simulations
  Cell-by-cell observations
Update on coherent motion observations
  Considerations on Fast Beam-Ion Instability
Outline

## Slide 4
25 ns
50 ns
A fill with 50 ns bunch spacing was performed on Saturday afternoon in order to probe the impact of the bunch spacing on losses and other observations in 16L2
We aimed at changing only the bunch spacing:
Used same filling pattern as for production physics fills, replacing each 25-ns train of 48 bunches with a 50-ns train of 24 bunches
1284 b/beam. Avg. bunch intensity at 6.5 TeV: 1.07e11 p/bunch
Used non-BCMS scheme in the PS  gave transverse emittances similar to BCMS 25 ns
No change in machine settings
The planned set of measurements was performed rather quickly, still the fill was kept 6.7 h in Stable Beams as beam from the injectors was not available for refill with 25 ns
Test fill with 50 ns

## Slide 5
25 ns
50 ns
Test fill with 50 ns
Electron cloud suppression with 50 ns confirmed by heat load measurements on the beams-screens
Consistent with expectations from impedance and synchrotron radiation
Large differences between sectors observed with 25 ns are not visible with 50 ns

## Slide 6
Electron cloud suppression with 50 ns confirmed by heat load measurements on the beams-screens
Consistent with expectations from impedance and synchrotron radiation
Large differences between sectors observed with 25 ns are not visible with 50 ns
25 ns
50 ns
Test fill with 50 ns

## Slide 7
Cell-by-cell comparison
50 ns
25 ns
50 ns
25 ns
Reduction of normalized heat load is observed in all cells
Sector 12
For high load sectors distributions of normalized heat loads do not overlap
16L2

## Slide 8
50 ns
25 ns
50 ns
25 ns
Sector 23
For high load sectors distributions of normalized heat loads do not overlap
Cell-by-cell comparison
Reduction of normalized heat load is observed in all cells

## Slide 9
50 ns
25 ns
50 ns
25 ns
Sector 34
For low load sectors normalized heat loads are more similar
e-cloud contribution not dominant anymore
Cell-by-cell comparison
Reduction of normalized heat load is observed in all cells

## Slide 10
Instrumented magnets
Observation on instrumented magnets and LSS matching quadrupoles are consistent with observations on the arc averages:
Heat loads are reduced and large differences are suppressed

## Slide 11
50 ns
No anomalous behavior compared to the other arc half-cells
No changes in heat loads observed when changing the current in dipole correctors
Heat loads on the beam-screens at 16L2 and close-by

## Slide 12
50 ns
Zoom
No anomalous behavior compared to the other arc half-cells
No changes in heat loads observed when changing the current in dipole correctors
No correlation with measured steady state losses
Heat load reduction with 50 ns similar to other half-cells
Heat loads on the beam-screens at 16L2 and close-by

## Slide 13
Test with 50 ns beams:
  e-cloud observations
Electron cloud effects in dipole correctors
  Simulations
  Cell-by-cell observations
Update on coherent motion observations
  Considerations on Fast Beam-Ion Instability
Outline

## Slide 14
PyECLOUD simulations
25 ns, 1 beam
2800 bunches
Do we expect an effect on the heat load when changing the corrector setting?
Not really: there is a dependence on the magnetic field, but heat load values quite low (Lcorr = 68 cm over 50 meter cell length)
Effect of the dipole correctors on the cell heat load
A. Romano
SEYmax

## Slide 15
B1 B2
Impact of correctors on cell-by-cell heat loads
Any correlation between corrector settings and cell heat load?
Nothing evident when looking at the cell-by-cell patterns…

## Slide 16
Correlation plot produced for a fill with only B1 in the machine (~2000b), to avoid arbitrary assumptions in combining the effect of the two correctors in the same half cells  no dependence could be identified
Correctors settings at high energy did not change much during Run 2 (see next slide)
this plot practically also shows the dependence on the integrated current in the MCBs
Impact of correctors on cell-by-cell heat loads

## Slide 17
Jul 2017
Jul 2015
Corrector settings 2016 vs 2017
Correctors settings at high energy did not change much during Run 2

## Slide 18
Jul 2017
Jul 2016
Corrector settings 2016 vs 2017
Correctors settings at high energy did not change much during Run 2

## Slide 19
Test with 50 ns beams:
  e-cloud observations
Electron cloud effects in dipole correctors
  Simulations
  Cell-by-cell observations
Update on coherent motion observations
  Considerations on Fast Beam-Ion Instability
Outline

## Slide 20
Coherent motion observations: update
All dumps in the last week has features similar to those described by Elias and Xavier in the last two LMC meetings:
  Coherent motion is observed after the sharp increase of beam losses in 16L2 right before the dump
  At high energy the dynamics is too fast (10-20 turns) to perform spectral analysis on the beam motion
We had one dump at injection on Sat 15 July. In that case the beam stayed longer, allowing to get a better insight on the instability:
  Clear indication of coupled bunch motion
  Large positive tune shift of the unstable mode
D. Amorim
X. Buffat
L. Carver
B. Salvant

## Slide 21
Coherent motion observations: update
Summary table with main observations:

## Slide 22
The presence of localized losses and coherent beam motion suggests that the underlying mechanism for the beam oscillation could be a Fast Beam-Ion Instability (FBII)
Coupled-bunch (FBII), typically encountered in electron machines due to ion trapping
 Not expected with positively charged beams due to the repulsion of the ions
Fast beam-ion instability?
However (first calculations by L. Mether and G. Rumolo presented at LBOC 82):
Simulations show that for high enough density (1e13 ion/m3) ions can drive an instability even with protons
The presence of electron cloud in the chamber could enhance the ionization mechanism and change the dynamics (trapping?)
  This can be quantitatively assessed only with simulations of the full three-stream system (beam-electrons-ions)  requires some development work…
Involved ions and electrons have energies in the order of 101-102 eV
  their motion can be strongly influenced by “weak” magnetic fields (as those introduced by the MCBs)
IMCB= 1 A
B = 50mT

## Slide 23
In the 50 ns fill performed on Sat 22 Jul, the expected e-cloud suppression was clearly visible on the heat loads in all twin-bore magnets in the machine
  No particular behavior is observed at 16L2 and neighboring cells
  In particular there is no correlation of heat load with beam losses when changing the current in the MCBs
  It would be desirable to perform a scan during a 25 ns fill with same number of bunches and bunch intensity to have a clear comparison (e.g. if at some we need an intermediate intensity fill for MP reasons)
The contribution of the corrector magnets to the heat load per half cell is expected to be small
  No evident correlation is found between cell-by-cell heat loads and corrector settings
As observed before, coherent beam motion was present right before all dumps
  Too fast at high energy to allow for a meaningful spectral analysis
  In the case of the dump at 450 GeV the beam stayed for a longer time after becoming unstable  observed clear coupled bunch motion, large positive tune shift
  First simulations show that a Fast Beam Ion Instability (FBII) could be a possible driving mechanism for the coherent motion (for large enough ion density)  some development work needed to make quantitative estimates
Summary and conclusions

## Slide 24
Thanks for your attention!

## Slide 25
100 mA
1 A
100 mA
1 A
100 mA
1 A

## Slide 27: Fill 5979 (21 Jul 2017)
25 ns, 2556b/beam, 6.5 TeV

## Slide 28
B1 B2

## Slide 29
B1 B2

## Slide 30
B1 B2

## Slide 31
B1 B2

## Slide 32
B1 B2

## Slide 33
B1 B2

## Slide 34
B1 B2

## Slide 35
B1 B2

## Slide 36
Instrumented quadrupoles
Consistent with observations on the arc averages:
Heat loads are reduced and large differences are suppressed

## Slide 37
Stand alone quadrupoles: Q5s
Consistent with observations on the arc averages:
Heat loads are reduced and large differences are suppressed

## Slide 38
Stand alone quadrupoles: Q6s
Consistent with observations on the arc averages:
Heat loads are reduced and large differences are suppressed

## Slide 45
50 ns
25 ns
50 ns
25 ns
Sector 45
Cell-by-cell comparison
Reduction of normalized heat load is observed in all cells

## Slide 46
50 ns
25 ns
50 ns
25 ns
Sector 56
Cell-by-cell comparison
Reduction of normalized heat load is observed in all cells

## Slide 47
50 ns
25 ns
50 ns
25 ns
Sector 67
Cell-by-cell comparison
Reduction of normalized heat load is observed in all cells

## Slide 48
50 ns
25 ns
50 ns
25 ns
Sector 78
Cell-by-cell comparison
Reduction of normalized heat load is observed in all cells

## Slide 49
50 ns
25 ns
Sector 81
50 ns
25 ns
Cell-by-cell comparison
Reduction of normalized heat load is observed in all cells

## Slide 50: Observations of Coherent Motion
Clear coupled bunch coherent motion in B1V was observed for fill 5951 at injection energy on Saturday July 15th from ADT Post Mortem.
30-40 turns of large signal amplitude allows basic tune analysis to be performed.
Tune shift is seen when comparing bunch by bunch tunes before and after the instability.

## Slide 51: Observations of Coherent Motion
Clear tune shift is seen which is on the order of 3Qs. To be understood.
Clear coupled bunch coherent motion in B1V was observed for fill 5951 at injection energy on Saturday July 15th from ADT Post Mortem.
30-40 turns of large signal amplitude allows basic tune analysis to be performed.
Tune shift is seen when comparing bunch by bunch tunes before and after the instability.

## Slide 52
Weak coherent motion observed in dumps at flat top for both beams, with usually a single bunch pattern (head of trains). Coupled bunch motion observed in some cases.
Data from the ADTObsBox show few turns (~20) with increasing oscillation amplitude → Spectral analysis is more difficult
This behaviour is typical among most high energy dumps.
→ We could try to probe the instability mechanism with dedicated studies at injection energy (assuming that an instability can be triggered within a reasonable time).
Observations of Coherent Motion