## Slide 1: Updates on TCLIA
C. Bracco, V. Baglin, O. Aberle, J. Jowett, W. Reiegler

## Slide 2: Outline
Motivation
Proposed changes
Next steps

## Slide 3: Motivation
Extreme positions of ZDC, ±100 µrad
Showing 100 µrad neutron cones
LHC Design:
Since RLIUP workshop 2013 the 50 ns basic bunch spacing has become the baseline for HL-LHC Pb-Pb collisions.
N.B. HL-LHC Pb-Pb starts after LS2.
For safety, we should have several sigma separation at the closest encounters which means larger crossing angles  aiming for 100 rad. At present the TCLIA defines the main aperture limitation
J. Jowett and W. Riegler

## Slide 4: TCLIA, present situation and possible gain
Opening limitation is the opening in the vacuum tank at the level of the edge welded bellow
TCLIA jaw opening adjusted to 56 mm full opening.
Use maximum opening in the bellow
Maximum opening distance by design:
120 mm (Beam axis to axle centre line)
+ 40 mm (Bellow passage)
- 19 mm (Axle radius) - 1 mm (welding seam)
- 108 mm jaw thickness (at axle centre) - 1 mm end stop setting - 1 mm switch setting
= 30 mm (half gap) (theoretical maximum achievable half gap)
Metrology measurements on spare TCLIA:
Operational half-opening can be increased by ~1.8 mm  parking gap from 56 mm to  59 mm
O. Aberle

## Slide 5: Proposed modifications
Q1 beam screen / cold bore assembly
BPM
VAB
TCLIA
VCTCY
VCTCP
BPM
VAB
TCLIA
VCTCY
VCTCP
VAMGQ
Side view
Top view
V. Baglin

## Slide 6: Proposed modifications
Q1 beam screen / cold bore assembly
BPM
VAB
TCLIA
VCTCY
VCTCP
BPM
VAB
TCLIA
VCTCY
VCTCP
VAMGQ
Side view
Top view
Move TCLIA by ~2.2 m towards IP2
Move TCLIA by ~2.2 m towards IP2
V. Baglin

## Slide 7: New VCTCP
LHCVCTCP0001
Transition circular ID212 to elliptical 180/70
Length 500
If VCTCY+VAMGQ+VTCTP replaced by new VCT : ID90 to elliptical 180/70
  Gain in length of ~ 2.2 m
  In this case, the TCLIA is very close to the VAB, be careful with induced interlock in case of pressure rise due to malfunctioning
BPM
VAB
TCLIA
VCTCY
VCTCP
VAMGQ
V. Baglin

## Slide 8: Possible gain
Increase the maximum gap of the TCLIA for parking position to 59 mm, displace the TCLIA 2.2 m closer to IP2
 | Max full gap [mm] | Distance from IP2 [m] | Half-crossing [urad] | Separation [sigma]
Present | 56 | 74.248 | 70.1 | 4.0
New | 59 | 72.048 | 102.4 | 6.1
Assuming:
50 ns bunch spacing
Nominal Pb emittance (1.5 µm same beam size as 3.75 µm p emittance)
Beam energy E=7. Z TeV, β*=0.5 m at IP2

## Slide 9: Next steps
Official approval:
Report on cost + manpower at the HL-LHC project steering meeting on October 26th 2017  Budget and BC (before next HL-LHC C&S review)
Prepare ECR and layout/integration studies (end 2017)
Present at LMC for final approval (end 2017, March 2018 latest deadline also for ECR)
Activity in PLAN
Once (if) approved:
Production of new vacuum components and validation (<2019)
Uninstall TCLIA.4R2.B1  transport to surface  HW modification  new vacuum components installed in tunnel  transport and installation of modified TCLIA.4R2.B1 at new location (LS2)