## Slide 1
8b+4e MD
The MD aims at testing 8b+4e beams with large bunch intensity (up to 1.6e11 p/bunch) at 6.5 TeV for e-cloud, collimation and beam-beam studies
It is worth underlining that:
  The 8b+4e scheme has been already used for tests up to 1800 bunches at 6.5 TeV in 2015
  Single bunches with larger bunch intensities have been taken multiple times for MDs and tests (and used routinely in 50 ns operation during Run 1)
  The total intensity in the machine will not exceed 3e14 p/beam (similar values were used in operation this year)
The major concern that was identified is beam-induced heating which can be significantly different due to the different beam spectrum and large bunch intensity:
  Proposed an intensity ramp-up in three steps: 100b  600b  1900b
  The high pile-up run requested by the experiments will be used as a first step
  At each step beam induced heating on sensitive items will be monitored as done for intensity ramp-up in physics
  Plan to spend ~3h at high energy at each step

## Slide 2
8b+4e MD
For all steps we plan to use the operational cycle to bring the beams in collisions at b*=40 cm
Octupole current during the cycle will be increased to improve beam stability with larger bunch intensity
ADT settings for high intensity already exist and were used previously this year  expert to be called at the beginning of the MD to load them. Possibly the gain along the cycle will be increased to improve stability
No change on the RF system is required
No identified problem with diagnostics. Anything to be expected? Will orbit measurement and feedback operate correctly?
  Issues, if any, should be identified early, i.e. at the first ramp with ~100 bunches

## Slide 3
8b+4e MD: beam-beam studies
Beam-beam studies. Proposed procedure:
During the 600b fill, the crossing angles in IP1&IP5 will be reduced in steps following the procedure used in physics
We plan to use small steps of 5 urad (10 urad used in physics) monitoring the evolution of the beam lifetime
To prevent fast losses during the Xing angle changes, we will limit the speed of the angle change to 0.25 urad/sec (0.5 urad/sec used in operation)
Small tune trims will be performed at each step to optimize lifetime
Octupoles and Q’ might also be reduced in steps (in collisions there should be margin for stability)
If lifetime is under control we would use the full range that has been commissioned for Xing angle leveling, down to 90 urad
Open questions
  Stable beams will be declared. Should we move to adjust for the test?
  If time allows, and this is compatible with the other planned tests, can we repeat the same in the fill with the 1900b?