## Slide 1: Upcoming longitudinal MDs
Intensity limit with standard 25 ns beam
  Finemet cavity running reliably with 6 gaps since ITS2
  Try to push beyond 2 · 1011 ppb
  Then BCMS
Bunch rotation using 2  40 MHz and 3  80 MHz cavities
  With and without phase jump in PS
  Studies must be completed before ion run
  What is the penalty of the additional 80 MHz cavity in the PS?
  Then PS-SPS transfer
Measurement of (20 MHz,) 40 MHz and 80 MHz cavity impedances
  Calibration of probe attenuation (Tomoscope)
  Measure beam induced voltage
  Important input for longitudinal impedance model

## Slide 2: Preparation/follow-up for RF MDs
10/40 MHz double-harmonic RF during end of acceleration and flat-top
  Investigate bandwidth difference between both 40 MHz cavities
  Maximum allowed pulse length too short
  Increase AVC loop window duration during ITS3?
40 MHz fixed frequency acceleration at flat-top
  Energy offset and required duration of acceleration
  Check increased flat-top length