## Slide 1
EDM ring at CERN, rf system requirements
?

## Slide 2
EDM ring at CERN, rf system requirements
So far two systems mentioned in different reports:
Rf cavity in the ring for acceleration and bunch manipulations (One cavity or two ?)
RF solenoid or dipole
RF cavity requirements: “A storage ring experiment to detect a proton electric dipole moment”
RF frequency: 35.878 MHz, harmonic number 100
RF voltage: 6 kV Particle per bunch: 1.5 108
Pulse length: ?
Band width: ?
Control: Amplitude, Phase, how well? , how fast ?
Other constraints: Size, material (no ferrites ?), alignment
RF dipole requirements: “COSY paper”, two 4-turn air-core copper coils
Needed or not ?
RF frequency: 1.2 MHz, fine tuneable for some kHz
RF voltage: 6.6 kV

## Slide 3
EDM ring at CERN, rf system requirements
RF cavity requirements: “Yannis Semertzidis, talk by Lebedev at collaboration meeting”
RF parameters depend on lattice which is not chosen yet.
RF frequency: 47.75 MHz, harmonic number 70
RF voltage: 13 kV Particle per bunch: 2.5 108
Pulse length: ?
Band width: ?
Control: Amplitude, Phase, how well? , how fast ?
Other constraints: Size, material (no ferrites ?), alignment
Looks like field and frequency have to be quite stable, how stable ? Radial magnetic field due to Eddy currents in the cavity
Beam offset in cavity centre < 0.35 nm ? CLIC type stabilisation needed?

## Slide 4
EDM ring at CERN, rf system requirements
RF system itself does not seem to be very demanding if I am not mistaken. Existing system in the PS could be used for rough costing.
But what about the auxiliary requirements. Need of more information and parameters !