## Slide 1
Scintillating Fibres – Tracking Particles With (a little) Light
The new Fibre Tracker for LHCb
Christian Joram
CERN, EP-DT
CBPF, Rio de Janeiro
01/09/2017

## Slide 2
LHCb LS2 upgrade
What are scintillating fibres and how do they work?
How can we track particles with scintillating fibres ?
A bit of history
A few slides on Silicon Photomultipliers (SiPM)
The LHCb SciFi Tracker
What makes it difficult (and interesting)?
Outline

## Slide 3
LHCb is an atypical collider experiment with classic fixed target geometry.
Its mission is to measure rare phenomena in the beauty and charm sector in particular CP violation, and to look for signs of new physics (beyond the standard model).
For this purpose it has powerful vertexing, tracking, calorimetry, particle identification
It’s in operation since 2010.
LHC pp
collision point

## Slide 4
New VELO, Si pixel based
New Upstream tracker (UT), Si-mstrip
SciFi Tracker, scintillating fibres
In 2019/2020 (during LHC Long Shutdown 2), LHCb will undergo a very major upgrade.
5x higher instantaneous luminosity. Aim for 50 /fb over 10 years.
Three detectors will be replaced. All other detectors obtain fast 40 MHz readout electronics.
Full software trigger for every bunch crossing.

## Slide 5
Why to replace the Outer Tracker?
OT technology: Straw tubes, i.e. cylindrical drift tubes
Issues when upgrading the luminosity at LHCb by a factor 5 and switching to 40 MHz readout:
drift time will spill over to next measurement
occupancy of straws will approach 100%
Drift time ≤ 50 ns
Ar/CO2/O2
Performance:
ehit = > 99%
sx = 180 mm
3% X0 / station
OT
5m
6m

## Slide 6
Why to replace also the Inner Tracker?
The region close to the beam pipe is complemented by the Inner Tracker (Si micro strip technology).
2% of the area
20% of the tracks
1.08 m
IT
0.4 m
No intrinsic performance issue.
New 40 MHz readout needed
IT area would need to be enlarged
Integration of a Si tracker in the middle of another detector is a mess  up to 30% X0 of material.
 Replace both IT and OT by a single technology

## Slide 7
What are scintillating fibres and how do they work?

## Slide 8
scintillator
photodetector
Energy deposition by an ionizing particle or photon (g)
 generation
transmission of scintillation light
detection
What is a scintillator ?
particle
Light guide

## Slide 9
Inorganic (crystals)
More light (up to 70000 ph/MeV)
High density r ~ 5-10 g/cm3
Expensive
Two categories
Organic scintillators
(plastics or liquid solutions)
Polystyrene + some dopants
Little light (<10’000 photons / MeV)
Low density r ~ 1g/cm3
Fast (ns)
Cheap
Radiation “soft”
Can be used for fibres!
Don’t confuse scintillators with lead glass !
The light generation in lead glass is actually based on the Cherenkov effect. Lead glass is the poor man’s crystal. High density, but little light output.

## Slide 10
Refraction Total internal reflection
ain
aout
ain
aout
nhi
nlo
ain > acrit  aout = ain R = 100%
acrit = asin(nlo/nhi)
acrit

## Slide 11
Jean-Daniel Colladon, a 38-year-old Swiss professor at University of Geneva, demonstrated (by accident) light guiding or total internal reflection for the first time in 1841.
He had actually studied law (!) and worked on speed of sound in water and water jets.

## Slide 12
Basics of scintillating fibres
Scintillating fibre = Polystyrene (PS) core + plexiglass (PMMA) cladding
n ~ 1.59
n ~ 1.49
(per side)
PS
PMMA
Why ≥ ?
There are also 'cladding rays' and helical paths. They usually survive only over short distances.

## Slide 13
Double cladded fibres make use of an extra layer of a fluorinated polymer with lower refractive index (n = 1.42) (CERN RD7 / Kuraray 1990). This is still state-of-the art!
Scintillating fibres exist also in other geometries and flavours
C.D. Ambrosio et al.,
NIM A 325 (1993), 161
Square fibres
hexagonal fibres
glass capillaries with
liquid scintillator
Annis P, et al. NIM A367
(1995) 377
23 mm
60 mm
Micro-fluidic detector study
A. Mapelli et al., IEEE TNS 58, NO. 3, JUNE 2011
63.3°
(per side)

## Slide 14
Chart: wavelength (nm)
Emission spectrum of Kuraray SCSF-78 fibre
(baseline for LHCb Tracker TDR)
as function of distance from excitation point
d
excitation
spectrometer
Light is attenuated during propagation
Blue light is stronger absorbed than green and red
Non-irradiated
L(l) attenuation length

## Slide 15
Attenuation in a 3.5 m long SCSF-78 fibre (Ø 0.25 mm) in air, averaged over emission spectrum
Long component: Ll = 3.6 m
Rayleigh scattering, self absorption of WLS, imperfection of core/cladding interface
Short component: L ~ 0.3 m
helical paths, cladding light (depends on fibre environment (air, glue, …)

## Slide 16
How can we track particles with scintillating fibres ?
Tracking = localising particles along their path
High resolution  use thin fibres
High efficiency  use thick fibres
Low background  low noise photodetectors
particle path
(in a magnetic field)
Future location of our SciFi tracker in LHCb

## Slide 17
+ ….
2D
stereo
cylindrical
Fibres give lots of geometrical flexibility
They have low mass and are (almost) self supporting
All non-active material can be at the end of the fibres
But …
Fibres give relatively little light
They are non very radiation hard
Building a fibre tracker is a lot of work (companies just deliver fibres)
a)
b)
Trackers based on scintillating fibres

## Slide 18
Back-of-the-envelope estimate of photoelectric yield in a 0.25 mm double cladded fibre, 2 m from photodetector. Non-irradiated.
MIP  dE/dx = 2 MeV/cm (Bethe Bloch)
Scintillation yield: dYg/dE = 8000 ph / MeV  Yg = 320
Trapping inside fibre (1 hemisphere): 5.4%  Yg ~ 16
Attenuation losses over 2 m: 50%  Yg ~ 8
Efficiency of photodetector (typ. PMT): 20%  Yp.e. ~ 1-2
dx = 0.022 cm (active)  dE = 0.04 MeV
(when passing through axis … optimistic!)
 Need more traversed fibre thickness
 Need higher photodetector efficiency
 Need to recover light in the second hemisphere
photodetector
VERY little light !

## Slide 19
A bit of SciFi history

## Slide 20
A bit of history
After the discovery of Colladon (1841), it took 116 years before scintillating fibres were used as particle detectors
Rev. Sci. Instrum. 28, 1098 (1957);
First (?) non-cladded scintillating plastic fibre.
……

## Slide 21
Outer tracking and pre-shower measurement for electron identification.
60,000 single-clad, blue-emitting scintillating fibres of 1 mm in diameter and 2.1 m long
developed and produced (!) at Saclay. L > 1.5 m.
Light propagates to 32 collector plates which are readout by 32 image-intensified CCDs (32000 pixels each).
J. Alitti et al. , NIM A 273 (1988) 135
collector plate
Upgrade of the UA2 experiment (1985-87).
The first major collider application of scintillating fibre tracking technology.

## Slide 22
UA2 readout system
Performance
2.8 p.e. per fibre (1mm)
Single fibre efficiency: >91%
shit = 0.35 mm, strack = 0.2 mm
Readout time ~10 ms
CCD image (circles show calculated fibre positions)
R.E. Ansorge et al., NIM A265 (1988) 33-49
3-stage image intensifier (II)

## Slide 23
CHORUS
106 scintillating fibres of Ø 500 mm
58 image-intensifier chains + CCD,
similar to UA2.
They also tested a micro-vertex tracker based on the liquid-in-capillary concept (see photo on slide 14).
Annis P, et al. NIM A367 (1995) 367
The scintillating fibre-tracking layers provide pre-localisation of the regions to be scanned in the emulsion.

## Slide 24
DØ The upgraded DØ detector comprises a 80,000-channel central fiber tracker (CFT).
Ø 835 mm fibres are arranged in 'Doublet' structure
8 concentric layers (axial + stereo)
Lfibre ~ 2 m + O(10)m clear waveguide
Total = 200 km of scintillating and 800 km of clear fibres
~1 m
V.M. Abazov et al, A 565 (2006) 463–537

## Slide 25
Very innovative readout in D0: Visible Light Photon Counters (VLPC)
Si:As avalanche photodetector
Very high QE: ~ 75%
High gain: ~40.000
! Needs to be operated at T=9K!
D0 used chips with 8 VLPCs (Ø 1mm).
128 chips fit in a cassette
88 cm
Bundles of clear fibres
Performance (partly from test stand)
Yield: ~10 pe / fibre
Hit efficiency: 99.5%
Doublet hit resolution: 100 mm
Fast readout: CFT contributes to the L1 trigger (every 132 ns)
B. Baumbaugh et al. IEEE TNS 43, NO. 3, JUNE 1996
Same technology is also used in the MICE experiment http://mice.iit.edu/
LED calibration spectrum

## Slide 26
ATLAS ALFA
LHC
Beam
4 RP stations are located at ±240 m from ATLAS in LHC tunnel
Total ~11.000 fibres, 500 µm squared, ~35 cm long, aluminized for reduced cross-talk.
UV geometry with 2x10 staggered layers. Active area is only about 3 x 3 cm2.
Readout (at 40 MHz) by 184 Multi-anode (64 ch.) PMTs.
Forward detector in Roman Pots for luminosity and stot(pp) measurement
Performance:
Yield: ~4 pe / fibre
Track resolution: ~25 mm
S. Ask et al., NIM A 568 (2006) 588–600
S. Abdel Khalek, 2016 JINST 11 P11013
500 µm

## Slide 27
A short recap
of SiPM technology

## Slide 28
Silicon Photomultipliers (SiPM) -
What makes them so attractive for SciFi ?
A photodetector for reading the scintillation light from a fibre requires
 | Image intens. CCD | (MA)PMT | SiPM
High sensitivity (PDE) | O | O | +
High charge amplification | + | + | +
High speed (multi-MHz) | - | + | +
Small size | O | - | +
Low cost (per channel) | - | - | +
Immunity to magnetic field | - | - | +
Radiation tolerant | O | 0 | -
~ 40%
~ 107
~ mm2
few CHF

## Slide 29
h e
p+ i(n) n+
g
PIN photodiode
g
g
Avalanche Photodiode
(APD)
SiPM
High QE (~80%)
Ubias = small (or even 0)
No charge gain (G=1)
1 photon  0 or 1 electron
Can’t detect single/few photons
High QE (~80%)
Ubias = few 100 V
‘small’ avalanche, self terminating
Charge gain G ~ few 100
Can’t detect single/few photons
g
Multi-pixel array of APD
operated in Geiger mode, i.e. above break down
G ~ 106 - 107
forced quenching
Every pixel is just a binary detector (0/≥1)
Parallel connection of all pixels gives a quasi-analog detector
A = 1cm2
CMS ECAL

## Slide 30
GM-APD
quench
resistor
1mm
100 – several 10000 pix / mm2
bias bus
20 x 20 pix
-Vbias


g
Q
Q
2Q
Quench
resistors
Sizes up to 6×6 mm2 now standard.
Only part of surface is photosensitive!
Photon detection efficiency
PDE = QE · egeom · eavalanche
1 pixel fired
2 pixels fired
3 pixels fired
=f(OV)
1 GM-APD is a binary device.
The operation of many GM-APDs in parallel leads to a quasi-analog detector with photon counting properties.

## Slide 31
The LHCb
SciFi Tracker

## Slide 32
General layout of the detector geometry:
3 stations with 4 planes each X-U-V-X (like the OT)
Requirements:
sx < 100μm (bending plane)
Low mass, 1% X0 per layer
Readout every 25 ns
Radiation tolerant up to 35 kGy and 1012 n/cm2

## Slide 33
SciFi Module
Detector Layer
× 12
× 4 (stereo angles
0°, +5°, -5°, 0°)
Tracking Station
× 3
Scintillating Fibre Tracker
1× SciFi Module
1024 mats, 128 modules
340 m2 total area
almost 11,000 km of fibre
4096 SiPM arrays  525’000 SiPM channels
5m
6m
Beam pipe
SciFi in numbers
Fibre mat
× 8
mirror
SiPM
SiPM

## Slide 34
QA on scintillating fibres (11’000 km, 880 spools)
Every mm of fibre is scanned for diameter anomalies (bumps)
Big bumps (DD > 100 mm) are shrunk / removed.
Every spool is characterised in terms of attenuation length and scintillation light yield.
A fraction of spools is checked for radiation hardness, decay time, bendability
Significant contribution from CBPF: A.B.R. Cavalcante 2014 – 2016 (PhD 08/2017)

## Slide 35
Fibre mat &module production
Ø80 cm wheel with fine thread (p=0.275 mm)
40 mm
2.5 m
6 layers + epoxy glue
Dfibre = 0.25 mm
Winding machine, produced in industry
mirror

## Slide 36
single channel:
0.25×1.5mm2
96 pixels
single pixel
SiPM array
+
Kapton flex-PCB
32.59±0.10mm
128 channels
Principle of readout

## Slide 37
Principle of electronics
Hit fibres form clusters of 2-3 SiPM channels
Analog centroiding would give optimum spatial resolution.
Signal per channel up to ~20 pe  require 6 bits resolution.
Remember: 525 k channels × 40 MHz readout × 6 bits = 126 Tb/s  Not affordable
Second best solution: a 3-thresholds binary readout
4.5 pe
2.5 pe
1.5 pe
3 thresholds = 2 bits
Achieved in test beam:
sx ≤ 84 mm

## Slide 38
64 channels
Principle of electronics
Clusterisation
FPGA
Pacific(5) FE ASIC
GBT (data and controls)
V1 master & 4 cluster boards on cooling plate
64 differential lines
Significant contribution from CBPF: PACIFIC emulator set-up (8x256 channels). A. Massafferri et al.

## Slide 39
What makes LHCb SciFi challenging
(= interesting)?
Radiation
Large size
High precision
Complex integration

## Slide 40
LHCb Radiation Environment
Ionization dose:
Neutron fluence
35 kGy in hottest region
at SiPMs: 6 1011 neq / cm2
decrease of fibre transparency
Increase of SiPM dark noise

## Slide 41
3 m long SCSF-78 fibres (Ø 0.25 mm), embedded in glue (EPOTEK H301-2)
irradiated at CERN PS with 24 GeV protons (+ background of 5·1012 n/cm2)
before irradiation
after irradiation
0 kGy
3 kGy
at 6.25 Gy/s
22 kGy
at 1.4 Gy/s
Ll = 439 cm
Ll = 422 cm
Ll = 126 cm
Ll = 52 cm
Example: LHCb fibre irradiation test (CERN PS, 2012)

## Slide 42
SiPM position
beampipe level
~35 kGy
~1 kGy
Fluka
M. Karacson
SciFi irradiation tests
Dose along fibre will be very non-uniform
R. Ekelhof, PhD thesis
Many radiation test  reasonably good understanding of radiation damage over full dose range.
Attenuation length L
Attenuation factor a = 1/L
a = a0 + airr
airr ~ k· D
airr

## Slide 43
The (almost*) ultimate irradiation test
We irradiated two mirrored SciFi mats in the PS Irrad facility at CERN to the expected steep dose profile.
Only a 25 mm wide band along
the mat was irradiated.
From previous results, the expected signal loss at the mirror end of the mat was 40%.
~35%
Scan across the mat (13 cm), at 2 cm from mirror
10 pe
(* the ultimate test would be to irradiate at the correct (non-accelerated) dose date, which would have taken 5 years. However, we have so far no indications that rate matters).

## Slide 44
3·1011 n/cm2
6·1011 n/cm2
12·1011 n/cm2
~7 MHz
~14 MHz
~28 MHz
A. Kuonen et al. CERN-LHCb-INT-2015-004
As in every Si device, neutrons damage the Si lattice  leakage current.
In a SiPM the main effect is the increase of the dark count rate (DCR), linearly with the neutron fluence: DCR = a·Fn,
At room temperature, DCR can reach GHz per SiPM channel
Neutrons fluence is about the same for all SiPMs  All SiPMs are equally affected.
Dark counts from a single channel of an irradiated SiPM detectors,
operated at T = -40°C
2 ms
Irradiated SiPM detectors become ‘noisy’

## Slide 45
Problem: noise hits have same amplitude as 1 pe signal hits. They can combine/pile up to signal-like noise clusters.  Noise Cluster Rate (NCR)
For efficient operation and reconstruction, NCR shall not exceed 50% of the smallest Signal Cluster Rate (SCR), which is 4 MHz.
Solutions:
  Cooling: Every 10 K reduction halves DCR. T = -40°C gives a factor 64 (26) reduction.
  Clustering. Noise hits don’t form clusters, except accidentally!
  Optimise SiPM for low cross-talk and after pulses.
  Use preamp with short shaping time.
  Neutron shielding.
Noise cluster rate (NCR) for different Pacific settings and thresh.
‘Holy’ Olivier Callot limit: NCR < 2 MHz/SiPM array

## Slide 46
~ 7 m
Lower service bar has a translational DOF in y-direction
CF cables
2 x 6 C-frames
Hanging under existing bridge, new rail system needed.
Precise positioning of 2 x (5)6 modules
Supply of Novec fluid (@-50C)
Supply of cooling water
HV & LV cables
Signal and control fibres
Mechanics and services

## Slide 47
Very challenging and complex integration
LHCC Review - 08 / 05 / 2017
47
Fibre modules
Cold box
Readout box
Flex cables
Novec manifold
Water cooling
roller
Novec manifold, vacuum insulated
A-side/C-side intersection

## Slide 48
Overall Status of Project
 | R&D | proto | pre-series | series | On schedule
Fibres |  |  |  |  | 
Mats |  |  |  |  | 
Modules |  |  |  |  | 
SiPM |  |  |  |  | 
Flex cable |  |  |  |  | 
Cold box |  |  |  |  | 
Pacific ASIC |  |  |  |  | 
FEE |  |  |  |  | 
C-frames |  |  |  |  | 
catching up
catching up
tight
tight
75%
45%
25%
ordered
ordered
still some issues
tight
Fully
operational
No but some tension in the planning.
x

## Slide 49
CERN weekly bulletin (30/08/2017)

## Slide 50
Summary and Outlook
Thanks to Silicon Photomultipliers (SiPM), there is new interest in scintillating fibres. One can build fast and light tracking detectors
LHCb SciFi tracker will be the largest and fastest fibre tracker ever built
Radiation levels pose major problems, but the chosen design is expected to cope with them (in Runs 3 & 4, 50 fb-1)
The detector construction is in an advanced state. The schedule is tense but there is (justified) hope that we’ll be ready for installation in autumn 2019.
Not covered in this talk but perhaps of interest to the younger generation: A further LHCb upgrade (LS4, 2030) to 2×1035 and 300 fb-1 would require a modified SciFi and to complement it with an Si-based Inner Tracker, for R ~ 1-1.5 m around beam pipe.

## Slide 51
SciFi Tracker: ~20 participating institutes
  Brazil (CBPF)
  China (Tsinghua)
  France (LPC, LAL, LPNHE)
  Germany (Aachen, Dortmund, Heidelberg, Rostock)
  Netherlands (Nikhef)
  Poland (Warsaw)
  Russia (PNPI, ITEP, INR, IHEP, NRC KI)
  Spain (Barcelona, Valencia)
  Switzerland (CERN, EPFL)

## Slide 52
6 m
cleaner
LN
3015
AccuScan
6400
cladding
Test
NI 6009
Fast IO
tensioner 50 g
unwinding spool
CERN (built together with Aachen), which allows to scan fibres with 40 mm step size and <1 mm resolution. A 12.5 km fibre spool can be scanned in ~3.5 hours.
X and Y diameter
(look perfect on linear scale)
350 mu

## Slide 53
Distance 295 mm
Distance 321.3 mm
Distance 333.2mm
Distance 562.0 mm
314 mm
319 mm
~1.1 mm
290 mm
Projection x
Projection y
Projection 1 (~ x)
Projection 2 (~y)
Distance 306.7 mm
298 mm
N.B. Correspondence between projections x,y and 1,2 is only approximate.

## Slide 54
Set-up for measuring the light yield with ionising radiation (Sr-90 source)
Calibrated
in p.e.
Manual set-up at CERN.
Chart: Scint. yield (p.e.)
| 60 | 90 | 120 | 150 | 180 | 210 | 240 | 270
SCSF-78MJ | 5.6 | 4.45 | 4.04 | 3.88 | 3.55 | 2.88 | 2.61 | 2.24
Fit SCSF-78MJ | 5.8872 | 5.3628 | 4.8851 | 4.45 | 4.0536 | 3.6926 | 3.3637 | 3.0641 | 2.7911 | 2.5425
SCSF-L2MJ | 4.42 | 3.55 | 3.04 | 2.52 | 2.23 | 1.88 | 1.72 | 1.51
Fit SCSF-L2MJ | 5.6064 | 4.8109 | 4.1284 | 3.5426 | 3.04 | 2.6087 | 2.2386 | 1.921 | 1.6484 | 1.4145
SCSF-L1MJ | 5.07 | 4.14 | 3.55 | 3.29 | 2.88 | 2.6 | 2.41
Fit SCSF-L1MJ | 5.8487 | 5.2091 | 4.6394 | 4.132 | 3.6802 | 3.2777 | 2.9192 | 2.6 | 2.3157
Points at 60 cm are not included in fit

## Slide 55
Complex irradiation of a 2.5 m long
fibre module in the new PS IRRAD zone
(Oct 2015)
Requested dose profile varies by a factor 1000 along the module

## Slide 56
S. A. Ponomarenko et al., Nature Scientific Reports 4, Article number: 6549.
Spin-off company Luminnotech
Find better fibres which give more light
LuminnoTech (Rus), Kuraray (JP) and CERN work on a new type of scintillating fibre.
Nanostructured Organo-silicon Luminophores (NOL)
On paper, it’s a little revolution. In practice, the quality isn’t good enough yet. Perhaps a solution for SciFi upgrade?
Conventional scintillator
NOL scintillator

## Slide 58
Geometrical precision
Fibre mats are produced by winding fibres, layer by layer, on a fine-pitch threaded wheel
p = 270 mm
~150 mm
~ Ø 900mm
addition of very fluid epoxy glue, TiO2 loaded
Fibre winding (at Univ. of Dortmund)
Dedicated machine, in-house production
feeder
Test winding (at Univ. of Aachen)
Use of a large CNC lathe.

## Slide 59
Geometrical precision
Alternative technique: replace thread by a kapton film, structured with coverlay(© Dupont). PCB technique, R. de Oliveira.
~150 mm
~ Ø 900mm
Kapton film becomes part of fibre mat.
Allows use of precise alignment marks.
3 m long and 16 cm wide Kapton film used
for a full-size 6 layer mat (march 2014).
p = 270 mm
Inspection at CERN
After winding at Univ. Dortmund

## Slide 60
Optical 3D coordinate measurement machine (CMM) in PH/DT bond lab.
Scan of fibre mat end faces (after cut with diamond tool)
defect
defect
defect
1.5 mm
RMS = 4-12 mm
layer 1 - layer 6

## Slide 61
Get enough light  produce high quality mirror at non-read fibre end
Chart: Plate 1&2, intensity ratio at mirror
| Ratio Al.M. | Ratio ESR | Ratio TFC
Ratio Al.M. | 0.799 | 0.6 | 0.795
 | 0.808 | 0.704 | 0.817
We studied three different mirror technologies
Aluminised mylar foil
3M Extended Specular Reflectance (ESR) foil
Aluminium thin film coating (TFC)
and measured the intensity gain (mirror/no mirror*)
It remains unclear why ESR results are so low. Would have expected ≥ Al. Mylar.
We checked for possible influence of angle of incidence as well as glue type. No change.
50% of the scintillation light is emitted in the wrong hemisphere.
Chart: Expected relative light yield (with/without mirror Llong = 438 cm, R=0.8)
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120 | 130 | 140 | 150 | 160 | 170 | 180 | 190 | 200 | 210 | 220 | 230 | 235 | 240 | 245 | 250
rel. yield | 0.98436 | 0.90112 | 0.84647 | 0.80767 | 0.778 | 0.75374 | 0.73279 | 0.71393 | 0.69646 | 0.67994 | 0.66412 | 0.64886 | 0.63406 | 0.61966 | 0.60563 | 0.59194 | 0.57858 | 0.56552 | 0.55276 | 0.54029 | 0.52811 | 0.5162 | 0.50456 | 0.49318 | 0.48759 | 0.48206 | 0.4766 | 0.47119
rel. yield | 1.1975 | 1.1192 | 1.0696 | 1.0359 | 1.0115 | 0.99263 | 0.97719 | 0.96398 | 0.95227 | 0.94165 | 0.93187 | 0.92279 | 0.91431 | 0.90637 | 0.89896 | 0.89203 | 0.88559 | 0.87961 | 0.8741 | 0.86904 | 0.86444 | 0.86029 | 0.85659 | 0.85333 | 0.85187 | 0.85052 | 0.84928 | 0.84815
rel. yield | 0.98436 | 0.90112 | 0.84647 | 0.80767 | 0.778 | 0.75374 | 0.73279 | 0.71393 | 0.69646 | 0.67994 | 0.66412 | 0.64886 | 0.63406 | 0.61966 | 0.60563 | 0.59194 | 0.57858 | 0.56552 | 0.55276 | 0.54029 | 0.52811 | 0.5162 | 0.50456 | 0.49318 | 0.48759 | 0.48206 | 0.4766 | 0.47119
80% gain
20% gain

## Slide 62
Get enough light  maximise fibre attenuation length
Optical rail, 3.5 m
UV-VIS-photodiode*
Teflon ‘cavity’ with 4 UV-LEDs
(+ PIN-diode for intensity monitoring)
Mechanical fixation
AquaDAG (black paint)
Supresses cladding mode + rear reflection
CERN set-up for measurement of attenuation length
fibre
*May be replaced by a SiPM, to have correct sensitivity characteristics.

## Slide 63
Latt. in cm
<Latt. > = 293 cm
(Lot 1-8)
Measurements of 8 spools + older Dortmund sample (unknown Lot no.)
KURARAY SCSF-78, 250 mm, double cladded)
We are currently investigating with Kuraray whether lower or higher concentrations of dopants have a sizable impact on L or whether we have to live with L~3-4 m.
Side remark: We are also maintaining / building up relations to 2 other potential fibre producers: Saint-Gobain (Bicron), ELJEN Technologies (new in the SciFi market).

## Slide 64
Scintillation in organic materials
Molecular states (pi orbitals)
singlet states
triplet states
S
0
T
1
T
2
S
1
S
2
S
3
singlet states
triplet states
S
0
T
2
S
1
S
2
S
3
non-
radiative
fluorescence
10
-8
- 10
-9
s
phosphorescence
>10
-
4
s
10
-11
s
The organic scintillation mechanism is based on the pi-electrons (molecular orbitals) of the benzene ring (C6H6).
ionization energy
fast
slow
ultra fast
Organic scintillators exist as
Crystals (anthracene)
Liquids (solutions)
Plastics (polymerized solutions)
Organic scintillators are fast. Scintillation light decay time ~ few ns.

## Slide 65
In HEP, we use mainly
Polyvinlyltoluene (PVT) ==> plastic scintillator tiles
Polystyrene (PS) ==> scintillating fibres
A 'fluor' has non-overlapping absorption and emission spectra. The energy/wavelength difference is called Stokes shift
Solvent
DE = dE/dx·Dx
Scintillator
fast and local energy transfer via non-radiative dipole-dipole interactions. Förster transfer.
fluorescence light
wavelength
shifter (‘fluor’)
radiative transfer
UV
(~300 nm)
Visible
( 400 nm)
>
~
ionizing particle
In pure form, both PVT and PS, have a very low scintillation yield.
One adds therefore dopants in ‰ - % concentrations.
(Producers normally don't disclose the details about the additives and their concentrations.)
Typical yield
8000 ph/MeV