## Slide 1: CERN: From Particle Physics to Medical Applications
Evangelos N. Gazis
Professor of Particle Physics
National Technical University of Athens
CERN High School Teachers, 26 Aug-01 Sep 2018

## Slide 2
Medical Applications
From X-rays to Medical Physics
Natural Radioactivity
Synergy of sciences
CERN Collaboration for the deceases
Cancer: Diagnosis – Treatment
Medical Imaging
PET Imaging
Medical Imaging Collaborations: Crystal Clear & Medipix
Digital Imaging
Multimodality Imaging CT – PET
MRI
Accelerators for cancer : diagnosis - treatment
Hadron Therapy - Timeline
Carbon Ions – HIT
PIMMS – CNAO
ISOLDE – Isotopes Production
Outline

## Slide 3
• Fundamentals of Radiation Physics
• Medical Diagnostic Techniques
• Imaging technics (basic)
• Radiation Therapy
Not covered in this talk:
• Advanced Imaging
• Radiation Protection and Dosimetry
• Radiobiology
• Anatomy and Physiology
• Molecular and cellular oncology
Medical Applications

## Slide 4
November 8, 1895 Wilhelm Röntgen discovered X-Rays
December 22, 1895 he takes the first image of his wife’s hand
Röntgen received the first Nobel prize in physics in 1901
X-rays
Beginning of Modern Medical Physics

## Slide 5
1896: Discovery of natural radioactivity
1898: Discovery of radium used immediately for “Brachytherapy”
Natural Radioactivity
Beginning of Modern Medical Physics
Henri Becquerel
Marie Curie Pierre Curie
(1867 – 1934) (1859 – 1906)
Thesis of Mme. Curie – 1904
α, β, γ in magnetic field

## Slide 6
….or why should YOU study medical physics?
…or why should senior physicists care about medical research?
…and why care medical researchers/industry about physics???
What is the added value of the Physics of Medicine?

## Slide 7
1st Answer: Synergy
Accelerator physics
X-.‐ray
source
physics
detector
physics
image
reconstruction
medical
doctors

## Slide 8
2nd Answer: Overcoming Limits!

## Slide 9
The 4th Pilar of Technology

## Slide 10
More than 3 million new cancer cases in Europe each year and 1.75 million associated deaths
Increase by 2030: 75% in developed countries and 90% in developing countries
CANCER a growing challence

## Slide 11
CERN Technologies & Innovation

## Slide 12
Medical Imaging

## Slide 13
Electromagnetic Waves Used in Medical imaging

## Slide 14
Medical Imaging

## Slide 15
Medical Imaging then Treatment
Particle Detection
Breast imaging (Clear PEM)
Imaging
PET Scanner

## Slide 16
PET Imaging
Idea of PET

## Slide 17
PET : Operation

## Slide 18
PET : Scan

## Slide 19
• New scintillating materials
  – LuAP, phoswich LuAP-LSO (CERN patent)
  – Other crystals
• New photodetectors (Avalanche Photo-Diodes)
• New low noise electronics
New intelligent DAQ
systems with pipeline
and parallel architectures
better simulation GEANT 4
better reconstruction algorithms
Crystal Clear Collaboration

## Slide 20
• PET dedicated to breast
cancer screening
– Extremely sensitive to small
tumor masses
• Spatial resolution (1-2mm)
• High counting sensitivity
• Short PET exam
• Coupled to ultrasound
Crystal Clear Collaboration (PEM)

## Slide 21
• High Energy Physics original development:
– Particle track detectors
• Allows counting of single photons in contrast to traditional charge integrating devices like film or CCD
• Main properties:
– Fully digital device
– Very high space resolution
– Very fast photon counting
– Good conversion efficiency of low energy X-rays
MEDIPIX

## Slide 22
• an electronic chip similar to the electronic imaging chip in a digital camera
  – sensitive to x-rays instead of visible light
• it can create the first true color images with x-rays.
  – it permits us to move from black and white x-ray images to full color x-ray images
• can be read out very rapidly.
  – allows the use of the chip for color x-ray digital movies or for fast color x-ray CT scans
WHAT IS MEDIPIX ?

## Slide 23
Current
– Limited contrast
– High dose
• Restricted screening
• Limited access to preventive health care
Digital Imaging
Digital
– High contrast
– Lower dose
• Opportunity for screening
• Access to preventive health care

## Slide 24
PET – CT David Townsend
Multimodality Imaging

## Slide 25
Morphology Metabolism
Multimodality Imaging : PET - CT

## Slide 26
Magnetic Resonance Imaging - MRI
First human body scan

## Slide 27
Accelerators for Cancer Treatment

## Slide 28
E. O. Lawrence is awarded Nobel Prize in 1939
Ffor inventing the cyclotron 1937
The 1st Cyslotron

## Slide 29
Use of Accelerators Today

## Slide 30
Over 3 million cancer cases in Europe each year
Cancer a growing societal challenge !

## Slide 31
After diagnosis some diseases like hyperthyroidism, cancer, blood disorders, etc… can be treated using radiotherapy
Three main methods:
• Unsealed source radiotherapy
• Brachytherapy (sealed source therapy)
• External beam: x-‐rays, electrons, p, n, heavy ions
Stages in the radiotherapy process:
QA, Imaging, Planning, Simulation,
Treatment, Verifikation, Modelling Outcome
Physics, engineering, imaging, technology based
Radiotherapy
"seeds”‐ small radioactive rods implanted directly into the tumor

## Slide 32
20 000 patients per year every
10 tumor million inhabitants
1 linac every <250,000 inhabitants
Conventional Radiotherapy
More than 7000 linacs in the world for radiotherapy

## Slide 33
3 "Cs" of Radiation
Cure (~ 45% cancer cases are cured)
Conservative (non-invasive, few side effects)
Cheap (~ 5% of total cost of cancer on radiation)
There is no substitute for RT in the near future
The rate of patients treated with RT is increasing
Present Limitation of RT:
~30% of patients treatment fails locally
Radiotherapy in the 21st Century

## Slide 34
Two Opposite Photon Beams

## Slide 35
Two Opposite Photon Beams

## Slide 36
• Accelerator technologies to improve treatment : higher dose
• Detectors/imaging: accuracy, multimodality, real-time, organ motion
• Biology: fractionation, radio-resistance, radio-sensitization
• Data: storage, analysis and sharing
• Collaboration in this multidisciplinary field is key
Raymond Miralbell, HUG
How to decrease the failure rate?

## Slide 37
In 1946 Robert Wilson:
– Protons can be used clinically
– Accelerators are available
– Maximum radiation dose can be placed into the tumor
– Particle therapy provides sparing of normal tissues
Hadron Therapy : All started in 1946
Conventional: X-Rays Ion Radiation
- Tumors near critical organs
- Tumor in children
- Radio-resistant tumors

## Slide 38
Optimization of the natural distribution of dose
Hadron Therapy

## Slide 39
Hadron Therapy Timeline

## Slide 40
Tumors near critical organs
Tumors in children
Radio-resistant tumors
Why Hadron Therapy

## Slide 41
Photons vs Protons

## Slide 42
• GSI – Darmstadt (1997 – 2008)
• G. Kraft (GSI) & J. Debus (Heidelberg)
– 450 patients treated with carbon ions
Carbon Ions Project : pilot project in Europe

## Slide 43
HIT - Heidelberg
Ion source
Synchrotron
Treatment rooms
Siemens Medical
Gantry
Quality
control
Beam transport line

## Slide 44
HIT - Heidelberg

## Slide 45
Modeling of beta+ emitters:
        Cross section
        Fragmentation cross section
        Prompt photon imaging
        Advance Monte Carlo codes
Real time Monitoring
On-line determination of the dose delivered
First time in 110 years !
MC simulated
measured

## Slide 46
Proton Ion Medical Machine Study
PIMMS project at CERN (1996-2000)

## Slide 47
CNAO – Pavia Italy

## Slide 48
ISOLDE
Isotopes for detection and treatment
In collaboration with University Hospital Geneva
1.4 GeV protons from PS-Booster
GPS
HRS Target station
Beam lines

## Slide 49
Nuclear
Reactions
Accelerators
          Circular
          Linacs
Radio-Isotopes production

## Slide 50
LINAC for Radio-Isotopes production

## Slide 51
LINAC for Radio-Isotopes production

## Slide 52
Radio-Isotopes for PET
Isotope
Maximum
Energy (MeV)
Range in H2O
(mm)
Half -time

## Slide 53
Thank you for your attention