## Slide 1: Crab cavity aperture and alignment
R. De Maria

## Slide 2: Crab cavity
Cavity aperture: circle 84 mm
Parallel pipe: circle 84 mm
Separation: 194 mm
Beam screen
needed in the parallel pipe
~ 2 m
cryomodule
Parallel beam pipe
Crab cavity side

## Slide 3: Crab Cavity Alignment
D2
Q4
+1.06 mm
-0.69 mm
D2
Q4
+3.31 mm
+0.47 mm
Parallel pipe will be will be misaligned with respect to the beam closed orbit.
Still margin (>5 mm in radius) to add a beam screen.
Crossing angle orbit is not zero in the in the center of the cavities.
IP offset implemented with orbit corrector generate orbit at the cavities in the opposite direction
Crosssing +-295 murad
Offset -2 mm
Cavities needs to be aligned on the closed orbit (potentially no margin left after alignment).

## Slide 4: Crab Cavity Aperture
Parallel pipe without beam screen
beta*=7.5 cm, 14.2 sigma with usual tolerance

## Slide 5: Protected Apertures
Δµx MKD-TCT [°] | Aperture [σ@2.5µm]
0-20 | 11.2
30 | 11.9
40 | 12.9
50 | 13.8
60 | 14.5
70-90 | 14.6
No TCT | 19.4
Injection | 12.6
Parameter | 7 TeV | 0.45 TeV
Radial CO [mm] | 2 | 
Mom offset | 2 10-4 | 
Dispersion | 0.1 | 
Beam size | 1.1 | 1.025
R. Bruce et al. CERN-ACC-2017-0051

## Slide 6: Aperture Margins: Round 15 cm, 12.5 σ
 | Bare | Mech | Beam | Crab | Offset
TAXS | 24.0 | 21.4 | 17.3 | 17.3 | 15.1
MQXFA.[AB]1 | 21.2 | 19.4 | 16.4 | 16.4 | 15.1
MQXF[AB]..[23] | 15.5 | 14.4 | 12.2 | 12.0 | 11.0
MBXF | 16.9 | 16.0 | 13.6 | 13.5 | 12.7
TAXN | 22.3 | 20.9 | 17.7 | 17.2 | 15.5
MBRD | 26.7 | 23.7 | 19.9 | 19.0 | 16.4
MCBRD | 29.2 | 26.3 | 22.1 | 21.2 | 18.3
TCLMB.4 | 24.9 | 23.3 | 19.0 | 18.0 | 14.7
MCBY[HV].[AB]?4 | 26.2 | 24.1 | 19.6 | 18.6 | 15.1
MQY.4 | 29.2 | 26.6 | 21.7 | 20.7 | 17.1
TCLMB.5 | 36.3 | 34.3 | 28.7 | 28.5 | 25.2
MCBY[HV].[AB]?5 | 37.5 | 35.3 | 29.4 | 29.4 | 26.2
MQY.5 | 39.4 | 37.1 | 31.0 | 31.0 | 27.9
TCLMC.6 | 37.0 | 34.4 | 28.1 | 28.1 | 25.6
MCBC[HV].6 | 38.2 | 35.9 | 29.4 | 29.4 | 27.2
MQML.6 | 38.6 | 35.8 | 29.3 | 29.3 | 27.1
θc= ± 295 μrad;
dsep= ± 0.75 mm;
Aperture in σ at 2.5 μm/γ at 7 TeV
needs phase <=30° and slightly reduced margins

## Slide 7: Nominal crossing bump
Baseline closed in MCBY.4 (acby.4=0.2 acbrd)
D2
AB
Q4
AB
CD
CD
Crossing angle:
  x,y: ±1.15 mm (Beam 1, AB)
  x,y: ±(-0.5) mm (Beam 2, AB)
  For cryomodules:
  average offset 0.3 mm
  shear 1.65 mm
Impact on crab cavity alignment
Beam 1
Beam 2

## Slide 8: Orbit knobs - offset
Beam 1
Beam 2
IP Offset knob: x,y= ±2 mm same for the two beams to accommodate alignment needs of the experiments with machine realignment, besides crab cavities.
D2
AB
Q4
IP offset:
  x,y: ±3.4 mm (Beam 1, CD),
  x,y: ±1mm (Beam 2, CD),
  For cryomodules:
  avg. offset 2.2 mm
  shear 2.4 mm
AB
CD
CD

## Slide 9: Correctors Budget requirements
Correct quadrupole misalignments and dipole tilt and transfer function errors:
  uniformly distributed, uncorrelated error distribution (2 σ cut in the strengths):
    quadrupoles triplets and arc: 0.5 mm max transverse displacement, 1 mrad max roll
    dipoles D1, D2 and arcs: 10 mm max longitudinal displacement, 0.5 mrad max roll, 0.2% max field error
  Reduced estimates compared with LHC design (worst case) based on LHC experience
Adjust the IP position limiting the realignment of HW components (crab cavities only):
  offset in H/V planes: ±2.0 mm
Align beam in the crab cavities in both planes:
  Adjust for average offset and separation (±0.5 mm) between cavities in Beam 1 and Beam 2.
  Adjust for average offset between cavities of the same beam but in different cryomodules (±0.25 mm, relevant for 4 cavities per beam per plane per side).
For the Right and Point 1 symmetries apply:
Left B1 -> Right B2,
Left B2 -> Right B1
H Point 5 -> V Point 1