## Slide 1: Liquid-Noble Bubble Chambers Prospects for neutrino and WIMP detection
Eric Dahl, Northwestern University
COFI seminar
July 13, 2017

## Slide 2: Outline
Motivation: GeV WIMPs and reactor neutrinos
The scintillating bubble chamber technique
  On Paper
  In Practice
First Results from a 30-gram xenon prototype
Lowering thresholds – current status
arXiv:1702.08861 [PRL 118, 231301]

## Slide 3: What could you do with a liquid-noble bubble chamber?
Discriminating
  Only sensitive to nuclear recoils (neutrons, neutrinos, and WIMPs)
Scalable
  Largest bubble chamber to date: 35 m3 (BEBC)
  Ton-scale low-background bubble chamber in works (PICO)
Low threshold?
  Sub-keV recoil energy threshold is moving from “plausible” to “realistic”

## Slide 4: What could you do with an argon bubble chamber?
1 ton-year at 1-keVr threshold
(76 8B neutrino events expected)
(DRAFT of upcoming Cosmic Visions white paper)
Up to an event-per-minute in a m3 target,
Only background is neutrons

## Slide 5: Bubble Chambers
Superheated Target
  CF3I, C3F8, …
Particle interactions nucleate bubbles
Cameras and acoustic sensors capture bubbles
Chamber recompresses after each event

## Slide 6: Bubble Chambers
Superheated Target
  CF3I, C3F8, …
Particle interactions nucleate bubbles
Cameras and acoustic sensors capture bubbles
Chamber recompresses after each event

## Slide 7: Scintillating Bubble Chambers
Superheated Scintillator
  Xe, Ar, C6F6, …
Particle interactions nucleate bubbles and produce scintillation
Cameras and acoustic sensors capture bubbles and photodetectors collect scintillation light
Chamber recompresses after each event
PMT
PMT
PMT
PMT

## Slide 8: Bubble Chamber Thermodynamics
What is a meta-stable state?
Superheated Liquid

## Slide 9: Bubble Chamber Thermodynamics
Consider a bubble with
  Tl = Tb (thermal equilibrium)
  ml = mb (chemical equilibrium)
Then Pb is (approx) the vapor pressure at temperature T
Pb > Pl , so bubble should grow… until we consider surface tension
Pl, Tl
Pb, Tb
Ps

## Slide 10: Bubble Chamber Thermodynamics
Inward pressure from surface tension!
  Ps = 2s/r
Bubble will grow if
  Pb > Pl + Ps
  r > rc = 2s / (Pb – Pl)
Bubbles with r < rc collapse and re-condense
Pl, Tl
Pb, Tb
Ps

## Slide 11: Bubble Chamber Thermodynamics
What does it take to produce critical bubble?
Pl=30 psia, Tl=14oC
Pb= 89.7 psia
C3F8
rc=23.7nm
1.81 keV
-0.15 keV
1.53 keV
Surface energy, Bulk energy, Reversible Work
= 3.19 keV total

## Slide 12: Bubble Chamber Discrimination
Electron recoil sensitivity in C3F8 and CF3I from various PICO calibration and dark-matter chambers

## Slide 13: Nuclear Recoil Threshold
Neutron Calibrations in C3F8 @ ET = 3.2 keV

## Slide 14: Bubble Chamber Backgrounds
All bubbles look the same!
  1-mm diameter bubble has drawn 10 PeV from superheated fluid
  Nuclear recoil visually indistinguishable from alpha-decay
C. Amole et al. Phys. Rev. D 93, 061101(R) (2016) [arXiv:1601.03729]
214Po
(7.7 MeV)
222Rn, 218Po
(5.5, 6.0 MeV)
Nuclear Recoils
(3-500 keV)
~1-MeV energy resolution in acoustic channel
10 keV
6 MeV

## Slide 15: Bubble Chamber Backgrounds
C. Amole et al. Phys. Rev. D 93, 061101(R) (2016) [arXiv:1601.03729]
ALL of these are easily identifiable with scintillation signal
More information always key to background discrimination
1 MeV
100 eV
6 MeV
Eliminated via
Acoustics
Eliminated via particulate control measures,
removal of buffer fluid

## Slide 16: Scintillating Bubble Chamber History
Glaser built a xenon bubble chamber in 1956 and found:
  No bubbles in pure xenon even at ~1 keV threshold (with gamma source)
  Normal bubble nucleation in 98% xenon + 2% ethylene (scintillation completely quenched)
Phys.Rev. 102, 586 (1956)

## Slide 17: Scintillating Bubble Chamber History
Scintillation suppresses bubble nucleation!
  Electrons should be even less likely to make bubbles than in freon chambers
  Greater superheat (lower thresholds) possible
  Nuclear Recoils should be largely unaffected, thanks to Lindhard Effect
Phys.Rev. 102, 586 (1956)
Experimental verification needed!

## Slide 18: NU Xenon Bubble Chamber Schematic

## Slide 19: NU Xenon Bubble Chamber Model
NU Prototype
  30-gram xenon target
  No buffer fluid
  30-psia, –50oC superheated state
  IR illumination for cameras
  IR-blind PMT (R6834) for 175nm scintillation

## Slide 20: NU Xenon Bubble Chamber
First Bubbles June 2016
June 2015
Sept 2015
Feb 2016
April 2016

## Slide 21: Sample Nuclear Recoil Event
z
z

## Slide 22: Annulus Boiling

## Slide 23: NU Xenon Bubble Chamber v 2.0
¼” Sapphire Window
(Blackbody absorber)
Minimum ET decreased from 30 keV to 4 keV

## Slide 24: Sample Nuclear Recoil Event
z
z
Dt

## Slide 25: Acoustic – Scintillation Coincidence
< 1% accidental coincidence rate in calibration data
Slope = speed of sound in xenon (to 20%)

## Slide 26: Light Collection
57Co calibration (122-keV photo-peak)
No bubbles over background rate
Same signal in normal and superheated states
Poor resolution due to position dependence
Average 1 phe per 25 keVr (0.4% photon detection efficiency)

## Slide 27: Gamma Rejection
Without scintillation, xenon would be slightly worse than CF3I
Xe

## Slide 28: Nuclear Recoil Efficiency
Can determine nuclear recoil bubble nucleation threshold from bubble rate and multiplicity as before…
  252Cf not the best source for this
  Not many multi-bubble events in small chamber
2 doubles, 160 singles at ET=8.2 keV
  Recoil energy threshold 19 ± 6 keV
Check with scintillation channel!

## Slide 29: Scintillation Spectrum for Bubble Events
ET = 8.2 – 8.6 keV
ET = 8.6 – 15 keV
*Simulation assumes 15-keV threshold for bubble nucleation
Bubbles with no PMT Trigger
No ET dependence observed in other bins
*

## Slide 30: NU Xenon Bubble Chamber v 3.0
Removed inner jar to eliminate narrow (.5mm) annular region
Minimum ET decreased from 4 keV to 0.8 keV (and still falling…)
–43 oC

## Slide 31: Gamma Rejection
Turns out Glaser wasn’t kidding about gammas not making bubbles in xenon…
Xe
PRELIMINARY

## Slide 32: Nuclear recoil sensitivity
Threshold analysis ongoing at ET=1.0 keV
  Much larger 252Cf exposure to work with
    Determine threshold from bubble multiplicity
    Position corrections for scintillation signal from 40-keV inelastic scatters -> higher resolution in scintillation channel
  207Bi-9Be (g,n) source
    97 keV neutrons (max 3.0 keV recoil)
    Source is weak, but may see rate over background (and over bare 207Bi gamma source)
  Will soon have higher-activity (g,n) sources
  Meanwhile, just began data taking at ET=0.8 keV

## Slide 33: Next Steps
Low-threshold calibrations in xenon (summer/fall)
  Easy reconfig to get to -40oC (ET=0.5 keV)
  New gamma-n sources coming
  Lots of analysis, simulation work coming to nail down recoil threshold
Switching to argon (fall/winter/spring)
  New thermal control scheme (same cryostat)
  Waveshifter deposition on jar (w/o obscuring images)
R&D for larger detectors (anytime…)
  Need pressure-resistant photo-detector system compatible with camera illumination and immersion in hydraulic fluid (e.g. CF4) (SiPM’s very likely candidate…)
  Site selection and background sims for future proposals

## Slide 34
Funding:
  Department of Energy Award DE-SC0012161
Paper:
  arXiv:1702.08861 [PRL 118, 231301]
Jianjie Zhang
Miaotianzi Jin
Dan Baxter
Jon Chen
Dylan Temples
Our Group

## Slide 35
Funding:
  Department of Energy Award DE-SC0012161
Paper:
  arXiv:1702.08861 [PRL 118, 231301]
Jianjie Zhang
Miaotianzi Jin
Dan Baxter
Jon Chen
Dylan Temples
Our Group

## Slide 37: Summary
Scintillating bubble chambers work!
  Confirmed coincident scintillation and bubble nucleation by nuclear recoils
  Electron discrimination better than in freons (still finding out out how much better…)
  Low-threshold performance looking very promising, stay tuned (or jump in!)

## Slide 38: Annulus Boiling

## Slide 39: “Bright” event (Muon track with nuclear recoil)
0.2 phe/keVee, from 57Co 122-keV gamma calibration

## Slide 40: “Medium Bright” Event (alpha-decay candidate)
0.2 phe/keVee, from 57Co 122-keV gamma calibration

## Slide 41: “Dim” Event (nuclear recoil)
0.2 phe/keVee, from 57Co 122-keV gamma calibration

## Slide 42: Gamma Discrimination
Without scintillation, we would expect poorer discrimination in xenon than CF3I
Xenon (90% CL, no bubbles from gammas so far)

## Slide 43: Ongoing R&D
Lower thresholds (higher superheat)
  Look for gamma sensitivity
  Precision nuclear recoil calibrations
Alternate targets
  Argon
    Hydraulics -> pneumatics
    Expect better gamma-discrimination than xenon
  Organic scintillators
    Superheated fluid -> supersaturated gas+liquid solution
    Many light-nuclei available (C, F, H)