## Slide 1: HOM power in RF cavities of FCC-ee rings (old and new parameters)
Ivan Karpov
Acknowledgments: O. Brunner, A. Butterworth, R. Calaga, J. F. Esteban Müller, R. Rimmer, N. Schwerg, E. Shaposhnikova, D. Teytelman
FCC RF R&D coordination meeting 15 27.09.2017

## Slide 2: HOM power loss calculations
Simulated cavity
impedance
Normalized
Fourier harmonics
of beam current
– average beam current
– revolution frequency
– revolution harmonic number
Estimations of the power loss are required to determine parameters for high order mode (HOM) absorbers.

## Slide 3: Recap on the progress
Power losses were evaluated for all FCC-ee machines (Z, W, H, ) and different cavity designs (single cell, two cells and four cells)
  The highest power loss from continuous cavity impedance spectrum is for the Z machine a single-cell design is preferable. around 2kW can be extracted using several HOM couples (max 1kW/coupler);
  For other machines it is below 1kW
Contribution of taper impedance can be reduced using proper taper dimensions (length of 3m for 12 ps bunches and transitions for beam pipe radii from 15 cm to 5 cm)
Different filling schemes were analyzed for the Z machine
  Critical cases were identified for the single-cell cavity design (a spectral line hits HOM below cut-off frequency) filling schemes which should be avoided in operation were determined
Calculations for new parameters were performed

## Slide 4: Parameters for Z machine
Parameter | Old | New
Beam current, [A] | 1.4 | 1.385
Bunch population, | 0.4 × 1011 | 1.5 × 1011
Bunch length (in collision), [ps] | 7 (12) | 12 (37)
Number of bunches, | 71200 | 18800
Total RF voltage, [MV] | 255 | 100 (?)
RF frequency, [MHz] | 400.79 | 
Harmonic number, | 130680 | 
Parameter | Old | New
 | 1.4 | 1.385
 | 0.4 × 1011 | 1.5 × 1011
 | 7 (12) | 12 (37)
 | 71200 | 18800
 | 255 | 100 (?)
 | 400.79 | 
 | 130680 | 
For new parameters the bunch spacing can be different due to a smaller number of bunches ( = 2.5 ÷ 15 ns)
Smaller RF voltage – to be studied

## Slide 5: LHC-like layout of cryomodule
Taper length,
Taper-out
Taper-in
mm
mm
Axisymmetric structure
+
Gaussian bunch
Wake potential
Impedance
Impedance calculation using ABCI
400 MHz LHC cavities with modified shape (input from R. Calaga)

## Slide 6: Single-cell cavity impedance
“Continuous” spectrum
Cut-off frequency
HOM
Fundamental mode
HOM parameters: MHz, (CST EMS simulations)
Only one mode below cut-off frequency can affect power losses
1/e – decrease of the
beam spectrum,
New (in collisions)
Old (in collisions)

## Slide 7: Beam spectrum for different filling schemes
Abort gap,
Bunch trains
Train spacing,
Spectrum is dominated by:
lines (always present)
+ lines (depending on number of trains)
Bunch spacing,

## Slide 8: Power loss above cut-off frequency
Power loss is moderate for the present cavity design for bunches in collisions
There is a weak dependence on train spacing and bunch spacing
Old parameters + collisions on
Constant parameters: total current ≤ 1.4 A, abort gap length, bunch population
Variable parameters: number of bunches in the train, number of trains, train spacing
Old parameters

## Slide 9: Impedance below 3 GHz
For CST
Four single-cell cavity displaced by 3λ/2 + 3 m long tapers from 15 cm to 5 cm
There are still a few modes below cut-off frequency of the cavity with high R/Q.
Higher frequency HOMs have small R/Q values

## Slide 10: Power loss for HOM below cut-off frequency
Power losses of few 100 W are for small + “resonant” cases with high
Damping of the mode for longitudinal stability should moderate
Resonant cases should be identified
Longitudinal coupled-bunch instability growth rate
If stability
– growth time
– radiation damping time
– slip factor
– beam energy
– synchrotron tune
Stability threshold for 1 MV/cavity accelerating gradient
For new parameters
MHz,

## Slide 11: Shift of the resonant frequency
→ There are many cases when the spectrum line hits the resonant line → Not all of them are dangerous
“Resonant” condition

## Slide 12: Power losses for old parameters
Damped HOM is not dangerous if
Calculation parameters:
Constant total current
Abort gap length
Bunch population
Max power extracted by a single HOM coupler

## Slide 13: Power losses for new parameters
More values of train spacing should be avoided in operation
Strong power losses for 7.5 ns and 10 ns bunch spacings

## Slide 14: More “general” case
Operation settings define recommendations for the cavity design (position of HOMs)
Safe
Dangerous
Acceptable frequencies

## Slide 15: Summary of power loss for a single-cell cavity design for the Z machine
Contributions from continuous spectrum:
  Power losses are around 2 kW and 3 kW for old and new parameters, correspondingly (bunches are in collisions).
  Taper length can be reduced for new parameters
Below cut-off frequency there is one HOM with high R/Q (can split in 4 modes for the full structure) that can significantly contribute to power losses
Critical filling schemes were identified and should be avoided in operation for the given cavity design
For new parameters:
  For the single-cell cavity design 7.5 ns and 10 ns bunch spacings are not feasible
  Other bunch spacings can be used, but some particular filling schemes () should be avoided in operation
  HOM frequency ranges for new cavity designs which are “safe” for all bunch spacings were identified

## Slide 16: Thank you for your attention!

## Slide 17: Contribution of tapers
If distance between tapers >> , contributions of taper-in and taper-out are compensated for
For , impedance of step transition at high frequencies
Transition region from to depends on taper length.

## Slide 18: FCC-ee options
 | Z | W | H | 
Bunches / beam, | 71200 | 6000 | 740 | 62
Bunch spacing, [ns] | 2.5 | 50 | 400 | 4000
Bunch population, | 0.4 × 1011 | 0.5 × 1011 | 0.8 × 1011 | 2.1 × 1011
Bunch length, [ps] | 12 | 8.3 | 7.7 | 9.2
Beam current, [mA] | 1399 | 147 | 29 | 6.4
 | Z | W | H | 
 | 71200 | 6000 | 740 | 62
 | 2.5 | 50 | 400 | 4000
 | 0.4 × 1011 | 0.5 × 1011 | 0.8 × 1011 | 2.1 × 1011
 | 12 | 8.3 | 7.7 | 9.2
 | 1399 | 147 | 29 | 6.4
Harmonic number, = 130680
Ring circumference, = 97.75 km