## Slide 1: Gaseous and dual-phase time projection chambers for imaging rare processes
Diego Gonzalez Diaz, Francesc Monrabal, Sebastien Murphy
26/09/2017
*link to appear in arXiv soon
(60 pages, 450 references)

## Slide 2
from scopus (efficiency and purity of selections verified to be within 20%)

## Slide 3
ALICE
NEXT-NEW
DUNE Far Detector
(dual phase prototype)
LUX
AT-TPC
DarkSide-50
…
*many more in text

## Slide 4
…
*more in text

## Slide 5
A generic TPC for rare event searches
A generic image formation process in a TPC
Aimed at complex topologies and maximal collection
of event information.
Seamless! (no beam pipe).
Usually no space-charge issues.
No ageing issues (interaction rate is low).
Radiopurity issues (in some cases).
B-field seldom found.
point spread function
impulse response function

## Slide 6
TUNL TPC
[photo-dissociation of 12C
into 3 α tracks]
DMTPC-related R&D
(214keVr F nucleus)
Warsaw TPC
[β-delayed proton emission from 46Fe]
NEXT-MM
(1.25MeV e-)
HARPO
(pair production by 74.3GeV photon)
AT-TPC
(α-α scattering)
DMTPC-related R&D
(~30keV e-)
DUNE-FD R&D
(cosmic ray- induced
nuclear breakup
ILC-related R&D
(low energy e-)
…
*more in text

## Slide 7
Aim: reconstruct the effective position at various track segments and
develop a track model (to obtain curvature and vertex)
Topology reconstruction in collider/tracker TPCs
Position ‘resolution’ is paramount (pixel size is not!). Typical: few 100’s μm.
Ambiguities due to high track multiplicity enforce pixel/pad-based (3D) readout.
T0 obtained from trigger.
(e.g., for conventional Micromegas)

## Slide 8
(frequent) aim: reconstruct the energy loss path with high accuracy (to obtain particle(s) type, direction and energy, and event multiplicity)
Fine track sampling and energy resolution is paramount (fine-pitch readout and high S/N needed).
Low track multiplicity can allow 2D+2D o 2D+1D readouts but small pitch relative to track size is essential.
T0 often obtained by additional means! (scintillation, minority carriers)
Topology reconstruction in rare event TPCs
xy projection
z projection
signal
background

## Slide 9
Problem: tracks are usually not contained and Landau fluctuations dominate
Energy reconstruction in collider/tracker TPCs
A popular phenomenological formula by Walenta, Allison
and Cobb (still in use):
T2K-TPC

## Slide 10
Advantage: tracks are usually contained and Landau fluctuations are absent!
xy projection
z projection
Energy reconstruction in rare event TPCs

## Slide 11
charge recombination
Landau fluctuations
(some) other primary processes
Primary processes of interest
photo-ionization
P~10bar
density
ionization ‘quenching’
scintillation ‘quenching’
Fano fluctuations
scintillation mechanisms and wls
IR emission (1250nm) for Xe and Ar+Xe.
Heat (bubble-formation of low energy nuclei recently demonstrated in liquid xenon).
Negative ions formation.
Positive ions formation.
Appearance of daughter nuclei in nuclear reactions (e.g., 136Ba in 136Xe).
Jesse effect / Penning transfers

## Slide 12
Technical problems /enabling assets
energy resolution and sensitivity limits
HV
cryogenics
light transparency/collection
VUV-quenching
attachment / purification
(Ar gas)
(Ar liquid)
contained events
uncontained events
fluctuations during multiplication
readout layout and electronics
simulation tools

## Slide 13
Gas magic I (pressure dependencies)

## Slide 14
Gas magic II (gas mixture)
argon mixtures

## Slide 15
Ionization detection (I): multiplication in quenched gases
maximum gain decreases the heavier
the noble gas
maximum gain increases the lower
the charge density
results consistent with an overall charge density limit ~2x109 e/mm2
(see also P. Gasik’s presentation at WG2)

## Slide 16
Ionization detection (II): operation under extreme conditions
ultra-pure argon
‘pure’ SF6 at 40mbar!
‘pure’ helium

## Slide 17
Ionization detection (III): secondary scintillation
electroluminescence
avalanche scintillation
uniform field
3-GEM

## Slide 18
some paradigmatic examples

## Slide 19
Active targets
ACTAR TPC
AT-TPC
…
General-purpose TPC for reaction (but also decay) studies, with a size of 25cm x 25cm x 25cm.
High density readout (2mm x 2mm pixels) with gas-tight punch-through pins for socket connection.
Micromegas readout.
16384 channels.
Operation from -1 to 3 bar.
Makes use of the AGET chip.
Under commissioning.
General-purpose cylindrical TPC for reaction studies in a variety of gases (H2, He, Ar, CO2…) with a size of 100 cm x π302 cm.
At FRIB in Michigan.
10240 radial pads.
Microbulk Micromegas readout.
Makes use of the AGET chip.
Magnetic field available up to 2T.
Can be tilted (!).
Running.
*more in text

## Slide 20
Decay/implantation
Warsaw TPC
General-purpose TPC for decay studies, with a size of ~(20 cm)3.
2D+1D readout (CCD camera + PM).
~100μm equivalent pixel size at the object plane.
Operation at ~1bar.
(Ar)+He+N2+(CH4).
Scintillation generated via a 4-GEM structure.
Running since around 10y.
2p-decay (45Fe)

## Slide 21
Neutrino-less double beta decay
NEXT phase-I 10bar-TPC for the measurement of ββ0 in 136Xe, with a size of ~ 50 cm x π202 cm2.
Double readout: PM (3inches) + SiPM (10mm-pitch).
Optical TPC operated in electroluminescent mode.
Radiopure.
Running at Laboratorio Subterraneo de Canfranc (LSC).
NEXT-NEW

## Slide 22
DRIFT
Negative-ion (CS2+O2) 1m3 wire-based TPC at ~50mbar.
50μm voxel-size in z-direction (much coarser in x,y directions).
Radiopure.
Running at Boulby mine.
*see talk of K. Miuchi at WG2 as well
DMTPC
nucleus in CF4
About 1m3 optical-TPC at ~100mbar of pure CF4.
Scintillation produced with meshes.
Double CCD+PM readout.
Radiopure.
Scheduled to run at SNOLab in 2017.
Directional Dark Matter detectors

## Slide 23
CAST
Solar axions
3x6x6cm3 mini-TPC for solar axion detection (via conversion to ~3keV x-rays), in Ar/i-C4H10 at 1.4bar.
Microbulk Micromegas (x-y readout, 500μm-pitch).
InGrid readout (50μm-pitch).
Radiopure.
Just ended.

## Slide 24
Near-Detectors in ν-oscillation experiments
3-module tracker for the ND of the T2K oscillation experiment.
Each module’s size ~2.5 x 2.5 x 1 m3.
Pad-readout (1cm x 1cm).
First implementation of bulk Micromegas in a large particle physics experiment.
Magnetic field at around 0.2T for PID.
Makes use of the AFTER electronics.
Running since 2010.
T2K-ND

## Slide 25
Far-Detectors in ν-oscillation experiments
5ton detector
Recent results!
(see talk by S. Murphy)
DUNE-FD

## Slide 26
Xenon-based Dark Matter detectors (not directional)
Several dual-phase TPCs (LZ, PandaX, Xenon-1t) approaching the 1m3 active volume.
Very similar technology in all 3 cases.
Double PM plane.
Extraction from liquid to gas and electroluminescence achieved with meshes.
Excellent reflectivity of Teflon panels (>95%).
Single electron identification capability.
Electron and nuclear recoils well separated when considering ionization (S2) and scintillation (S1) signals.
Radiopure.
Running through successive upgrades since about 7years.
PANDAX, LZ, XENON-1T

## Slide 27
Argon-based Dark Matter detectors (not directional)
DarkSide50
DarkSide: Dual-phase argon TPC with size 35 x π0.1782 cm3.
Based on underground argon, for the first time!.
Double PM plane.
Extraction from liquid to gas and electroluminescence achieved with meshes.
Surfaces coated with TPB to allow detection of Ar-light.
Electron and nuclear recoils well separated when considering ionization (S2) and scintillation (S1) signals.
Prevalence of singlet component in the scintillation signal of nuclei allows to suppress electron backgrounds to ppms.
Radiopure.
Running since recently.

## Slide 28
TREX-DM
Ar-DM
NEWAGE
Other TPCs
NEWS
Mu-Cap
…
*more in text

## Slide 29
columnar recombination
bubble-assisted scintillation
Other ideas
barium tagging with laser
positive ion TPC
low diffusion electroluminescent TPC
direct charge detection
bubble-chamber TPC
barium tagging via SMFI
…
*more in text

## Slide 30
Conclusions
thanks!