## Slide 1
Plasma Accelerators / Compact Accelerators
Ralph W. Assmann (DESY)
Coordinator EuPRAXIA Lead Scientist DESY Accelerator R&D
African Conference on Fundamental Physics and Applications, or African Conference on Physics (ACP), June 28–July 4, 2018, Namibian University of Science and Technology (NUST), Windhoek Namibia
Can we broaden accelerator impact with compact and cost-efficient accelerators?
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.

## Slide 2: Particle Accelerators: Discovery Machines and Innovation Drivers
For Science, Industry and Society
Today: world-wide operate about 30,000 particle accelerators for science, medicine and industry
Most accelerators are used for industrial applications
Accelerators produced data for dozens of discoveries that were rewarded with nobel prizes.
Accelerators help saving lifes and curing people.
Physics: Cyclotron
Physics:
Stochastic
Cooling
Physics: Higgs particle
Chemistry: ribosoms

## Slide 3: Probing for New Particles and Forces
Fundamental Research Particle Physics
Higgs
Seminar
4.7.
2012
27 km LHC at CERN (Europe)
Understanding fundamental laws
LHC at CERN as a Masterpiece of Accelerator Science
Protons at 6 thousand billion electron Volt  27 km

## Slide 4: Producing X Rays for Inspection
Industry and Security
X-Ray radiography – Cargo inspection with a compact 6 MeV linear electron accelerator
Varian (USA)
Protecting people
Nuctech (China)
Electrons at 6 million
Electron Volt

## Slide 5: Irradiating and Destroying Tumor Cells
Medicine and Health
Heidelberg Ion-Beam Therapy Center (HIT)
Curing people
Varian TrueBeam STx Linac with BrailLab ExacTrac system at University Hospital Düsseldorf.
Proton therapy
Electron therapy
up to 12 million electron Volt

## Slide 6: Producing Light and Filming Molecular Movies
1900
2000
future
you are here
Lab-Based X-ray Sources
Synchrotron radiation
from accelerators
X-Ray Laser accelerators
+ High Brilliance SR accelerators
Locally Ordered Structures, Nonequilibrium Phenomena, Transient States
Era of Complex Matter
Era of Crystalline Matter
Ordered Structures, Equilibrium Phenomena, Phase Diagrams
Fundamental Research Physics, Structural Biology, Chemistry, Material Science
State of the art accelerators for the best light possible

## Slide 7: Particle Accelerators at DESY – Excellence in Photon Science
Hamburg (Germany): from 50 years ago to today (electrons up to 17 billion electron Volt)…
PETRA III
2010
FLASH
2005
4,2nm - 45nm
1,7nm 3rd harm
P3X Nord
2015
P3X Ost
2015/16
FLASH II
2015
variable gap U
NanoLab
DESY
1962
EU.XFEL
2017
FEL
1,25 GeV
SR
6 GeV
FEL
17,5 GeV
BUT:
Progress in Hamburg-based colliders limited by practical considerations on size and cost.

## Slide 8: Germany Today
Accelerator-Based Photon Science Research Affecting Everyday Life

## Slide 9: Germany Today
Accelerator-Based Photon Science Research Affecting Everyday Life
Mobile Phone
SAW Structures
Air Bag
Accelaration Sensors
MEMS
Cosmetics
TiO2 Nanoparticle
GMR Read Head
Magnetic
Multilayers
Bike Frame
Carbon Fibres
Composite Materials
Digital Camera
CCD Chip
Intelligent Credit Card
Integrated Circuits
LED Display
Photonic Materials
GPS Navigation
Functional Materials
Glasses and Coatings
Optical Materials
UV Filter
Artificial Lens
Biocompatible
Polymers
Artificial Hips
Biocompatible
Materials
Exact Time via satellite
Semiconductíng devices
Micro-Batteries
Pace Maker
Li-Batteries
New Materials for Energy
Taylored Materials at Work ….

## Slide 10: Frontier Electron Beams and Directions for New Beams
Towards ultra-dense, highest brightness electron beams
Increase kinetic energy of particles (MeV – GeV – TeV)
More particles per bunch (1 million – 100 billion)
Smaller transverse area (1 nm – 1 mm smallest diameter)
Shorter bunches for access to ultra-fast science (100 nm – 100 mm)
More bunches (1 – 1000)
MORE C O M P A C T TECH???
Transverse area
Length of bunch
(packet)

## Slide 11: Slow Down in RF and Invention of A New Technology
Complementing RF based Accelerators with Plasma Accelerators!?
27 km
100 km
100 m

## Slide 12: Slow Down in RF and Invention of A New Technology
Complementing RF based Accelerators with Plasma Accelerators!?
Shows potential of plasma acceleration for very high energies  HEP
27 km
100 km
100 m

## Slide 13: Slow Down in RF and Invention of A New Technology
Complementing RF based Accelerators with Plasma Accelerators!?
Shows potential of plasma acceleration for very high energies  HEP
Plasma acc. today in regime required for FEL’s  Photon Science!
27 km
100 km
100 m

## Slide 14: Slow Down in RF and Invention of A New Technology
Complementing RF based Accelerators with Plasma Accelerators!?
Shows potential of plasma acceleration for very high energies  HEP
Plasma acc. today in regime required for FEL’s  Photon Science!
Acceleration length (new versus conventional):
9 cm versus 100 m
27 km
100 km
100 m  9 cm

## Slide 15: Hamburg: ANGUS Laser Laboratory for Accelerator R&D
200 TW Ti-Sa laser from Thales, laboratory at DESY & University Hamburg
22 thousand billion Volt per meter
(“LHC energy in 30 cm instead of 27 km”  not really)

## Slide 16: The Plasma Accelerator Concept
Overcome high-field limitations of metallic walls with dynamic plasma structures (undestructible)
New idea in 1979 by Tajima and Dawson: Wakefields inside a homogenous plasma can convert transverse forces into longitudinal accelerating fields
Options for driving wakefields:
Lasers: Industrially available, steep progress, path to low cost Limited energy per drive pulse (up to 50 J)
Electron bunch: Short bunches (need mm) available, need long RF accelerator More energy per drive pulse (up to 500 J)
Proton bunch: Only long (inefficient) bunches, need very long RF accelerator Maximum energy per drive pulse (up to 100,000 J)
Pondero-motive force of a laser
Space charge force of a charged particle bunch (e-, p+)
or
Accelerating gradients of 10 GeV/m to 1,000 GeV/m
Courtesy M. Kaluza

## Slide 17: Plasma Acceleration
Internal injection
Works the same way with an electron beam as wakefield driver. But then usually lower plasma density. Ponderomotive force of laser is then replaced with space charge force of electrons on plasma electrons (repelling).
Like wakes left behind by a boat in water

## Slide 18: Plasma Acceleration
Internal injection
Like wakes left behind by a boat in water

## Slide 19: Plasma Acceleration
Internal injection  strong fields in the bubble suck in plasma electrons to form the electron beam
Like wakes left behind by a boat in water

## Slide 20: Plasma Acceleration
Internal injection (“bubble regime”)
Like wakes left behind by a boat in water

## Slide 21: Laser Plasma Accelerator for Electron Beams
“Bubble regime”, invented in Europe
Laser pulse
200 TW – 1 PW
Laser pulse
Electron beam
Plasma channel

## Slide 22: ...and it is really much smaller!
A few cm’s of plasma create as much energy as the 100 m long S.C. FLASH linac
Accelerator size becomes almost negligible!
Do not forget the size of the laser, which is the dominant size here:
Fit a 10 billion electron Volt accelerator in 300 square-meter laboratory instead of 500 meter long accelerator tunnel!
$
£
¥
€

## Slide 23: University Hamburg / DESY: LUX (A. Maier et al)
An laser-driven plasma R&D approach  towards FEL applications
About 400 MeV electrons from plasma accelerator, guide beam out of plasma, transport to undulator, generate X rays in undulator, dump electron beam, measure X rays (8 nm), first 24h operation. Latest: 1 GeV electron beam.
Next steps: towards harder X rays, lasing (saturation not possible in available length of undulator)
A. Maier et al

## Slide 24: The European Opportunity
EUROPEAN
PLASMA RESEARCH
ACCELERATOR WITH
EXCELLENCE IN
APPLICATIONS
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.

## Slide 26: EuPRAXIA Horizon2020 Design Study
European Plasma Accelerator Infrastructure with Pilot Users
Collaboration brings together:
  Big science labs: photon science, particle physics
  Laser laboratories: high power lasers
  International laboratories: CERN, ELI (associated)
  Universities: accelerator research, plasma, laser
125 scientists in our work list
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
Start: 1 Nov 2015
End: 31 Oct 2019
Deliverable: Conceptual Design Report
www.eupraxia-project.eu

## Slide 27: Collaboration of 40 institutes
From Europe, Asia and United States
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
16 EU laboratories are beneficiaries. 24 associated partners from EU, Europe, Asia and US contribute in-kind.

## Slide 28: Where is Africa in EuPRAXIA?
Missing an African Collaborator while we have Asian and US institutes involved
Inviting African groups to collaborate with us.
Compact, laser-based accelerators are a medium term way to build up scientific infrastructure and research in additional countries.
We will look for resources to fund such a work.
Examples for possibilities:
  Doctors interested in medical applications (defining your needs with us)
  Groups interested in 3D design of facilities and technical components (students can work in Africa on PC’s and software that we organize, addressing our problems)
  Groups interested to send young scientist for participating in our experimental work in Germany, then analyzing data in Africa.
  Groups interested in lasers and their operation.
Email to: ralph.assmann@desy.de

## Slide 29: Management Structure
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
Heads of Project and of Supervisory Boards
Steering Committee

## Slide 30: A European Strategy for Accelerator Innovation
Required intermediate step between proof of principle and production facility One accelerator unit!
PRESENT EXPERIMENTS
Demonstrating 100 GV/m routinely
Demonstrating GeV electron beams
Demonstrating basic quality
EuPRAXIA INFRASTRUCTURE
Engineering a high quality, compact plasma accelerator
5 GeV electron beam for the 2020’s
Demonstrating user readiness
Pilot users from FEL, HEP, medicine, ...
PRODUCTION FACILITIES
Plasma-based linear collider in 2040’s
Plasma-based FEL in 2030’s
Medical, industrial applications soon
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.

## Slide 31: EuPRAXIA Objectives
EuPRAXIA is a conceptual design study for a 5 GeV electron plasma accelerator
Address quality. Show plasma accelerator technology is usable
Show benefit in size and cost versus established RF technology
Note: EuPRAXIA will initially be low power and low wall-plug power efficiency
Baseline (10 Hz): 10s of Watt with ~ 1 mJ/photon pulse energy
Efforts with industry and laser institutes to improve rep. rate & efficiency (incorporate fiber-based lasers with 30 % efficiency)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.

## Slide 32: The 50 Billion Volt per Meter Linear Accelerator
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
RF injector
S-band linac
1 GeV
5 GeV
> 200 MeV
Laser-Driven Stages to 5 GeV
A

## Slide 33: The 50 Billion Volt per Meter Linear Accelerator
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
RF gun & S-band structures
PWFA
accelerator
X-band structures
1 GeV
500 MeV
> 200 MeV
Beam-Driven Stages to 1 GeV
B

## Slide 34: Targets in Facility Parameters
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
Overview of EuPRAXIA technical goals. Not self-consistent cases. Detailed and self-consistent parameter tables are available upon request.

## Slide 35: The EuPRAXIA Facility (Under Design)
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
RF and TW laser system
PW laser system
Plasma accelerator and user lines are on 1st level
RF and laser infrastructure are on 2nd level
~ 30 m

## Slide 36: Fits on the Parking Lot of the Hospital Copenhagen
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
Rigshospitalet Copenhagen
Illustrative example prepared for IPAC17 talk in Copenhagen

## Slide 37: Versatile – Designed for Multiple Applications
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
High Energy – Accelerator R&D – Photon Science – Material – Medical – Industrial

## Slide 38: Versatile – Designed for Multiple Applications
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
High Energy – Accelerator R&D – Photon Science – Material – Medical – Industrial

## Slide 39: Medical Imaging with Plasma Accelerators
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
Some Unique Advantages – Already Working Today – Too Slow at the Moment
2015 publication from J.M. Cole et al., John-Adams-Institute, UK: “Laser-wakefield accelerators as hard x-ray sources for 3D medical imaging of human bone”. Nature Scientific Reports 5, 13244 (2015)
Laser plasma based betatron X ray source

## Slide 40: Can the Facility REALLY Do ALL of This?
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
Another Advantage of Plasma Accelerators
PLASMA ACC.
capture
switch yard
transport
undulator
FEL
user area
diagnostic line
“HOPA”
user area
HEP
Medicine Industry
Material
PLASMA ACC.
PLASMA ACC.
capture
transport
PLASMA ACC.
capture
transport
LASER
RF Driver
Injector
Laser pulses distributed to “small” plasma accelerators to drive many applications!

## Slide 41: EuPRAXIA at SPARClab in Frascati
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.

## Slide 42: Impression of EuPRAXIA@SPARC_LAB at LNF
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.

## Slide 43: Hamburg Infrastructure – SINBAD
Under construction – will house laser-driven novel accelerators at DESY  ATHENAe project at DESY
Ex-DORIS

## Slide 45: Accelerator R&D Program of Helmholtz Association
Latest news: ATHENA project approved for 29.99 M€ investment.
Funded by Helmholtz strategic funding and BMBF “Pakt für Forschung”
Accelerator science as independent research

## Slide 46: Press and Public Understand the Huge Potential
Examples from Germany
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
“Can we have smaller machines?”
“Bigger, faster, more expensive: no way!”
“The tiny particle accelerator”
“Yes, we can!”

## Slide 47: Conclusions
Europe developing new high tech and compact accelerators
The long-term future is bright: there will be plenty of opportunities as technology advances!
EuPRAXIA Goals on 10-15 year time-scale:
  Demonstrate plasma-wakefield accelerated multi-GeV-scale electron beams with stability and quality sufficient for first pilot user experiments
  Contribute to the conception of new European accelerator facility
Compact accelerators broaden the use and benefits of accelerators for our societies, also opening new possibilities for Africa
We look for African collaborators and will try to find funds for supporting this...

## Slide 48: Thank you for your attention
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under grant agreement No 653782.
Looking for African collaborators
Email to: ralph.assmann@desy.de
Compact accelerators are a chance for everybody.
Plenty of things to do – we need your help!
Inviting African groups to collaborate with us.
We will look for resources to fund such a work.