## Slide 1
Medical accelerators
Marco Silari
CERN, 1211 Geneva, Switzerland
marco.silari@cern.ch

## Slide 2
Particle accelerators operational in the world
A. P. Chernyaev and S. M. Varzar, Particle Accelerators in Modern World, Physics of Atomic Nuclei, 2014, Vol. 77, No. 10, pp. 1203–1215.
Three main applications: 1) Scientific research, 2) Medical applications 3) Industrial uses
Medical applications

## Slide 3
Particle accelerators operational in the world
A. P. Chernyaev and S. M. Varzar, Particle Accelerators in Modern World, Physics of Atomic Nuclei, 2014, Vol. 77, No. 10, pp. 1203–1215.
Three main applications: 1) Scientific research, 2) Medical applications 3) Industrial uses
Medical applications
Chart: Particle Accelerators in Modern World
| 1968 | 1970 | 1989 | 1994 | 1998 | 2000 | 2004 | 2007 | 2009 | 2012 | 2014
Total | 2000 | 3000 | 6500 | 9700 | 13500 | 15000 | 18000 | 27500 | 30000 | 39500 | 41000
Industrial | 2000 | 2700 | 4000 | 4500 | 7500 | 8500 | 8500 | 17900 | 22500 | 25300 | 27000
Medicine | 306 | 2500 | 4200 | 4700 | 5200 | 8500 | 9650 | 11600 | 13000 | 14000
Science | 1000 | 1200 | 1200 | 1200 | 1200 | 1200 | 1200 | 1200

## Slide 4
Particle accelerators for medical uses
Production of radionuclides with (low-energy) cyclotrons
  Imaging (PET and SPECT)
  Therapy
Electron linacs for conventional radiation therapy
  Including advanced modalities
Medium-energy cyclotrons and synchrotrons for hadron therapy with protons (250 MeV) or light ion beams (400 MeV/u 12C-ions)
  Accelerators and beam delivery

## Slide 5
The cyclotron – The work horse for radionuclide production
Scanditronix MC40

## Slide 6
J. Long, “The Science Creative Quarterly”,scq.ubc.ca
Mini-Cyclotron
Radiochemistry
PET camera
Positron Emission Tomography (PET)

## Slide 7
The rationale of radiation therapy
Treatment planning and dose delivery to tumour volume

## Slide 8
Past radiation therapy equipment
Radiation therapy is much more than the radiation source. One also needs:
diagnostic equipment, CT scanners
treatment planning software
patient set-up devices
computers
a broad range of professional figures
Co-60 unit
45 MeV Betatron
Photo: Wikipedia

## Slide 9
Medical electron linacs
e– + target  X-rays
target
Varian Clinac 1800
Multi-leaf collimator
Energy: 6-25 MeV
Dual e─ / g beams
Courtesy Varian Medical

## Slide 10
Cyber-knife robotic surgery system
http://www.accuray.com/Products/Cyberknife/index.aspx
6 MV Linac mounted on a robotic arm
No flattening filter
Uses circular cones of diameter 0.5 to 6 cm
Non-Isocentric
Average dose delivered per session is 12.5 Gy
Dose rate @ 80 cm = 400 cGy/min

## Slide 11
Intra-operative radiation therapy (IORT)
Small electron linac
Energy 6 – 12 MeV
Treatment with electrons only
Single irradiation
Three models of linac from three manufacturers

## Slide 12
Helical tomotherapy
www.tomotherapy.com
Integrated CT guidance
  Integrated CT scanner allowing efficient 3D CT imaging for ensuring the accuracy of treatment
A binary multi-leaf collimator (MLC) for beam shaping and modulation
A ring gantry design enabling TomoHelical delivery
  As the ring gantry rotates in simultaneous motion to the couch, helical fan-beam IMRT is continuously delivered from all angles around the patient
  Very large volumes can be treated in a single set-up

## Slide 13
Hybrid MRI linac

## Slide 14
Volumetric Modulated “ARC” Radiation Therapy
Rotate linac gantry while modulating the beam
Fixed 6 or so gantry angles
VMAT
Name-Prof Peter Metcalfe
BSOC lecture 08

## Slide 15
Particle therapy (hadron therapy)
Courtesy INFN, Italy

## Slide 16
Treatment planning

## Slide 17
Cyclotrons, synchrotrons and gantries for proton therapy
Accel-Varian
(superconducting cyclotron)
Hitachi synchrotron
IBA cyclotron
IBA proton gantry

## Slide 18
The LLUMC proton synchrotron
Loma Linda University Medical Center

## Slide 19
PROSCAN at Paul Scherrer Institut (PSI), Switzerland
ACCEL
SC cyclotron
250 MeV protons
Courtesy PSI and U. Amaldi , TERA
J.M. Schippers et al., NIM BB 261 (2007) 773–776

## Slide 20
Proton versus carbon-ion synchrotrons
G. Coutrakon, Accelerators for Heavy-charged-particle Radiation Therapy,
Technology in Cancer Research & Treatment, Volume 6, Number 4 Supplement, August 2007
Hitachi proton synchrotron Siemens ion synchrotron

## Slide 21
National Centre for Oncological Hadrontherapy, CNAO, Italy
Ion sources
Low Energy Beam Transport components
Injector linac
Courtesy S. Rossi, CNAO
Dipole magnets
RF cavity
Quadrupole magnets

## Slide 22
Mevion Medical Systems – single room facility
Synchrocyclotron

## Slide 23
Multi-room versus single-room facilities
29 m (87ft)
14 m (41 ft)
13 m (39 ft)
Other Proton Systems
28 m (84 ft)
812 m2
182 m2
2,240 m2
714 m2
Courtesy L. Bouchet, Still River Systems
Advantages of single-room facility:
Modularity
Reliability / back-up
PT treatment available at more hospitals
(Hopefully) cost

## Slide 24
Availability of radiation therapy worldwide

## Slide 25
Challenges and expected developments in radiation therapy
September 2015
https://indico.cern.ch/event/560969/
CERN-ICEC workshop, CERN, November 2016
CERN-ICEC-STFC workshop, CERN, October 2017
https://indico.cern.ch/event/661597/

## Slide 26
Global cancer burden and need for radiotherapy
According to estimates made by the International Agency for Research on Cancer (IARC), there are about 15 million new cancer cases per year worldwide, of which two thirds occur in developing countries.
IAEA, Setting up a radiotherapy program, 2008
Need for
qualified professionals (radiation oncologists, medical radiotherapy physicists, radiotherapy technicians, radiation protection officers, maintenance engineers, etc.)
development of medical infrastructure for cancer treatment
The age distributions of cancer are, however, quite different between developed and developing countries; there are significantly more cancer cases in childhood, adolescence and young adults in developing countries, while cancer in the elderly dominates in developed countries

## Slide 27
Challenges in Radiation Therapy in Africa
Technology
23 of 54 countries have teletherapy services
20 had high- or low-dose brachytherapy resources
293 radiotherapy machines serving 1 billion individuals
1 machine per 3.6 million people
Abdel-Waheb et al, Lancet Oncology, 2013 / Grover et al, Front in Oncology, Jan 2015 / Balogun et al, Radiation Oncology, Aug 2016
Taken from Surbhi Grover’s lecture at the CERN-ICEC-STFC workshop, CERN, October 2017
Human resources
a gap of 7,500 oncologists, 6,000 physicists and 20,000 technicians in LMICs (in Africa: 1600 medical oncologists, 1000 medical physicists and 4000 technicians)
Taken from Andras Fehervary’s lecture at the CERN-ICEC workshop, CERN, November 2016

## Slide 28
RT resources needed in 20 years from now
Taken from Mary Gospodarowicz’s lecture at the CERN-ICEC workshop, CERN, November 2016
LMICS = Low Medium Income Countries

## Slide 29
Developing RT for challenging environments
Linacs
Ability to operate in a difficult environment
  Interruptions in electricity / power supply
  Heat / problem with temperature control
  Dust and humidity
Highly modular, so that faulty parts can easily be replaced
Self-diagnosing, in case of accelerator malfunctioning
Low power consumption
…
Screening
Improve screening and early diagnosis to make RT more effective
Need for
Qualified professionals: radiation oncologists, medical radiotherapy physicists, radiotherapy technicians, radiation protection officers, maintenance engineers, etc.
Related training programmes
Development of medical infrastructure

## Slide 30
Guidelines