## Slide 1: Machine Aspects of Future pp Colliders
Work supported by the European Commission under the HORIZON 2020 project ARIES, grant agreement 730871
Frank Zimmermann
CERN, Pisa School on Future Colliders

## Slide 2
LHC: today’s frontier collider
excellent performance at Ecms=13 TeV

## Slide 3
very large circular hadron collider - only feasible approach to reach 100 TeV c.m. collision energy in coming decades
access to new particles (direct production) in few-TeV to 30 TeV mass range, far beyond LHC reach
much-increased rates for phenomena in sub-TeV mass range → much increased precision w.r.t. LHC
energy frontier in ~25 years
circular hadron collider energy reach
cf. LHC: factor ~4 in radius, factor ~2 in field  O(10) in Ecms
M. Mangano

## Slide 4
why not build a linear hadron collider?

## Slide 5
ILC real-estate gradient:
250 GeV/11 km ~23 MeV/m
length of a 100 TeV linear collider
based on ILC technology:
100 TeV/(23 MeV/m) > 4000 km !
for me it is clear, we need a circular tunnel

## Slide 6
international FCC collaboration (CERN as host lab) to design:
pp-collider (FCC-hh)  main emphasis, defining infrastructure requirements
80-100 km tunnel infrastructure in Geneva area, site specific
e+e- collider (FCC-ee), as a possible first step
p-e (FCC-he) option, one IP, FCC-hh & ERL
HE-LHC w FCC-hh technology
~16 T  100 TeV pp in 100 km
Future Circular Collider Study
Goal: CDR for European Strategy Update 2019/20
suggested
in 2010
HE-LHC

## Slide 7
Constr.
Physics
LEP
Construction
Physics
Proto
Design
LHC – in operation
Construction
Physics
Design
HL-LHC - ongoing project
Physics
Construction
Proto
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2035
~20 years
Design
FCC – design study
CERN Circular Colliders & FCC
2040
must advance fast now to be ready for the period 2035 – 2040
milestone: CDR by end 2018 for next update of European Strategy

## Slide 8: past, present & proposed hadron colliders

## Slide 9: peak luminosity limited by SR power & beam-beam
synchrotron radiation power / beam:
total beam-beam
tune shift
luminosity
limited
with
maximum
acceptable
luminosity formula for SR-power and
tune-shift limited hadron collider
r: bending radius
C: circumference
nb: #bunches/beam
Nb: #p/bunch
E: beam energy
rp: class. proton radius

## Slide 10: peak luminosity limited by pile up
event
pile up / Xing
luminosity
maximum
acceptable
luminosity formula for
pile-up limited hadron collider
σtot [mbarn] ≈ 42.1s -0.467-32.19 s-0.540 +35.83 +0.315 ln2(s/34); s in units of GeV2
~112 mbarn at 14 TeV, ~156 mbarn at 100 TeV
σinel [mbarn] ≈ σtot-11.7 +1.59 ln s - 0.134 ln2s
~83 mbarn at 14 TeV, ~110 mbarn at 100 TeV
shorter bunch spacing could help?!
(e.g. 25→ 5 ns would increase nb 5x!)

## Slide 11
parameter | FCC-hh |  | HE-LHC | HL-LHC | LHC
collision energy cms [TeV] | 100 |  | 27 | 14 | 14
dipole field [T] | 16 |  | 16 | 8.33 | 8.33
circumference [km] | 97.75 |  | 26.7 | 26.7 | 26.7
beam current [A] | 0.5 |  | 1.1 | 1.1 | 0.58
bunch intensity [1011] | 1 |  | 2.2 | 2.2 | 1.15
bunch spacing [ns] | 25 |  | 25 | 25 | 25
synchr. rad. power / ring [kW] | 2400 |  | 101 | 7.3 | 3.6
SR power / length [W/m/ap.] | 28.4 |  | 4.6 | 0.33 | 0.17
long. emit. damping time [h] | 0.54 |  | 1.8 | 12.9 | 12.9
beta* [m] | 1.1 | 0.3 | 0.45 | 0.15 (min.) | 0.55
normalized emittance [mm] | 2.2 |  | 2.5 | 2.5 | 3.75
peak luminosity [1034 cm-2s-1] | 5 | 30 | 16 | 5 (lev.) | 1
events/bunch crossing | 170 | 1000 | 460 | 132 | 27
stored energy/beam [GJ] | 8.4 |  | 1.3 | 0.7 | 0.36
FCC-hh collider parameters

## Slide 12
two high-luminosity experiments (A & G)
two other experiments combined with injection (L & B)
two collimation insertions
  betatron cleaning (J)
  momentum cleaning (F)
extraction insertion (D)
clean insertion with RF (H)
compatible with LHC or SPS as injector
FCC-hh layout 2017
circumference: 97.75 km

## Slide 13
phase 1: b*=1.1 m, xtot=0.01, tta=5 h, 250 fb-1 / year
phase 2: b*=0.3 m, xtot=0.03, tta=4 h, 1000 fb-1 / year
  for both phases:
  beam current 0.5 A, unchanged!
  total synchrotron radiation power ~5 MW.
radiation damping: t~1 h
FCC-hh luminosity over 24 h
PRST-AB 18,
101002 (2015)

## Slide 14
FCC-hh - 100 TeV c.m., 25 ns
burn off slower than emittance
damping → emittance control

## Slide 15
FCC-hh - 100 TeV c.m., 25 ns
in phase 2, b* 1.1→0.3 m,
without (or with less)
emittance control:
tune shift increases during fill
until reaching maximum of 0.03

## Slide 16: impact of luminosity levelling
luminosity levelling with 25 ns beam is an option
(green curve)
limited luminosity loss for 500 events per bunch crossing
maybe still acceptable at 330 events
lines show average luminosities
for closer bunch spacing
A. Langner, D. Schulte
pile up mitigations: 25 ns w luminosity levelling or closer bunch spacing

## Slide 17
Baseline:
LHC @ 3.3 TeV
Alternative:
scSPS @ 1.3 TeV
Total of O(5.5 km) superconducting bends in transfer lines from LHC, at 7.2 T
O(6.5 km) normal-conducting bends from SPS, at 1.8 T
FCC-hh injector options
Current baseline: Injection energy 3.3 TeV LHC  Field-swing FCC-hh like LHC
Alternative options: Injection from SPSupgrade around 1.3 TeV
SPSupgrade could be based on fast-cycling SC magnets, 6-7T, ~ 1T/s ramp, cf. SIS 300 design
SPSupgrade would also be an ideal injector for HE LHC (as alternative to the 450 GeV SPS)

## Slide 18
cost ~ Ecms 0.28
P. Lebrun, RFTech 2013
1959
1971
2008
cost of future accelerators
by extrapolation:
100 TeV collider
~1.8x cost of LHC?

## Slide 19
HL-LHC/FCC technology change: Nb-Ti →Nb3Sn
O. Bruning

## Slide 20
B. Strauss, data by courtesy of J. Parrell (US DOE OST)
US-CDP
ITER wires
SC wire production: Nb-Ti and Nb3Sn
HL-LHC wires

## Slide 21
FCC Nb3Sn conductor program
Nb3Sn is one of the major cost & performance factors for FCC-hh and must be given highest attention
main development goals until 2020:
Jc increase (16T, 4.2K) > 1500 A/mm2 i.e. 50% increase wrt HL-LHC wire
reference wire diameter 1 mm
potentials for large scale production and cost reduction
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 22
Main development goal is wire performance increase:
Jc (16T, 4.2K) > 1500 A/mm2 50% increase wrt HL-LHC wire
Reduced coil & magnet cross-section
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
~10% margin
FCC ultimate
5400 mm2
after only one year development, prototype Nb3Sn wires from several new industrial FCC partners (Japan, Korea, Russia) already achieve HL-LHC performance
Conductor activities for FCC started in 2017:
Bochvar Institute (production at TVEL), Russia
KEK (Jastec and Furukawa), Japan
KAT, Korea
Columbus, Italy
University of Geneva, Switzerland
Technical University of Vienna, Austria
SPIN, Italy
University of Freiberg, Germany
  In addition, agreements under preparation:
  Bruker, Germany
  Luvata Pori, Finland
worldwide FCC Nb3Sn program

## Slide 23
short model magnets (1.5 m lengths) built from 2018 – 2022
Russian 16 T magnet program launched by BINP recently
16 T dipole design activities & options
M. Benedikt

## Slide 24
All coil parts, structural components and tooling are available at FNAL
Coil fabrication and the work with mechanical structure are in progress
First magnet test in September 2018
Iron Laminations
AL I-Clamps
Fillers
Axial Rods
End Plates
StSt Skin
15 T dipole demonstrator (US MDP)
A. Zlobin

## Slide 25
Coil fabrication
Winding of the first coil has been completed. Preparation for reaction on-going. All tooling for coil production ready
First ERMC coil winding
Coil Reaction Tool
Coil Impregnation Tool
Aluminum shell
Magnet yoke
Axial rods
Dummy coils
Magnet assembly
Components and tooling ready. Dummy assembly to characterize the structure behavior on-going.
16 T ERMC construction at CERN
D. Tommasini

## Slide 26
FCC 16 T magnet R&D schedule
total duration of magnet program: ~20 years
would follow HL-LHC Nb3Sn program with long models w industry from 2023/24
M. Benedikt, L. Bottura

## Slide 27
HE-LHC is not an easy machine
push for “cheap” injection from SPS at 450 GeV
poor field quality and much larger beam than for FCC-hh
less physical aperture than for LHC,
  complicating collimation and protection at injection
limited length of straight section (LEP tunnel)
cannot apply length scaling with energy used for FCC-hh design,
  complicating collimation at top energy
magnets must be bent, while FCC-hh magnets are straight
can magnets made from Nb3Sn (brittle) be bent mechanically?
  additional complication
limited tunnel cross section
- restricted transverse size of magnet cryostats

## Slide 28
field errors limit dynamic aperture
Nb3Sn wire with 20 mm instead of 50 mm filaments
in addition must introduce artificial pinning centres
sextupole
field errors
in Nb3Sn dipole
as a function of
dipole field
3 injection
energies
(450, 900
and 1300
GeV) are
indicated
S. Izquierdo Bermudez

## Slide 29
HE-LHC integration aspects
integration and design strategy:
development of optimized 16 T magnet, compatible with HE LHC requirements
new cryogenic layout to limit QRL dimension
  LHC tunnel diameter 3.8 m
  working hypothesis for HE LHC design:
  no major CE modifications on tunnel and caverns
  similar geometry and layout as LHC machine & experiments
  maximum magnet cryostat diameter 1200 mm
  maximum QRL diameter 830 mm
V. Mertens, M. Benedikt

## Slide 30
16 T dipole evolution & HE-LHC cryogenics
Cosine-theta (baseline)
Block-type coils
Common-coils
2015 2017
800 mm 600 mm
Coil optimization and margin 18  14%
Stray-field < 0.1 T at cryostat
Half-sector cooling instead of full sector (as for LHC)
to limit cross section of cryogenic distribution line
higher heat load and integration limitations:
8 additional 1.8 K refrigeration units wrt. LHC
8 new higher-power 4.5 K cryoplants

## Slide 31
HE-LHC IR layout
triplet lengths:
LHC: 30.4 m
HL-LHC: 41. 8 m
HE-LHC: 56 m (13.5 TeV);
ca. 11 m
for crab cavities
L. van Riesen Haupt

## Slide 32
HE-LHC IR optics & triplet shielding
General optics design work ongoing for HE LHC with focus on: injection (energy), field quality, physical & dynamic aperture, protection
  collision optics
  with b*=0.25 m
l* = 23 m,
TAS 1.8 m long
(as for HL-LHC,
different radius)
rriplet quadrupole design with 2 cm inner tungsten shielding
for 10 ab-1 integral luminosity: 40 MGy peak dose (peak at Q3 can be reduced w addt’l shielding)
J. Abelleira
L. van Riesen Haupt

## Slide 33
Parameter | Unit | SPPC |  |  | FCC |  | 
 |  | PreCDR | “CDR” | “Ultimate” |  |  | 
Circumference | km | 54.4 | 100 | 100 | 100 |  | 
c.m. energy | TeV | 70.6 | 75 | 125-150 | 100 |  | 
dipole field | T | 20 | 12 | 20-24 | 16 |  | 
injection energy | TeV | 2.1 | 2.1 | 4.2 | 3.3 |  | 
#IPs |  | 2 | 2 | 2 | 2 |  | 
luminosity per IP | 1035 cm-2s-1 | 1.2 | 1.0 | - | 0.5 |  | 3.0
norm. emittance | mm | 4.1 | 2.4 | ? | 2.2 (0.44) |  | 
IP beta function | m | 0.75 | 0.75 | - | 1.1 |  | 0.3
beam current | A | 1.0 | 0.7 | - | 0.5 |  | 
bunch separation | ns | 25 | 25 | - | 25 (5) | 25 (5) | 
bunch population | 1011 | 2.0 | 1.5 | - | 1.0 (0.2) | 1.0 (0.2 | 
SR power /beam | MW | 2.1 | 1.1 | - | 2.5 |  | 
SR heat load/ap | W/m | 45 | 13 | - | 30 |  | 
SPPC main parameters
J. Tang

## Slide 34
SppC layout 2017
coexistence ee, pp, ep
two high-luminosity pp experiments
two other experiments for AA & ep
one (combined) collimation insertion
one RF insertion
extraction insertion
injection insertion
greenfield injector chain
circumference: 100 km
J. Gao
J. Gao, X. Lou, J. Tang

## Slide 35
p-Linac: proton superconducting linac
p-RCS: proton rapid cycling synchrotron
MSS: Medium-Stage Synchrotron
SS: Super Synchrotron
ion beams: dedicated linac (I-Linac) and RCS (I-RCS)
SppC injector chain
J. Gao

## Slide 36
Chinese 10-year R&D target
for SPPC collider
SppC: wire from Fe-based HTS*
*discovered at TIT/Japan in 2008

## Slide 37
In October 2016, A consortium for High-temperature superconducting materials, industrialization and applications was formed in China, with participation of major research and production institutions on HTS.
China is actually leading the development of Fe-HTS technology in the world; world-first 100-m Fe-HTS wire was made by CAS-Institute of Electrical Engineering in the last year .
SppC: China-Domestic Collaboration on HTS
J. Gao,
J. Tang,
Q. Xu

## Slide 38
SppC Design of 12-T Fe-based Dipole Magnet
Yoke OD
500mm
Table 1: Main parameters of the cables
Table 2: Main parameters of the strand
Cable | Hight | Width-i | Width-o | Ns | Strand | Filament | Insulation
IRONBASED1 | 8 | 1.5 | 1.5 | 20 | IRON-BASED | FE-BASED | 0.15
IRONBASED2 | 5.6 | 1.5 | 1.5 | 14 | IRON-BASED | FE-BASED | 0.15
IRONBASED3 | 5 | 1.5 | 1.5 | 12 | IRON-BASED | FE-BASED | 0.15
Strand | diam. | cu/sc | RRR | Tref | Bref | Jc@ BrTr | dJc/dB
IRON-BASED | 0.802 | 1 | 200 | 4.2 | 10 | 4000 | 111
One meter of such magnet requires iron-based HTS strand length of 6.08 km
C. Wang, E. Kong (USTC), Q. Xu et al.

## Slide 39
FCC-hh cryogenic beam vacuum system
FCC-hh beam-screen test set-up at ANKA/Germany:
beam tests since June 2017, for prototypes,
confirming vacuum design simulations
X-ray fan
2.5 GeV ANKA/KIT storage ring
synchrotron radiation (~ 30 W/m/beam (@16 T field) (cf. LHC <0.2W/m) ~ 5 MW total load in arcs
absorption of synchrotron radiation at higher temperature (> 1.8 K) for cryogenic efficiency
provision of beam vacuum, suppression of photo-electrons, electron cloud effect, impedance, etc.
ANKA e- photon spectrum
= FCC –hh spectrum

## Slide 40
FCC-hh cryoplants – energy efficiency
BS temperature choice through overall optimisation:
cryoplant power consumption
vacuum system performance
impedance and beam stability
100MW
200MW
300MW
optimum beam screen operation temperature 40 - 60 K
electrical power for beam screen cooling ~100 MW .
L. Tavian, P. Lebrun

## Slide 41
FCC implementation - footprint baseline
present baseline position established considering:
lowest risk for construction
fastest and cheapest construction
feasible positions for large span caverns (most challenging structures)
next step: review of surface site locations and machine layout
J. Osborne, J. Stanyard

## Slide 42
1)
2)
3)
4
1
2
3
4
5
6
CEPC Site Selections
1) Qinhuangdao, Hebei Province（Completed in 2014）
2) Huangling, Shanxi Province（Completed in 2017)
3) Shenshan, Guangdong Province(Completed in 2016)
4) Baoding (Xiong an), Hebei Province (Started in August 2017)
5) Huzhou, Zhejiang Province (Started in March 2018)
6) Chuangchun, Jilin Province (Started in May 2018)
J. Gao

## Slide 43
Item | Huangling | Shenshan | Funing
Project layout |  |  | 
Construction difficulty | Moderate | Relatively difficult | Relatively easy
Funing (100 km)
Huangling (100 km)
Shenshan (100 km)
X. Lou
Notes: Huangling: The site is mainly on the loess plateau. The buried depth of the tunnel and the depth of the shafts are quite different. The construction access layout is relatively simple.
Shen-Shan: The site is mainly the low mountain area. The buried depth of the tunnel and the depth of the shafts are large, and the construction access layout is relatively complicated.
Funing: The site is generally the low hilly areas; underground burial depth is not big; the construction site conditions are better; the construction access layout is relatively simple.

## Slide 44
FCC – tunnel integration in arcs
  FCC-ee FCC-hh
  5.5 m inner diameter
V. Mertens

## Slide 45
  6.0 m width, hosting 5 rings simulatenously
CEPC/SppC – tunnel integration in arcs
J. Gao

## Slide 46
4.5yrs
6.5yrs
Total construction duration 7 years
First sectors ready after 4.5 years
CE schedule studies

## Slide 47
schedule constrained by 16 T magnets & CE
→ earliest possible beam operation dates
FCC-ee: 2039
FCC-hh: 2043
HE-LHC: 2040 (with HL-LHC stop LS5 / 2034)
technical schedule for each of three options

## Slide 48
Global FCC Collaboration
30
Companies
32
Countries
124
Institutes
EC
H2020
  from Italy
  CNR-SPIN, Genoa
  CSIL, Milan
  INFN, Frascati (Roma)
  Sapienza, Rome
  UNICAL, Arcavacata di Rende
  UNIGEOA, Genova
  UNIMI, Milan
  UNIROMA3, Roma

## Slide 49
Scope:
FCC-hh collider
Optics Design (arc and IR)
Cryogenic beam vacuum system design including beam tests at ANKA
16 T dipole design, construction folder for demonstrator magnets
EU H2020 Design Study EuroCirCol
European Union Horizon 2020 program
Support for FCC-hh study
3 MEURO co-funding
Started June 2015, ends in May 2019
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 50
SC wires at low temperatures for magnets (Nb3Sn, MgB2, HTS)
Superconducting thin films for RF and beam screen (Nb3Sn, Tl)
Electrohydraulic forming for RF structures
Turbocompressor for Nelium refrigeration
Magnet cooling architectures
13 Beneficiaries
12 Partners
EASITrain Marie Curie Training Network
I-CUBE
European Advanced Superconductivity Innovation and Training Network
selected for funding by EC in May 2017, started 1 October 2017
Horizon 2020 program
Funding for 15 Early Stage Researchers over 3 years & training
J. Gutleber

## Slide 51
FCC Planning – CDR Production
CDR Concise summary volumes 1 (PH), 2 (hh), 4 (ee), 6 (HE):
  Completion of design work, coherent and consistent; contents for concise volumes by end June 2018
  Overall final editing July – August 2018; Proof reading and approval September – October
  “Print-ready” versions by November 2018
CDR long technical volumes 3, 5, 7:
  Collection of input (from status June 2018) during July – October 2018.
  Overall volume editing November 2018 – January 2019; Proof reading and approval February – March 2019
Cost study based on CDR status (June 2018), other documents for ESU, June - November 2018
M. Benedikt

## Slide 52: CEPC Accelerator from Pre-CDR to CDR
CEPC accelerator CDR completed in June 2018 (released on Spet. 2 2018)
  Executive Summary
  Introduction
  Machine Layout and Performance
  Operation Scenarios
  CEPC Collider
  CEPC Booster
  CEPC Linac
  Systems Common to the CEPC Linac, Booster
  and Collider
  8. Super Proton Proton Collider
  9. Conventional Facilities
  10. Environment, Health and Safety
  11. R&D Program
  12. Project Plan, Cost and Schedule
  Appendix 1: CEPC Parameter List
  Appendix 2: CEPC Technical Component List
  Appendix 3: CEPC Electric Power Requirement
  Appendix 4: Advanced Partial Double Ring
  Appendix 5: CEPC Injector Based on Plasma Wakefield Accelerator
  Appendix 6: Operation as a High Intensity -ray Source
  Appendix 7: Operation for e-p, e-A and Heavy Ion Collision
  Appendix 8: Opportunities for Polarization in the CEPC
  Appendix 9: International Review Report
March 2015
April 2017
Draft CDR for
Mini International
Review in Nov. 2017
CDR International Reviewed June 28-30, 2018, final CDR (accelerator) released on Sept. 2, 2018
J. Gao

## Slide 53
a few conclusions
FCC study develops high-performance energy frontier circular colliders for post-LHC era – input to ESU’19/20
parallel effort in China (CEPC/SppC) – Chinese decision could come within 2 to 5 years
worldwide R&D programs on key technologies: Nb3Sn superconductor, high-field magnets, highly-efficient SC RF
international FCC collaboration growing steadily, many R&D opportunities; all of the community invited to join
FCC concept supports attractive staged long-term strategy for particle physics: FCC-ee → FCC-hh → FCC-mm
highest-luminosity collisions up to very high energies; collider program extending well into the 22nd century

## Slide 54
Brussels
24-28 June, 2019
EuroCirCol Final Meeting
& FCC Week 2019
https://indico.cern.ch/event/727555

## Slide 55
appendix: path to FCC-mm

## Slide 56
how to go further – beyond FCC-hh?
muon collider* is back !
3 recent new ideas :
LEMMA m production by e+ annihilation
Gamma factory for e+ generation
full exploitation of FCC complex
*first proposed by Gersh Budker in 1969

## Slide 57
LHeC-class e+ source & e+ acceleration at 45 GeV
(circular/linear options)
e+ ring
100 KW target
m+
m-
isochronous rings
Positron Beam
key challenges
~1011 m / sec from e+e-gm+m-
key
R&D
1015 e+/sec, 100 kW class target, NON destructive process in e+ ring
key challenges
~1013-1014 m / sec
tertiary particle pgpgm:
fast cooling
(t=2ms)
by 106 (6D)
fast acceleration
mitigating m decay
background
from m decay
from US-MAP (2015) to LEMMA scheme (2017)
M. Antonelli, M. Boscolo, P. Raimondi et al.

## Slide 58
high photon energies,
high cross section
W. Krasny
FCC based Gamma Factory could provide >1017 e+/s
“Gamma Factory” based on “PSI”
Compton back scattering at LHC or FCC

## Slide 59
g factory proof-of-principle experiment in the LHC
Pb+81 beam lifetime 38 hours
(and first electrons in the LHC…)
“… this was a HUGE deal! One of the main scientiﬁc advances in the whole of physics this year!”
Dima Budker

## Slide 60
Cost-figure-of-merit versus power-figure-of-merit for future lepton colliders (Jean-Pierre Delahaye)
cost & power efficiency of future lepton colliders

## Slide 61
100 TeV m collider in C=100 km FCC tunnel with B=16 T → L>1034 cm-2s-1
Combining Gamma Factory, LEMMA,
FCC-ee and FCC-hh